## Slide 1: beyond 5g ai-Enabled Security and Resilience (BASIL) framework
3GPP TSG SA2 #160 Ad Hoc e-meeting
January 22 – 29, 2024
Agenda Item: 19.15
TDOC#: S2-2400100
For: Discussion
Source: Dell Technologies, Defense Information Systems Agency EM, The MITRE Corporation
TSG SA2 #160 Ad Hoc e-meeting
January 22 – 29, 2024
S2-2400100

## Slide 2: What are the issues within 5G “Security”?
Today’s 5G security network faces a critical challenge with the absence of a robust threat detection mechanism.
Many security threats and vulnerabilities are detected through manual detection process or primitive ML schemes which are not only resource-intensive but also deficient in accuracy.
It also needs extensive personnel training and expertise to be able to catch up with the rapidly evolving threat landscape, making network vulnerable to sophisticated attacks.
To address this gap, there is a need to equip AI-enabled threat detection and active mitigation framework on top of 5G capabilities. Hence, the BASIL framework.

## Slide 3: Beyond 5G AI-Enabled Security and Resilience (BASIL) Framework
BASIL envisions an AI-enabled threat detection and active mitigation framework on top of 5G capabilities such as network automation (ENA) architecture and Network Data Analytics Function (NWDAF). BASIL leverages existing industry 5G threat vectors databases.
BASIL focuses on utilizing comprehensively trained AI/ML models to detect and predict the threats with high precision.
BASIL aims to conform to protocols of 3GPP standards to provide additional capabilities in threat detection, classification and mitigation as well as resilience.

## Slide 4: Current NWDAF Capabilities (R-18 TS 23.288*)
Data Analytics: NWDAF standardizes network analytics data to be collected in real-time. The data can be leveraged by network functions (NFs) and Operation, Administration, and Maintenance (OAM) as analytics consumers to support network performance optimization, service orchestration, and service quality enhancement. See slide 6 for the data that can be collected.
Architecture and Design: It outlines the architectural design of NWDAF and how it interfaces with other network components.
Data Collection and Processing: It collects a wide range of network data, processes, and analyzes it to provide insights for network optimization.
Interaction with Network Functions: It defines interactions and data exchange protocols with other NFs.
AI/ML Integration: It integrates AI/ML algorithms for network performance optimization and service quality enhancement.
*”Architecture enhancements for 5G System (5GS) to support network data analytics services”

## Slide 5: Current NWDAF Capabilities (R-18 TS 29.520*)
Defines the services (e.g., subscribe or request) offered by NWDAF as well as their corresponding application programming interfaces (APIs) to provide analytics information and ML models.
*”5G System; Network Data Analytics Services; Stage 3”

## Slide 6: Current NWDAF Capabilities (R-18 TS 29.520*) (Cont’d)
Analytics Information that can be collected:
  Load level information of network slice instance
  Service experience (per application, per UE or per slice)
  NF load for a specific NF or a list of NFs (to support future load prediction)
  Network performance
  Expected behaviour information for a group of UEs or a specific UE
  Abnormal behaviour information for a group of UEs or a specific UE including unexpected UE location; unexpected long-live/large rate flows; unexpected wakeup; suspicion of distributed denial of service (DDoS) attack; too frequent service access; unexpected radio link failures; and ping-ponging across neighboring cells
  Mobility related information for a group of UEs or a specific UE
  Communication pattern for a group of UEs or a specific UE (to support mobility management, traffic routing, or QoS improvement)
  Congestion information of user data in a specific location
  QoS sustainability (for a certain area and time period, reports QoS change statistics or predicts the likelihood of a QoS change)

## Slide 7: Gap Analysis of NWDAF
Focus on Threat Detection: While NWDAF provides events, data and metrics to support data analytics for network optimization, there is a potential gap in its focus on threat detection and security-specific analytics.
Specialized Data Handling for Threat Detection: While NWDAF handles a variety of network data, it may require enhancements in securely managing data related to threats and intelligence.
Dynamic Threat Mitigation: NWDAF’s architecture may not currently support dynamic network adjustments as mitigation in real-time in response to threats.
Threat Detection Specific AI/ML Models: There is likely a gap in NWDAF's existing AI/ML models, which may be more oriented towards performance optimization than threat detection.
Extended Capability: Compared to NWDAF only addressing the 5GC, BASIL has extended capability for all stratums of the network, including Radio Access Networks (RANs).
Enhanced Resilience: NWDAF did not mention resilience while BASIL also provides mechanisms to enhance resilience for both 5GC and RAN autonomously.

## Slide 8: Next Steps
Plan to submit contributions for the gaps identified as part of key issues in R-19 SID “Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML)”.