## Slide 1: Discussion on Network Controlled Slice Selection
KDDI CORPORATION

## Slide 2: Summary
Network Slicing was standardized since Rel-15. From operators’ perspective, it is required to improve the customer experience by providing the optimal network slice in accordance with the characteristics of the applications on the UE.
The URSP rules are defined and the UE can use them to determine the slice for the PDU Session when the UE requests a PDU Session for an application. Whether and how to support URSP rule is left to UE implementation. Thus, the operators are constrained in providing network slices that are most suitable for the applications.
Thus, it is beneficial for operators to have an option to select the network slice triggered by a notification from the Application Function.
Proposal
Slice switching request from AF via NEF
・Define new NEF API
・Re-use PDU session modification procedure of slice replacement in Rel-18

## Slide 3
Slice #1
(Default)
RAN
AMF
SMF
PCF
UPF
UE
Background
AF
Slice #2
(eMBB)
RAN
AMF
SMF
PCF
UPF
・Application on UE
(AF and UE are pre-negotiated)
・The user‘s environmental information.
(congestion, radio coverage)
Slice switch request for existing PDU session
PDU session
Normal
High
quality
Operators want to provide the optimal network slice according to the characteristics of the application and the user's environmental information.

## Slide 4: Proposal
Slice #1
(Default)
Data NW
RAN
RAN
Slice #2
(eMBB)
NEF
API for slice selection
RAN
Application
Server
UPF
NRF
AMF
PCF
NRF
AMF
SMF
PCF
UPF
SMF
Switch to Slice #2
①
②
③
④
⑤
⑥
⑥
⑦
Call flow assumption for the implementation of proposed feature
The user activates the application on the UE.
The application negotiates with the application server via the default slice.
The application server requests to switch the specific session from the default slice to the other slice (eMBB slice in this example) via NEF, based on the business agreement with the operator.
NEF requests PCF to switch the session.
PCF requests AMF a slice replacement w/ alternative S-NSSAI determination. This procedure is based on the verification of the subscription of the user.
AMF executes a PDU session modification w/ alternative S-NSSAI determination procedure.
A PDU session is established then UL/DL data is transferred via the PDU session.
Slice switching request from AF via NEF
  Define new NEF API providing slice related information
  Re-use PDU session modification procedure of slice replacement in Rel-18

## Slide 5: Proposal Assumptions
Slice #1
(Default)
RAN
AMF
SMF
PCF
UPF
UE
AF
Slice #2
(eMBB)
RAN
AMF
SMF
PCF
UPF
Normal
High
quality
AF aware of Application status
AF knows Alternative S-NSSAI
which the operator provides
AF and UE are pre-negotiated. AF can aware of application status on the UE.
AF is authenticated by the operator. The operator provides alternative S-NSSAI to AF in advance.
(Out of 3GPP scope)

## Slide 6: DRAFT solution

## Slide 7: Alternative S-NSSAI in AF request
AF
NEF
PCF
UE
step1.Nnef_new API service
UE identification
AF ID
Source S-NSSAI
Alternative S-NSSAI
Step 0. Negotiation between AF and UE
AMF
Step4.
UE identification
Source S-NSSAI
Alternative S-NSSAI
PDU session transfer procedure (AMF trigger)
TS23.502 4.3.3.2 UE or network requested PDU Session Modification (non-roaming and roaming with local breakout)
■Detailed procedure
0, Negotiation between AF and UE.
UE sends UE identification(UE IP&DNN&S-NSSAI, UE ID) to AF.
1, AF sends a source S-NSSAI and an alternative S-NSSAI with
UE identification and AF ID to NEF.
・ UE identification
pattern a, UE ID
pattern b, UE IP address & DNN & S-NSSAI
2, NEF→PCF NEF transfers step1 message to PCF.
3, PCF checks if the session can be moved from
the source slice to the alternative slice.
4, PCF notifies AMF of the alternative S-NSSAI
5, AMF determines whether to replace the alternative S-NSSAI.
6-8, AMF, PCF and NEF reply to AF whether the session can be
moved or not.
Then, step1h of “UE or network requested PDU Session Modification (non-roaming and roaming with local breakout)” is excuted.
Step2.Npcf_new API service
UE identification
Source S-NSSAI
Alternative S-NSSAI
Step3. PCF checks
・Whether UE has a session for the source S-NSSAI.
・Whether alternative slice is available
Step5. AMF determines
・Whether a session can be moved.
Step6,7,8. response
whether the session can be moved or not.

## Slide 8: Appendix

## Slide 9: Appendix①
■Update URSP triggered by AF
■This proposal
Slice #1
(Default)
New
URSP
rule
②UE configuration Update procedure
③UE needs to request New PDU session
Slice #1
(Default)
UE doesn’t need to request new PDU session
We can apply SSC mode 3 to the PDU session
①AF requests to PCF via NEF
②PDU session modification procedure
①AF requests to update URSP
Slice #1
(Default)
New
URSP
rule
AF
AF
Slice #1
(Default)
Slice #2
(eMBB)
Slice #1
(Default)
Slice #2
(eMBB)
New request
SSC mode 3 is available
This proposal allows simpler and more convenience slice switching compared to URSP.

## Slide 10: Appendix②
Commercial usecase
Transfer a PDU session using the default slice to the high priority slice with ticket/time billing
  Trigger a slice switching to make the user more comfortable with the game app