## Slide 1: Subscription control for reference time distribution in EPS
Qualcomm Incorporated, Vodafone
S2-2400833

## Slide 2: Background
Timing as a service refers to providing timing information to UEs as a monetizable operator service.
Rel-18 enabled timing as a service for NR by introducing subscription control for timing distribution to individual UEs. This enables operators to control whether timing information is to be delivered to a particular UE.

## Slide 3: Motivation
Timing as a service is only supported for NR.
This is an issue since NR coverage is still quite limited and may not be available in many areas for quite some time.
As a result, operators cannot offer timing as a service nation-wide but only in areas where NR connected to 5GC has been deployed.
This limits business opportunities for operators.

## Slide 4: Motivation
WB-EUTRA RRC already supports delivering reference time to individual UEs (see TS 36.331 clause 6.2.2).
  As a result, this WID does not have any RRC impacts.
The eNB however does not know whether a particular UE is subscribed for receiving timing information.
Therefore, this WID focuses on
  extending the EPS Subscription with an indication that the UE is subscribed for reference time delivery;
  based on this, the MME to indicate to the eNB to distribute reference time to the UE;
  and finally, based upon this indication from the MME, the eNB to deliver reference time to the UE.

## Slide 5: Objectives
WT-1: Enable reference time distribution based on subscription for WB-EUTRA
  EPS Subscription enhancement: Indication whether UE is subscribed for reference time delivery
  Based on subscription indication for reference time distribution, MME to indicate to eNB to distribute reference time to the UE
  eNB to deliver reference time to a UE based on the indication from MME

## Slide 6: RAN impacts
RAN2: No impact since WB-EUTRA RRC already supports delivering reference time to individual UEs (see TS 36.331 clause 6.2.2).
RAN3: Only impact is a new Time Distribution indication in S1AP and X2AP to request the eNB to provide reference time to a UE.