## Slide 1: How to progress the work on FS_5G_ProSe_Ph3
Intel

## Slide 2: Enhancements to IP address/prefix allocation (1/2)
TS 23.304 clause 5.5.1.1 defines IP address/prefix allocation on the local link between Relay UE and End UE as follows:
DHCP-based IPv4 address allocation with one of the two UEs acting as a DHCP server.
IPv6 Stateless Address auto configuration specified in RFC 4862 for assignment of IPv6 prefix, with one of the two UEs acting as IPv6 default router.
NOTE: Which UE acts as a DHCPv4 server or IPv6 default router is negotiated during secure layer-2 link establishment by exchanging the IP Address Configuration as described in clause 6.4.3.
Once the IP address/prefix allocation is complete, the source End UE can send user plane packets to the target End UE by using the IP address/prefix of the target End UE as Destination IP address
IP addresses in a single-hop UE-to-UE Relay

## Slide 3: Enhancements to IP address/prefix allocation (2/2)
In contrast, with multi-hop Relay there is a need for allocation of IP address/prefix on multiple interfaces
It is FFS whether the IP address/prefix allocation can be done across the ad hoc network without some sort of inter-relay coordination, especially if diverse multi-hop topologies (e.g. full mesh, partial mesh, linear, hierarchical, etc) need to be supported
IP addresses in a multi-hop UE-to-UE Relay

## Slide 4: IP routing functionality
Once the IP address/prefix allocation is complete, the ad hoc network needs to make routing decisions because the target UE can potentially be reached via multiple paths.
  There is a need for IP routing functionality
The IP routing functionality in wireless and mobile environment can be a complex task due to frequent changes of the link state of the link between a pair of neighbouring relays
IP routing for multi-hop UE-to-UE Relay

## Slide 5: Recommendation
Given that…
  The specification of IP routing functionality for ad hoc mobile network can be a complex task
  SA2 time budget for FS_5G_ProSe_Ph3 is very limited (only 2 TUs for the study part)
  The IP routing functionality falls in the application domain and therefore corresponds to SA6 WG’s remit
… it is proposed to:
  Limit the scope of the SA2 WG study on the “lower layer” aspects, such as IP address/prefix allocation
  Delegate the work on the IP routing functionality to the SA6 WG