## Slide 1: Rel-19 Discussion on enhancements to traffic management/monitoring for TCP/UDP traffic in a PDU session
S2-2312091
3GPP SA2#160
Agenda Item : 30.1
SK Telecom

## Slide 2
Background
In 5GS, it is possible to create new PDU sessions or QoS flows based on the type of device or service. However, millions of applications such as SNS, music, web-browser which is registered in App Store are usually provided in a single PDU Session/QoS Flow
Various methods (e.g., Sponsored Id, Reflective QoS, Network Slice, URSP) have been introduced to distinguish applications. However, accurately distinguishing the usage patterns of the UE or adapting to real-time changes in the Application Server IP in a PDU session/Qos flow can be challenging.
S2-2312091

## Slide 3
Use Case / Requirement
[Use Case#1] The 5G Core should be able to distinguish services based on the access method, even when receiving the same service over the Data Network. (ex. Personal Assistant Application request 3rd party service. It should be able to distinguish to connect service directly)
Data
Network
① connect service-a via Application
App.
5G Core should distinguish ① and ②
for different policy and charging
②connect service-a directly
service-a.com
service-a.com
[Use Case#2] When different applications share the same destination server, 5G Core should be possible to distinguish the services. (ex. different application use same cache server or 3rd party API such as advertisement banner)
Data
Network
① 3rd party service in App#1
App #1
5G Core should distinguish ① and ②
for different policy and charging
3rd-party-service.com
3rd-party-service.com
App #2
② 3rd party service in App#2
[Requirement #1] Operator want to distinguish services(same QoS service such as internet) without allocating new PDU Session which is costly.
[Requirement #2] The operator wants to be aware of service IPs that change in real-time such as cloud environment without AF interworking.
S2-2312091

## Slide 4
Proposal(add new Work-Task)
WT-4 : Traffic management and monitoring enhancement for TCP/UDP traffic in a PDU session and QoS flow
  WT-4a : Study that 5GC distinguish TCP/UDP traffic based on the access method(directly or via other application) for traffic management and monitoring, even when receiving the same service over data network.
  WT-4b : Study that 5GC should be possible to know which application the traffic is coming from, when different applications share the same destination server(e.g, cache server, advertisement server).
  WT-4c : Study how 5GC detect changes of service IP within the Data Network without AF interworking.
S2-2312091
Rel-19 study on Enhanced Traffic Management (FS_ETM)