## Slide 1: Discussion on Dual Steer for TN + TN Scenario
China Telecom, KDDI, vivo, Broadcom, Rakuten, OPPO

## Slide 2: Scenario 1
A live network may have poor signal at the edge of 5G cells, especially at suburb areas, while the 4G cells have good signal and continuous coverage. The 4G fills up the gaps between neighboring 5G coverage.
When UE moves in areas where 5G cells has unsatisfying performance at the edge:
  UE needs to handover between EPS and 5GS, or lost radio resource connection (if not hand over to EPS), while moving in the 5G discontinuous area, resulting in service interruption for SA 5GC.
  By utilizing the radio resource from one 4G cell plus one 5G cell, or two 5G cells at the same time, e.g., throughput might be raised.
OBSERVATION 1: TN+TN DualSteer helps to improve the performance at 5G cell margin.

## Slide 3: Scenario 2
There are operators with 4G-only network and share the 5G network with other operators with business agreement.
  For specific high demand services, e.g., XR, need 5G capability, UE needs to handover to the visited 5G network.At the same time, all other traffic does not need 5G capability, uses the visited 5G network as well. (Fig.1)
  Dual steer could help to identify hight demand services require 5G capablity and steer the traffic to the right path simutaleously.(Fig.2)
OBSERVATION 2: DualSteer reduces the cost of the home network and preserves the resource of the visited network .
Home 4G Network
Visted 5G Network
Specific Services, e.g., XR
Common Services, e.g., voice, SMS.
Home 4G Network
Visted 5G Network
Specific Services, e.g., XR
Common Services, e.g., voice, SMS.
Fig.1 All traffic uses the Visited Network
Fig.2 Specific traffic uses the Visited Network

## Slide 4: Dual Steer Compare to NR-NR CA and EN-DC
 | NR-NR CA EN-DC | TN-TN Proposed by DualSteer
Inter-RAN activities | Strong dependency on X2/Xn interface No LTE+5G CA | not needed*
Traffic aggregation point | The main RAN node (high requirement on RAN). | UPF or AF*
Traffic direction decision | By the main RAN node, on radio condition and QFI-based only. | By 5GC, on more reference conditions and AI method*, e.g., Application-based, NWDAF outputs, etc.
Differentiated charging | Unable to distinguish the RAN path as charging criteria | Able to apply Different charging rules over different paths*
Additional traffic in the Datacom and traffic detour | Additional traffic on datacom network UL Traffic goes through from the secondary RAN node needs to be sent to the convergence node, e.g., a router, then to the main node, aggregating by the main node, then again send to the 5GC. DL Traffic has similar detour. | No additional traffic for datacom network or traffic detour
Examples of the use cases
NR+LTE, Intra PLMN (TR 22.841)
NR+NR, Intra PLMN
*Subjected to the conclusion of SID
RAN1 and RAN2 might be connect to different AMFs and UPFs
  OBSERVATION 3: TN+TN DualSteer overcomes some of the drawbacks of the existing NR-NR CA/EN-DC.

## Slide 5: Proposal
It is proposed to investigate how to support UE’s access via NR+LTE or NR+ NR simultaneously and non-simultaneously with single subscription to improve user experience and increase operator benefits.
Considering the TU limits, in R19, the TN + TN scenario of intra-PLMN/inter-PLMN in steering and switching could be prioritized as well as of the NTN+TN/NTN scenarios.