## Slide 1: Discussion for Rel-20 Topics on 5G Integration with Industrial Communication
Ling Zhang
Siemens

## Slide 2: Background
Continued enhancements on 5G System are expected to better support manufacturing and digital transformation.
References for the selected requirements
  5G-ACIA
    5G-ACIA work has been looking into 5G as a logical bridge recently
    Integration of 5G with Time-Sensitive Networking for Industrial Communications (link)
    Integration of Industrial Ethernet Networks with 5G Networks (link)
  3GPP
    TS 22.104 - Service requirements for cyber-physical control applications in vertical domains

## Slide 3: 5GS as Logical Bridge in Industrial Ethernet
Further architectural and functional enhancements supporting 5GS as logical bridge
Enhancements of 5GS as logical bridge so that it can react to Ethernet/virtual network/IEEE 802.1 protocols and dynamic events (e.g. handling of multicast/broadcast addresses, support for LLDPv2/LRP/RAP, support of Virtual Networks)
Support interoperable bridged time-sensitive networks profiled by IEC/IEEE 60802
  How to translate IEC/IEEE 60802 TSN configurations to the TSN-related configurations within 5GS
  How 5GS is enhanced for features, options, configurations, defaults, protocols, and procedures of bridges profiled by IEC/IEEE 60802
Support Multiple Spanning Tree Protocol (MSTP)
  Evaluate the topologies or architectures that create a loop
  Evaluate the architectures (enhancements) that support MSTP operations (e.g. BPDU forwarding)
  How 5GS is configured for MSTP communication between the 5GS logical bridge and IEEE 802.1Q bridge

## Slide 4: Features required by TS 22.104 Cyber-physical Control Applications in Vertical domains
Enhancements for supporting Traffic model/patterns in more general scenarios as factories, process automation, human-machine interfaces and production IT, logistics and warehousing, and monitoring and maintenance
  Setup of the Deterministic (a)periodic traffic, Non-deterministic traffic and burst traffic, Mixed traffic
  Network exposure enhancements
Coexistence of eight traffic classes (e.g. Hard-RT or isochronous traffic following a time-aware schedule) and lower priority traffic (e.g. Alarms and Events), when integrated with/support with high performance Ethernet applications
  Translation of the eight traffic classes (as in IEC/IEEE 60802)
  End-to-end QoS characteristics support
Direct device connection for 5G LAN-type private communication

## Slide 5: Integrated End-to-end Capabilities for Industrial Scenarios
Enhancements for E2E service continuity for time-sensitive / deterministic communication in handover, traffic steering/aggregation operations
Enhancements of service reliability, service availability, latency, latency jitter and network exposure when integrating the 5G capabilities for time-sensitive / deterministic communication in the (integrated / combined) deployments of:
  Network slicing
  Non-public network
  MEC / Edge computing