## Slide 1: PGW handling of UE Init Procedures in 2G/3G and LTE ***DRAFT*** Nokia Siemens Networks

## Slide 2: UE-init procedures in EPS
In LTE,
  The decision for bearer binding is completely with the BBF.
    For new flows, UE signals QOS and flows in TAD. The BBF decides to map the flows to an existing bearer or create a new bearer.
    For modification of already existing flows, the UE identifies the bearer on which the flow is admitted and sends modification request.
  Multiple IP-flows (UE-init and PGW-init) may get mapped to a bearer.
In 2G/3G with MS-only mode:
  Bearer-binding is fully controlled by UE.
    For new flows, the UE signals the bearer onto which the flow is mapped along with QoS of the bearer.
In 2G/3G with MS/NW mode:
  Bearer-binding is “split” between UE and NW (BBF).
    For UE-init new flows, the UE can decide that a new bearer should be allocated and signal this in the setup message (“UE-init secondary PDP context creation”), or can decide to add the new flow to an existing bearer (“UE-init PDP context modification”).
  NW(BBF) can add (multiple) NW-init SDFs to any (UE-init or NW-init) bearer.

## Slide 3: UE Init Procedures in LTE

## Slide 4: Overview
At the NAS level there are two separate procedures:
  UE requested bearer resource allocation procedure
  UE requested bearer resource modification procedure
On the S11 and S5 interface there is only a single command (GTPc-v2)
  Bearer Resource Command

## Slide 5: UE-initiated resource (SDF) request/modification in LTE
 | UE-initiated resource request use case | NAS Signalling | S11/S5 Signaling | Notes | Gx Related behavior
1 | Create initial reservation for IP-flows (SDF filters, Qos Info) | BEARER RESOURCE ALLOCATION REQUEST No bearer identity, LBI, QCI, GBR (only for GBR request) TFT (TFT_operation = “Create a new TFT”, filter, no filter ID, precedence) | BEARER RESOURCE COMMAND No bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message |  | 
2 | Add SDF filters to existing bearer and increase QoS (only GBR), no change in QCI (all flows must belong to the same bearer) | Not allowed |  | The UE should use the “Resource allocation for new IP flow” procedure, even if there is already a bearer with the QCI corresponding to the new flow that the UE wants to add. | 
3 | Remove some filters from an existing IP-flow reservation and decrease QoS (only GBR), no change in QCI | BEARER RESOURCE MODIFICATION REQUEST Bearer identity, LBI New QoS (GBR) of the EPS Bearer (GBR only) TFT (TFT_operation = “delete pkt filters from existing TFT”, filter ID, no precedence) | BEARER RESOURCE COMMAND Bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message | Enough to include Filter Id, i.e. filter content and precedence not needed. The deleted PF ID enable BBF to identify which QoS rule to request modification from PCRF. | 
4 | Increase/Decrease of QoS related to IP-flow(s) (no QCI change0 | BEARER RESOURCE MODIFICATION REQUEST Bearer identity, LBI New QoS (GBR) of the EPS Bearer (GBR only) TFT (TFT_operation = “No Operation”, Filter ID(s) of IP-flow(s) in parameter list) | BEARER RESOURCE COMMAND Bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message | The filter-IDs are not in the filter list but in the parameters list. The filter IDs in the parameter list enable BBF to identify the QoS rule to request modification from PCRF. | 
6 | Change QCI of IP-flows | Not allowed |  | Not allowed to change QCI. The UE should delete the resource allocation and then request a new one. | 
7 | Add one or more filters to an existing SDF with or without change in QoS (no QCI change) | BEARER RESOURCE MODIFICATION REQUEST Bearer identity, LBI, New QoS (GBR) of the EPS Bearer (GBR only) (not included for non-GBR flow) TFT (TFT_operation = “Add packet filters to existing TFT”, new pkt filters, Filter ID(s) of existing linked SDF in parameter list) | BEARER RESOURCE COMMAND Bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message |  | 
8 | Replace one or more filters in an IP-flows with new one(s) with or without change in QoS (no QCI change) | BEARER RESOURCE MODIFICATION REQUEST Bearer identity, LBI New QoS (GBR) of the EPS Bearer (GBR only) TFT (TFT_operation = “replace pkt filters in existing TFT”, list of filter(s) which will form the TFT, filter ID (for existing filters, no IDs for new filters, precedence) | BEARER RESOURCE COMMAND Bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message | The filter list will not contain the filters that are being replaced. The missing filters enable the BBF/PCRF to figure out which SDF is being modified and request the update of the appropriate QoS rule with PCRF. | 
9 | Increase/Decrease of QoS of a bearer, TFT filters not specified | Not allowed |  | Filter IDs must be listed so PCC can authorize the QoS change. | 
10 | Deletion of an IP-flow reservation with decrease in QoS | BEARER RESOURCE MODIFICATION REQUEST Bearer identity, LBI New QoS GBR) of the EPS Bearer (GBR only) TFT (TFT operation = “delete pkt filters from existing TFT”, list of filters IDs to delete) | BEARER RESOURCE COMMAND Bearer identity, LBI, QCI, GBR (only for GBR request) TAD from NAS message | If the full TFT is deleted for a dedicated bearer, the dedicate bearer is then released. | PGW identifies the PCC rule corresponding to the filters and requests PCRF for QoS Rule Update. NOTE: The filters to be deleted should belong to on e PCC rule, otherwise the PGW will not know what QoS reduction needs to occur.

## Slide 6: UE Init procedures for 2G/3G via S4-SGSN

## Slide 7: Overview
In 2G/3G with MS-only mode:
  Bearer-binding is fully controlled by UE.
    For new flows, the UE signals the bearer onto which the flow is mapped along with QoS of the bearer.
In 2G/3G with MS/NW mode:
  Bearer-binding is “split” between UE and NW (BBF).
    For UE-init new flows, the UE can decide that a new bearer should be allocated and signal this in the setup message (“UE-init secondary PDP context creation”), or can decide to add the new flow to an existing bearer (“UE-init PDP context modification”).
  For PDP Context Modification procedure (6.1.3.2.2, TS 24.008)
    If the selected Bearer Control Mode is 'MS/NW' and the MS wants to modify the QoS, it shall include a TFT with packet filter(s), or if no packet filters are proposed to be either added, replaced or deleted, it shall include packet filter identifier(s) to indicate which packet filter(s) in the TFT is associated with the QoS change.
    If a PDP context is associated with a TFT containing packet filters established by both the MS and the network, the only parameters in the QoS profile of that PDP context the MS is allowed to modify are the bitrate parameters.
  NW(BBF) can add (multiple) NW-init SDFs to any (UE-init or NW-init) bearer.

## Slide 8: UE-initiated EPS bearer request/modification/deletion in 2G/3G in MS-only mode (Table 3A 23.060, augmented)
 | UE-initiated resource request use case | Procedure/Information provided by UE in NAS signalling | Procedure/Information on S4 to SGW and S5 to PGW | NOTES | PGW Behaviour Impact on Gx
1 | Create a new bearer (secondary PDP Context) | ACTIVATE SECONDARY PDP CONTEXT REQUEST Linked TI, Requested NSAPI (EBI), TI QoS params TFT (TFT_operation = “create new TFT”, filter, filter ID, precedence) | BEARER RESOURCE COMMAND LBI (= Linked TI), No EBI QCI, GBR (only for GBR request) TFT | The RAT Type = 2G/3G along with “create new TFT” in TFT operation indicates to the PGW that a new bearer needs to be created. NOTE: The EBI is not assigned by the PGW in the Create bearer request. The EBI(=NSAPI) is created by SGSN and forwarded back to PGW by SGW. | The RAT Type = 2G/3G along with “create new TFT” in TFT operation indicates to the PGW that a new bearer needs to be created. The PGW MUST initiate Create Bearer request. For LTE the PGW can add to the flow to an existing bearer and hence initiate modify bearer request. On Gx, New PCC rule is request ed. The TFT filter-IDs used are the ones provided by the UE in the create secondary PDP context request.
2 | Add TFT filters to a bearer with existing TFT and with or without increase QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context, (optional) TFT (TFT_operation = “add pkt filters”, new filter, filter ID, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), QoS related to EPS Bearer (optional), TFT | The parameter list does not consist of the existing TFTs. | There is no linked packet filters in the parameters field in the TFT (as opposed to LTE case, where UE adds IP-flows to an existing SDF). For MS-only there can only be one PCC rule per bearer. Hence PGW is able to identify the PCC rule associated with the bearer to communicate with PCRF. On Gx, the PGW asks for modification of an existing PCC rule
3 | Add TFT filters to a bearer without existing TFT and increase QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context, TFT (TFT_operation = “Create a new TFT”, new filter, filter ID, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), QoS related to EPS Bearer, TFT | UE can use “create a new TFT” for PDP context that already have a TFT. This is a syntactic error stated in stage-3 but can still continue and replace the existing TFT. (Sec. 6.1.3.3.3, 24.301) UE can “create a new TFT” for PDP context established without TFT (first PDP context. This is the typical use-case. | Compared to #1, the EBI in included in Bearer Resource Command. Hence, the PGW will figure out that an existing bearer needs to be updated. Hence, modify bearer request is use . The PCC rule correspodning to the bearer is requested to be updated with the new filters.
4 | Increase/Decrease of QoS, TFT filters not specified | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context, TFT (TFT_operation = “no op”) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), QoS related to EPS Bearer, TFT |  | Not supported in LTE (TFT filters need to be specified for LTE.) For MS-only there can only be one PCC rule per bearer. Hence PGW is able to identify the PCC rule associated with the bearer to communicate with PCRF. On Gx, the PGW asks for modification of an existing PCC rule
5 | Remove some (not all) TFT filters with or without decrease QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context TFT (TFT_operation = “delete pkt filter from existing TFT”, filters to be added/deleted, filter ID, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS of the PDP context TFT |  | Same as LTE. On Gx, the PGW asks for modification of an existing PCC rule corresponding to the bearer.
6 | Remove TFT with or without decrease QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context TFT (TFT_operation = “delete existing TFT”, no pkt filter list) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS of the PDP context TFT | ERROR: TFT operation = "Delete existing TFT" when there is already another PDP context with the same PDP address and APN without a TFT. (Sec. 6.1.3.3.3, 24.301) | Corresponding to the case when a SDF flow is requested to be removed by UE in LTE which leads to no TFT on the bearer. On Gx, the PGW asks for modification of an existing PCC rule corresponding to the bearer (to remove the TFTs)
7 | Replace one or more filters in an TFT with new one(s) with or without change in QoS (no QCI change) | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS (GBR) of the EPS Bearer (GBR only) (if needed) TFT (TFT_operation = “replace pkt filters in existing TFT”, list of filter(s) which will form the TFT, filter ID (for existing filters, no IDs for new filters, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS (GBR) of the EPS Bearer (GBR only) TFT |  | Same as LTE. On Gx, the PGW asks for modification of an existing PCC rule
8 | Delete a bearer | DEACTIVATE PDP CONTEXT REQUEST TI (NSAPI) , No LBI Teardown Indicator | If Teardown Indication: DELETE SESSION REQUEST LBI Otherwise: DELETE BEARER COMMAND EBI (NSAPI), NO LBI |  | On Gx, the PGW asks for deletion of PCC rule corresponding to the bearer.

## Slide 9: UE-initiated EPS bearer request/modification/deletion in 2G/3G in MS/NW mode (Table 3B 23.060, augmented)
 | UE-initiated resource request use case | Procedure/Information provided by UE in NAS signalling | Procedure/Information on S4 to SGW and S5 to PGW | NOTES | PGW Behaviour Impact on Gx
1 | Create a new bearer (secondary PDP Context) | ACTIVATE SECONDARY PDP CONTEXT REQUEST Linked TI, Requested NSAPI (EBI), TI QoS params TFT (TFT_operation = “create new TFT”, filter, filter ID, precedence) | BEARER RESOURCE COMMAND LBI (= Linked TI), No EBI QCI, GBR (only for GBR request) TFT | The RAT Type = 2G/3G along with “create new TFT” in TFT operation indicates to the PGW that a new bearer needs to be created. NOTE: The EBI is not assigned by the PGW in the Create bearer request. The EBI(=NSAPI) is created by SGSN and forwarded back to PGW by SGW. | The RAT Type = 2G/3G along with “create new TFT” in TFT operation indicates to the PGW that a new bearer needs to be created. The PGW MUST initiate Create Bearer request. For LTE the PGW can add to the flow to an existing bearer and hence initiate modify bearer request. On Gx, New PCC rule is request ed. The TFT filter-IDs used are the ones provided by the UE in the create secondary PDP context request.
2 | Add TFT filters to a bearer with existing TFT and with or without increase QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context (optional), TFT (TFT_operation = “add pkt filters”, new filter, filter ID, precedence, associated filters) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), QoS related to EPS Bearer (optional), TFT | The parameter list SHALL consist of filters to which the new filter need to be associated with. | There is no linked packet filters in the parameters field in the TFT (as opposed to LTE case, where UE adds IP-flows to an existing SDF). For MS-only there can only be one PCC rule per bearer. Hence PGW is able to identify the PCC rule associated with the bearer to communicate with PCRF. On Gx, the PGW asks for modification of an existing PCC rule
3 | Add TFT filters to a bearer without existing TFT and increase QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context, TFT (TFT_operation = “Create a new TFT”, new filter, filter ID, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), QoS related to EPS Bearer, TFT | UE can use “create a new TFT” for PDP context that already have a TFT. This is a syntactic error stated in stage-3 but can still continue and replace the existing TFT. (Sec. 6.1.3.3.3, 24.301) UE can “create a new TFT” for PDP context established without TFT (first PDP context. This is the typical use-case. | Compared to #1, the EBI in included in Bearer Resource Command. Hence, the PGW will figure out that an existing bearer needs to be updated. Hence, modify bearer request is use . The PCC rule correspodning to the bearer is requested to be updated with the new filters.
4 | Increase/Decrease of QoS, TFT filters not specified | NOT SUPPORTED |  |  | Not supported in LTE (TFT filters need to be specified for LTE.)
5 | Remove some (not all) TFT filters with or without decrease QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context TFT (TFT_operation = “delete pkt filter from existing TFT”, filters to be added/deleted, filter ID, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS of the PDP context TFT | The parameter list SHALL consist of filters to which the new filter need to be associated with. | Same as LTE. On Gx, the PGW asks for modification of an existing PCC rule corresponding to the bearer.
6 | Delete TFT with or without decrease QoS | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS of the PDP context TFT (TFT_operation = “delete existing TFT”, no pkt filter list) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS of the PDP context TFT | ERROR: TFT operation = "Delete existing TFT" when there is already another PDP context with the same PDP address and APN without a TFT. (Sec. 6.1.3.3.3, 24.301) | Corresponding to the case when a SDF flow is requested to be removed by UE in LTE which leads to no TFT on the bearer. On Gx, the PGW asks for modification of an existing PCC rule corresponding to the bearer (to remove the TFTs)
7 | Replace one or more filters in an TFT with new one(s) with or without change in QoS (no QCI change) | MODIFY PDP CONTEXT REQUEST TI (NSAPI) , No LBI New QoS (GBR) of the EPS Bearer (GBR only) (if needed) TFT (TFT_operation = “replace pkt filters in existing TFT”, list of filter(s) which will form the TFT, filter ID (for existing filters, no IDs for new filters, precedence) | BEARER RESOURCE COMMAND LBI, EBI (NSAPI), New QoS (GBR) of the EPS Bearer (GBR only) TFT |  | Same as LTE. On Gx, the PGW asks for modification of an existing PCC rule
8 | Delete a bearer | DEACTIVATE PDP CONTEXT REQUEST TI (NSAPI) , No LBI Teardown Indicator | If Teardown Indication: DELETE SESSION REQUEST LBI Otherwise: DELETE BEARER COMMAND EBI (NSAPI), NO LBI |  | On Gx, the PGW asks for deletion of PCC rule(s) corresponding to the bearer(s).

## Slide 10: Some Observations

## Slide 11: PGW Behavior Changes between LTE and 2G/3G
Create Secondary PDP Context Request (2G/3G) and UE Requested Bearer Resource Allocation (LTE):
  There is no EBI. The TFT operation is “Create new TFT” for both 2G/3G and LTE.
    If RAT type = 2G/3G, the PGW will setup a new bearer.
    If RAT type = LTE, the PGW may create new bearer or modify existing bearer.
Modify PDP Context Request (2G/3G) and UE Requested Bearer Resource Modification (LTE):
  EBI is always included.
    If BCM = UE/NW, TFT contains sufficient information (eg. linked filters in the parameter field) for PGW to identify the specific PCC rule which is mapped to the bearer.
    If BCM = UE-only, there is only one PCC rule on the bearer.

## Slide 12: Handling of TFT operation code in PGW for LTE and 2G/3G
TFT operations code and contents are similar for LTE and UE/NW mode for 2G/3G.
The main difference is between {LTE, UE/NW 2G/3G} on one hand and {UE-only mode in 2G/3G} on the other.

## Slide 13: Mapping from Bearer parameters to Gx parameters for 2G/3G connected to EPS
For mapping from EPS bearer parameters to Gx:
  For MS-only mode: It is essential that there is only one PCC rule per PDP context/EPS bearers in the PGW. This is because UE in MS-only mode can do procedures like add filters to bearer without specifying a subset of filters on the bearer that this new filter needs to be associated it. If there are multiple PCC rules on a particular bearer, then it becomes impossible for the PGW to determine which PCC rule needs to be modified.
  For MS/NW mode: For modification (QoS and/or add/replace/delete filters): Since there can be multiple PCC rules that map to a bearer, it is important that the UE provides which specific PCC rule is being modified. Hence, for “add filter” the existing SDF to which the filter is to be added must be specified.

## Slide 14: On handling of TFT filter IDs for new UE requested SDFs in PGW
Background:
  In 2G/3G, the UE provides the TFT filter-IDs in the PDP creation/modification requests.
  In LTE, the UE does not provide the TFT filter-IDs in bearer resource request.
    The TFT filter-ID field is always present in the TFT, so the UE needs to fill in some value even in LTE. The UE may fill-in zeros. Whatever, the UE fills in is ignored by the PGW. The reason that UE providing filter-ID in TFT does not make sense is because the mapping of the SDF to bearer is controlled by the PGW and not dictated by UE, as it does in 2G/3G. So UE does not know if a new bearer will be created or the flow will be mapped to an existing bearer.
The PGW knows the RAT from where the UE is signalling.
  IF RAT Type = 2G/3G, the PGW does not change the TFT filter IDs in the SM message. When the PCRF provides PCC rule with Gx Packet Filter ID, the PGW assigns the flow to a bearer and creates a mapping from Bearer-ID+TFT Filter ID : Gx Packet Filter ID.
  If RAT Type = LTE, the PGW ignores the TFT filter ID in the SM message. When the PCRF provides PCC rule with Gx Packet Filter ID, the PGW assigns the flow to a bearer, creates TFT filter IDs. The PGW also creates a mapping from Bearer-ID+TFT Filter ID : Gx Packet Filter ID.
ACTIONS:
  Add in 23.060 and annex- D of 23.401, that in both “Secondary PDP context creation” and “PDP Context Modification procedure”, the PGW does not modify the filter-ID provided by the UE.
    NOTE: In 23.401 for LTE, UE bearer modification procedure, it is already clarified that UE does not provide filter-ID, but the PGW creates it after getting PCC rule from the PCRF. So no change required to 23.401.

## Slide 15: Mapping between SDF Filter IDs, on Gx/Gxx and TFT Filter IDs for LTE and 2G/3G

## Slide 16: Assumptions
During Addition operation the TAD contains only filter content (but no filter identifiers)
The Filter IDs conveyed in the TAD during Modification or Deletion operation are unique per EPS Bearer and go only as far as the PCEF (GTP) or BBERF (PMIP)
The combination of [per-bearer unique] Filter ID + EPS Bearer ID uniquely identifies an SDF inside the “transport” layer (i.e. below Gx/Gxx)
  This combination is equivalent to [per-PDN unique] Filter ID
On Gx (and/or Gxx) the SDF is identified with a unique Gx (or Gxx) identifier
  The Gx (or Gxx) SDF identifiers are local interface “handles” e.g. may change upon BBERF relocation
  However there is 1:1 mapping between a Gx (or Gxx) handle and a [per-bearer unique] Filter ID + EPS Bearer ID combination
In E-UTRAN the Filter IDs are always assigned by the PCEF/BBERF
For EPC-connected GERAN/UTRAN the Filter IDs can also be assigned by the UE

## Slide 17: Establishment of UE-init resource in E-UTRAN
S5
S1-MME
S10
MME
S11
Serving Gateway
UE
E-UTRAN
SGi
PGW
S1-U
Operator’s IP services
PCEF
Gx
PCRF
1-UE Requested Bearer Resource Modification (URBRM); the TAD contains filter description, but no Filter ID
  Filter-ID field is always present in TFT and filled in by the UE, but PGW ignores this value.
2-PCEF does not assign any identifier requests a PCC rule for the filter
  The PCRF provides the ID in step 3. y.
3-PCRF creates a PCC rule, creates filter-identifier Y and sends the PCC rule to the PCEF; the PCC rule is signalled along with Y
  The filter-identifier Y is within the scope of the PCRF is unique per UE
4-PCEF decides how to bind the SDF to an EPS bearer, assigns a Filter ID=X, stores the (Y:X) mapping and triggers Dedicated Bearer Activation (DBA)
  the TFT associated to the EPS bearer contains TFT(X) i.e. the filter assigned by the PCEF; the UE can use “EPS Bearer ID + X” as a reference for any future modification
1- URBRM (TAD(filter))
2°
3° PCC rule + Y
4- DBA (Bearer ID, TFT(X))
BID,X : Y
Y