## Slide 1: AS-NAS Capability Mismatch SRVCC
S2-120675
ZTE Corporation

## Slide 2: Summary of timeline (the story so far…)
Issue started from LS from RAN2 S2-113914
Discussed in Joint SA2/CT1/RAN2 meeting in SF where 4 proposals were discussed (Ericsson, NTT Docomo, Samsung,NSN)
Discussion in RAN#54 led to RP-111753
Topic in the agenda for S2#89

## Slide 3: Problem statement
NAS
  Only one NAS SRVCC capability parameter
AS
  Two FGI bits in AS layer (for E-UTRAN) indicate different caps for SRVCC HO to GERAN (FGI bit 9) or UTRAN (FGI bit 27)
  No AS capability bits in UTRAN
  No differentiation between FDD/TDD in E-UTRAN(and UTRAN of course)
MME/SGSN do not know whether the UE is capable to perform SRVCC HO in AS layer
If we can also include FDD/TDD combinations in EUTRAN/UTRAN mismatch multiplies further
Handover to 1xRTT is not considered- should we consider this as well?

## Slide 4: Problem statement (cont.)
What is the problem with that?
  MME/SGSN (may) take into account NAS SRVCC Capability and not AS capabilities to determine whether to provide IMSVoPS indication in GMM/EMM accept message
  If set incorrectly IMSVoPS may lead the UE to select wrong domain for normal and emergency calls  Call drops!!
How often can this happen?
  Normally in roaming, assuming operators would have IOT-ed the UE and RAT “combinations” for their HPLMN
  It may be considered a “transitional” issue if the end goal is that SRVCC will become mandatory in all RATs a UE supports
  Emergency call domain selection uses similar principles with normal calls and this may cause regulatory issues

## Slide 5: Current Proposals
Alternative 1: Increasing the bits of SRVCC NAS capability
  Add NAS SRVCC capability for each RAT
  AS and NAS capabilities can be aligned
Pros
  Clean solution that solves the problem once and for all
  Not very heavy MME impacts
Cons
  Significant UE impacts
    If it does not cover “earlier releases” it may become irrelevant i.e. if it is not applied from rel.8/9 we are missing the boat for IR.92/IR.58 UEs
  Providing a solution to a transitional issue requiring UE changes

## Slide 6: Current Proposals (cont.)
Alternative 2: Fix rules on how the UE provides SRVCC capability
  Define some rules on which AS FGI bits can drive the NAS to set the SRVCC capability
Pros
  No impacts in the protocols, better for transitional issue
  Minimal to no impact in standards
Cons
  Difficult to agree on most widely deployed combinations e.g. E-UTRAN FDD to GERAN may be more popular in Europe, whereas E-UTRAN FDD to UTRAN appropriate for Japan
  It cannot solve one important scenario: dual mode E-UTRAN (FDD/TDD) UEs supporting only UMTS (FDD) SRVCC roaming to LTE TDD operator where UMTS (TDD) is only supported (e.g. CMCC)
  Configuration (OMA DM) as proposed by Docomo not suitable for emergency calls

## Slide 7: Current Proposals (cont.)
Alternative 3: MME analyse the AS capabilities
  Different ways to provide the AS capabiltiies to MME i.e. whether to analyse RAC directly provided from UE or fetch from eNB/RNC when needed
Pros
  Solves the issue for both SRVCC from E-UTRAN and SRVCC from UTRAN HSPA
  No UE impact for SRVCC from E-UTRAN
Cons
  Layer violation (MME is required to analyse AS specific info)
  Cannot provide the right IMSVoPS for the first TAU after GERAN/UTRAN attach (MME does not have UE RAC at this point)
  Requires new RAC for HSPA
  Relates to FDD/TDD discussion – i.e. how can the MME obtain the RAC when mixed FDD/TDD RAN is used

## Slide 8: New proposal (partial solution)
Alternative 4: eNB/RAN takes into account the SRVCC AS FGI before initiating SRVCCC handover
  Currently in Annex A.2 TS 23.216 it is not defined that eNB/RAN should take into account the FGI bits of the UE before initiating a handover (only existence of QCI-1 and “SRVCC operation possible” from S1-AP are listed as possible conditions)  We can add that
  This way at least no SRVCC handover to a RAT the UE does not support SRVCC will be initiated
Pros
  Easy solution (no normative impacts, only internal handling)
  Very small impact in standards (no impacts to the UE/MME, only internally in eNB/RAN)
  It can equally work for normal and emergency cases
Cons
  Does not solve the “setting of IMSVoPS” in EMM/GMM accept
  If the coverage of LTE/HSPA is limited and relies in frequent SRVCC handovers, the UE that does not have AS capability will fail
  Requires new RAC for HSPA

## Slide 9: Way forward
No solution has been identified so far as “clear winner”
Impacts on frozen releases esp. in the UE should be avoided and ideally IR.92/IR.58 should not be impacted
It is not clear how common the use case will be, it depends on:
  Timescales for VoIP roaming will be before or after “large scale” LTE coverage
  Deployment of VoIP over HSPA and SRVCC (requires UTRAN RAC changes)
  Emergency calls, a serious issue that is currently disregarded in SA2 discussion so far
  Need to consider some inter-mode SRVCC handovers (e.g. from LTE TDD  UMTS FDD may be the most common)
Possible way forward
  Combination of alt. 2 and 4 for previous releases (Rel.8-10 negotiable) provides a remedy to the problem (do not solve 100%)
  Clarification for emergency calls in TS 23.167 (rel.9) that the SRVCC UE shall not initiate emergency calls in PS domain if both FGI bits are set to 1 despite IMSVoPS
  Alt. 1 for new releases (rel.11)