## Slide 1: SaMOG Wireless LAN Control Protocol (WLCP) Introduction

## Slide 2: Introduction
“Layer 2.5 protocol”: sits below IP and is transported over existing layer 2
  Transported over WLAN, different mechanisms are available how to carry control protocol messages; e.g. using a new Ethertype
Provides session management in the 3GPP sense
  PDN connections management
    Establishment of PDN connections
    Handover of PDN connections
    Tear down of PDN connections
    IP address assignment
    PDN parameters management (including network providing PDN identifier for L2 transport, e.g. GRE key, VLAN ID, etc.)
  Applies to multiple PDNs scenario
Enables device behavior similar to behavior over cellular link
  Can be expanded to consider features like low priority indications, etc.
    Anything defined for cellular NAS can be added and used here directly
    Ready for further network-initiated procedures such as TFT modifications in the UE (e.g. for VoIMS)
  Limited of course to the functionality available over WLAN
    No QoS support
    No MM (e.g. area updates, etc.)
    See appendix for more details

## Slide 3: Design Assumptions
24.008 is the starting point for the WLCP protocol design
  WLCP can be a subset of SM
  24.008 more in line with SaMOG concepts, i.e. that UE first “attaches” and then establishes PDN connections
    SM is already written to use this philosophy, ESM would require more modifications due to interactions with EMM
    In 24.301 the trigger to setup a PDN connection can come from lower layers (EMM), whereas in SM it can only come from the application
We do not need GMM part of NAS
  MM functionality provided by EAP authentication and negotiations
  WLCP assumes the equivalent of a GMM REGISTERED state upon successful EAP authentication
Comments:
  Only basic Primary PDP Context Activation/Deactivation procedure is needed
    Some parameters not needed (e.g. QoS, etc.) others possibly updated (e.g. protocol options)
  No secondary PDP context management is considered, but in order to provide QoS the control protocol can be easily extended to adopt this.
  No eMBMS is considered
  IP address allocation of SM can be re-used
  No support of emergency PDN, leave it open for further releases
  LIPA functionality not required
  Leave up to stage 3 aspects such as segmentation, retransmission, all issues already been solved by stage 3 for current NAS.
Details of the protocol are for stage 3 to define

## Slide 4: Protocol Stack For WLCP
(*) established using EAP authentication and SaMOG parameters exchange

## Slide 5: WLCP Functionality
Messages for PDN management:
  PDN Connection Activation Request/Accept/Reject  ACTIVATE PDP CONTEXT REQUEST/ACCEPT/REJECT
  No secondary PDP context management from 24.008 required
  No PDN context modification from 24.008 required
  PDN Connection Deactivation Request/Accept  DEACTIVATE PDP CONTEXT REQUEST/ACCEPT
IP address allocation
  As per current NAS mechanisms

## Slide 6: WLCP state machine

## Slide 7: WLCP : a parallel to GPRS services (refer to 24.007)
Provided by EAP, no actual GMM in place.
WLCP used/usable only once EAP is successfully completed
Mapping of services to EAP state machine
A subset of the services is provided to the upper layers, but the subset is provided in the same way

## Slide 8: Session Management Services for SMREG-SAP for WLCP
PRIMITIVE | PARAMETER (message, info elements of message, other parameters) | REFERENCE
SMREG-PDP-ACTIVATE-REQ | PDP address, QoS, NSAPI, APN, Protocol configuration options | 6.5.1.1
SMREG-PDP-ACTIVATE-CNF | PDP address, QoS, NSAPI, Protocol configuration options | 6.5.1.2
SMREG-PDP-ACTIVATE-REJ | Cause, NSAPI, Protocol configuration options | 6.5.1.3
SMREG-PDP-ACTIVATE-IND | PDP address, APN, protocol configuration options | 6.5.1.4
SMREG-PDP-ACTIVATE-REJ-RSP | Cause, PDP address, APN, protocol configuration options, MBMS protocol configuration options | 6.5.1.14
SMREG-PDP-DEACTIVATE-REQ | NSAPI(s) tear down indicator, cause, protocol configuration options, MBMS protocol configuration options | 6.5.1.5
SMREG-PDP-DEACTIVATE-CNF | NSAPI(s), protocol configuration options, MBMS protocol configuration options | 6.5.1.6
SMREG-PDP-DEACTIVATE-IND | NSAPI(s) (s), tear down indicator, cause, protocol configuration options, MBMS protocol configuration options | 6.5.1.7
SMREG-PDP-MODIFY-IND | QoS, NSAPI, protocol configuration options | 6.5.1.8
SMREG-PDP-MODIFY-REQ | QoS, NSAPI, TFT, protocol configuration options | 6.5.1.18
SMREG-PDP-MODIFY-CNF | QoS, NSAPI, protocol configuration options | 6.5.1.19
SMREG-PDP-MODIFY-REJ | Cause, NSAPI, protocol configuration options | 6.5.1.20
SMREG-PDP-ACTIVATE-SEC-REQ | QoS, NSAPI, TFT, Primary NSAPI, protocol configuration options | 6.5.1.15
SMREG-PDP-ACTIVATE-SEC-CNF | QoS, NSAPI, protocol configuration options | 6.5.1.16
SMREG-PDP-ACTIVATE-SEC-REJ | Cause, NSAPI, protocol configuration options | 6.5.1.17
SMREG-MBMS-ACTIVATE-REQ | Multicast address, supported MBMS bearer capabilities, NSAPI, APN, MBMS protocol configuration options | 6.5.1.21
SMREG-MBMS-ACTIVATE-CNF | Multicast address, NSAPI, MBMS protocol configuration options | 6.5.1.22
SMREG-MBMS-ACTIVATE-REJ | Cause, NSAPI, MBMS protocol configuration options | 6.5.1.23
SMREG-MBMS-ACTIVATE-IND | Multicast address, APN, MBMS protocol configuration options | 6.5.1.24

## Slide 9: Impacts on functionality
UE:
  Implements interactions between EAP state machine and SM state machine (primitives)
  Implements relevant parts of SM state machine
TWAG:
  Implements WLCP layer based on SGSN SM state machine (simplified)
  Implements interactions between EAP state machine and SM state machine