3GPP TSG-SA3 Meeting #100e 	S3-201590-r1

# e-meeting, 17 – 28 August 2020

# Source:	Nokia, Nokia Shanghai Bell

# Title:	Multiple TSN working domains

# Document for:	Approval

Agenda Item:	5.11

# 1	Decision/action requested

KI addressing security threats by TSN multiple working domains.

# 2	Rational

3GPP Rel-16 included support for multiple TSN working domains. DS-TT and NW-TT are required to determine to which working domain an incoming or outgoing communication belongs. This is implemented by a specific domainNumber (3GPP TS 23.501 [3], clause 5.27.1.3).

Downlink Time Sync is considered in Rel-16 (TS 23.501 [3], clause 5.27.1.3), such that multiple gPTP messages are sent transparently in the UP to the UE/DS-TT for all cases of Time Domains identified by the IE 'domainNumber'.

However, a compromised TSN node may send a tampered domainNumber to access other than the intended TSN working domains, which is addressed by this KI.

## References

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 33.501

[3]	3GPP TS 23.501

[4]	3GPP TR 23.700-20

[5]	IEEE 802.1Qcc

[6]	IEEE 1588-2008

[7]	RFC 7384

## Abbreviations

5G				Fifth Generation

5GS				Fifth Generation System

ARP				Address Resolution Protocol

BMCA				Best Master Clock Algorithm

CNC				Centralized Network Configuration

CP				Control Plane

CUC				Centralized User Configuration

DS-TT				Device Side Translator

DoS				Denial of Service

gPTP				generalized Precision Time Protocol

IIoT				Industrial Internet of Things

IP				Internet Protocol

KI				Key Issue

Ln				Layer n

MAC				Media Access Control

NW-TT				Network Side Translator

PTP				Precision Time Protocol

TSC				Time Sensitive Communication

Rel				Release

UE				User Equipment

TSN				Time Sensitive Networking

TSN AF				TSN Application Function

UPF				User Plane Function

UP				User Plane

****** START OF CHANGES

## 5.X	Key issue #X: Multiple TSN working domains

## 5.X.1	Key issue details

3GPP Rel-16 included support for multiple TSN working domains. DS-TT and NW-TT are required to determine to which working domain an incoming or outgoing communication belongs. This is implemented by a specific domainNumber (3GPP TS 23.501 [3], clause 5.27.1.3).

Downlink Time Sync is considered in Rel-16 (TS 23.501 [3], clause 5.27.1.3), such that multiple gPTP messages are sent transparently in the UP to the UE/DS-TT for all cases of Time Domains identified by the IE 'domainNumber'. This allows any integrity and replay protected TSN bridge to transfer time synchronisation messages to another TSN bridge. This KI is to further study how to protect the 5GS acting as a TSN bridge being accessed by an unauthorized TSN bridge. I.e., a compromised TSN node may send a tampered domainNumber to access other than the intended TSN working domains.

### 5.X.2	Threats

A compromised TSN node (a non-5GS bridge) may send a tampered domainNumber to access other domains than the intended TSN working domains (i.e. the 5GS bridge).

TSN domains not verifying the domainNumber parameter by any means may be vulnerable to spoofing attacks:

A malicious node may send a tampered domainNumber parameter to access other than the intended TSN working domains. This may lead to unauthorized access to the (g)PTP communication within a TSN working domain. This attack may be the initial attack vector for further exploitation, such as rogue master clock attacks and (g)PTP message spoofing.

The impact of this attack may be DoS, accuracy degradation and false times being synchronized.

### 5.X.3	Potential security requirements

TBD

****** END OF CHANGES