3GPP TSG-SA3 Meeting #100e 	S3-201755

# e-meeting, 17 – 28 August 2020

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 33.535 | CR | 0013 | rev | - | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Re-authentication in AKMA |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S3 |
| Work item code: | AKMA |  | Date: | 2020-8-17 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The current text messed up the first time authentication and reauthenticaiton by saying “The AAnF shall store the latest information sent by the AUSF”. If the primary authentication runs first time, then the meaning of “lastest” is not clear. So the content is further divided into primrary authentication and re-authentication. |
| qu |  |
| Summary of change: | When re-authentication happens, the AAnF shall send the new generated AKMA material to the AAnF, and the AAnF shall delete the old stored AKMA material. |
| Consequences if not approved: | The behviour of AAnF is not clear when reauthentication happens. |
| Clauses affected: | 6.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

********** START OF 1st CHANGE **********

## 6.1	Deriving AKMA key after primary authentication

There is no separate authentication of the UE to support AKMA functionality. Instead, it reuses the 5G primary authentication procedure executed e.g. during the UE Registration to authenticate the UE. A successful 5G primary authentication results in KAUSF being stored at the AUSF and the UE.

Figure 6.1-1: Deriving AKMA root key after primary authentication

During the primary authentication procedure, the AUSF interacts with the UDM in order to fetch authentication information such as subscription credentials (e.g. AKA Authentication vectors) and the authentication method using the Nudm_UEAuthentication_Get Request service operation. In the response, the UDM may also indicate to the AUSF whether AKMA keys need to be generated for the UE. If the AUSF receives the AKMA indication from the UDM, the AUSF shall store the KAUSF and generate the AKMA Anchor Key (KAKMA) and the A-KID from KAUSF after the primary authentication procedure is successfully completed.

After AKMA key material is generated, the AUSF shall send the generated A-KID, and KAKMA to the AAnF together with the UE SUPI using the Naanf_AKMA_KeyRegistration Request service operation. The AAnF shall store the information sent by the AUSF.

NOTE 1:	The AUSF need not store any AKMA key material after delivery to the AAnF.

When re-authentication runs, the AUSF shall generate a new A-KID, and a new KAKMA and send the new generated A-KID and KAKMA to the AAnF. After receiving the new generated A-KID and KAKMA, the AAnF shall delete the old A-KID and KAKMA and store the new generated A-KID and KAKMA. This means the AAnF shall store the latest information senty by the AUSF.

The UE shall generate the AKMA Anchor Key (KAKMA) and the A-KID from the KAUSF before initiating communication with an AKMA Application Function.

A-KID identifies the KAKMA key of the UE from which other AKMA keys are derived.

A-KID shall be in NAI format as specified in clause 2.2 of IETF RFC 7542, i.e. username@realm. The username part includes the Routing Identifier and the A-TID (AKMA Temporary UE Identifier), and the realm part shall include Home Network Identifier.

The A-TID shall be derived from KAUSF as defined in clause A.3.

NOTE 2:	The chance of A-TID collision is not zero but practically low as the A-TID derivation is based on KDF specified in Annex B of TS 33.220 [4]. The detection of A-TID collision as well as potential handling of collision is not addressed in the present document.

The key derivation of KAKMA shall be performed using the key derivation function (KDF) specified in TS 33.220 [4]. KAKMA is computed (as per Annex A.2) as KAKMA=KDF (KAUSF, "AKMA", SUPI), where the key derivation parameters consist of a static string "AKMA", and SUPI.

Since AKMA keys are based on KAUSF from primary authentication run, the AKMA keys can only be refreshed by running a fresh primary authentication.

********** END OF CHANGE **********