3GPP TSG-SA3 Meeting #100e 	S3-201856

# e-meeting, 17-28 Augest 2020													Revision of S3-20xxxx

# Source:	Huawei, Hisilicon

# Title:	IMS SCAS: new test case on high-priority algorithm selection in the P-CSCF

# Document for:	Approval

Agenda Item:	4.15

# 1	Decision/action requested

This contribution proposes a new test case on high-priority algorithm selection in the P-CSCF.

# 2	References

[1]	3GPP TS 33.203	3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G security;Access security for IP-based services

[2]		S3-201855

# 3	Rationale

As specified in TS 33.203 [1], clause 7.2, the P-CSCF selects the first algorithm combination on its own list which is also supported by the UE.. Otherwise, the P-CSCF could end up using a weaker algorithm forcing the system into a lowered security level making the system easily attacked and/or compromised.

The threats analysis can be found in the S3-201855 [2].

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the changes ****************

#### 4.2.2.X	Security functional requirements on the P-CSCF deriving from 3GPP specifications and related test cases

##### 4.2.2.X.1	High-priority algorithm selection

Requirement Name: High-priority algorithm selection

Requirement Reference: TS 33.203 [XX], clause 7.2

Requirement Description:

"In order to determine the integrity and encryption algorithm the P-CSCF proceeds as follows: the P-CSCF has a list of integrity and encryption algorithms it supports, ordered by priority. The P-CSCF selects the first algorithm combination on its own list which is also supported by the UE. If the UE did not include any confidentiality algorithm in SM1 then the P-CSCF shall either select the NULL encryption algorithm or abort the procedure, according to its policy on confidentiality. "

as specified in TS 33.203 [XX], clause 7.2.

Threat References: TBD

Test case:

Test Name: TC_HIGH_PRIORITY_ALGORITHM_SELECTION

Purpose:

Verify the P-CSCF selects the first algorithm combination on its own list which is also supported by the UE.

Procedure and execution steps:

Pre-Conditions:

-	P-CSCF network product are connected in simulated/real network environment.

-	The list of ordered integrity and encryption algorithms are configured on the P-CSCF under test by the tester.

-	The UE supporting IMS AKA may be simulated.

-	The UE supports a list of integrity and encryption algorithms.

-	The tester has access to the Gm interface between the UE and P-CSCF.

Execution Steps

This test is performed in the registration procedure, the UE sends a Register message towards the S-CSCF through the P-CSCF to register the location of the UE and to set-up the security mode.

1) The UE sends SM1 with integrity and encryption algorithms list to the P-CSCF under test.

2) The P-CSCF under test receives the SM1 with integrity and encryption algorithms list. The P-CSCF under test selects algorithms.

3) The tester examines the selected algorithm in the SM6 sent from the P-CSCF under test to the UE via the Gm interface.

Expected Results:

The selected algorithms are the first algorithm combination on its own list which is also supported by the UE.

Expected format of evidence:

Provide evidence of the check of the product documentation in plain text. Save the logs and the communication flow in a .pcap file.

*************** End of the changes ****************