3GPP TSG-SA3 Meeting #100e 	S3-201960-r1

# e-meeting, 17 -28 August 2020													Revision of S3-20xxxx

# Source:	Samsung

# Title:	Key Issue on key management in 5G ProSe for UE-to-Network relay communication

# Document for:	Approval

Agenda Item:	5.10

# 1	Decision/action requested

It is requested to approve this key issue for TR 33.847.

# 2	References

[1]	3GPP TR 33.847: "Study on security aspects of enhancement for proximity based services in the 5G System (5GS)".

# 3	Rationale

This key issue is to describe the security issues when the remote UE accesses the network via relay. It is proposed to approve this key issue in TR 33.847.

# 4	Detailed proposal

*****Start of 1stchange*****

# 2	References

[1]	3GPP TS 23.303: "Proximity-based services (ProSe); Stage 2".

[2]	3GPP TS 23.752: " Study on system enhancement for Proximity based Services (ProSe) in the 5G System (5GS) (Release 17)".

[3]	3GPP TS 23.287: "Architecture enhancements for 5G System (5GS) to support Vehicle-to-Everything (V2X) services".

[4]	3GPP TS 33.536: " Security aspects of 3GPP support for advanced Vehicle-to-Everything (V2X) services (Release 16)".

*****Start of 2nd change*****

## 5.X	Key Issue #X: Key management in 5G Proximity Services for UE-to-Network relay communication

### 5.X.1	Key issue details

This key issue covers both Layer-2 and Layer-3 relays in 5G Proximity Services.

SA2 TR 23.752 [aa] has candidate solution for both layer 2 and layer 3 UE-to-network relay. There are security solutions which will be adapted for PC5 unicast communication for ProSe from 5G V2X.

Currently, Rel-16 V2X does not support relay communication (both UE-to-network or UE-to-UE relay).

Based on V2X security TS 33.536 [bb], the Direct Provisioning Function (DPF) defined in TS 23.303 [cc] is replaced by PCF, based on the V2X architecture as defined in TS 23.287 [dd], and is not supported by the DDNMF. The architecture reference model as described in clause 2 User Plane based architecture, with the following additional considerations:

- each PLMN deploys one logical 5G DDNMF

- the 5G DDNMF interacts with PCF for the authorization of the ProSe discovery service

Fig 5.X.1-1. User Plane architecture for ProSe

In LTE ProSe, the ProSe Key Management Function supports the key derivation required to support the UE-to-network relay communication.

Whereas in 5G the existing entity can support the key derivation, authentication and authorization of the remote UE and UE-to-Network relay.

In order to attach to the network via a UE-to-network relay, a remote UE may have to authenticate to the network and vice versa. Because the UE-to-network relay sits in between the remote UE and the network, it may have the possibility to perform MitM, DoS, and replay attacks in between.

### 5.X.2	Security Threats

Following are the possible threats

-	A man-in-the-middle attack by the relay UE;

-	A denial of service attack by the relay UE on the remote UE;

-	Impersonation of the remote UE by the relay UE.

### 5.X.3	Potential Requirements

-	5GS shall support secure communication between the remote UE and the network via UE-to-Network relays.

-	5GS shall support generation of separate security contexts for remote UEs for ProSe relay communication.

*****End of changes*****