3GPP TSG-SA3 Meeting #100e 	S3-201962

# e-meeting, 17 -28 August 2020													Revision of S3-20xxxx

# Source:	Samsung

# Title:	Key Issue on security policies handling in L2 relay communication

# Document for:	Approval

Agenda Item:	5.10

# 1	Decision/action requested

It is requested to approve this key issue for TR 33.847.

# 2	References

[1]	3GPP TR 33.847: "Study on security aspects of enhancement for proximity based services in the 5G System (5GS)".

# 3	Rationale

This key issue describes the issue with two security policies handling when the remote UE accesses the network via relay and PC5 unicast link (remote UE to relay UE) and Uu (relay UE to network) is established. It is proposed to agree this key issue in TR 33.847.

# 4	Detailed proposal

*****Start of change*****

## 5.Z	Key Issue #Z: Key issue on handling security policies in L2 relay communication

### 5.Z.1	Key issue details

This key issue is to describe the issue with two security policies handling when the remote UE accesses the network via L2 relay and PC5 unicast link (remote UE to relay UE) and Uu (relay UE to network) is established.

The provisioned security policy for PC5 unicast link between remote UE and relay UE may not be same as security policy pre-provisioned for Uu interface between the relay UE and network. This may lead to different protection applied at PC5 level and Uu level.

NOTE: 	This key issue is applicable only if Layer-2 relay is adopted.

### 5.Z.2	Security Threats

Different protection applied at PC5 link and Uu may lead to degraded data protection and an attacker can eavesdrop and modify the sensitive user data sent over PC5 or Uu.

### 5.Z.3	Potential Requirements

### The encryption and integrity protection enabled over both Uu and PC5 shall be same.

*****End of change*****