3GPP TSG-SA3 Meeting #100e 	S3-202019

# e-meeting, 17 -28 August 2020													Revision of S3-20xxxx

# Source:	THALES

# Title:	pCR to TR 33.846: editorial corrections for solution #2.4

# Document for:	Approval

Agenda Item:

# 1	Decision/action requested

Editorial corrections to solution#2.4 in 3GPP TR 33.846

# 2	References

[1]	3GPP TR 33.846 v0.6.0

# 3	Rationale

This contribution proposes editorial corrections to the description of the solution #2.4 in clause 6.2.4.2 of 3GPP TR 33.846 [1] in order to have consistent numbering of the steps in the figure 6.2.4.2-1 and in the description.

# 4	Detailed proposal

It is proposed that SA3 review and approve the following pseudo-CR to 3GPP TR 33.846 [1].

*** START of CHANGE ***

#### 6.2.4.2	Solution details

The procedure works as follow when the USIM detects a MAC failure or a synchronisation failure during the authentication procedure.

Figure 6.2.4.2-1: Mitigation against linkability issue

- The home network sends an authentication request.

- The SEAF sends the authentication request to the UE.

- The USIM verifies the freshness of the 5G authentication vector by checking whether the AUTN can be accepted.

If the USIM detects a MAC failure, then the USIM returns a synchronisation failure message (AUTS) consisting of a random number.

If the USIM detects a synchronisation failure, then the USIM generates a random value RAND_SQN, returns an AUTS containing RAND_SQN instead of the SQNMS and the corresponding MAC-S based on RAND_SQN.

- The UE sends the authentication response to the SEAF.

- The SEAF sends to the home network a Nausf_UEAuthentication_Authenticate Request with a synchronization failure indication.

- The home network checks the MAC-S value send by the USIM.

If the MAC-S verification is successful then the home network knows that the failure corresponds to a synchronization failure. Otherwise, the home network concludes that the failure corresponds to a MAC failure.

The home network can take the decision to create a new authentication vector either to run a new authentication procedure or to run an authentication procedure for resynchronisation in order to retrieve the SQNMS value from the UE.

In case of authentication procedure for resynchronisation

- The home network decides to perform authentication procedure.

The home network retrieves RAND_SQN from the AUTS previously sent by the USIM, generates a new random RAND_SVR and computes RAND_Sync, where RAND_Sync = RAND_SQN || RAND_SVR

The home network computes an authentication vector built with RAND_Sync, sets AMF field to indicate a resynchronization procedure, and sends the authentication vector to the SEAF.

- The home network sends an authentication request.

- The SEAF sends the authentication request to the UE.

- The USIM verifies the freshness of the 5G authentication vector by checking whether the AUTN can be accepted.

If the MAC is valid and if the AMF field indicates a resynchronization procedure, then the USIM verifies that the received RAND_Sync has been generated based on the USIM Random_SQN previously sent. If the verification of the RAND_Sync is successful, then the USIM computes AK = f5K (RAND_Sync), and returns AUTS (SQNMS ( AK || MAC-S).

- The UE sends the Authentication response to the SEAF.

- The SEAF sends to the home network a Nausf_UEAuthentication_Authenticate Request with a synchronization failure indication.

- The home network checks the MAC-S value sent by the USIM.

If the MAC-S verification is successful then the home network knows that the failure corresponds to a synchronization failure. Additionnaly, the home network knows that an authentication procedure for resynchronisation procedure is ongoing. Consequently, the home network uses RAND_Sync to compute AK and retrieves SQNMS.

Additionally, in order to improve the security, the following steps can take place:

- The USIM records all authentication errors (MAC and Sequence Number errors)

- The USIM informs the user of potential attack when counters reaches a pre-defined threshold

- Once the connection is established, the USIM reports the attack location and attack scenario.

The solution impacts only the USIM and the home network. The solution requires change of the USIM.

Editor’s Note: Threat analysis for authentication resynchronization will need to be done.

Editor’s Note: The need for unified failure cause is FFS.

# Text boxes

2. Authentication request

10. Authentication Response

- AV)

11. Nausf_UEAuthentication_Authenticate Request

(synchronisation failure)

5. Nausf_UEAuthentication_Authenticate Request

(synchronisation failure)

1. Authentication request (5G SE AV)

4. Authentication Response

9. Authentication request

UE

Home network

AUSF/ UDM/ARPF

3. The USIM checks AUTN and detects a MAC failure or a synchronization failure

The USIM returns AUTS parameter

AMF/SEAF

10. The USIM verifies the MAC, RAND_Sync and AMF field.

The USIM returns AUTS with SQNMS

Authentication for resynchronization

The USIM returns AUTS parameter

7. The home network generates new authentication vector with RAND_Sync and uses the AMF field to indicate a synchronization procedure

6. The home network checks MAC-S value to determine the type of the failure.

8. Authentication request (5G SE AV)

12. The home network verifies the integrity of MAC-S using AK computed with RAND_Sync and retrieves SQNMS.

2. Authentication request

11. Authentication Response

- AV)

12. Nausf_UEAuthentication_Authenticate Request

(synchronisation failure)

5. Nausf_UEAuthentication_Authenticate Request

(synchronisation failure)

1. Authentication request (5G SE AV)

4. Authentication Response

9. Authentication request

UE

Home network

AUSF/ UDM/ARPF

3. The USIM checks AUTN and detects a MAC failure or a synchronization failure

The USIM returns AUTS parameter

AMF/SEAF

10. The USIM verifies the MAC, RAND_Sync and AMF field.

The USIM returns AUTS with SQNMS

Authentication for resynchronization

The USIM returns AUTS parameter

7. The home network generates new authentication vector with RAND_Sync and uses the AMF field to indicate a synchronization procedure

6. The home network checks MAC-S value to determine the type of the failure.

8. Authentication request (5G SE AV)

13. The home network verifies the integrity of MAC-S using AK computed with RAND_Sync and retrieves SQNMS.