## Slide 1: [SA3#103-e][4.22, oauth][S3-212249]
Summary of discussion: NRF services authorization and OAuth 2.0 client registration from Rel-15 onwards

## Slide 2: NRF services in general (13.3.1)
NRF services: NF Register, NF Discovery, NF Request access token
Current text in NOTE says, Oauth access token for authorization is not needed
General agreement: For NF Request access token, Oauth 2.0 access token is not needed
Discussion on
Oauth 2.0 access token for NF Register or NF discovery (status: optionaly allowed in CT4, this is in line with SA3 NOTE, which says „not needed“)
  Rel-15/16 – compromise proposal could be to say „is not recommended“ (+ CT4 discouragement of the feature in their specs)
  Note: „shall not be used“ would be stronger than „not needed“ and companies that followed stage 3 may already have this feature, so better to say not recommended ?
  Rel-17 – allow this option with „may be used“ in line with CT4 specs

## Slide 3: NRF service - NF registration (13.4.1)
Current spec text mandates NF Register in connection with Oauth client registration
proposal is to make it optional (seems in geneal fine by companies), but
  There is a need to add some explanation, if one does not want to use the (only) option; also how to deal with NF consumer that do not use NF Register
  Important from Nokia point of view to clarify „An NF that does not implement this option shall still be able to get Access tokens (and NRF services).”
In compromise discussion, local configuration and static authorization was mentioned
Proposal to split description in 2 parts
  Oauth 2.0 client registration (any NF who wants to have a token, need to be known)
  NF Service registration

## Slide 4: Open issue: How to capture, if Oauth 2.0 client registration is not done together with NF Register?
How is OAuth 2.0 client registered at the NRF if no NF service registration takes place?
As explained during CT4/SA3 calls, there are NFs that do not need NF Service registration, thus, those would not be known as OAuth client then, if the only way to register a Oauth client is by NF service registration.
In this case, spec should mentions sth along the lines: If OAuth 2.0 client registration is not done by NF service registration, the client can be registered at the NRF by local configuration.

## Slide 5: Proposal (Nokia)
Rel-15, 16:
Using Oauth 2.0 for NF access token request shall not be used.
Using Oauth 2.0 for NF discovery and registration services is not recommended.
NF service registration may be used for client registration.
NF that has not registered by NF service registration can still get access token.
Rel-17:
Using Oauth 2.0 for NF access token request shall not be used.
Using Oauth 2.0 for NRF discovery and registration services may be used.
NF service registration may be used for client registration.
NF that has not registered by NF service registration can still get access token.
Local configuration may be used for client registration.