# 3GPP TSG-SA3 (Security)	S3-100473

# SA3#59, 26-30 Apr 2010, Lisbon, Portugal	revision of S3-10xyzw

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.320 | CR | 0022 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction to description of H(e)NB-GW |
| --- | --- |
| Source to WG: ( | Huawei |
| Source to TSG: ( | SA3 |
| Work item code: ( | EHNB-Sec |  | Date: ( | 18/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Current description of H(e)NB-GW is not exact. H(e)NB-GWs have other functionalities besides the concertrator for control plane traffic to/from multiple H(e)NBs. Functionalities of H(e)NB-GW are specified in specifications defined in RAN group. It is proposed to refer to RAN specifications. In addition, it’s proposed to delete section 4.2.7 since there is no text in this section. Some editorial changes are also needed. |
| Summary of change: ( | Definition of H(e)NB-GW is refered to RAN specifications. Title of section 4.2.7 is changed to void. Some editorial changes are also made. |
| Consequences if ( not approved: | Inaccurate description of H(e)NB-GW. Mistakes in specification. |
| Clauses affected: ( | 2, 4, |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*****************************Start of the first changes******************************

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

For a specific reference, subsequent revisions do not apply.

For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: “Vocabulary for 3GPP Specifications”.

[2]		3GPP TS 32.583: “Telecommunications management; Home Node B (HNB) Operations, Administration, Maintenance and Provisioning (OAM&P); Procedure flows for Type 1 interface HNB to HNB Management System (HMS)”.

[3]	IETF RFC 4187: “Extensible Authentication Protocol Method for 3rd Generation Authentication and Key Agreement (EAP-AKA)”.

[4]	IETF RFC 4306: “Internet Key Exchange (IKEv2) Protocol”.

[5]	IETF RFC 4301: “Security Architecture for the Internet Protocol”.

[6]  	IETF RFC 4739: “Multiple Authentication Exchanges in the Internet  Key Exchange (IKEv2 Protocol”, Nov 2006.

[7]	3GPP TS 33.310: “Network Domain Security (NDS); Authentication Framework (AF)”.

[8]  	3GPP TS 23.003: “Numbering, addressing and identification”.

[9]	3GPP TS 33.210: “3G security; Network Domain Security (NDS); IP network layer security”.

[10] 	3GPP TS 33.234: “3G security; Wireless Local Area Network (WLAN) interworking security”.

[11]	3GPP TS 32.593: “Telecommunication management; Procedure flows for Type 1 interface H(e)NB to H(e)NB Management System (H(e)MS)”.

[12] 		GPP TS 25.467: “UTRAN architecture for 3G Home Node B (HNB); Stage 2”.

[13]	3GPP TS 24.008: “Mobile radio interface Layer 3 specification; Core network protocols; Stage 3”.

[14]	3GPP TS 24.301: “Non-Access-Stratum (NAS) protocol for Evolved Packet System (EPS); Stage 3”.

[15]	The Broadband Forum TR-069: “CPE WAN Management Protocol v1.1”, Issue 1 Amendment 2, December 2007.

[16]	IETF RFC 4346:  “The Transport Layer Security (TLS) Protocol Version 1.1”.

[17]	IETF RFC 5246:  “The Transport Layer Security (TLS) Protocol Version 1.2”.

[18]	ETSI ES 282 004 (V1.1.1): Telecommunications and Internet Converged Services and Protocols for Advanced Networking (TISPAN); NGN functional architecture; Network Attachment Sub-System (NASS), 2006.

[19]	ETSI ES 283 035 (V1.1.1): "Telecommunications and Internet Converged Services and Protocols for Advanced Networking (TISPAN); Network Attachment Sub-System (NASS); e2 interface based on the DIAMETER protocol",,2006.

[20]	3GPP TS 33.102: “3G security; Security architecture”

[21]	3GPP TS 33.401: “3GPP System Architecture Evolution (SAE): Security architecture”

[22]	IETF RFC 2560: “X.509 Internet Public Key Infrastructure Online Certificate Status Protocol – OCSP”

[23]	Open Mobile Alliance OMA-WAP-OCSP V1.0: "Online Certificate Status Protocol Mobile Profile". URL: http://www.openmobilealliance.org/

[24]	IETF RFC 4806: “Online Certificate Status Protocol (OCSP) Extensions to IKEv2”

[25]	IETF RFC 4366: “Transport Layer Security (TLS) Extensions”

[26]	IETF RFC 5280:” Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile”

[x]	3GPP TS 36.300: “Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Overall description; Stage 2”

****************************End of the first changes*******************************

****************************Start of the second changes******************************

# 4	Overview of Security Architecture and Requirements

## 4.1	System architecture of H(e)NB

Figure 4.1.1: System Architecture of H(e)NB

Description system architecture:

-	Air interface between UE and H(e)NB should be backwards compatible air interface in UTRAN or E-UTRAN;

-	H(e)NB access operator’s core network via a Security Gateway. The backhaul between H(e)NB and SeGW may be insecure.

-	Security Gateway represent operator’s core network to perform mutual authentication with H(e)NB.

-	AAA server authenticates the hosting party based on the authentication information retrieved from HSS when hosting party authentication is performed.

-	Security tunnel is established between H(e)NB and Security Gateway to protect information transmitted in backhaul link. IPsec use for this security tunnel is mandatory to implement but optional to use based on an operator policy. If the operator chooses not to use IPsec, the interface between the H(e)NB and SeGW shall be secured with a mechanism that provides layer 2 security for confidentiality and integrity protection of communications. This mechanism then shall also bind this secure communications to device authentication and optional HPM authentication.

Editor's Note: The consistency of the above statement with the rest of the present document needs to be checked further carefully. According to IETF RFCs, IKEv2 and IPsec ESP must always be used jointly. However, there is a draft in IETF in the early stage on separating IKE and IPSec.

NOTE: The details of this layer 2 security mechanism and the binding are out of scope of this standard.

-	HNB-GW performs the mandatory access control and HNB performs the optional access control in case non-CSG capable UEs or non-CSG capable HNBs. SeGW and HNB-GW are logically separate entities within operator’s network. If the SeGW and the HNB-GW are not integrated, then the interface between the HNB-GW and the SeGW may be protected using NDS/IP [9].

-	HeNB-GW is optional to deploy. If HeNB-GW is deployed, then SeGW may be integrated into HeNB-GW. If the SeGW and the HeNB-GW are not integrated, then the interface between the HeNB-GW and the SeGW may be protected using NDS/IP [9].

-	H(e)MS, H(e)NB-GW, or MME performs location verification of H(e)NB [12].

-	Secure communication is required to H(e)NB Management System (H(e)MS).

## 4.2	Network Elements

### 4.2.1	H(e)NB

The H(e)NB is a network element that connects User Equipment via its radio interface to the operator’s core network. The backhaul link to the operator’s core network is a broadband connection. A H(e)NB is typically deployed in customers’ premises.

NOTE: 	The term H(e)NB refers to both Home NodeB (HNB) and Home eNodeB (HeNB), when both are meant without distinction.

### 4.2.2	Security Gateway (SeGW)

The SeGW is a network element at the border of the operator’s core network. After successful mutual authentication between the H(e)NB and the SeGW, the SeGW connects the H(e)NB to the operator’s core network. Any connection between the H(e)NB and the core network is tunnelled through the SeGW.

### 4.2.3	H(e)NB Management System (H(e)MS)

The H(e)MS is a management server that configures the H(e)NB according to the operator’s policy. H(e)MS is also capable of installing software updates on the H(e)NB. The H(e)MS server may be located inside the operator’s core network (accessible on the MNO Intranet) or outside of it (accessible on the public Internet).

The HMS is specified in TS 32.583 [2].

The HeMS is specified in TS 32.593 [11].

### 4.2.4	UE

UE is a standard user equipment for UMTS (for HNB) or LTE (for HeNB).

### 4.2.5	H(e)NB Gateway (H(e)NB-GW) and MME

HNB-GW is specified in TS 25.467 [12] and HeNB-GW is specified in TS 36.300 [x]. The H(e)NB-GW and the SeGW may be co-located. The HeNB-GW is optional, while the HNB-GW is mandatory. In the absence of a HeNB-GW, the HeNB is directly connected to the MME via the SeGW.

### 4.2.6	AAA Server and HSS

HSS stores the subscription data and authentication information of the H(e)NBs. When hosting party authentication is required, AAA server authenticates the hosting party based on the authentication information retrieved from HSS.

### 4.2.7	Void

## 4.3	Interfaces (Reference Points)

### 4.3.1	Backhaul Link

The backhaul link used between H(e)NB and SeGW provides a secure tunnel carrying both the user plane data and the control plane data that are transmitted between the H(e)NB and network elements in the core network.

H(e)MS traffic is also tunnelled through this secure backhaul link, if the H(e)MS is accessible on the MNO Intranet.

The backhaul link may also carry other data between H(e)NB and core network, e.g. time protocol traffic.

### 4.3.2	H(e)MS Interface

The H(e)MS Interface between the H(e)NB and the H(e)MS server shall provide a secure connection carrying configuration data., SW updates and additional data, e.g. location information.

### 4.3.3	Interface between SeGW and AAA Server, AAA Server and HSS

The interface between the SeGW and AAA Server provides a secure connection carrying authentication, authorization, and related information.

The interface between AAA Server and HSS provides a secure connection for the retrieval of authentication vectors (e.g. for hosting party authentication) and retrieval of H(e)NB access-related information for HPM.

## 4.4	Security Requirements and Principles

### 4.4.1	Operation

The requirements on operation are:

-	Only algorithms of adequate cryptographic strength shall be used for authentication and protection of confidentiality and integrity.

-	Modifications of Hosting Party controlled information by the operator shall only be allowed with the permission of the Hosting Party.

-	The extent of Hosting Party controllable information shall be controlled by the operator.

-	IMSIs of UEs connected to H(e)NB shall not be revealed to the Hosting Party of the H(e)NB.

### 4.4.2	Requirements on H(e)NB

The requirements on the H(e)NB are:

-	The integrity of the H(e)NB shall be validated before any connection into the core network is established.

-	The H(e)NB shall be authenticated by the SeGW based on a globally unique and permanent H(e)NB identity.

- 	The H(e)NB shall authenticate the SeGW.

-	Optionally the hosting party of the H(e)NB may be authenticated.

-	If hosting party authentication is used, the H(e)NB shall shut down its air interface and disconnect from the operator’s core network on removal of the HPM which was used for authentication towards the MNO.

-	The H(e)NB shall authenticate the H(e)MS, if the H(e)MS is accessed on the public Internet.

-	The H(e)NB shall be authenticated by the H(e)MS using the same identity as for authentication to the SeGW, if the H(e)MS is accessed on the public Internet.

-	The configuration and the software of the H(e)NB shall only be updated in a secure way, i.e. the integrity of the configuration data including the licensed radio parameters and the integrity of the software updates must be verified.

-	Sensitive data including cryptographic keys, authentication credentials, user information, user plane data and control plane data shall not be accessible at the H(e)NB in plaintext to unauthorized access.

-	The time base of the H(e)NB shall be synchronized to the core network.

-	The location of the H(e)NB shall be reliably transferred to the network.

-	The H(e)NB shall be capable of filtering unauthenticated traffic received from the access network. Operator policy shall control which types of unauthenticated traffic are filtered.

-	All security requirements of the eNB secure environment of TS 33.401 [21] clause 5.3 shall apply to the HeNB. Security measures to establish this secure environment shall be assured by the TrE (subclause 5.1.2) where they fall under the capability of the TrE.

### 4.4.3	Requirements on SeGW

The requirements on the SeGW are:

-	The SeGW shall be authenticated by the H(e)NB using a SeGW certificate. The SeGW certificate shall be signed by a CA trusted by the operator.

- 	The SeGW shall authenticate the H(e)NB based on H(e)NB certificate.

-	The SeGW may authenticate the hosting party of the H(e)NB in cooperation with the AAA server using EAP-AKA [3].

-	The SeGW shall allow the H(e)NB access to the core network only after successful completion of all required authentications.

-	Any unauthenticated traffic from the H(e)NB shall be filtered out at the SeGW.

### 4.4.4	Requirements on H(e)MS

The requirements on the H(e)MS are:

-	The H(e)MS shall be authenticated by the H(e)NB if the H(e)MS is accessible on the public Internet and may be authenticated by H(e)NB if the H(e)MS is accessible on the MNO Intranet using a H(e)MS certificate. The H(e)MS certificate shall be provided by a MNO trusted CA.

-	The H(e)MS shall authenticate the identity of the H(e)NB if the H(e)MS is accessible on the public Internet and may authenticate the identity of the H(e)NB if the H(e)MS is accessible on the MNO Intranet, using a H(e)NB certificate. This identity shall be the same as used during backhaul link establishment (cf. sub-clause 4.4.5 of this document).

-	If the H(e)MS is accessible on the MNO Intranet and the mutual authentication between H(e)MS and H(e)NB is not performed the identity of H(e)NB has to be transferred over the H(e)MS link.

NOTE 1:	In case of H(e)MS accessible on the MNO intranet there may be an additional secure end-to-end tunnel between H(e)NB and H(e)MS carried inside the secure backhaul link.

NOTE 2: 	Mutual authentication between H(e)MS and H(e)NB may not be necessary if the H(e)NB is connected to the H(e)MS through the core network and mutual authentication between H(e)NB and SeGW has taken place.

### 4.4.5	Requirements on Backhaul Link

The requirements on the backhaul link are:

-	The establishment of the secure backhaul link shall be based on IKEv2 [4] comprising the required authentications as given in subclauses 4.4.2 and 4.4.3 of this document.

-	The backhaul link shall provide integrity, confidentiality and replay protection of the transmitted data.

-	The security solution for the backhaul link shall be based on IPsec ESP tunnel mode [9].

-	Any connection between the H(e)NB and the core network shall be tunnelled through the Backhaul Link.

-	The security solution for the backhaul link shall be compatible with common network address and port translation variations and support firewall traversal.

### 4.4.6	Requirements on H(e)MS Link

The requirements on the H(e)MS link are:

-	The establishment of the secure H(e)MS link shall be based on the authentication principles as given in subclauses 4.4.2 and 4.4.4 of this document.

-	The H(e)MS link shall provide integrity, confidentiality and replay protection of the transmitted data data between H(e)MS and H(e)NB.

****************************End of the second changes*******************************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

# Text boxes

AAA Server/HSS

H(e)MS

H(e)MS

H(e)NB-GW

Operator’s core network

insecure link

SeGW

H(e)NB

UE