# 3GPP TSG-SA3 (Security)	S3-100611

# SA3#59, April 26-30, 2010, Lisbon, Portugal	revision of S3-100523

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.320 | CR | 0027 | ( rev | 1 | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Section 4.1 Editor’s Note Resolution |
| --- | --- |
| Source to WG: ( | Huawei |
| Source to TSG: ( | SA3 |
| Work item code: ( | EHNB-Sec |  | Date: ( | 04/26/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | SA2 and RAN3 work has completed, there is no need for the editor’s note. |
| Summary of change: ( | Remove the editor’s note in Sections 4.1 |
| Consequences if ( not approved: | Incomplete specification. |
| Clauses affected: ( | 4.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

************************** start of changes ************************

## 4.1	System architecture of H(e)NB

Figure 4.1.1: System Architecture of H(e)NB

Description system architecture:

-	Air interface between UE and H(e)NB should be backwards compatible air interface in UTRAN or E-UTRAN;

-	H(e)NB access operator’s core network via a Security Gateway. The backhaul between H(e)NB and SeGW may be insecure.

-	Security Gateway represent operator’s core network to perform mutual authentication with H(e)NB.

-	AAA server authenticates the hosting party based on the authentication information retrieved from HSS when hosting party authentication is performed.

-	Security tunnel is established between H(e)NB and Security Gateway to protect information transmitted in backhaul link. IPsec use for this security tunnel is mandatory to implement but optional to use based on an operator policy. If the operator chooses not to use IPsec, the interface between the H(e)NB and SeGW shall be secured with a mechanism that provides layer 2 security for confidentiality and integrity protection of communications. This mechanism then shall also bind this secure communications to device authentication and optional HPM authentication.

Editor's Note: The consistency of the above statement with the rest of the present document needs to be checked further carefully. According to IETF RFCs, IKEv2 and IPsec ESP must always be used jointly. However, there is a draft in IETF in the early stage on separating IKE and IPSec.

NOTE: The details of this layer 2 security mechanism and the binding are out of scope of this standard.

-	HNB-GW performs the mandatory access control and HNB performs the optional access control in case non-CSG capable UEs or non-CSG capable HNBs. SeGW and HNB-GW are logically separate entities within operator’s network. If the SeGW and the HNB-GW are not integrated, then the interface between the HNB-GW and the SeGW may be protected using NDS/IP [9].

-	HeNB-GW is optional to deploy. If HeNB-GW is deployed, then SeGW may be integrated into HeNB GW. If the SeGW and the HeNB-GW are not integrated, then the interface between the HeNB-GW and the SeGW may be protected using NDS/IP [9].

-	H(e)MS, H(e)NB-GW, or MME performs location verification of H(e)NB [12].

-	Secure communication is required to H(e)NB Management System (H(e)MS).

************************** end of changes *********************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

# Text boxes

AAA Server/HSS

H(e)MS

H(e)MS

H(e)NB-GW

Operator’s core network

insecure link

SeGW

H(e)NB

UE