# 3GPP TSG-SA3 (Security)	S3-100614

# SA3#59, 26-30 April 2010, Lisbon, Portugal	revision of S3-100502

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.320 | CR | 0028 | ( rev | 1 | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network | X | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Addition of missing trust relation requirement for CA issuing H(e)NB device certificate |
| --- | --- |
| Source to WG: ( | Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( |  |
| Work item code: ( | EHNB-Sec |  | Date: ( | 08/04/2010 |
| Category: ( | F |  | Release: ( | 9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | TS 33.320 requires a successful device integrity validation as prerequisite for the execution of the mutual device authentication with the network. This implies that a H(e)NB device with valid device certificate may indicate such integrity validation to the network. Therefore the CA issuing the device certificate must be trusted by the vendor or manufacturer, whoever of both guarantees the device integrity. TS 33.320 contains in the requirements for the H(e)NB device certificate explicitly only the fact that the CA issuing the device certificate must be trusted by the operator. This CR adds the explicit text that the CA issuing the device cert must also be trusted and authorized by the manufacturer or vendor. In addition, the text in clause 5.2 on trust in the CA issuing the device certificate is clarified. |
| Summary of change: ( | The explicit requirement is added in clauses 7.1 and 8.3.2.2 on device validation that the vendor/manufacturer of the H(e)NB has to trust and to authorize the CA issuing the device certificate. This requirement is also added to the specific certificate requirements in clauses 7.2.5.2.1 and 8.3.3.1. The text in clause 5.2 on trust in the CA issuing the deivce certificate is clarified, to the extent, that the last few words “trusted by the operator” apply to the whole list of instances, and not only to the “another party”. |
| Consequences if ( not approved: | An implicit assumption of the solution selected for device integrity validation is not stated explicitly as requirement. The meaning of one sentence in clause 5.2 could be mis-understood, that there is no trust of the operator required in the vendor or manufacturer when providing the device certificate. |
| Clauses affected: ( | 5.2, 7.1, 7.2.5.2.1, 8.3.2.2, 8.3.3.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

********************** start of 1st change ***************************

## 5.2	Device Mutual Authentication

The device mutual authentication is mandatory for H(e)NB.

Device mutual authentication shall be performed using certificates. The H(e)NB’s credentials and critical security functions for device authentication shall be protected inside a TrE.

The device mutual authentication shall be securely bound to device integrity validation. This procedure, when successful, leads to mutual authentication between the H(e)NB and the SeGW.

The certificate-based device authentication shall have the following parts:

-	The H(e)NB shall be provisioned with a device certificate. This device certificate allows the authentication of the H(e)NB by the SeGW (and thus the operator network). The device certificate shall be provided by a CA trusted by the operator, e.g. the operator, the manufacturer or the vendor of the H(e)NB, or by another party trusted by the operator.

-	The SeGW shall be configured with a certificate. This certificate allows the authentication of the SeGW by H(e)NB. The certificate shall be provided by an operator trusted CA.

-	A Fully Qualified Domain Name (FQDN) formatted identifier shall be used for certificate based authentication of the H(e)NB and of the SeGW. For the H(e)NB this FQDN shall be globally unique. If no DNS is available for resolution of the FQDN of the SeGW, then the IP address of SeGW shall be used as identifier.

-	The H(e)NB may check the revocation status of certificates using OCSP.

-	The SeGW may check the revocation status of certificates using CRLs or OCSP.

********************** start of 2nd change ***************************

## 7.1	Device Validation

The H(e)NB shall support a device validation method where the device implicitly indicates its validity to the SeGW or H(e)MS by successful execution of device authentication. To achieve this, the following requirement applies:

-	If the device integrity check according to clause 6.1 failed, the TrE shall not give access to the sensitive functions using the private key needed for H(e)NB device authentication with the SeGW.

-	The CA issuing the H(e)NB device certificate need to be trusted by the manufacturer or vendor of the H(e)NB, whoever of both is responsible for the device integrity of the H(e)NB.

NOTE:	This trust in the CA issuing the device certificate is in addition to the requirements given in clause 5.2.

********************** start of 3rd change ***************************

##### 7.2.5.2.1	IKEv2 Entity Certificates

The H(e)NB and SeGW certificates shall both conform to the requirements set out in clauses 6.1.1 and 6.1.3 of TS 33.310 [7] with the following additions and exceptions:

-	The H(e)NB certificate shall be signed by an entity that is authorized by the operator, e.g. the manufacturer or the vendor. In addition, the entity signing the H(e)NB certificate shall be authorized by the manufacturer or vendor.

-	The H(e)NB certificate shall carry the H(e)NB identity in FQDN format in the subjectAltName.  This identity shall be the same as the identity in the IDi payload of the first IKE_AUTH request.

-	If the manufacturer or vendor provides a CRL or OCSP server, the H(e)NB certificate shall carry the CRL distribution point as specified in TS 33.310 [7] or the OCSP server information (AIA extension) as specified in RFC5280 [26] and RFC 2560 [22].

NOTE: Server information for CRL and/or OCSP servers deployed in operator network may be configured in SeGW.

-	If the operator provides an OCSP server, the SeGW certificate shall carry the OCSP server information as specified in RFC 2560 [22]. This OCSP server information is not mandatory, if OCSP extension according to RFC 4806 [24] is used.

Editor’s Note:  The H(e)NB identity should be specified by CT4 as “HNB unique identity” in a new sub-clause of clause 4 in TS 23.003 [8]. Once this is done, this editor’s note should be replaced by a reference to this new sub-clause.

********************** start of 4th change ***************************

#### 8.3.2.2	Device Validation

The H(e)NB shall support a device validation method whereby the device implicitly indicates its validity to the H(e)MS by successful execution of device authentication. To achieve this, the following requirement applies:

-	If the device integrity check according to clause 6.1 failed, the TrE shall not give access to the sensitive functions using the private key needed for H(e)NB device authentication with the H(e)MS.

-	The CA issuing the H(e)NB device certificate need to be trusted by the manufacturer or vendor of the H(e)NB, whoever of both is responsible for the device integrity of the H(e)NB.

NOTE:	This trust in the CA issuing the device certificate is in addition to the requirements given in clause 5.2.

********************** start of 5th change ***************************

#### 8.3.3.1 	TLS entity certificates

The H(e)NB and H(e)MS certificates for use with TLS shall both conform to the requirements set out in clauses 6.1.1 and 6.1.3a of TS 33.310 [7] with the following additions and exceptions:

-	The H(e)NB certificate shall be signed by an entity that is authorized by the operator, e.g. the manufacturer or the vendor. In addition, the entity signing the H(e)NB certificate shall be authorized by the manufacturer or vendor.

-	The H(e)NB certificate shall carry the H(e)NB identity in FQDN format in both the subjectAltName extension of type dNSName and in the common name field.

-	If the manufacturer or vendor provides a CRL or OCSP server, the H(e)NB certificate shall carry the CRL distribution point as specified in TS 33.310 [7] or the OCSP server information (AIA extension) as specified in RFC 5280 [26] and RFC 2560 [22].

NOTE 1: Server information for CRL and/or OCSP servers deployed in operator network may be configured in H(e)MS.

Editor’s Note:	The H(e)NB identity should be specified by CT4 as “HNB unique identity” in a new sub-clause of clause 4 in TS 23.003 [8]. Once this is done, this editor’s note should be replaced by a reference to this new sub-clause.

- The H(e)MS certificate shall carry the identity of the H(e)MS in FQDN format in both the subjectAltName extension of type dNSName and in the common name field.

NOTE 2: The reason for carrying the identities in the common name field is compatibility.

-	If an OCSP server is provided for the H(e)MS certificates, the H(e)MS certificate shall carry the OCSP server information as specified in RFC 2560 [22]. This OCSP server information is not mandatory, if OCSP extension to TLS according to RFC 4366 [25] is used.

NOTE 3: In general, it is possible to use a TLS client certificate in accordance with this specification also for IKEv2, if key exchange algorithm and used key length for both TLS and IKEv2 are chosen identically.

********************** end of changes ***************************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.