3GPP TSG-SA3 (Security) 	( S3-100621

# SA3#59, 26-30 Apr 2010, Lisbon, Portugal

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.328 | CR | 0026 | ( rev | 1 | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | X | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | TS 33.328 e2ae indications |
| --- | --- |
| Source to WG: ( | Alcatel Lucent |
| Source to TSG: ( | SA3 |
| Work item code: ( | MEDIASEC |  | Date: ( | 12/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | An indication "e2ae-security confirmed by network" that needs to be returned in SDP answer from P-CSCF to the IMS UE is currently not defined in CT1 documents. |
| Summary of change: ( | Indication "e2ae-security confirmed by network" that needs to be returned in SDP answer from P-CSCF to the IMS UE is removed. |
| Consequences if ( not approved: | Misalignment between CT1 and SA3 specifications. |
| Clauses affected: ( | 5.4.1, 7.2.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

************* START OF 1. CHANGE *************

### 5.4.1 	Authentication and authorization for e2ae protection

E2ae security implies that no other IMS nodes, apart from P-CSCF (IMS-ALG) and IMS Access GW will terminate IMS media security.

The IMS UE and the P-CSCF (IMS-ALG) rely on SIP signalling security to authenticate each other. This is consistent with the fact that the security of the use of SDES entirely relies on SIP signalling security, cf. clause 5.5.

The P-CSCF (IMS-ALG) on the terminating side tells the IMS UE by an explicit indication, cf. clause 7.3.1, that e2ae security is provided, i.e. that the IMS UE shares the media keys with the P-CSCF (IMS-ALG) and not with some other entity. For the originating side see Note 3 in clause 7.2.1. Provided the IMS UE trusts SIP signalling security it can rely on this explicit indication for the following reasons: the IMS UE knows from registration that the P-CSCF (IMS-ALG) is capable of e2ae security, and that such a P-CSCF (IMS-ALG) will remove any such indication if inserted by another party, cf. clauses 7.2.1 and 7.3.1.

The IMS UE and the IMS Access GW authenticate each other by means of implicit key authentication: the IMS UE believes that only the IMS Access GW can have the media keys to protect the media because it trusts the P-CSCF (IMS-ALG) to give the keys only to the IMS Access GW. Similarly, the IMS Access GW trusts the P-CSCF (IMS-ALG) that the keys are shared only with this IMS UE.

The IMS UE implicitly authorizes the P-CSCF (IMS-ALG) and the IMS Access GW to perform e2ae security by indicating support for e2ae security during the registration in line with the IMS UE’s policy, cf. clause 7.1.

Conversely, an IMS UE is always authorized to participate in e2ae security if the network policy allows e2ae security, cf. clause 7.1.

************* END OF 1. CHANGE *************

************* START OF 2. CHANGE *************

### 7.2.1	IMS UE originating procedures for e2ae

Figure 5 shows the originating call set-up procedures for one RTP media stream using e2ae security.

NOTE:	The procedures shown in the figure apply to users located in their home service area. The same concepts apply to roaming users.

Figure 5: Originating call flow for e2ae case

The IMS UE A performs an IMS originating session set-up according to 3GPP TS 23.228 [3], with modifications as described in the following. If both IMS UE and network indicated support for e2ae-security during registration, then the IMS UE shall request e2ae-security for RTP media streams to be established as described in this clause, unless the IMS UE prefers e2e-security for a RTP media stream. The originating procedures for establishing a RTP media streams with e2e-security are described in clauses 7.2.2 and 7.2.3 of this specification. The IMS UE may learn of a preference for e2e-security for a particular RTP session or media stream by explicit user action via the user interface or by the security policy implemented on the IMS UE.

The procedure in the above figure for requesting e2ae-security for a RTP media stream is now described step-by-step.

1.	IMS UE A sends an SDP Offer for an SRTP stream containing one or more SDES crypto attributes, each with a key K11 and the other security context parameters required according to RFC 4568 [13], together with an indication "e2ae-security requested by UE",  to the P-CSCF (IMS-ALG). The optional key lifetime field shall be omitted.

NOTE 1: 	The omission of the key lifetime field is, according to RFC 4568 [13], a way to implicitly signal the default values for the key lifetime as defined in RFC 3711 [9]. The default values are 2^48 SRTP packets and 2^31 SRTCP packets.

2.	The P-CSCF (IMS-ALG) checks for the presence of the indication "e2ae-security requested by UE". If the indication is present and the P-CSCF (IMS-ALG) indicated support of e2ae-security during registration, the P-CSCF (IMS-ALG) allocates the required resources and includes the IMS Access GW in the media path. If the indication is not present the P-CSCF (IMS-ALG) proceeds as described in TS 23.228 [3].

NOTE 2: 	The inclusion of the IMS Access GW in the media path is required for the purposes of e2ae security even if it was not required otherwise.

3.	The P-CSCF (IMS-ALG) changes the transport from SRTP to RTP in the SDP Offer, selects one SDES crypto attribute and removes all received SDES crypto attributes and the indication "e2ae-security requested by UE". The P-CSCF (IMS-ALG) then sends the changed SDP offer towards the S-CSCF.

4.	The S-CSCF performs the required procedures according to TS 23.228 [3] and forwards the SDP Offer to the terminating network.

5.	The S-CSCF receives the SDP Answer from the terminating network.

6.	The S-CSCF forwards the SDP Answer to the P-CSCF (IMS-ALG).

7.	The P-CSCF (IMS-ALG) creates a key K12 for protecting the RTP media stream towards IMS UE A between the IMS Access GW and IMS UE A. The P-CSCF (IMS-ALG) communicates the established keys K11 and K12, as well as the other security context parameters required according to RFC 4568 [13], to the IMS Access GW. The P-CSCF (IMS-ALG) instructs the IMS Access GW to check integrity / decrypt the media stream arriving from IMS UE A using K11, to integrity protect / encrypt the media stream arriving from the terminating network using K12, and to set the key lifetime to the default values as defined in RFC 3711 [9].

8.	The P-CSCF (IMS-ALG) changes the transport from RTP to SRTP in the SDP Answer, includes one SDES crypto attribute with key K12 and other security context parameters, required according to RFC 4568 [13], and sends the SDP Answer to IMS UE A. The optional key lifetime field shall be omitted. After receiving this message IMS UE A completes the media security setup.

NOTE 3:  	The IMS UE can deduce that e2ae security is used from two facts: first, that the P-CSCF (IMS-ALG) indicated its support for e2ae security during registration; and second, that the IMS UE requested e2ae security in the SDP Offer.

9.	When the full session setup has been completed, and media can be sent, the protected media stream  is sent between IMS UE A and the IMS Access GW. IMS UE A integrity protects / encrypts and checks integrity / decrypts the media stream sent to and received from the network. The IMS Access GW checks integrity / decrypts the media stream arriving from IMS UE A before passing it on towards the terminating network. The IMS Access GW integrity protects / encrypts the media stream arriving from the terminating network before passing it on to IMS UE A.

A P-CSCF (IMS-ALG) supporting e2ae-security shall remove any indication "e2ae-security confirmed by network" if inserted in a SIP message by another party.

************* END OF CHANGES *************

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.