3GPP TSG-SA3 (Security) 	(S3-100445

Meeting SA3#59, 26 – 30 April, 2010, Lisbon, Portugal

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.328 | CR | 0030 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of text on SDES parameters for e2ae security |
| --- | --- |
| Source to WG: ( | Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( | SA3 |
| Work item code: ( | MEDIASEC |  | Date: ( | 12/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | For end-to-access-edge security, the IMS-ALG transfer all those parameters contained in the SDES crypto attributes exchanged between the UE and the IMS-ALG over the Iq interface to the IMS Access GW. The current wording in clauses 7.2.1 and 7.3.1 says that the transferred parameters are those “security context parameters required according to RFC 4568”. This could be read to mean that only those parameters that are mandatory according to RFC 4568 may be included in the SDES crypto attribute and transferred over Iq, which is not true. Furthermore, the current text seems to unintentionally rule out the option of providing several master keys in one SDES crypto attribute. Clause 7.1 is also included to take the opportunity to correct a few typos. |
| Summary of change: ( | Provide more appropriate wording to reflect the reason for change. |
| Consequences if ( not approved: | Misleading text and possibly incorrect stage 3 specifications. |
| Clauses affected: ( | 7.1, 7.2.1, 7.3.1 |
|  | Y | N |  |  |
| Other specs ( | x |  | Other core specifications ( | 23.334, 29.334, 24.229 |
| affected: |  | x | Test specifications |  |
|  |  | x | O&M Specifications |  |
| Other comments: ( |  |

* * * Start of changes * * * *

## 7.1	IMS UE registration procedures

The IMS UE performs an IMS registration according to 3GPP TS 23.228 [3], with modifications as described in the following. When performing the registration, an IMS UE supporting the mechanisms required for e2ae protection according to this specification shall include an indication "e2ae-security supported by UE" in the initial REGISTER message unless the IMS UE’s policy dictates otherwise.

When receiving indication "e2ae-security supported by UE" in the initial REGISTER message from the IMS UE the network shall store it. This indication shall be stored by an appropriate network node such that they are, or can be made, available to the P-CSCF (IMS-ALG) when receiving a terminating session set-up request. It is left to the stage 3 specification whether this requires storage of the indication at the P-CSCF (IMS-ALG), or the S-CSCF, or both during registration, and which node shall remove the indication. For this reason no figure with an information flow is given here.

When the P-CSCF (IMS-ALG) is capable of supporting the mechanisms required for e2ae protection according to this specification, and the network policy is to prefer e2ae protection for this registration, the network shall include an indication "e2ae-security supported by network" in a message to the IMS UE during registration. The IMS UE shall store this indication for use with originating session set-up procedures.

NOTE 1: 	The names "e2ae-security supported by UE" and "e2ae-security supported by network" of the above indications are just placeholders for the purposes of this specification. Their syntax is defined in the corresponding stage 3 specification.

NOTE 2: 	The network policy regarding e2ae protection could differ e.g. depending on the type of access network. Therefore, the policy may depend on the registration. This does not imply that the network policy depends on the individual subscription.

When an IMS UE initiates a call and both the IMS UE and the P-CSCF has indicated support of e2ae security, then the IMS UE shall secure all RTP media streams, either e2ae or e2e. When a P-CSCF on the terminating side receives an INVITE and the P-CSCF and the terminating IMS UE has indicated support of e2ae security, it shall secure all unprotected RTP streams towards the terminating IMS UE. A request for e2ae security from an IMS UE is only allowed if both the IMS UE and P-CSCF has indicated support of e2ae security. On the terminating side, the P-CSCF is only allowed to initiate e2ae security if both IMS UE and P-CSCF have indicated support of e2ae security.

NOTE 3:	A call may contain a mixture of protected (e2ae and/or e2e) and unprotected media streams/sessions.

* * * Next change * * * *

### 7.2.1	IMS UE originating procedures for e2ae

Figure 5 shows the originating call set-up procedures for one RTP media stream using e2ae security.

NOTE:	The procedures shown in the figure apply to users located in their home service area. The same concepts apply to roaming users.

Figure 5: Originating call flow for e2ae case

The IMS UE A performs an IMS originating session set-up according to 3GPP TS 23.228 [3], with modifications as described in the following. If both IMS UE and network indicated support for e2ae-security during registration, then the IMS UE shall request e2ae-security for RTP media streams to be established as described in this clause, unless the IMS UE prefers e2e-security for a RTP media stream. The originating procedures for establishing a RTP media streams with e2e-security are described in clauses 7.2.2 and 7.2.3 of this specification. The IMS UE may learn of a preference for e2e-security for a particular RTP session or media stream by explicit user action via the user interface or by the security policy implemented on the IMS UE.

The procedure in the above figure for requesting e2ae-security for a RTP media stream is now described step-by-step.

1.	IMS UE A sends an SDP Offer for an SRTP stream containing one or more SDES crypto attributes, together with an indication "e2ae-security requested by UE", to the P-CSCF (IMS-ALG). Each of these SDES crypto attributes contains at least one master key K11, and other security context parameters chosen by IMS UE A in accordance with RFC 4568 [13]. The optional key lifetime field shall be omitted.

NOTE 1: 	The omission of the key lifetime field is, according to RFC 4568 [13], a way to implicitly signal the default values for the key lifetime as defined in RFC 3711 [9]. The default values are 2^48 SRTP packets and 2^31 SRTCP packets.

2.	The P-CSCF (IMS-ALG) checks for the presence of the indication "e2ae-security requested by UE". If the indication is present and the P-CSCF (IMS-ALG) indicated support of e2ae-security during registration, the P-CSCF (IMS-ALG) allocates the required resources and includes the IMS Access GW in the media path. If the indication is not present the P-CSCF (IMS-ALG) proceeds as described in TS 23.228 [3].

NOTE 2: 	The inclusion of the IMS Access GW in the media path is required for the purposes of e2ae security even if it was not required otherwise.

3.	The P-CSCF (IMS-ALG) changes the transport from SRTP to RTP in the SDP Offer, selects one SDES crypto attribute and removes all received SDES crypto attributes and the indication "e2ae-security requested by UE". The P-CSCF (IMS-ALG) then sends the changed SDP offer towards the S-CSCF.

4.	The S-CSCF performs the required procedures according to TS 23.228 [3] and forwards the SDP Offer to the terminating network.

5.	The S-CSCF receives the SDP Answer from the terminating network.

6.	The S-CSCF forwards the SDP Answer to the P-CSCF (IMS-ALG).

7.	The P-CSCF (IMS-ALG) creates one SDES crypto attribute, containing at least one master key K12,, and other security context parameters chosen by the P-CSCF (IMS-ALG) in accordance with RFC 4568 [13], for protecting the RTP media stream towards IMS UE A between the IMS Access GW and IMS UE A. The P-CSCF (IMS-ALG) communicates the parameters contained in the SDES crypto attribute selected in step 3 as well as those in the SDES crypto attribute created in step 7 to the IMS Access GW. The P-CSCF (IMS-ALG) instructs the IMS Access GW to check integrity / decrypt the media stream arriving from IMS UE A using K11 (and possibly further master keys), to integrity protect / encrypt the media stream arriving from the terminating network using K12 (and possibly further master keys), and to set the key lifetime to the default values as defined in RFC 3711 [9].

8.	The P-CSCF (IMS-ALG) changes the transport from RTP to SRTP in the SDP Answer, includes the SDES crypto attribute created in step 7, as well as an indication "e2ae-security confirmed by network", and then sends the SDP Answer to IMS UE A. The optional key lifetime field shall be omitted. After receiving this message IMS UE A completes the media security setup.

NOTE 3:  	The indication "e2ae-security confirmed by network" would not be needed on the originating side, as the originating IMS UE knows from the registration that the P-CSCF (IMS-ALG) supports e2ae security and as the IMS UE requested e2ae-security in the SDP Offer. Therefore the IMS UE can deduce that e2ae-security is used from these facts. Note that this is different in the terminating case. To give an explicit conformation also in the originating case is provided in order to ensure conformance with the procedures for the terminating session setup.

9.	When the full session setup has been completed, and media can be sent, the protected media stream is sent between IMS UE A and the IMS Access GW. IMS UE A integrity protects / encrypts and checks integrity / decrypts the media stream sent to and received from the network. The IMS Access GW checks integrity / decrypts the media stream arriving from IMS UE A before passing it on towards the terminating network. The IMS Access GW integrity protects / encrypts the media stream arriving from the terminating network before passing it on to IMS UE A.

A P-CSCF (IMS-ALG) supporting e2ae-security shall remove any indication "e2ae-security confirmed by network" if inserted in a SIP message by another party.

* * * Next change * * * *

### 7.3.1	UE terminating procedures for e2ae

Figure 8 shows the terminating call set-up procedures for one RTP media stream using e2ae security.

NOTE 1:	The procedures shown in the figure apply to users located in their home service area. The same concepts apply to roaming users.

Figure 8: Terminating call flow for e2ae case

The IMS UE performs an IMS terminating session set-up according to 3GPP TS 23.228 [3], with modifications as described in the following. If both IMS UE and network indicated support for e2ae-security during registration and the P-CSCF (IMS-ALG) receives an SDP Offer for an RTP media stream from the S-CSCF, then the P-CSCF (IMS-ALG) shall establish e2ae-security as described in this clause.

NOTE 2: 	The P-CSCF (IMS-ALG) will not establish e2ae security if the SDP offer received from the S-CSCF indicates that e2e security is being offered (i.e. the offer is for an SRTP stream), cf. clauses 7.3.2 and 7.3.3 for the establishment of e2e security on the terminating side.

The procedure in the above figure is now described step-by-step.

1.	The S-CSCF in the terminating network receives an SDP Offer for an RTP media stream from the originating network.

2.	The S-CSCF performs the required procedures according to TS 23.228 [3] and forwards the SDP Offer for an RTP media stream to the P-CSCF (IMS-ALG).

3.	The P-CSCF (IMS-ALG) checks whether both the IMS UE and the P-CSCF (IMS-ALG) indicated support of e2ae-security during registration. If this is the case the P-CSCF (IMS-ALG) proceeds as described in this clause and allocates the required resources and includes the IMS Access GW in the media path. If this is not the case the P-CSCF (IMS-ALG) continues as described for a call without IMS media plane security.

NOTE 3: 	The inclusion of the IMS Access GW in the media path is required for the purposes of e2ae security even if it was not required otherwise.

4.	The P-CSCF (IMS-ALG) changes the transport from RTP to SRTP in the SDP Offer, includes one or more SDES crypto attributes, as well as an indication that e2ae security is offered by the network, and sends it to IMS UE B. Each of these SDES crypto attributes contains at least one master key K21, and other security context parameters chosen by the P-CSCF (IMS-ALG) in accordance with RFC 4568 [13]. The optional key lifetime field shall be omitted.

5.	IMS UE B selects one of the received SDES crypto attributes, and then replies with an SDP Answer for an SRTP media stream, including one SDES crypto attribute containing at least one master key K22, and other security context parameters chosen by IMS UE B in accordance with RFC 4568 [13]. The optional key lifetime field shall be omitted.

6.	The P-CSCF (IMS-ALG) communicates the parameters contained in the SDES crypto attribute selected by IMS UE B in step 5 as well as those in the SDES crypto attribute sent by IMS UE B in step 5 to the IMS Access GW. The P-CSCF (IMS-ALG) instructs the IMS Access GW to check integrity / decrypt the media stream arriving from IMS UE B using K22 (and possibly further master keys), to integrity protect / encrypt the media stream arriving from the originating network using K21 (and possibly further master keys), and to set the key lifetime to the default values as defined in RFC 3711 [9].

7.	The P-CSCF (IMS-ALG) changes the transport from SRTP to RTP in the SDP Answer, removes the SDES crypto attribute, and then sends the SDP Answer to the S-CSCF.

8.	The S-CSCF forwards the SDP Answer towards the originating network.

9.	When the full session setup has been completed, and media can be sent, the protected media streams are sent between the IMS UE B and IMS Access GW. IMS UE B integrity protects / encrypts and integrity check / decrypts the media streams sent to and received from the network. The IMS Access GW integrity checks / decrypts the media stream arriving from IMS UE B before passing it on towards the originating network. The IMS Access GW integrity protects / encrypts the media stream arriving from the originating network before passing it on to IMS UE B.

A P-CSCF (IMS-ALG) supporting e2ae-security shall remove any indication "e2ae-security offered by network" if inserted in a SIP message by another party.

* * * End of changes * * * *

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.