3GPP TSG SA WG3 Security - S3#59	( S3-100503

# Lisbon, Portugal, 26 - 30 April 2010 												revision of S3-10xxxx

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.328 | CR | 0032 | ( rev | - | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Alignment with the updated MIKEY-TICKET draft |
| --- | --- |
| Source to WG: ( | Ericsson, ST-Ericsson |
| Source to TSG: ( | SA3 |
| Work item code: ( | MEDIASEC |  | Date: ( | 19/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The IETF last call for the MIKEY-TICKET draft has ended and a new version that takes the received comments into account has been submitted. The TS needs to be aligned with this updated version. |
| Summary of change: ( | The reference in clause 2 is updated. The editor’s note in annex D is removed as the draft is very close to becoming an RFC. The profiling in clauses D.3 and D.4 is aligned with the updated draft. |
| Consequences if ( not approved: | An obsoleted draft is referenced. The editor’s note remains. The flags in the Ticket Policy are set errornously. |
| Clauses affected: ( | 2, D |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*** BEGIN CHANGES ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 23.002: "Network architecture".

[3]	3GPP TS 23.228: "IP Multimedia (IM) Subsystem".

[4]	3GPP TS 33.203: "3G Security; Access security for IP-based services".

[5]	3GPP TS 33.210: "3G Security; Network domain security; IP network layer security".

[6]	3GPP TS 33.220: "Generic Authentication Architecture (GAA); Generic bootstrapping architecture".

[7]	IETF RFC 1035: "DOMAIN NAMES - IMPLEMENTATION AND SPECIFICATION".

[8]	IETF RFC 2616: "Hypertext Transfer Protocol -- HTTP/1.1".

[9]	IETF RFC 3711: "The Secure Real-time Transport Protocol (SRTP)".

[10]	IETF RFC 3550:  "RTP: A Transport Protocol for Real-Time Applications".

[11]	IETF RFC 3830: "MIKEY: Multimedia Internet KEYing".

[12]	IETF RFC 4567: "Key Management Extensions for Session Description Protocol (SDP) and Real Time Streaming Protocol (RTSP)".

[13]	IETF RFC 4568: "Session Description Protocol (SDP) Security Descriptions for Media Streams".

[14]	draft-mattsson-mikey-ticket-03 (April 2010): "MIKEY-TICKET: An Additional Mode of Key Distribution in Multimedia Internet KEYing (MIKEY)".

Editor's note: The above document cannot be formally referenced until it is published as an RFC.

[15]	IETF RFC 4771: "Integrity Transform Carrying Roll-Over Counter for the Secure Real-time Transport Protocol (SRTP)".

[16]	Otway, D. and Rees, O. 1987: "Efficient and timely mutual authentication." SIGOPS Oper. Syst. Rev. 21, 1 (Jan. 1987), 8-10.

[17]	IETF RFC 4566:  "SDP: Session Description Protocol".

[18]	3GPP TS 24.229: "IP multimedia call control protocol based on Session Initiation Protocol (SIP) and Session Description Protocol (SDP)".

[19]	3GPP TS 24.109: "Bootstrapping interface (Ub) and network application function interface (Ua); Protocol details".

*** NEXT CHANGE ***

Annex D (Normative):
MIKEY-TICKET profile for IMS media plane security

# D.1	Scope

The profiling given in this Annex is with respect to MIKEY-TICKET [14]. The profiling is for the default implementation of KMS based IMS media plane security using GBA for user authentication and establishment of a shared key between KMS and IMS UE.

The profiling is based on what is needed to support SRTP as defined in RFC 3711 [9] and enhancements in terms of new SRTP transforms using 256 bit keys.

# D.2	General

A KMS based IMS media plane security default implementation:

-	Shall support MIKEY-TICKET Mode 1 and Mode 3 (cf. clause 4.1.1 in [14]).

-	Does not have to support REQUEST_INIT_PK and RESOLVE_INIT_PK, i.e. it does not have to support public key based exchanges.

-	Shall use the recommended payload order for all messages in the exchanges.

-	Shall not add any extra payloads.

# D. 2A 	Keys, RANDs and algorithms

A KMS based IMS media plane security default implementation:

-	Shall support use of keys of length 128 and 256 bit.

-	Shall support use of RANDs of length 128 and 256 bit.

-	Shall support the PRFs MIKEY-1 and PRF-HMAC-SHA-256 in all HDR and TP payloads.

-	Shall for KEMAC protection support AES-CM-128 and AES-CM-256 encryption algorithms and the NULL authentication algorithm.

-	Shall support HMAC-SHA-1-160 and HMAC-SHA-256-256 as authentication algorithm in V payloads.

# D.3	Exchanges

## D.3.1 	Ticket Request

A KMS based IMS media plane security default implementation:

-	Shall support timestamp of type NTP-UTC-32 and COUNTER.

-	Shall populate payloads in REQUEST_INIT_PSK as defined here:

-	IDRi: shall contain the Initiator’s KMS user identity.

-	IDRkms: optional, URI for target KMS.

-	TP: must specify (IDRr), i.e. the intended recipients of the requested ticket. IDRapp shall be set to SRTP.

-	IDRpsk: B-TID.

-	Shall populate payloads in REQUEST_RESP_PSK as defined here:

-	IDRkms: optional, URI for responding KMS.

## D.3.2	Ticket Transfer

A KMS based IMS media plane security default implementation:

-	Shall support timestamp of type NTP-UTC-32.

-	Shall use CSB ID map type of type GENERIC-ID.

-	Shall populate payloads in TRANSFER_INIT as defined here:

-	IDRi: shall be present. Contains initiator's KMS UID.

-	IDRr: shall be present. Contains KMS UID or KMS group identity.

-	Shall populate payloads in TRANSFER_RESP as defined here:

-	RANDRr: shall be present.

-	RANDRkms: shall be present (used in key forking).

-	IDRr: shall be present (used in key forking).

## D.3.3	Ticket Resolve

A KMS based IMS media plane security default implementation:

-	Shall support timestamp of type NTP-UTC-32 and COUNTER.

-	Shall populate payloads in RESOLVE_INIT_PSK as defined here:

-	IDRr:  shall contain the Responder’s KMS UID.

-	IDRkms: optional, URI.

-	IDRpsk: shall contain B-TID.

-	Shall populate payloads in RESOLVE_RESP_PSK as defined here:

-	IDRkms: optional, URI.

-	RANDRkms: shall be present (used in key forking).

# D.4	Profiling of tickets

The default ticket for KMS based IMS media plane security

-	Shall support use of keys of length 128 and 256 bit.

-	Shall support use of RANDs of length 128 and 256 bit.

-	Shall for KEMAC protection support AES-CM-128 and AES-CM-256 as encryption algorithm and the NULL Authentication algorithm.

-	Shall support HMAC-SHA-1-160 and HMAC-SHA-256-256 as authentication algorithm in V payloads.

-	Shall support timestamps of type NTP-UTC-32.

The TP payload (section 6.10 in [14]) in the default ticket for KMS based IMS media plane security shall be populated as defined here:

-	Has ticket type value 2 (defined in MIKEY-TICKET).

-	Has subtype value 0 (zero) and version value 0 (zero).

-	E flag shall have value 1 due to forking.

-	F flag shall have value 1 due to forking.

-	G flag shall have value 1.

-	H flag shall have value 1.

-	I flag shall have value 1 prescribing forking.

-	L flag shall have value 0.

-	M flag shall have value 0.

-	N flag shall have value 1 prescribing that no extensions are used.

-	O flag shall have value 1 prescribing that no extensions are used.

-	All sub-payloads specified shall be present.

The ticket data of the Ticket payload (Appendix A in [14]) in the default ticket for KMS based IMS media plane security shall be populated as defined here:

-	THDR: the first 48bits of the THDR Data shall contain a globally unique identifier of the issuing KMS.

-	IDRpsk: shall contain B-TID if the ticket is generated by the initiator. If the KMS generates the ticket it is implementation specific.

*** END OF CHANGES ***

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.