3GPP TSG SA WG3 Security - S3#59	( S3-100595

# Lisbon, Portugal 26 – 30 April 2010 													revision of S3-100456

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.401 | CR | 409 | ( rev | 1 | ( Current version: | 9.3.1 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | x | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Emergency Context Lifetime |
| --- | --- |
| Source to WG: ( | NEC Corporation |
| Source to TSG: ( | SA3 |
| Work item code: ( | IMS_EMER_GPRS_EPS |  | Date: ( | 27/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The current 33.401 does not give any description on: - the lifetime of security context used for a emergency call, i.e. lifetime of NULL algorithms and associated NAS COUNTS. - the reachability of UE during EMM-IDLE when emergency attached to avoid re-attach for subsequent emergency call, see 23.401. |
| Summary of change: ( | Added a sentence giving that the context should be kept during EMM-IDLE and that it can be removed when the UE goes to EMM-DEREGISTERED or when another EPS NAS security context is activated. |
| Consequences if ( not approved: | Lifetime of NULL algorithms and associated NAS COUNTS is unclear that can lead to situations where the UE will have to do emeregency attach again unnecessarily. |
| Clauses affected: ( | 15.1 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

* * * 1st change * * * *

## 15.1	General

Support for EPS emergency calling is defined in the TS 23.401 [2]. Limited service state of a UE is defined in TS 23.122 [26]. Emergency calls can be made by normally attached UEs or emergency attached UEs in limited service state. Emergency calls may be authenticated or unauthenticated as defined in clauses below. It depends on the serving network policy if unauthenticated emergency calls are allowed. Emergency call behaviour not explicitly specified is handled in accordance to non-emergency calls.

The E-UTRAN Initial Attach procedure is used for Emergency Attach by UEs that need to perform emergency services but cannot gain normal services from the network.

For an Emergency Attach the UE shall set the Attach Type to "Emergency" and the IMSI shall be included if the UE does not have a valid GUTI or a valid P-TMSI available. The IMEI shall be included when the UE has no IMSI, no valid GUTI, or no valid P-TMSI according to [2].

For an Emergency Attach the MME applies the parameters from MME Emergency Configuration Data for the emergency bearer establishment. Any potentially stored IMSI related subscription data is ignored by the MME according to [2].

For an Emergency Attach the MME shall not send any Notify Request to an HSS for an unauthenticated UE.  For authenticated emergency attached UEs, the MME performs HSS notification similar to that for normal attached UEs if the subscription data indicates that the user is allowed to perform handover to non-3GPP accesses [2].

An emergency attached UE using NULL algorithms shall keep the NULL algorithms and corresponding NAS COUNTs when in EMM-IDLE mode so that it is reachable for subsequent emergency service without a need to emergency attach again. The NULL algorithms shall be de-selected and corresponding NAS COUNTs shall be removed when the UE goes to EMM-DEREGISTERED state or when another EPS NAS security context is activated.

* * * End of change * * * *

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.