# 3GPP TSG-SA3 (Security)	S3-100643

# SA3#59, 26-30 April 2010, Lisbon, Portugal	revision of S3-100629

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.310 | CR | 0030 | ( rev | 2 | ( Current version: | 8.3.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Correction of SEG CA and TLS client/server CA certificate profiles |
| --- | --- |
| Source to WG: ( | Nokia Corporation, Nokia Siemens Networks |
| Source to TSG: ( | SA3 |
| Work item code: ( | TEI8 |  | Date: ( | 28/04/2010 |
| Category: ( | F |  | Release: ( | Rel-8 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | The current text in clauses 6.1.4 and 6.1.4a only refers to the case where the element certificates issued by the SEG or TLS CA are used for interconnection of security domains with different root CA. SEGs and network elements using TLS may also need certificates which may be validated using the root CA of the same security domain, if e.g. used for Zb interface. Thus the SEG or TLS CA shall also be allowed to have a certificate signed by the root CA of the same security domain. |
| Summary of change: ( | In addition to the interconnection scenario, also SEG and TLS CA certificates signed by the “local root CA” are allowed. In addition, the key usage identifiers are corrected to the exact format used in the X.509 recommendation. |
| Consequences if ( not approved: | SEG and TLS certificates can only be used for establishment of connections with security domains with different root CA from the local root CA. |
| Clauses affected: ( | 6.1.2, 6.1.4, 6.1.4a |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*********************** start of 1st change ************************

### 6.1.2	Interconnection CA Certificate profile

In addition to clause 6.1.1, the following requirements apply:

-	The RSA key length shall be at least 2048-bit;

-	Extensions:

-	Optionally non critical authority key identifier;

-	Optionally non critical subject key identifier;

-	Mandatory critical key usage: At least keyCertSign and cRLSign should be asserted;

-	Mandatory critical basic constraints:  CA=True, path length unlimited or at least 1.

*********************** start of 2nd change ************************

### 6.1.4	SEG CA certificate profile

In addition to clause 6.1.1, the following requirements apply:

-	The RSA key length shall be at least 2048-bit;

-	Subject name is the same as the issuer name in the SEG certificate;

-	Issuer name depends on the usage of the certificates issued by the SEG CA:

-	if used for interconnections between security domains with different root CAs the issuer name is the same as the subject name in the Interconnection CA certificate;

-	if used for connections with elements having the the same root CA certificate installed as used in the domain the SEG CA is located in, the issuer name is the subject name of either this root CA or an intermediate CA whose certificate has a valid certificate chain up to this root CA;

-	Extensions:

-	Optionally non critical authority key identifier;

-	Optionally non critical subject key identifier;

-	Mandatory critical key usage: At least keyCertSign and cRLSign, should be asserted;

-	Mandatory critical basic constraints:  CA=True, path length 0.

### 6.1.4a	TLS client/server CA certificate profile

In addition to clause 6.1.1, the following requirements apply:

-	The RSA key length shall be at least 2048-bit;

-	Subject name is the same as the issuer name in the TLS entity certificate;

-	Issuer name depends on the usage of the certificates issued by the TLS client/server CA:

-	if used for interconnections between security domains with different root CAs the issuer name is the same as the subject name in the Interconnection CA certificate;

-	if used for connections with elements having the the same root CA certificate installed as used in the domain the TLS client/server CA is located in, the issuer name is the subject name of either this root CA or an intermediate CA whose certificate has a valid certificate chain up to this root CA;

-	Extensions:

-	Optionally non critical authority key identifier;

-	Optionally non critical subject key identifier;

-	Mandatory critical key usage: At least keyCertSign and cRLSign, should be asserted;

-	Mandatory critical basic constraints:  CA=True, path length 0.

*********************** end of changes ************************

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.