3GPP TSG-SA3 Meeting #59 	(S3-100627

# Lisbon, Portugal, 26 – 30 April 2010													revision of S3-100508

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.203 | CR | 0179 | ( rev | 1 | ( Current version: | 9.3.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | X.509 Certificate profile aligment |
| --- | --- |
| Source to WG: ( | Ericsson, ST-Ericsson |
| Source to TSG: ( | SA3 |
| Work item code: ( | TEI10 |  | Date: ( | 19/04/2010 |
| Category: ( | C |  | Release: ( | Rel-10 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | Removal of Editor’s note and aligning X.509 profiles between technical specifications. See discussion paper S3-100506. |
| Summary of change: ( | Aligns the profiles by removing the current certificate profiling and refering to the profiling in 33.310. Also updates the reference to the PKIX RFC from RFC 3280 to RFC 5280, to be aligned with TS 33.310. |
| Consequences if ( not approved: | Editor’s note remains. Misalignment betweet technical specifications. Several different profiles have to be implemented and updated. |
| Clauses affected: ( | 2, O.5.1, O.5.2, O.5.3 |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

*** BEGIN CHANGES ***

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TS 33.102: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Security Architecture".

[2]	3GPP TS 22.228: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Service Requirements for the IP Multimedia Core Network".

[3]	3GPP TS 23.228: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; IP Multimedia (IM) Subsystem".

[4]	3GPP TS 21.133: "3rd Generation Partnership Project; T Technical Specification Group Services and System Aspects; Security Threats and Requirements".

[5]	3GPP TS 33.210: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Network domain security; IP network layer security".

[6]	IETF RFC 3261 "SIP: Session Initiation Protocol".

[7]	3GPP TS 21.905: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects; Vocabulary for 3GPP specifications".

[8]	3GPP TS 24.229: "3rd Generation Partnership Project: Technical Specification Group Core Network; IP Multimedia Call Control Protocol based on SIP and SDP".

[9]	3GPP TS 23.002: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects, Network Architecture".

[10]	3GPP TS 23.060: "3rd Generation Partnership Project: Technical Specification Group Services and System Aspects, General Packet Radio Service (GPRS); Service Description".

[11]	3GPP TS 24.228: "3rd Generation Partnership Project: Technical Specification Group Core Network; Signalling flows for the IP multimedia call control based on SIP and SDP".

[12]	IETF RFC 2617 (1999) "HTTP Authentication: Basic and Digest Access Authentication".

[13]	IETF RFC 2406 (1998): "IP Encapsulating Security Payload (ESP)".

[14]	IETF RFC 2401 (1998): "Security Architecture for the Internet Protocol".

[15]	IETF RFC 2403 (1998): "The Use of HMAC-MD5-96 within ESP and AH".

[16]	IETF RFC 2404 (1998): "The Use of HMAC-SHA-1-96 within ESP and AH".

[17]	IETF RFC 3310 (2002): "HTTP Digest Authentication Using AKA". April, 2002.

[18]	IETF RFC 3041 (2001): "Privacy Extensions for Stateless Address Autoconfiguration in IPv6".

[19]	IETF RFC 2402 (1998): "IP Authentication Header".

[20]	IETF RFC 2451 (1998): "The ESP CBC-Mode Cipher Algorithms".

[21]	IETF RFC 3329 (2003): "Security Mechanism Agreement for the Session Initiation Protocol (SIP)".

[22]	IETF RFC 3602 (2003): "The AES-CBC Cipher Algorithm and Its Use with IPsec".

[23]	IETF RFC 3263 (2002): "Session Initiation Protocol (SIP): Locating SIP Servers".

[24]	3GPP TS 33.310: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Network Domain Security (NDS); Authentication Framework (AF)".

[25]	Void.

[26]	ETSI ES 282 001: "TISPAN - Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); NGN Functional Architecture for NGN Release 1".

[27]	IETF RFC 3947 (2005): "Negotiation of NAT-Traversal in the IKE".

[28]	IETF RFC 3948 (2005): "UDP Encapsulation of IPsec ESP Packets".

[29]	IETF RFC 3323 (2002): "A Privacy Mechanism for the Session Initiation Protocol (SIP)".

[30]	IETF RFC 3325 (2002): "Private Extensions to the Session Initiation Protocol (SIP) for Asserted Identity within Trusted Network".

[31]	3GPP TS 23.167: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; IP Multimedia Subsystem (IMS) emergency sessions”.

[32]	IETF RFC 5626 (2009): "Managing Client Initiated Connections in the Session Initiation Protocol (SIP)".

[33]	IETF RFC 3268 (2002): "Advanced Encryption Standard (AES) Ciphersuites for Transport Layer Security (TLS)".

[34]	IETF RFC 2246 (1999): "The TLS Protocol Version 1.0".

[35]	Void.

[36]	ETSI ES 282 004: “NGN Functional Architecture; Network Attachment Sub-System (NASS)”

[37]	ETSI TS 187 001: " Telecommunications and Internet converged Services and Protocols for Advanced Networking (TISPAN); NGN SECurity (SEC); Requirements"

[38]	3GPP TS 33.178: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Security aspects of early IP Multimedia Subsystem (IMS)".

[39]	3GPP TS 29.228: "3rd Generation Partnership Project; Technical Specification Group Core Network and Terminals; IP Multimedia (IM) Subsystem Cx and Dx interfaces; Signalling flows and message contents".

[40]	3GPP2 X.S0011: "cdma2000  Wireless IP Network Standard".

[41]	3GPP2 C.S0023: "Removable User Identity Module for Spread Spectrum Systems".

[42]	Void.

[43]	3GPP2 S.S0055: "Enhanced Cryptographic Algorithms".

[44]	3GPP2 S.S0078: "Common Security Algorithms".

[45]	3GPP2 C.S0065: "cdma2000 Application on UICC for Spread Spectrum Systems".

[46]	3GPP TS 23.003: "3rd Generation Partnership Project; Technical Specification Group Core Network and Terminals; Numbering, addressing and identification".

[47]	IETF RFC-2407: "The Internet IP Security Domain of Interpretation for ISAKMP".

[48]	IETF RFC-2408: "Internet Security Association and Key Management Protocol (ISAKMP)".

[49]	IETF RFC-2409: "The Internet Key Exchange (IKE)".

[50]	3GPP TS 23.292: "IP Multimedia Subsystem (IMS) Centralized Services; Stage 2".

[51]	3GPP TS 31.103: "3rd Generation Partnership Project: Technical Specification Group Core Network and Terminals; Characteristics of the IP Multimedia Services Identity Module (ISIM) application".

[xx]	IETF RFC 5280: "Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile".

*** start of next CHANGE ***

### O.5.1	TLS Certificate

X.509 digital certificates [xx] shall be used for authentication in TLS. All X.509 certificates shall be signed by a trusted party. The certificates shall be profiled as specified in clause 6.1 in TS 33.310 [24] with the following additions:

-	for TLS entity certificates:

-	CRL distribution point in the certificates shall not be mandatory.

-	The common name CN shall be the FQDN (Fully Qualified Domain Name) of the server. Only a single FQDN is allowed in the CN field.

-	The subjectAltName shall contain the FQDN (Fully Qualified Domain Name) of the server.

-	for TLS CA certificates:

-	TLS CA certificates shall have no restriction in the issuer name.

### O.5.2	Certificate validation

TLS certificates shall be verified as part of a certificate chain that chains up to a trusted Root certificate.  The chain may contain intermediate Certification Authority (CA) certificates.

Usually the first certificate in the chain is not explicitly included in the certificate chain that is sent by the P-CSCF to the UE. In the cases where the first certificate is explicitly included, it shall already be known to the verifying party ahead of time and shall not contain any changes to the certificate, with the possible exception of the certificate serial number, validity period and the value of the signature.  If changes other than the certificate serial number, validity period and the value of the signature exist in the root certificate that was sent by the P-CSCF to the UE in comparison to the known root certificate, the UE shall conclude that the certificate verification has failed.

UEs shall build the certificate chain and validate the TLS certificate according to the "Certification Path Validation" procedures described in [xx]. In general, X.509 certificates support a liberal set of rules for determining if the issuer name of a certificate matches the subject name of another. The rules are such that two name fields may be declared to match even though a binary comparison of the two name fields does not indicate a match. [xx] recommends that certificate authorities restrict the encoding of name fields so that an implementation can declare a match or mismatch using simple binary comparison. Accordingly, the DER-encoded tbsCertificate.issuer field of a certificate shall be an exact match to the DER-encoded tbsCertificate.subject field of its issuer certificate.  An implementation may compare an issuer name to a subject name by performing a binary comparison of the DER-encoded tbsCertificate.issuer and tbsCertificate.subject fields.

### O.5.3	Certificate Revocation

Certificate Revocation Lists (CRLs) may be checked as part of certificate path validation. CRL infrastructure is optional to implement. The CRL, if used, should be profiled as specified in clause 6 in TS 33.310 [24].

*** END OF CHANGES ***

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.