# 3GPP TSG-SA3 (Security)	S3-100634

# SA3#59, 26-30 April, Lisbon, Portugal	revision of S3-100547

| CR-Form-v9.6 |
| --- |
| CHANGE REQUEST |
| ( | 33.234 | CR | 0105 | ( rev | 1 | ( Current version: | 9.1.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/specs/CR.htm. |

| Proposed change affects: ( | UICC apps( |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Deprecation of SHA-1 |
| --- | --- |
| Source to WG: ( | Vodafone |
| Source to TSG: ( | SA3 |
| Work item code: ( | TEI9 |  | Date: ( | 28/04/2010 |
| Category: ( | F |  | Release: ( | Rel-9 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: R99 (Release 1999) Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) |
| Reason for change: ( | SHA-1 is vulnerable to collision attacks and should not be recommended for use when generating new certificates and CRLs. |
| Summary of change: ( | The use of SHA-1 is not recommended for newly created certificates and CRLs. |
| Consequences if ( not approved: | Attackers could exploit SHA-1 weaknesses to generate fake certificates in order to launch attacks. |
| Clauses affected: ( | 2, 6.6A |
|  | Y | N |  |  |
| Other specs ( |  | X | Other core specifications ( |  |
| affected: |  | X | Test specifications |  |
|  |  | X | O&M Specifications |  |
| Other comments: ( |  |

## ** start of changes **

# 2	References

The following documents contain provisions, which, through reference in this text, constitute provisions of the present document.

- References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

- For a specific reference, subsequent revisions do not apply.

- For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	Void

[2]	Void

[3]	IETF RFC 3748: "Extensible Authentication Protocol (EAP)".

[4]	IETF RFC 4187, January 2006: "Extensible Authentication Protocol Method for 3rd Generation Authentication and Key Agreement (EAP-AKA)".

[5]	IETF RFC 4186, January 2006: "Extensible Authentication Protocol Method for Global System for Mobile Communications (GSM) Subscriber Identity Modules (EAP-SIM)".

[6]	IEEE 802.11i-2004: "IEEE Standard for Information technology - Telecommunications and information exchange between systems - LAN/MAN  - Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications-Amendment 6: MAC Security Enhancements".

[7]	IETF RFC 5216, March 2008: "The EAP-TLS Authentication Protocol".

[8]	Void

[9]	ETSI TS 101 761-1 v1.3.1B: "Broadband Radio Access Networks (BRAN); HIPERLAN Type 2; Data Link Control (DLC) layer; Part 1: Basic Data Transport".

[10]	ETSI TS 101 761-2 v1.2.1C: "Broadband Radio Access Networks (BRAN); HIPERLAN Type 2; Data Link Control (DLC) layer; Part 2: Radio Link Control (RLC) sublayer".

[11]	ETSI TS 101 761-4 v1.3.1B: "Broadband Radio Access Networks (BRAN); HIPERLAN Type 2; Data Link Control (DLC) layer; Part 4 Extension for Home Environment".

[12]	ETSI TR 101 683 v1.1.1: "Broadband Radio Access Networks (BRAN); HIPERLAN Type 2; System Overview".

[13]	3GPP TS 23.234: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3GPP system to Wireless Local Area Network (WLAN) Interworking; System Description".

[14]	IETF RFC 4282, December 2005: "The Network Access Identifier", (Obsoletes RFC2486)

[15]	IETF RFC 2865, June 2000: "Remote Authentication Dial In User Service (RADIUS)".

[16]	RFC 1421, February 1993: "Privacy Enhancement for Internet Electronic Mail: Part I: Message Encryption and Authentication Procedures".

[17]	Federal Information Processing Standard (FIPS) draft standard: "Advanced Encryption Standard (AES)", November 2001.

[18]	3GPP TS 23.003: "3rd Generation Partnership Project; Technical Specification Group Core Network; Numbering, addressing and identification".

[19]	IEEE P802.1X/D11 June 2001: "Standards for Local Area and Metropolitan Area Networks: Standard for Port Based Network Access Control".

[20]	3GPP TR 21.905: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; Vocabulary for 3GPP Specifications".

[21]	3GPP TS 33.102: "3rd Generation Partnership Project; Technical Specification Group Services and System Aspects; 3G Security; Security Architecture".

[22]	CAR 020 SPEC/0.95cB: "SIM Access Profile, Interoperability Specification", version 0.95VD.

[23]	RFC 4072, August 2005: "Diameter Extensible Authentication Protocol (EAP) Application".

[24]	IETF RFC 3588, September 2003: "Diameter base protocol".

[25]	IETF RFC 3576, July 2003: "Dynamic Authorization Extensions to Remote Authentication Dial In User Service (RADIUS)".

[26]	IETF RFC 3579, September 2003: "RADIUS (Remote Authentication Dial In User Service) Support for Extensible Authentication Protocol (EAP)".

[27]	IETF RFC 5247, August 2008: " Extensible Authentication Protocol (EAP) Key Management Framework".

[28]	E. Barkan, E. Biham, N. Keller: "Instant Ciphertext-Only Cryptoanalysis of GSM Encrypted Communication", Crypto 2003, August 2003.

[29]	IETF RFC 4306, December 2005: "Internet Key Exchange (IKEv2) Protocol".

[30]	IETF RFC 4303, December 2005: "IP Encapsulating Security Payload (ESP)".

[31]	RFC 4308, December 2005: "Cryptographic Suites for IPsec [32]	RFC 3948, May 2005: "UDP Encapsulation of IPsec ESP Packets ".

[33]	RFC 4307 December 2005: "Cryptographic Algorithms for use in the Internet Key Exchange Version 2 (IKEv2)".

[34]	IETF RFC 2104, February 1997: "HMAC: Keyed-Hashing for Message Authentication".

[35]	IETF RFC 2404, November 1998: "The Use of HMAC-SHA-1-96 within ESP and AH".

[36]	IETF RFC 2548, March 1999: " Microsoft Vendor-specific RADIUS Attributes".

[37]	Void

[38]	IETF RFC 3279 April 2002: "Algorithms and Identifiers for the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile".

[39]	IETF RFC 3280 April 2002: "Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile".

[40]	3GPP TS 27.007: "Technical Specification Group Terminals; AT command set for User Equipment (UE)".

[41]	ETSI TS 102.310: "Smart Cards; Extensible Authentication Protocol support in the UICC".

[42]	ETSI TS 102.221: "Smart Cards; UICC-Terminal interface; Physical and logical characteristics".

[43]	Open Mobile Alliance OMA-WAP-OCSP V1.0: "Online Certificate Status Protocol Mobile Profile". URL: http://www.openmobilealliance.org/

[44]	IETF RFC 4806, Februari 2007: Online Certificate Status Protocol ("OCS)P Extensions to IKEv2"..

[45]	IETF RFC 4739, November 2006: "Multiple Authentication Exchanges in the Internet Key Exchange (IKEv2) Protocol".

[46]	IETF RFC 4835, April 2007: "Cryptographic Algorithm Implementation Requirements for Encapsulating Security Payload (ESP) and Authentication Header (AH)".

[47]	3GPP TS 24.234: "3GPP System to Wireless Local Area Network (WLAN) interworking; WLAN User Equipment (WLAN UE) to network protocols; Stage 3"

[xx]	IETF RFC 3447, February 2003: "Public-Key Cryptography Standards (PKCS) #1: RSA Cryptography Specifications Version 2.1".

## ** next change **

## 6.6A	Profile for PDG certificates

Certificates used for authentication of the PDG shall meet the following profile of RFC 3280 [39].

a)	The certificate shall be encoded in DER format.

b)	The version shall be 2 ("v3").

c)	The certificate serial number shall meet the requirements in RFC 3280 [39], section 4.1.2.2.

d)	The signature algorithm shall be "sha1WithRSAEncryption" [38] or "sha256WithRSAEncryption" [xx], and the RSA public key used for signing shall not be longer than 2048 bits. For security reasons, the use of "sha1WithRSAEncryption" is not recommended for newly created certificates.

NOTE 1:	For interworking with pre-Release 9 elements, usage of SHA-1 in certificates may be required for some time. However, it is likely that in a future 3GPP release, certificates which use SHA-1 as the hash algorithm will be prohibited.

e)	The issuer name shall not be empty.

f)	The validity period shall meet the requirements in RFC 3280 [39], section 4.1.2.5.

f)	The subject name may be empty in PDG certificates and shall not be empty in CA certificates.

g)	The subject public key shall use algorithm "rsaEncryption" (RFC 3279 [38]), and the RSA public key shall not be longer than 2048 bits.

h)	The issuerUniqueID or subjectUniqueID fields shall not be present.

i)	The SubjectAltName extension shall be present if this is a PDG certificate, and shall contain at least one dNSName component.

j)	The BasicConstraints extension shall be present if this is a CA certificates with "CA" flag asserted. The pathLenConstraint may be present.

k)	CA certificates should contain the NameConstraints extension with appropriate dNSName components in the permittedSubtrees field.

l)	The KeyUsage extension shall be present in all certificates. The keyCertSign bit shall be set in CA certificates, and digitalSignature bit shall be set in PDG certificates.

m)	The CRLDistributionPoint extension may be present, and shall not be marked critical. At least one of the distribution points should use HTTP for retrieving the CRL.

n)	The AuthorityInformationAccess extension may be present with id-ad-ocsp access method, and shall not be marked critical.

o)	Other extensions should not be used; if they are, they shall not be marked as critical.

p)	The total length of a certificate shall not exceed 2000 bytes.

Certificate processing requirements:

a)	UE shall send one or more CERTREQ payloads with encoding value 4 (X.509 certificate - Signature).

b)	IKEv2 Certificate encoding value shall be 4 (X.509 certificate - Signature).

c)	UE shall not assume that any except the first IKEv2 CERT payload is ordered in any way.

d)	UE shall be able to support certificate paths containing up to four certificates (e.g. self-signed CA certificate, intermediate CA 1, intermediate CA 2, PDG certificate) (and may support longer path lengths), where the intermediate CA certificates and the PDG certificate are obtained from the IKEv2 CERT payload and the self-signed CA certificate is obtained from a UE local store of trusted root certificates.

e)	PDG shall not send paths containing more than four certificates.

f)	UE shall be prepared to receive irrelevant certificates, or certificates they do not understand.

g)	UE shall be able to process certificates (for e.g. chain building) even if naming attributes are unknown.

h)	UE shall support both UTCTime and GeneralizedTime encoding for validity time.

i)	UE shall check the validity time, and reject certificates that are either not yet valid or are expired.

j)	UE shall support processing of the BasicConstraints, NameConstraints, and KeyUsage extensions.

k)	UE may check the validity of the certificates using CRLs or OCSP [43]. Support for CRLs is optional in the UE. Support for OCSP is mandatory in the UE. In addition, the UE and the PDG may support the extensions to IKEv2, which enable the use of OCSP for in-band signalling of certificate revocation status, according to [44]. The signature algorithm for CRLs and OCSP responses shall be "sha1WithRSAEncryption" [38] or "sha256WithRSAEncryption" [xx]. For security reasons, the use of "sha1WithRSAEncryption" is not recommended for newly created CRLs and OCSP responses.

NOTE 2:	A WLAN UE that initiates 3GPP IP Access according to the tunnel full authentication and authorization procedure, may want to check the validity of the PDG certificate, but it might not gain access to the OCSP server. This situation can be handled in the following way: After the UE initiated tunnel is successfully established and before user data is transmitted in the tunnel, the UE sends an OCSP request message to OCSP server. When the UE receives the OCSP response, it checks the certificate status. If the certificate of PDG is valid, the UE will allow user data to be transmitted to the PDG in the tunnel. If the certificate is not valid, the UE may terminate the tunnel that just was established.

NOTE 3:	For interworking with pre-Release 9 elements, usage of SHA-1 in CRLs and OCSP responses may be required for some time. However, it is likely that in a future 3GPP release, CRLs and OCSP responses which use SHA-1 as the hash algorithm will be prohibited.

## ** end of changes **

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Windows ® applications, e.g. 19/02/2006.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.