## Slide 1
NSSAI in Access Stratum
3GPP TSG SA WG3 #93 Tdoc S3-183325
Spokane, Nov-12-14 2018
Nokia, Nokia Shanghai Bell, InterDigital, AT&T, Verizon

## Slide 2
Overall Background
Network slicing is an end to end feature that requires network slicing support in the CN and in the RAN.
Inclusion of NSSAI in RRC has been assumed in SA2 for several purposes:
  The RAN may use NSSAI in RRC Connection establishment to optimally select the AMF.
  Operators may support slices that implement Slice Aware policies to fulfil specific SLA with their customers or for own operational reasons.
    These may include AS aspects that apply before contacting the CN and retrieve allowed NSSAI to:
      take local (AS) actions to release connections that cannot be served in the RAN
      Instantly Protect the CN in cases it is overloaded by certain slices, but not others, or in cases certain slices need to be taken out of service at a certain AMF but not others (UAC is AMF agnostic).
      Following Slides show examples of how the RAN uses NSSAI in RRC in RAN to apply control plane policies in RAN2 and SA2 specifications

## Slide 3
RAN awareness: 38.300 text
The text points to:
There are policies in the RAN that require awareness of the slices the UE uses
some policies may use information in RRC PRIOR to contacting the CN: for these policies to work RRC needs to include NSSAI

## Slide 4
RAN awareness: 23.501 text (see clause 5.15.2.1“General”)
The (R)AN may use Requested NSSAI in access stratum signalling to handle the UE Control Plane connection before the 5GC informs the (R)AN of the Allowed NSSAI.

## Slide 5
AMF overload control: 23.501 text
Slice aware overload control is already there in TS and works on NSSAI in the RRC connection establishment…
if some connections establishment requests do not send NSSAI they use, these cannot be treated by RAN awareness of NSSAI.
UEs would be handled by default policy regardless of the importance of the UE

## Slide 6
Policy driven vs. static behaviour
SA2 endorsed two CRs
S2-1811403 endorses a static behaviour where the NSSAI is included only if the access type
provides Encryption at AS level.
  Not included in 3GPP access
  Can be included in non-3GPP access
S2-1811565 has the same default UE behaviour as in S2-1811403. In addition, subject to
regulations, if both HPLMN and serving PLMN allow, the UE can also include NSSAI in the 3GPP
access stratum to enable the features so far assumed in rel-15 to be enabled by NSSAI
Inclusion in RRC connection establishment procedure.
  Combines the default UE behaviour to not include NSSAI with the ability for operators to
  consciously enable RRC level inclusion.

## Slide 7
Conclusions
In CR S2-1811565 a default UE behaviour applies that omits NSSAI from RRC level in 3GPP access for Rel-15 UEs. This is the same UE behaviour in S2-1811403 .
In CR S2-1811565 subject to regulations and explicit HPLMN authorisation which is part of information retrieved from UDM, in Serving PLMNs where it is critical to apply RAN awareness to the initial contact with the RAN (e.g. due to routing to right AMF or other policies), PLMN wide or in specific area where e.g. critical applications are expected to run, operators should be able to configure UEs to send NSSAI in RRC connection establishment.
On this basis it is proposed that SA3 expresses that both CRs are acceptable to meet the privacy requirements and allows SA2 to choose what is most suitable for the ecosystem.