## Slide 1: 2018 LI concept car
Aligning LI with the rest of the network SA3LI14_027
1/27/2014 Greg Schumacher, Sprint gregory.schumacher@sprint.com

## Slide 2: Motivation
Address in a forward looking fashion the problem of capturing service specific content from SIP/RTP
Consider emerging LI architecture challenges such as cloud/SDN/virtualization
Foundation for migrating legacy LI service to a nextgen LI service (all IP, SIP, RTP, XML, etc.)
Standardize LI interfaces internal to operator networks
Reuse existing capabilities, protocols, architectures and architectural concepts

## Slide 3: 2014 model - LI service traits
Built on these network assumptions
Centralized network
Monolithic network elements
Monolithic mobile operators
Simple services and capabilities
Enhancements and changes are hard

## Slide 4: 2015-20 model – PLMN traits
Distributed network
Layered and decomposed network elements
More complex mobile provider eco-system
  3rd party services
  3rd party providing segments of network functions
  Network sharing
IP & SIP based networks
Complex and broader services and capabilities
Enhancements and changes are easier
IP/IMS networks expanding beyond deployment islands
Initial steps of SDN & virtualization

## Slide 5: LI concept car characteristics
Match the distributed and layered approach of the underlying network
Support mobile operator eco-system decomposition and specialization
Reuse current IP & SIP protocols deployed in the network
Define LI specific reference points
Exploit AAA and PCC similarities

## Slide 6: LI concept car under the hood - AAA
LI service has AAA functions
  Just as Dynamic Triggering is a AAA function, the LI concept car has AAA elements
    Authentication, Authorization and Accounting are key components
    Activating, arming and terminating triggers
  AAA aspects of the LI concept car should use Diameter
  LI Concept may provide a complement to Dynamic Triggering in having a “clean” interworking function
  Diameter provides extensibility, flexible deployments and improved fault recovery

## Slide 7: LI concept car under the hood - PCC
The LI service is very much like PCC
  The actions resulting from triggers are different
    PCC – “live” user plane packet modification or charging event creation
    LI service – control and user plane reporting and duplication
  PCC has been generalized into an enforcement function and a policy function
    The enforcement function uses rules to perform policy actions
    The policy function determines which rules are to be applied
    The enforcement function can be either standalone as an intermediate element in an interface, or can be incorporated into a FE.
    Some specialized enforcement function interfaces have been defined

## Slide 8: LI concept car under the hood - PCC
Using PCC framework as a starting point, the following LI concept car functions can be defined
  LI Detection and Reporting Function (LIDRF) ≈ PCEF
  LI Control Function (LICF) ≈ PCRF
Just as for a PCEF, a LIRDF can be:
  Embedded in a network service element or
  Placed in an interface path between FEs for passive probing (probe, tap or relay) if sufficient service state can be determined from the monitored interfaces
  Can probably start with a subset of PCC rules and extend as needed for specific service requirements
  Note that PCC rules the same as firewall rules with a couple of exceptions

## Slide 9: 2018 LI Concept car features

## Slide 10: Features
Reporting (IRI/CII & CC)
Triggering

## Slide 11: Reporting
X2 (IRI/CII) and X3 (CC) can continue to use existing interfaces
  Uses the reporting aspect of the LIDRF similarly as the current IAP
Target Information (CTI)
  A new capability needed for:
    Reporting static non-correlating information about the target
    Information not known or retained by reporting LIDRF (IAP/ICE)
    Information usually located in O&M subsystems or subscriber profiles
    Information reporting not associated with any CC or IRI/CII triggers
    Examples include such things as group memberships, cell site location, etc.
  One or more query/response transactions resulting in information report(s) (indication) sent by MF/DF to LEMF/CF

## Slide 12: Triggering
Current problem 1 – top level triggers are becoming multi-part where the firing of parts of a trigger are detected in separate FEs such as CSCF and IBCFs. The derived trigger to the media gateway functions should be based on dynamic information from the CSCF
Current problem 2 – based on service, network or signaling events, a target’s communication is removed from one network element and moved to another network element. Current triggering isn’t able to account for this service mobility
Solution – create trigger chains
  A trigger firing can spawn one or more derived triggers based on dynamic information such as address and port assignments or server allocation
  LICF is the top level and root of all trigger chains
  Allows dependent triggers to be deferred until dynamic resources are allocated (e.g. address and ports, servers) or a service specific event occurs when service serving FE discovery can be performed.

## Slide 13: Derived trigger example

## Slide 14: Trigger chain examples

## Slide 15: New reference point - LITC
LI Trigger Control Reference Point
  Diameter based
  LICF <-> LIDRF <-> LIDRF
  Basic primitives towards leaf LIDRF
    Create trigger (for pre-provisioning)
    Arm trigger
    Modify trigger
    Query trigger status
    Cancel trigger
    Suspend trigger (for overload control)
    Resume trigger (for overload control)
  Basic primitives toward root LICF
    Triggered event
    Reporting end
    Detected service change impacting trigger chain (such as call forward, media change to spawn another trigger chain)

## Slide 16: Operator benefits
Standardized interfaces
Reuse Diameter infrastructure and skills
Reuse Diameter security and availability capabilities
Allows flexibility for operator deployments
Extensible as new services and FEs are defined
Provides efficient use of network resources (interfaces can be sized to engineered LI traffic estimates)
May provide a clean IWF for dynamic triggering
The framework is applicable to cloud/SDN/virtual service deployments

## Slide 17: Topics for further discussion

## Slide 18: Reporting
The X2 & X3 reference points should be standardized
Further study on what the PCEF supports for sending copies of monitored traffic to a third network element and how to take advantage for the LI concept car
Target Information (CTI)
  Probably should create new reference points X4 & HI4
  At least a standard query (pull), maybe a push or subscribe/notify capability for updates
  Might be able to be used to report known state information for mid-call triggering
  Might have to have partial or segmented responses to the MF/DF depending on the response times of different server functions
  Do we allow an optional CF/LEMF to operator network query for CTI which would then spawn an internal CTI query by LICF

## Slide 19: Triggering
Trigger chains
  Should all derived trigger creation flow back through LICF or can LIDRF initiate a derived trigger directly to another LIDRF?
  Is there a role for a proxy function in LIRDF/LICF reference points
  Stage 2 & 3 details
  Diameter usage details

## Slide 20: Other
Mid-call LI requires further study, may be easier to specify, additional information about targeted service states at LI service startup is unclear
The trigger chain model needs to be further refined for the following configurations:
LICF -> LIDRF over Diameter
LIDRF -> LIDRF over Diameter (for both peer and parent/child)
LIDRF -> LIDRF (for parent/child) when Diameter is not currently used in the FE
  SIP is present such as in Mr
  H.248 is present such as in Ix