## Slide 1
3GPP TSG SA WG3LI (Security) Meeting #52 SA3LI14_028r2
4-6 February 2014; France(ETSI)
Source: Interdigital
Title: LI considerations for offload scenarios
Document for: Discussion
Agenda Item:
Work Item / Release:
Abstract of the contribution:
This presentation attempts to define a new problem space and to propose solutions for LI in traffic offload scenarios.

## Slide 2: Overview
Key LI requirements – in the Outtakes section
Selected IP Traffic Offload (SIPTO) and Local IP Access (LIPA)
Proposed Solutions
  Extending LI interfaces to local node
  Extending LI interfaces to ISP hosting local node backhaul

## Slide 3: SIPTO and LIPA
Done at a HeNB or SCGW (Small Cell GW)
Local IP Access Traffic (LIPA)
  Traffic routed between two local users
Selected IP Traffic Offload (SIPTO)
  Traffic routed between a cellular device and an application server on public Internet
LI is a problem that must be solved

## Slide 4: Proposed Solution 1 for LI of LIPA and SIPTO: Outline
Add an LI Function to the HeNB and/or the Small Cell Gateway (SCGW)
Extend the existing X1-1, X2, and X3 interfaces from within the core network to the HeNB/SCGW
  HeNB/SCGW becomes INE/ICE
Use existing secure tunnel between HeNB/SCGW and mobile core network
  IPSec tunnel to SeGW at edge of mobile core network

## Slide 5: Proposed Solution 1 LI Topology
Local traffic (LIPA)
Offloaded traffic (SIPTO)
LI Interface

## Slide 6: Proposed Solution 1LI Topology - Detailed

## Slide 7: Solution 1: Steps needed: Discovery
The HeNB/SCGW and LI Functions within the mobile core network will have to discover each other
The LI Functions could be provisioned with the ID of the HeNBs/SCGWs attached to the core network
  The LI Functions would then be discovering the HeNBs/SCGWs
The HeNBs/SCGWs could be provisioned with the ID of the LI Functions within the core network
Since the LI Functions are more under the control of the network operator, having the LI Functions discover the HeNBs/SCGWs is a better option

## Slide 8: Solution 1: Steps needed: Authentication
After discovery, the HeNB/SCGW and LI Function must perform some type of mutual authentication, which ensures
  only trusted entities are accessing the LI Function
  only the trusted LI Function is communication with a HeNB/SCGW
HeNB/SCGW requires use of TEE (Trusted Execution Environment)
  allows for authentication information to be kept private
  allows for the security of the LI information
HeNB/SCGW may also use a Hosting Party Module (UICC) to authenticate to the core network
  can also be reused to authenticate to the LI Function in the core network

## Slide 9: Proposed Solution 2 for LI of LIPA and SIPTO: Outline
Perform LIPA and SIPTO within ISP
Add a LI Function to an ISP that is servicing the HeNB and/or the SCGW
Extend the existing X1-1, X2, and X3 interfaces from within the core network to the HeNB/SCGW
ISPs usually have an LI Node that supports LI functions required for ISPs
  located outside of local network which lowers probability of target learning they are subject of surveillance

## Slide 10: Proposed Solution 2: ISP-Cellular Interfaces

## Slide 11: Proposed Solution 2: Offload Data Path

## Slide 12: Proposed Solution 2: LI of Offloaded Data

## Slide 13: Conclusion
Offload scenarios present challenge to traditional LI methods
LI might impede deployment of Small Cells in operators’ networks
Traditional LI architecture has to expand to allow LI in offload scenarios

## Slide 14: OUTTAKES

## Slide 15: Key LI Requirements (pasted from 3GPP LI specifications)
Target of surveillance is not to know they are the target of surveillance
Identity of those under surveillance is not to be public, only authorized personnel have this info
Surveillance enabled/disabled immediately upon receipt of the warrant from a law enforcement agency
Support two types of surveillance
  Event only
  Event and data
If data is encrypted, the network provides a means to decrypt the data (if available)

## Slide 16: Cellular Networks - Introduction
Current cellular networks typically funnel all data through a “core network”
  This makes LI “easy” since there is a focal point in the core network that allows for meeting LI requirements
  This focal point is within the core network, allowing for the surveillance to be done discretely, i.e. without tipping off the subject of surveillance

## Slide 17: Current Core Network LI Topology (I)

## Slide 18: Current Core Network LI (II)
Operators have many nodes in the mobile core network
  Each node performs a different function
LI Functional node
  Interfaces to law enforcement agencies
  Interfaces to other nodes in the core network
  Acts as a gateway between law enforcement agencies and core network nodes
Intercepting Control Elements (ICE)
  Control plane
Intercepting Network Elements (INE)
  Data plane

## Slide 19: Current Core Network LI Topology (III)

## Slide 20: Current Core Network LI (IV)
There are 3 defined handover interfaces (HI) that a cellular operator is required to support to a law enforcement agency
HI1 – Administration
  Allows law enforcement agency to deliver an electronic warrant, enable or disable surveillance, and query the cellular network as to the status of surveillance of a target
HI2 – Intercept Related Information (IRI)
  Allows cellular network to inform law enforcement when a target has connected/disconnected to the network and other events related to the target
HI3 – Content of Communication (CC)
  Allows cellular network to forward copies of the actual data packets sent to and by a target of surveillance.

## Slide 21: Current Core Network LI (V)
Defined interfaces between LI Function and ICE and INE nodes
  X1-1
    Interface to allow LI Function to command INE and ICE nodes to enable or disable surveillance of a particular user
  X2
    Interface to allow INE and ICE nodes to send IRI event data to the LI Function in the core network
  X3
    Interface to allow INE nodes to send CC data to the LI Function in the core network
These interfaces are located within the core network and do not travel outside the core network
  At least not currently

## Slide 22: Outtakes: Solution 2 Alternative – Adding LGW to ISP

## Slide 23: Outtakes: Solution 2 Alternative – Adding LGW to ISP