## Slide 1
VoIP IMS Roaming Scenarios
- From an LI perspective
Nagaraja (Nag) Rao
2015-07-14

## Slide 2
Introduction
  These slides illustrate a few cases of VoIP roaming scenarios.
  For LI, all the scenarios focus just the HPLMN or Home CSP.
  The illustrations show that in certain cases the media (call content) never enters the HPLMN and if the HPLMN is served with an intercept order, then interception of CC can be an issue.
  At the end, some options that were discussed in the past, but not documented so far, are presented.
  Illustrations also include some cases that are questionable and hence, may not be realistic. The purpose of including them here is to determine their validity, specially, if a case-by-case evaluation is used to determine the media path of an intercepted call.

## Slide 3
Overview
[Visible Cases]

## Slide 4
Case 1: S8HR - Just the Access Roaming, no IMS Roaming
        In this example, Party A is target in Home CSP#1 and Party B is the target in Home CSP #2.
        Interception of IRI and CC in the respective Home CSPs is not an issue.

## Slide 5
Case 2: RAVEL - IMS Roaming with Home Routed Media
        In this example, Party A is target in Home CSP#1 and Party B is the target in Home CSP #2.
        Interception of IRI and CC in the respective Home CSPs is not an issue.

## Slide 6
Case 3: RAVEL - IMS Roaming with Loopback
        In this example, Party A is target in Home CSP#1 and Party B is the target in Home CSP #2.
        Interception of IRI and CC in Home CSP #2 is not an issue. However, Home CSP #1 serving the intercept order for Party A does not have access to the CC and hence, CC interception is not possible. If the loop-back is not used, then this example will be same as Case 2 where interception of CC was not an issue.

## Slide 7
Special Cases

## Slide 8
Scenario 1: RAVEL - Roaming Party A (Target) calls Party B in another IMS network
        Here we focus only the originating network. In the example, Party A is target in Home CSP.
        Home CSP does not have access to the CC and hence, CC interception is not possible. If loop-back and the optimized media routing is not done, then CC would enter the HPLMN and hence, interception CC would not be an issue.

## Slide 9
Scenario 2: RAVEL - Roaming Party A (Target) calls Party B in PSTN
        Here we focus only the originating network. In the example, Party A is target in Home CSP.
        Home CSP does not have access to the CC and hence, CC interception is not possible. If loop-back and the optimized media routing is not done, then CC would enter the HPLMN and hence, interception CC would not be an issue.

## Slide 10
Scenario 3: RAVEL - Roaming Party A (Target) calls Party B in VPLMN
        Here we focus only the originating network. In the example, Party A is target in Home CSP.
        Home CSP does not have access to the CC and hence, CC interception is not possible. If loop-back and the optimized media routing is not done, then CC would enter the HPLMN and hence, interception CC would not be an issue.

## Slide 11
Scenario 4: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN
        In this example, Party A & Party B are the targets in Home CSP.
        Interception of IRI and CC for both Party A and Party B is not an issue.

## Slide 12
Scenario 5: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN, but roaming
        In this example, Party A & Party B are the targets in Home CSP.
        Interception of IRI and CC for both Party A and Party B is not an issue.

## Slide 13
Scenario 5-1: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN, but roaming in a different VPLMN with Optimized Media Routing
        In this example, Party A & Party B are the targets in Home CSP.
        If this scenario is possible, then the Home CSP does not have access to the CC and hence, the interception of CC is not possible.
Is this a realistic scenario?

## Slide 14
Scenario 6: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN, but roaming in the same VPLMN
        In this example, Party A & Party B are the targets in Home CSP.
        Interception of IRI and CC for both Party A and Party B is not an issue.

## Slide 15
Scenario 6-1: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN, but roaming in the same VPLMN with Optimized Media Routing
        In this example, Party A & Party B are the targets in Home CSP.
        If this scenario is possible, then the Home CSP does not have access to the CC and hence, the interception of CC is not possible.
Is this a realistic scenario?

## Slide 16
Scenario 7: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN who has call forwarding to Party C in the same VPLMN
        In this example, Party A & Party B are the targets in Home CSP.
        Interception of IRI and CC for both Party A and Party B is not an issue.

## Slide 17
Scenario 7-1: RAVEL - Roaming Party A (Target) calls Party B (Target) in HPLMN who has call forwarding to Party C in the same VPLMN with Optimized Media Routing
        In this example, Party A & Party B are the targets in Home CSP.
        If this scenario is possible, then the Home CSP does not have access to the CC and hence, the interception of CC is not possible.
Is this a realistic scenario?

## Slide 18
Summary
  With certain scenarios of IMS roaming, the call content may not be available for intercept in the HPLMN, specially, for target originated calls.
  Forcibly bringing the call content to the HPLMN may have security risk as the process may not be transparent enough.
  However, some LEAs have previously indicated that transparency related concerns Vs not receiving the information may have to be evaluated on a per case basis. Perhaps, a per target based provisioned parameter could be employed to determine such a case by case basis.
  In the ATIS standards (ATIS-1000678 and ATIS-0700005), a CCUnvailable message has been defined to report to the LEAs when the call content is required to be reported, but not available in the network. Perhaps, a similar indication could be added to the IRI messages when the above case-by-case based evaluation prevents conditionally altering the media path of an intercepted call.
  SA3 and SA3-LI have agreed that e2e encryption of the media can be done only if the LI does not apply to the network. The reason is same the security risk as seen in the optimized media routing case. Perhaps, similar approach could also be taken to the cases where call content does not come to the HPLMN. In other words, if the LI applies, then deploy the network configuration in such a way that call content always comes to the HPLMN. Perhaps, an office-based provisioned parameter could be employed to determine such an approach.