## Slide 1: Study Item proposal for dealing with S8HR
Joint contribution by Sprint and NTT Docomo
7/8/2015
Alf Zugenmaier, NTT Docomo – alf.zugenmaier@hm.edu
Greg Schumacher, Sprint – gregory.schumacher@sprint.com
S3i150188

## Slide 2: Study item LIV-8
No changes, thus no work required on regulated interfaces (X1, X2, X3) in 33.107 & 33.108
What should be covered in the study and to what level of detail
  Internal interfaces DFx -NE
    Should not be under regulatory aspect (e.g. CALEA), not normative per regulation (as defined in 106, 107, 108), i.e. as is today
  Gm (UE to P-CSCF)
    The current level of standardization in CT groups should be sufficient to extract information required for LI
  LTE Packet interception point
  Rx like Reference Point (AF to PCRF)
    PCC interface updated to activate LI (Application Function to PCRF)
Tentative title of 900 TR: Providing LI for VoLTE in the S8HR architecture

## Slide 3: Open issues (taken from LS)
Develop an architecture for the IAP which for LBO (P-CSCF) was an implied set of functionality.
  Three boxes: filtering function, maintain state and arm triggers, report on activated triggers -> already in 107, show in new document (TR out of study) where IAP would be located for S8HR
Investigate the possibility of reusing PCC architecture elements (PCRF and PCEF) to extract the targeted bearers and potentially other selection criteria.
  See separate slide
Specify the interworking function between the bearer extraction function and the LEA interfaces for both IMS signalling and media (HI2 & HI3).
  Would be output of three boxes, interfaces defined in 107 already, but not standardized
Specify a filtering or service selection or separation function to select the IMS services specified by the LEA in a warrant to deliver to the LEA.
  Same needs to be done for LBO, definition of format how to signal which IMS services needs to be intercepted
  Activation of PCC triggers -> Rx interface
Accommodate any potential impact of SGW changes resulting from mobility events.
  PCC can deal with this, MME is aware of and sets up new SGW, no loss of data traffic in SGW relocation if PCC triggers quickly
Specify the mechanisms to use to obtain network provided location (NETLOC NPLI).
  Obtain serving network provided location, information only available after first IMS registration, then mapping to LTE identifier is possible -> MME can provide location information
Provide the ability to report number resolution (e.g. short codes, toll free, premium service numbers) to the LEA by the VPLMN. This applies to both S8HR and LBO scenarios.
  Should be addressed by itself. Can become a standalone section in the TR.
Develop a capability by capability comparison of LBO and S8HR LI interception capabilities. This will help guide the work toward making S8HR LI in the VPLMN provide equivalent capabilities to LBO LI. It may also provide insights to possible improvements to LI service in roaming scenarios.
  This could become the conclusion of the TR

## Slide 4: PCC for LI
IAP
AF
PCRF
PCEF
bearer
Gx
Rx
Filtering
Triggering
Reporting
X2, X3
…

## Slide 5: Re-using PCC for LI in S8HR
Local application of PCC, i.e. no roaming interaction (i.e. Figures 5.1-3 and 5.1-4 in 23.203 don‘t apply)
Dealing with SGW relocation
  Reported to MME, PCRF would deal with orchestrating PCEFs
How could undetectability be realised
  Moderate (organizational) requirement – SW level partitioning/VPNs
  Strict (hardware) requirement – duplication of PCC elements, worst case separate PCC infrastructure
Roaming traffic less than local traffic, so less HW required for LI if PCEF is on roaming interfaces only.
Current proprietary VoLTE LI equipment in SGW is essentially DPI functionality, i.e. not using P-CSCF internal state.

## Slide 6: How to detect IMS registration– descriptive concepts for inclusion in study
Question: what QoS level do we request for S8HR, i.e. do we distinguish the bearers inside S8HR tunnel
How do we distinguish the IMS bearers inside the tunnel?
What could we trigger on for detecting registration of inbound roamers
  URN – DNS
  Special QoS level?
  Visited network would like to know which GTP tunnel is going to a P-CSCF
    Informed from home network?
    Enforced using PCC
Need to look at explicit and implicit registrations

## Slide 7: How to intercept – descriptive concepts for inclusion in study
Flow for when target is originating, when and where trigger is armed and fired
Flow for when target is terminating, when and where trigger is armed and fired

## Slide 8: Retained data
This topic is typically out of scope for 3GPP SA 3 LI specifications, but different approaches could be included in 900 TR.
GSMA might be able to solve this with roaming agreements
  Trying to resolve with charging information for roaming case
  GSMA should try to resolve this first
  Data known to home network is required in visited network for traffic over the S8 interface
  Potential solution: Send back all CDRs from roamers on VPLMN to that VPLMN
    Competitive issues?
If GSMA can‘t solve this:
  Use PCC infrastructure to create "shadow CDRs"