## Slide 1: Input to SA3LI Requirements regarding Location Information in IRI’s.

## Slide 2: Executive Summary
 | Support the requirement from many markets to provide up to date location information to LEA authorities in LTE.
 | 2 options are currently being evaluated: Gx/Rx based (location information is sent by PGW via PCRF to SBC) MME based (LI Cell Based IRI Reporting)
 | SA3 LI for further discussion and decision
Topic
Purpose
Input to

## Slide 3: NPLI (Network provided location information)

## Slide 4: 3GPP standard NPLI behavior
PGW
PCRF
SBC
AAR Specific-Action = Access_Network_Info_Report (12), Req_Access_Info=USER_LOCATION (0)
Gx
Rx
AAA
RAR ET=Access Network Info Report (45);
Dyn PCC Rule including Required-Access-Info=USER_LOCATION (0)
AAA
Further updates, if received by PCRF from Gx (CCRu), are not propagated to Rx
NetLoc procedure returns ULI value
CCRu ET=Access_Network_Info_Report [45]; <ULI>
CCAu
RAA
RAR Specific-Action=Access_Network_Info_Report (12),
Req_Access_Info (<ULI>)
VoLTE call start

## Slide 5: Option 1: Gx/Rx based (PGW, PCRF, SBC)

## Slide 6: Option 1: Gx/Rx based (location reporting in connected mode acc. 3GPP 23.401)
PGW
PCRF
SBC
AAR Specific-Action = Access_Network_Info_Report (12),
Req_Access_Info=USER_LOCATION (0)
Gx
Rx
AAA
RAR ET=Access Network Info Report (45); ET= ECGI_CHANGE (27);
Dyn PCC Rule including Required-Access-Info=USER_LOCATION (0)
RAA
NetLoc procedure returns ULI value
CCRu ET=Access Network Info Report (45); <ULI>
CCAu
RAA
RAR Specific-Action=Access_Network_Info_Report (12),
Req_Access_Info (<ULI>)
CCRi ( <ULI> )
CCAi (no Event-Trigger)
VoLTE call start
CCRu ET=ECGI_CHANGE [27]; <ULI>
CCAu
RAA
RAR Specific-Action=Access_Network_Info_Report (12),
Req_Access_Info (<ULI>)
Location Reporting update, new ULI value
Repeated any time user changes location
Non-standard behavior; RAR coding to be agreed between PCRF and SBC suppliers
STA
STR
VoLTE call end
RAR remove Dyn PCC Rule; remove ET27
RAA
NOTE: not supported by ALU PCRF current implementation, that has to wait until next CCRu to remove the rule
Same coding as in NPLI, the assumption is that PCRF behavior is driven by PCRF configuration
SBC sends SIP INFO with <ULI>

## Slide 7: Option 2: LI Cell Based IRI Reporting (MME)

## Slide 8: Generic Requirement noted in some markets
Some LEA’s have detected gaps in reporting location information in 3G and 4G mobile networks
Demand for more up-to date cell information in LI
  location information needs to be delivered with the greatest possible accuracy that the home network of the terminal equipment usually offers for this location "Location updates must be provided at least in all cases when the ME changes eNodeB (4G) / NodeB (3G)“
  in the case of an active warrant, ME's location must be observed in any mode (e.g. voice, data, idle, st.by, ...) "Location updates must be provided in any operation mode of the ME, e.g. data, voice, idle, stby...“
Intercept Related Information (IRI) - Call event information about the PS session, such as time and duration.

## Slide 9: S1 messages including ECGI Information (proposed and discussed in 3GPP)
Message | IRI | Comments
E-UTRAN attach | Already provide | 
E-UTRAN detach | Already provide | 
UE requested PDN connectivity | Already provide | 
UE requested PDN disconnection | Already provide | 
Tracking Area update | Already provide | 
Service request | To be added | Service request
HANDOVER NOTIFY | To be added | S1 based handover
PATH SWITCH REQUEST | To be added | X2 based handover
UPLINK NAS TRANSPORT | No need | Only used for SMS
LOCATION REPORT | No need | Only for LCS
CELL TRAFFIC TRACE | No need | Only be triggered once a UE is traced.
Note:
For the S1 message UPLINK NAS TRANSPORT and CELL TRAFFIC TRACE, these message are seldom triggered, so we suggest do not trigger any location report for these message.
For the S1 message LOCAITON REPORT, we suggest the LIG get the location information from the LCS server directly.

## Slide 10: IRI Message Format (to be proposed and discussed in 3GPP)
Parameter | MOC | Description/Conditions
observed MSISDN | C | Provide at least one and others when available.
observed IMSI |  | 
observed ME Id |  | 
event type | M | Provide EPS location Update event type.
event date | M | Provide the date and time the event is detected.
event time |  | 
network identifier | M | Shall be provided.
location information | M | Provide, when authorized, to identify location information for the intercept subject's MS.
The message format is the same the format of TAU, just:
New Event type is defined as 99 (EPS location Update).
Old location information and Failure reason are not included.
Impact: LIG need to do customization for this new event type.
Note : unless there will be a new event type defined by 3GPP for TS 33.107, the suggestion was to re-use the existing event type ‘Tracking area Update

## Slide 11: Evaluation (Pros & Cons) of option 1 and 2

## Slide 12: Option 1: Gx/Rx based (PGW, PCRF, SBC)
Benefit of this solution:
  Location reporting is available in some vnedors PS core
  Gap could be solved on Rx interface (PCRF/SBC nodes)
  Low impact on LI: SIP info can easily forwarded from SBC to LI Mediation device
  ECGI change will provide granularity down to cell-ID level (HO inside a eNB between ~1-3 cells is as well reported )
Drawbacks of this solution:
  Major capacity penalty due to increase of signaling load of EPC, PCRF and SBC (initially negligible since it is related to calls and not to sessions, but will become significant with VoLTE expansion)

## Slide 13: Option 2: LI Cell Based IRI Reporting (MME)
Benefit of this solution:
  Affecting a single node only as the MME will provide the up to date location information
  It is complete invisible to a mobile operator as it is done per LI provision
  No signaling impact for the nodes like S/P-GW, PCRF and SBC
  Option 2 Preferred
Drawbacks of this solution:
  ECGI change will provide granularity down to eNB level only (HO inside a eNB while UE is in connected mode is NOT reported, TBC yet)
  At present 3GPP specification is not completed, there is a risk to be a proprietary solution for VF DE
  Impact on LI mediation system:
    Customization of new IRI event type
    LI mediation will be in charge to correlate the subscriber and VoLTE related info received from MME and SBC node