## Slide 1: 3gPP Sa3Li - #74
CC-PAG location determination and pairing approaches Discussion Document
S3i190413

## Slide 2: Agenda
Cr1 – replace existing pic in Sec8.6.2, with X2 links, no other changes
Cr2 – propose new pic in Sec8.6.2 without the dually-homed Hybrid UPF option with additional qualifications and describe options for pairing CC-PAGs

## Slide 3
SA3LI 33.127
Overall LI architecture
showing LI
at SMF/UPF with
CC-POI (as in sec 6.2.3)

## Slide 4
SA3LI #73 –CR/3GPP R16
Sophia Antipolis
LI
Deployment
architecture
showing LI at
SMF/UPF with
CC-PAG
(CC-POI Aggregator)
Hybrid mode
Direct mode

## Slide 5
SA3LI#73–CR/3GPP R16
Sophia Antipolis
LI architecture
showing LI at
SMF/UPF with
optional
CC-PAG
(CC-POI Aggregator)
Simplified

## Slide 6: CC-PAG Location Determination & Pairing
Deployment Options to consider to ensure Operators are onboard and comfortable with provisioning
Direct Mode:
  Fixed/Static configuration based on LI bandwidth and mapping ‘N’ UPFs to a CC-PAG (1,3)
    UPF -> CC-PAG -> MDF (new option from Sophia Antipolis)
  UPF -> MDF (same as before Sophia Antipolis)
Hybrid Mode: on a per UPF basis (2)
  UPF -> is Dually homed to both CC-PAG AND MDF (new option from Sophia Antipolis)

## Slide 7: CC-PAG Location Determination & Pairing – The case for Direct mode
CC-PAG closer to UPF has advantages for deployment sizing based on number of LI session originations, close to DataCenters where UPFs are racked
CC-PAGs closer to UPF means easier to manage and operate (map N upfs to 1 CC-PAG, and incremental additional CC-PAGs added to scale out)
Reduced number of endpoints/fan-in on MDF3 when CC-PAG is closer to UPF
CC-PAG closer to UPF reduces first hop latency, (can be potentially on the same server as UPF vm’s)
Simple option Fixed CC-PAGs for all UPFs in the Data Center(option1)
Simple option Fixed MDF3 for all UPFs in the Data Center (option2)
CC-TF provisioning@SMF: The MDF3 or CC-PAG address is given to the CC-POI at the trigger time.
  A different non-trigger based provisioning message may be needed and the CC-POI will have to ignore what is being told in the trigger, this is for per warrant
  A LIPF functional requirement to map per warrant in UPF to CCPAG (per DC)

## Slide 8: Requirements for Direct Mode
UPF to CC-PAG should not be on a per warrant basis, it should be for ALL warrants
To support the above requirements:
Introduce a per DataCenter (DC) concept
LIPF has to know all the UPFs in a DC for deployment, to ensure mapping/config/provisioning is made easier
  All UPFs in a DC can go either to CC-PAG or to MDF3 for ALL warrants
  UPF to CC-PAGs, CC-PAG to MDF3 mapping is done by LIPF

## Slide 9: CC-PAG Location Determination & Pairing – The case against Hybrid Mode
Per warrant you may have to mix n match – this has overheads
Ability to provision per target granularity per SMF+UPF combination – does it need some signaling from LIPF->SMF to disambiguate the breakout
Deployment challenges for operators networks, when dual homing, since the SMF+UPF combination will need to be configured uniformly across all SMF+UPF pairs
(a)How will SMF be told or (b)will SMF make a choice itself to provision per warrant and when to send to CC-PAG and when to send to MDF3 - needs more clarification (Q:via CC-TF)
  CCTF will need to have a configuration to determine what/where goes to CC-PAG on a per target basis
The fan-in at MDF3 is not reduced with this option. Instead it would require more input ports at the MDF3., which defeats one of the original goals with CC-PAG
  UPF to CC-PAG & MDF association of full-mesh Vs partial mesh is a TBD
Q: Should we eliminate need for HybridMode

## Slide 10: The Proposal – a Simplified view of LI options
By eliminating Hybrid Mode option, we present a simpler view of the deployment possibility in the pic below
And share the changes needed in LIPF to support the Direct Mode

## Slide 11
LI Architecture
With options
Per DC

## Slide 12: LIPF : UPF, CC-PAG, MDF selection algorithm
All UPFs present within a Data Center will either (1) all be connected to the same CC-PAG, or to (2) one or more MDF3s.
For (1):
  CC-PAG address is given to the SMF during the provisioning of intercept data as the destination address for all warrants.
  The LIPF gives the MDF3 address to the CC-PAG on a per warrant basis.
For (2):
  MDF3 address is given to the SMF during the provisioning of intercept data as the destination address for LI_X3 on a per warrant basis.
For the above to work, the LIPF should have the configuration data on a per data center basis
For example
  LIPF Data (per Data Center):
    CC-PAG: YES/NO.
    If YES, CC PAG address.
    If NO, there is no CC-PAG, use MDF3
  LIPF Data (on a per warrant basis):
    If CC-PAG configuration data is YES, then destination address which is normally the MDF3 address is replaced by the CC-PAG address and the MDF3 address is given to that CC-PAG as a part of provisioning the intercept data for that warrant.
    If the CC-PAG configuration data is NO, then destination address is the MDF3 address. In this case, no provisioning of CC-PAG.

## Slide 13
LI architecture
Showing
How
Warrants
Are
Handled in both
Deployments

## Slide 14: How warrants are handled in DirectMode
The IRI-POI output (SMF) may go to the MDF2 based on the provisioned data for the warrant.
The CC-PAG output and CC-POI outputs go to MDF3 based on the provisioned data for the warrant.
The CC-POI output (UPF) may go to CC-PAG based on the provisioned data for the data center.
The CC-POI output (UPF) may also go to MDF3 based on the provisioned data for the warrant.