## Slide 1: 3gPP Sa3Li - #75
CC-PAG Provisioning and Deployment Discussion Document/Presentation
S3i190506
Cisco, Nokia/Nokia Shanghai Bell, NTAC, Eve-Compliancy

## Slide 2: Agenda
Identify needed extensions to ensure the provisioning of LI when CC-PAG is involved to support the 3 modes as defined in Sec 8.6 of 33.127

## Slide 3
SA3LI 33.127
Overall LI architecture
showing LI
at SMF/UPF with
CC-POI (as in sec 6.2.3)

## Slide 4
LI
Deployment
architecture
showing LI at
SMF/UPF with
CC-PAG
(CC-POI Aggregator)
Hybrid mode
InDirect mode
Direct mode

## Slide 5
LI architecture
showing LI at
SMF/UPF with
optional
CC-PAG
(CC-POI Aggregator)
Simplified
InDirect
Hybrid
Direct

## Slide 6: CC-PAG Deployment modes
Direct Mode:
  UPF -> MDF (sec 6.x)
InDirect Mode:
  Mapping ‘N’ UPFs to a CC-PAG
    UPF -> CC-PAG -> MDF (new option from Sophia Antipolis)
Hybrid Mode:
  UPF -> Dually homed to both CC-PAG AND MDF (new option from Sophia Antipolis)
NOTE: SMF in context means IRI-POI/CC-TF, and UPF means CC-POI for purposes of discussion

## Slide 7: What extensions do we need?
Do we want to choose to route towards CCPAG based on QFI/QCI or an explore alternate mechanism?
  If YES, then we need a way of identifying “flows” - which I think means we need a QFI (QCI) as a TargetIdentifier type (SMF+UPF) should be known to ADMF for all LI tasks
  Use deliveryDestination specification is already present in LI_X1 per task basis
Do we have a requirement for the ADMF/LIPF to be able to instruct the SMF TF that, for a given SMF TF Task, UPF POI tasks should be delivered to the CC-PAG while some shouldn't?

## Slide 8: Some Guiding Provisioning Principles
ADMF/LIPF
  ADMF/LIPF has knowledge of deployment topology (via MANO/NFV/ETSI principles)
  SMF+UPF & CC-PAG : how they are grouped when CC-PAG is present or when CC-PAG is absent (per deployment/per DC/per Rack of servers)
  SMF+UPF mapping – Static Vs Dynamic (static preferred) for simplicity
  LIPF tasking SMF/IRI-POI+CC-TF to steer traffic redirection to support the 3 modes
  LIPF knows presence of CCPAG with its IP address (in the context of a DC or group of servers)
Granularity of LI provisioning
  Per Warrant or Per warrant Per Flow or Per Flow Type based on QFI
  Classify flows and direct them to appropriate MDF (or CC-PAG) destinations
    Eg: Hipriority traffic to MDF, low-priority traffic to CC-PAG, or Multiple classes of service
Networking Connectivity/routing is setup so traffic is steerable among all the LI components
Decouple LI provisioning from actual networking. LI is a service on Network infra.
CC-PAG – Closer to UPF for performance reasons/benefits

## Slide 9: Touchpoints across LI components/interfaces
ADMF/LIPF – some change in functional behavior
SMF (IRI-POI/CC-TF) – some change in functional behaviour
UPF (CC-POI) – some change in functional behaviour
LI-T3 – some, change based on QFI-QCI/TargetIdentifier
LI-X1 – some, change based on QFI-QCI/TargetIdentifier, Choose destinations based on QFI/QCI filter
LI-X3 – no change
MDF3 – Detect presence of CCPAG (Source IP-address Validation)
CC-PAG – some change/new component

## Slide 10: Use of QFI/QCI: QFI (SMF->UPF)
Use QFI/QCI to perform flow identification and partitioning
Configure QFI/Class of service table in LIPF->SMF->UPF
Instruct UPF to Classify the flow types in UPF POI
Per QFI identifier -> perform IP redirect with deliveryDestination given

## Slide 11: Provisioning Components : ADMF-LIPF
  LIPF to know deployment posture, will need topo information (MANO/NFV), it is informed about the presence of all components in the LI framework
  LIPF keeps ‘state’, and presence of CCPAG
  LIPF instructs SMF/IRI-POI-CC-TF to use CC-PAG via an extension to the destinationObject, per deliveryDestination via LI_X1
    The LI_XI extension is part of the ETSI TC LI spec (to be confirmed)
    LIPF at this point empowers SMF/IRI-POI to act on the ‘flow type’ and determine its destination (in presence/absence of CC-PAG)

## Slide 12: Provisioning Components: SMF-UPF
SMF->UPF becomes responsible to drive the provisioning
Use LI_T3 to provide the delivery destination
If a flow-type is to be treated differently in different deployments, treat them as separate LI Tasks (easier and preferred)
  for ex1. the same flow-type can be realized in 3 ways when SMFs are deployed in 3 modes across 3 different DataCenters:
    User A – all flows go deliveryDestination MDF3 in DC-1
    User A – all flows go deliveryDestination CCPAG in DC-2
    User A – QFI Flows X,Y go deliveryDestination CCPAG, QFI Flow Z goes to deliveryDestination MDF3 in DC-3
  We can have multiple target identifiers per Task/flow-type with different XIDs. User is immaterial, Flow/QFI is material

## Slide 13: Provisioning Interface: LI_X1, LI_T3
LI_X1 - Is always per flow type (ex: voice, video, data, hi/med/lo priority) (not per TCP or UDP)
LI_X1 has the capability to carry the IP needed for the redirection to CCPAG or MDF3
LI_X1 has extension needed (TBD/deliveryDestination Object)
Carries the QFI and deliveryDestination IP address to UPF/CC-POI

## Slide 14: Provisioning Interface: LI_X3
LI_X3 has no change
MDF3 may need extra correlation info at MDF, so source IP of the payload received at MDF3 can be verified together with XID
Essentially MDF3 verifies the presence of CC-PAG

## Slide 15: Provisioning Component: CC-PAG
LI_X1 provides the config profile
LI_X1 provides the deliveryDestination IP (MDF3)
Transports xCC

## Slide 16: Some alternatives/Open questions …
using multiple target identities to help with XID triggering and use it to solve the problem of how to instruct the SMF TF to route based on QCIs
  assume we have an LIPF that wants to tell an SMF TF to trigger interception for traffic where SUPI = X.
  assume that the LIPF knows (via magical means as yet to be defined) that the SMF is in a DC with a group of UPFs that have a CC-PAG.
  assume that the LIPF only wants to route traffic for QCI = A to the CC-PAG, QCI = B to the MDF3.
  Do this by configuration (so the SMF TF just "knows" somehow - e.g. from LI_X0 - to set destination to CC-PAG for QCI = A)
  Do this by adding some sort of filtering criteria to the DestinationDetails in the X1 protocol (which requires a modification / extension to LI_X1)
  Create multiple target identifiers and multiple Tasks. Essentially, the LIPF creates two Tasks on the SMF TF:
    - Task 1 has target identifiers [SUPI = X, QCI = A] and deliveryDestination - CC-PAG, XID1
    - Task 2 has target identifiers [SUPI = X, QCI = B] and deliveryDestination = MDF, XID2
      supply the MDF both of these XIDs so that it knows to correlate the received xCC