## Slide 1
CC-PAG Provisioning and Deployment
Discussion Document/Sophia-Antipolis Jan 2020
3gPP Sa3Li - #76
s3i200051
Cisco, Nokia/Nokia Shanghai Bell, NTAC, Eve-Compliancy, Verizon

## Slide 2: Agenda
Clarifications/Corrections to ensure the provisioning of LI when CC-PAG is involved as defined in Sec 8.6 of 33.127

## Slide 3
SA3LI 33.127
LI architecture
showing LI
at SMF/UPF with
CC-POI (as in sec 6.2.3)

## Slide 4
LI Deployment
architecture
showing LI at
SMF/UPF with
CC-PAG
(CC-POI Aggregator)
Current 33.127
PIC
Sec 8.6.2

## Slide 5
LI Deployment
architecture
showing LI at
CC-PAG
(CC-POI Aggregator)
NEW PIC
Section 8.6.2

## Slide 6: CC-PAG Simplified pic
reason for change is that we can represent all possibilities in one pic, eliminating confusion (such as per DC, per network, per mode, per task etc)
With the new pic, we can enable:
  a. UPF -> MDF (sec 6.x)
  b. Mapping ‘N’ UPFs to a CC-PAG
    UPF -> CC-PAG -> MDF
  c. UPF dually homed to both CC-PAG AND MDF

## Slide 7: Provisioning
LI provisioning per Task across UPFs
    A. (SMF CONTROL):: SMF-UPF to use a generic X3 delivery destination that could be of type CCPAG (and local mechanism to choose a CCPAG) OR
    B. (ADMF-LIPF CONTROL):: LIPF indicates via a CCPAG flag per Task, if a UPF will home to a CCPAG or to a MDF3 destination. UPF could be preconfigured with which CCPAG to use (ETSI X1 spec needs a change or use a destination details attribute). LIPF instructs SMF-UPF.
Preconditions:
Networking Connectivity/routing is setup apriory so traffic is steerable among all the LI components
CC-PAG is placed Closer to UPF for performance reasons/benefits where applicable. Its not mandatory to have a CC-PAG in the deployment (per network/data-center) but useable when present

## Slide 8: Changes across LI components/interfaces
ADMF/LIPF – some change in functional behavior(CC-PAG presence flag)
SMF (IRI-POI/CC-TF) – some change in functional behaviour
UPF (CC-POI) – some change in functional behavior, can be configured with a CC-PAG address at init/bootstrap
LI-X1 – some change based on QFI-QCI/TargetIdentifier, Choose destinations based on per Task/QFI/QCI, add a extension deliveryType/deliveryDestinationAddress (CCPAG) in ETSI TC LI spec
LI-X3 – no change
MDF3 – No change (but it could Detect presence of CCPAG (via Source IP-address Validation if needed)
CC-PAG – new component, when present, its next-hop address is a MDF3