## Slide 1: 3GPP Event Exposure Framework
Joint call between SA2, CT3 and SA4
26th January 2022
Tdoc S4aI221290

## Slide 2: Meeting agenda
Topics:
  Review SA4 EVEX Work Item objectives, system architecture, and collaboration scenarios.
  Highlight areas for collaborative SA4 work with CT3 and SA2.
  Discuss specific topics and questions from SA4 in the context of ongoing EVEX work and recent LS exchanges
Objectives:
  Ensure clear understanding of EVEX and related tasks/deliverables across the three WGs.
  Agree on way forward for completion of EVEX-related technical specifications, including topics for further discussion, scheduling follow-up joint meeting (if necessary), etc.

## Slide 3: EVEX Work Item Description
SA2 defines in TS 23.288 a generic network data source, the Data Collection AF (DC-AF), from which the NWDAF can obtain network and UE related information via AF Event Exposure services.
SA2 requested SA4 to devise a system architecture supporting the provisioning, collection and event exposure of UE application-specific data (“UE data”) by the DC-AF to the NWDAF, which SA4 agreed to support as one of its Rel-17 EVEX Work Item objectives.
The other EVEX objectives are to:
  Extend Rel-16 5GMS (5G Media Streaming) functionality to support event exposure by the 5GMS AF, a domain-specific instantiation of the DC-AF, to multiple consumer entities – NWDAF, Application Service Provider (ASP), etc.
    5GMS-specific UE data deemed useful for event exposure include CDN access logging, QoS and charging policy modifications, network assistance, and reporting of service consumption and QoE metrics
  Enhance the 5GMS AF in support of both direct and indirect collection of UE data.
  Devise mechanisms that enable the ASP to control access by event consumers to UE data collected by the AF.

## Slide 4: EVEX reference architecture Reference point representation
This is an abstract reference architecture intended to be instantiated in different functional domains.
  The first such domain is the set of UE events already identified by SA2 in TS 23.502.
  The second domain identified is 5G Media Streaming, to be documented in TS 26.501.
  5G Multicast–Broadcast User Services, defined in TS 26.502, is a third domain envisaged.
Note that there is no indication of deployment architecture in this reference model.

## Slide 5: Collaboration A
All EVEX network functions deployed inside the Trusted domain.

## Slide 6: Collaboration B
Data Collection AF deployed inside the trusted domain.
Application Service Provider functions deployed outside the trusted domain.
Application Server (AS) deployed inside the trusted domain.
Consequences:
Reference points R1, R3 and R6 must now traverse the NEF.

## Slide 7: Collaboration C
Data Collection AF deployed inside the trusted domain.
Application Service Provider functions deployed outside the trusted domain.
Application Server (AS) deployed outside the trusted domain.
Consequences:
Reference point R4 must now additionally traverse the NEF.

## Slide 8: Collaboration D
Data Collection AF deployed outside the trusted domain.
Application Service Provider functions deployed outside the trusted domain.
Application Server (AS) deployed outside the trusted domain.
Consequences:
Reference point R5 now traverses the NEF.
Reference points R1, R3 and R6 no longer need to follow 3GPP standards.

## Slide 9: Collaboration E
Simplified UE functional architecture in which the Direct Data Collection Client is realised as a subfunction the UE Application.
Consequences:
Reference point R7 now subsumed inside the UE Application and is instead realised as an internal API.

## Slide 10: EVEX reference architecture Service-based representation

## Slide 11: EVEX reference architecture Service-based representation (variant)
Data Collection AF deployed in an External DN interacts with the NRF and NWDAF via the NEF.

## Slide 12: Instantiation of EVEX reference architecture for 5G Media Streaming functional domain
UE
5GMS Client
Media Session Handler
5GMS AF
5GMS
Application
Provider
Data Collection AF
R2
R1
NWDAF
R5
M8
5GMS AS
Direct Data
Collection Client
Indirect reporting via 5GMS Application Provider
5GMS AS
R4
Metrics
Collection &
Reporting
Consumption
Collection &
Reporting
Event subscription
Management by 5GMS AP,
Event
publication
to 5GMS AP
5GMS
-
Aware Application
Data Collection configuration,
Direct reporting
M6
M5
Service Access Information,
5GMS Reporting configurations
M1
5GMS reporting provisioning
Media Stream Handler
M6
Provisioning AF
Indirect
Data Collection
Client
Event Consumer
AF
R6
R3
Data Collection configuration,
Indirect reporting
Data Reporting provisioning
R4
Data Collection configuration,
Indirect reporting

## Slide 13: Naf_EventExposure – by DC-AF in Trusted domain to NWDAF
In principle no missing functionality for event types defined in TS 23.288 and TS 23.502, and corresponding Naf_EventExposure service API specified in TS 29.517.
SA4 asks SA2/CT3 to check whether QoE metrics as part of the Service Experience event type (Table 6.4.2-1 in TS 23.288) is fully specified at Stage 3 in TS 29.517 (Table 5.6.2.9 shows only MOS).
(TS 23.288)
(TS 29.517)

## Slide 14: Naf_EventExposure/Nnef_EventExposure – by Data Collection AF in Trusted domain to AF inside or outside Trusted domain
In LS, SA4 asked SA2 whether AF event exposure to system actors other than NWDAF (and which may reside outside Trusted domain) is acceptable in 5G architecture.
  SA2 replied that such is beyond the scope of their request (on generic data collection/reporting architecture development and the requirements of Rel-17 eNA).
  SA4 is unclear on the reply since
    TS 23.502 clause 5.6 indicates that example consumers of Nnef_EventExposure service includes AF;
    Also, TS 29.522 clause 4.3.1 states that NEF supports exposing events provided by 3GPP NFs to an AF.
     It would seem plausible that an example instance of such 3GPP NF is an AF deployed within the Trusted domain, e.g., a Data Collection AF (which exposes event information to an AF deployed outside the Trusted domain).
(TS 23.288) Table 5.2.6.1-1: NF Services provided by the NEF
(TS 29.522)

## Slide 15: 5G Media Streaming-related Events for AF exposure (1)
As described in TS 26.501 and TS 26.512 (both Rel-16), the UE application data defined by the 5G Media Streaming architecture and suitable for AF event exposure are:
  5GMS QoE metrics reports
    Reporting of QoE metrics information measured by the UE during one or more media streaming sessions.
  5GMS Consumption reports
    Reporting of media content consumption information measured by the UE during one or more media streaming sessions.
  5GMS downlink access logs
    Information on media content access by the UE as recorded by 5GMS AS during one or more media streaming sessions.
  Invocation of charging and/or QoS policy modifications to 5GMS sessions
    Invocation of dynamic modifications to charging and/or QoS treatment during one or more media streaming sessions.
  Invocation of Network Assistance in 5GMS sessions
    Invocation of dynamic bit rate recommendation and/or delivery boost request/response interactions between the UE and AF during one or more media streaming sessions.
SA2 has already adopted 5G Media Streaming QoE metrics (as well as QoE metrics for other SA4-defined application services) into TS 23.288.
The RESTful APIs associated with these event types are expected to be specified in TS 29.517.

## Slide 16: 5G Media Streaming-related Events for AF exposure (2)
It may be feasible to extend TS 23.502 by referencing TS 26.501 and TS 23.288 for these new events relating to 5G Media Streaming.
For example:
(TS 23.502)

## Slide 17: Additional events to support 5G Media Streaming: Stage 3 support in TS 29.517
Feature number | AfEventNotification.event value (from AfEvent enumeration) | AfEventNotification additional property | Data type of additional property
1 | SVC_EXPERIENCE | svcExprcInfos | array(ServiceExperienceInfoPerApp)
2 | UE_MOBILITY | ueMobilityInfos | array(UeMobilityCollection)
3 | UE_COMM | ueCommInfos | array(UeCommunicationCollection)
4 | EXCEPTIONS | excepInfos | array(ExceptionInfo)
7 | USER_DATA_CONGESTION | congestionInfos | array(UserDataCongestionCollection)
8 | PERF_DATA | perfDataInfos | array(PerformanceDataCollection)
9 | DISPERSION | dispersionInfos | array(DispersionCollection)
10 | COLLECTIVE_BEHAVIOUR | collBhvrInfs | array(CollectiveBehaviourInfo)
New | MS_ACCESS_LOG | mediaStreamingAccessInfos | array(MediaStreamingAccessLogEntry)
New | MS_UE_QOE | mediaStreamingUeQoeInfos | array(MediaStreamingUeQoeReport)
New | MS_UE_CONSUMPTION | mediaStreamingUeConsumption | array(MediaStreamingUeConsumptionReport)
New | MS_NETWORK_ASSISTANCE | mediaStreamingNetworkAssistance | array(MediaStreamingNetworkAssistanceReport)
New | MS_DYNAMIC_POLICY | mediaStreamingDynamicPolicy | array(MediaStreamingDynamicPolicyReport)

## Slide 18: Ndcaf_DataReporting service Stage 2 and Stage 3 (Collaboration A)
Enables data collection client (Direct Data Collection Client over R2, Indirect Data Collection Client over R3, or AS over R4) to obtain its data collection and reporting configuration from, and subsequently send data reports to, the Data Collection AF, assuming in each case that both endpoint entities reside in the Trusted domain.
  SA4 will specify the above functionality in TS 26.531 and TS 26.532.
  SA4 asks SA2 to confirm that R3 and R4 procedures should occur over the Control Plane SBI “bus”.
Application
Service Provider
UE
Data
Collection
AF
Direct
Data Collection
Client
R2
R1
NRF
R8
UE Application
R7
NWDAF
R5
NEF
N33
AS
R4
Indirect
Data Collection
Client
Event Consumer
AF
R6
R3
Provisioning AF

## Slide 19: Nnef_DataReporting service Stage 2 and Stage 3 (Collaboration C or D)
Same logical functionality as Ndcaf_DataReporting, except that either the data collection client or Data Collection AF is assumed to reside in the Trust domain, while its peer entity is assumed to reside outside the Trusted domain.
  SA4 will produce the Stage 2 text for this functionality in TS 26.501.
  CT3 is requested to specify the corresponding Stage 3 APIs in their specification (TS 29.522?).
NEF
Application
Service Provider
UE
Data
Collection
AF
Direct
Data Collection
Client
R2
R1
NRF
R8
UE Application
R7
NWDAF
R5
AS
R4
Indirect
Data Collection
Client
R6
R3
Trusted domain
Event
Consumer
AF
Provisioning
AF
or

## Slide 20: Nnef_NFManagement service Stage 2 and Stage 3 (Collaboration D)
Enables registration of externally-deployed Data Collection AF with the NRF (via NEF) for subsequent discovery by event service consumer functions.
  SA2 is asked to advise on whether such service should be defined in TS 23.288 and TS 23.502.
    SA4’s understanding is that SA2 has working assumption that such AF registration with the NEF is currently performed via implementation-specific mechanisms.
    Should SA2 decide in future to define such procedure as a standardized service, TS 23.288 and/or TS 23.502 will need to be correspondingly extended.
  If the SA2 answer is “no”, then the Nnef_NFManagement service will likely not be included as part of EVEX (and related Rel-17 5G Media Streaming) specifications.
NEF
NEF
Application
Service Provider
UE
Data
Collection
AF
Direct
Data Collection
Client
R2
R1
′
NRF
R8
UE Application
R7
NWDAF
R5
AS
R4
′
Indirect
Data Collection
Client
R6
′
R3
′
Trusted domain
Event Consumer
AF
Provisioning AF

## Slide 21: Stage 2 on PSS QoE metrics for Stage 3 specification
Service type | Metrics type | Brief Stage 2 description | Detailed “Stage 2.5” description | Stage 3 API description | Comments | EVEX support in Rel-17
PSS unicast RTP-based streaming* | Corruption duration | Length of corrupted media frame sequences | TS 26.234 clause 11.2.1 | TS 26.234 clause 5.3.2.3.3 | XML reporting format option | No
 | Rebuffering duration | Length of rebuffering events | TS 26.234 clause 11.2.2 | “ | “ | “
 | Initial buffering duration | Length of the initial buffering | TS 26.234 clause 11.2.3 | “ | “ | “
 | Successive loss of RTP packets | Number of RTP packets lost in succession | TS 26.234 clause 11.2.4 | “ | “ | “
 | Frame rate deviation | Deviation from nominal frame rate | TS 26.234 clause 11.2.5 | “ | “ | “
 | Jitter duration | Length of jitter events | TS 26.234 clause 11.2.6 | “ |  | 
 | Content switch time | Time to switch to another content | TS 26.234 clause 11.2.7 | “ |  | 
 | Average codec bitrate | Number of media bits rendered divided by duration of rendering | TS 26.234 clause 11.2.8 | “ | “ | “
 | Codec information | Identifies codec information (e.g., type, encoding, profile, level) | TS 26.234 clause 11.2.9 | “ | “ | “
 | Buffer status | Current buffer level | TS 26.234 clause 11.2.9 | “ | “ | “
* Presently, TS 23.288 does not reference TS 26.234 Packet-switched Streaming Service (PSS) as valid SA4-specified service type; probably an oversight to be corrected re. QoE metrics. |  |  |  |  |  | 

## Slide 22: Stage 2 on MBMS QoE metrics for Stage 3 specification
Service type | Metrics type | Brief Stage 2 description | Detailed “Stage 2.5” description | Stage 3 API description | Comments | EVEX support in Rel-17?
MBMS-based streaming | Corruption duration | Length of corrupted media frame sequences | TS 26.346 clause 8.4.2.1 | TS 26.346 clauses 9.4.6 and 9.5.3 |  | No
 | Rebuffering duration | Length of rebuffering events | TS 26.346 clause 8.4.2.2 | “ |  | “
 | Initial buffering duration | Length of the initial buffering | TS 26.346 clause 8.4.2.3 | “ |  | “
 | Successive loss of RTP packets | Number of RTP packets lost in succession | TS 26.346 clause 8.4.2.4 | “ |  | “
 | Frame rate deviation | Deviation from nominal frame rate | TS 26.346 clause 8.4.2.5 | “ |  | “
 | Jitter duration | Length of jitter events | TS 26.346 clause 8.4.2.6 | “ |  | “
 | Content access/switch time | Time to access/switch to new/another content | TS 26.346 clause 8.4.2.7 | “ |  | “
 | Network resource | Identity of cell used | TS 26.346 clause 8.4.2.8 | “ |  | “
 | Average codec bitrate | Number of media bits rendered divided by duration of rendering | TS 26.346 clause 8.4.2.9 | “ |  | “
 | Codec information | Identifies codec information (e.g., type, encoding, profile, level) | TS 26.346 clause 8.4.2.10 | “ |  | “
 | Object loss | Current buffer level | TS 26.346 clause 8.4.2.11 | “ |  | “
 | Symbol underrun | Symbol count underrun distribution for failed blocks | TS 26.346 clause 8.4.2.12 | “ |  | “

## Slide 23: Stage 2 on MTSI QoE metrics for Stage 3 specification
Service type | Metrics type | Brief Stage 2 description | Detailed “Stage 2.5” description | Stage 3 API description | Comments | EVEX support in Rel-17?
MTSI (Multimedia telephony ) | Corruption duration | Length of corrupted media frame sequences | TS 26.114 clause 16.2.1 | TS 26.114 clause 16.4 |  | No
 | Successive loss of RTP packets | Number of RTP packets lost in succession | TS 26.114 clause 16.2.2 | “ |  | “
 | Frame rate | Media frame rate | TS 26.114 clause 16.2.3 | “ |  | “
 | Jitter duration | Length of jitter events | TS 26.114 clause 16.2.4 | “ |  | “
 | Sync loss duration | Interval during which time difference in actual playback between last played video and audio/speech frames exceeds the expected difference by a defined threshold | TS 26.114 clause 16.2.5 | “ |  | “
 | Round-trip time | Round-trip time based on RTCP | TS 26.114 clause 16.2.6 | “ |  | “
 | Average codec bitrate | Bitrate for coding “active” media information during measurement interval | TS 26.114 clause 16.2.7 | “ |  | “
 | Codec information | Identifies codec information (e.g., type, encoding, profile, level) | TS 26.114 clause 16.2.8 | “ |  | “

## Slide 24: Stage 2 on 3GP-DASH QoE metrics for Stage 3 specification
Service type | Metrics type | Brief Stage 2 description | Detailed “Stage 2.5” description | Stage 3 API description | Comments | EVEX support in Rel-17?
3GP-DASH | Representation switch events | List of all Representation switch events during a DASH Media Presentation | TS 26.247 clause 10.2.3 (which points to ISO/IEC 23009-1 clause D.4.4) | TS 26.247 clause 10.5 | Subset of the play list metric | Yes
 | Throughput | Average throughput on TCP connection of associated access bearer | TS 26.247 clause 10.2.4 | “ |  | “
 | Initial playout delay | Duration between fetch of first Media Segment and when media is retrieved from buffer | TS 26.247 clause 10.2.5 | “ | Can also be derived from play list metric | “
 | Buffer level | List of buffer occupancy levels during playout | TS 26.247 clause 10.2.6 (which points to ISO/IEC 23009-1 clause D.4.5) | “ |  | “
 | Play list | List of all media playback periods | TS 26.247 clause 10.2.7 | “ |  | “
 | MPD information | List of media encoding characteristics | TS 26.247 clause 10.2.8 | “ | Almost identical to initial playout delay metric | “
 | Start-up playout delay | Time to start up media playback | TS 26.247 clause 10.2.9 | “ |  | “
 | Device information | Display video resolution and physical screen characteristics | TS 26.247 clause 10.2.10 | “ |  | “

## Slide 25: Stage 2 on VR Streaming QoE metrics for Stage 3 specification
Service type | Metrics type | Brief Stage 2 description | Detailed “Stage 2.5” description | Stage 3 API description | Comments | EVEX support in Rel-17?
Virtual Reality streaming | Comparable quality viewport switching latency | List of measured latencies for restoring normal video quality due to viewport movement | TS 26.118 clause 9.3.2 | TS 26.118 clause 9.4.3 |  | Yes
 | Rendered viewport metrics | List of rendered viewports during the Media Presentation | TS 26.118 clause 9.3.3 | “ |  | “
 | Device information | VR device information including device identifier, physical screen properties and time when the information logged | TS 26.118 clause 9.3.4 | “ |  | “

## Slide 26: Discussion and next steps
Above slides represent summary of key expected tasks for SA4, CT3 and possibly SA2 to perform to align specifications across the WGs in support of the EVEX Work Item.
SA2 and CT3 feedback on questions and suggested actions in slides 14-20; do we have consensus?
Identify areas for further discussion/agreement.
Agree on high level plan towards Rel-17 work completion.
Anticipate future coordination calls among CT3, SA2 and SA4.
Future meeting schedule of CT3, SA2 and SA4
  CT3#119-bis-e 17-21 Jan. 2022
  CT3#120-e 17-25 Feb. 2022
  CT3#121-e 6-12 Apr. 2022
  CT3#122-e 12-20 May. 2022
SA2#149-e 14-25 Feb. 2022
SA2#150-e April 2022
SA2#151-e May 2022
SA4#117-e 14-23 Feb. 2022
SA4#118-e 6-14 Apr. 2022
SA4#119-e 11-20 May. 2022

## Slide 27: Questions and asks recap
(Slide 13) Support for QoE metrics in TS 29.517? (note new info in slides 21-26)
(Slide 14) Is Naf_EventExposure offering to entity outside trusted domain already supported and specified in SA2 and CT3 specs?
(Slide 15 and 17) TS 29.517 specification of RESTful APIs for 5GMS-specific event types
(Slide 16) Potential support by Rel-17 SA2 spec(s) for additional (5GMS-related) event types?
(Slide 18) Should R3 and R4 procedures operate over the SBI “bus”?
(Slide 19) CT3 specification of APIs for R3 and R4 (and if so, in which spec(s))
(Slide 20) Should Nnef_NFManagement service and procedures be defined in SA2 specs (to enable registration of AF in untrusted domain to in the NRF)?