## Slide 1: Progressing Rel-17 Specs regarding EVEX
Joint call between CT3, SA2 and SA4
24th March 2022
Tdoc S4aI221341

## Slide 2: Meeting agenda
Topics:
  Review SA4 progress on Rel-17 stage 2 and stage 3 specifications regarding data collection and reporting between data collection client and Data Collection AF, and event exposure by Data Collection AF to NWDAF and Application Service Provider (its Event Consumer AF sub-function)
  Discuss Rel-17 stage 3 work by CT3 on relevant specifications in support of the Naf_EventExposure service, and mediation by NEF for data collection and reporting, and event exposure interactions (Nnef_EventExposure and Nnef_DataReporting services).
  Discuss potential Rel-17 SA2 spec changes with regards to AF event exposure, and data collection & reporting in relation to EVEX and 5G Media Streaming
Objectives:
  Agree on overall plan and schedule for completion of EVEX-related technical specifications

## Slide 3: EVEX Work Item
SA2 defines in TS 23.288 a generic network data source, the Data Collection AF (DC-AF), from which the NWDAF can obtain network and UE related information via AF Event Exposure services.
SA2 requested SA4 to devise a system architecture supporting the provisioning, collection and event exposure of UE application-specific data (“UE data”) by the DC-AF to the NWDAF, which SA4 agreed to support as one of its Rel-17 EVEX Work Item objectives.
The other EVEX objectives are to:
  Extend Rel-16 5GMS (5G Media Streaming) functionality to support event exposure by the 5GMS AF, a domain-specific instantiation of the DC-AF, to multiple consumer entities – NWDAF, Application Service Provider (ASP), etc.
    5GMS-specific UE data deemed useful for event exposure include media streaming access logging, QoS and charging policy modifications, network assistance, and reporting of service consumption and QoE metrics
  Enhance the 5GMS AF in support of both direct and indirect collection of UE data.
  Devise mechanisms that enable the ASP to control access by event consumers to UE data collected by the AF.
Request for SA Plenary approval of EVEX Work Item Exception submitted by SA4 at SA4#117-e.

## Slide 4: EVEX reference architecture Reference point representation
This is an abstract reference architecture intended to be instantiated in different functional domains.
  The first such domain is the set of UE events already identified by SA2 in TS 23.502.
  The second domain identified is 5G Media Streaming, to be documented in TS 26.501.
  5G Multicast–Broadcast User Services, defined in TS 26.502, and Edge Media Processing Extensions to 5G Media Streaming to be additionally documented in TS 26.501, are the third and fourth domains envisaged.
Note that there is no indication of deployment architecture in this reference model.

## Slide 5: Instantiation of EVEX reference architecture for 5G Media Streaming functional domain
UE
5GMS Client
Media Session Handler
5GMS AF
5GMS
Application
Provider
Data Collection AF
R2
R1
NWDAF
R5
M8
5GMS AS
Direct Data
Collection Client
Indirect reporting via 5GMS Application Provider
5GMS AS
R4
Metrics
Collection &
Reporting
Consumption
Collection &
Reporting
Event subscription
Management by 5GMS AP,
Event
publication
to 5GMS AP
5GMS
-
Aware Application
Data Collection configuration,
Direct reporting of UE data
M6
M5
Service Access Information,
5GMS Reporting configurations
M1
5GMS reporting provisioning
Media Stream Handler
M6
Provisioning AF
Indirect
Data Collection
Client
Event Consumer
AF
R6
R3
Data Collection configuration,
Indirect reporting of UE data
Data Reporting provisioning
R4
Data Collection configuration,
Indirect reporting of streaming media access activity

## Slide 6: 5G Media Streaming-related Events for AF exposure (1)
As described in Rel-17 TS 26.501 and TS 26.512 undergoing SA4 development, the following types of UE application data as defined in the 5G Media Streaming architecture are eligible for AF event exposure:
  5GMS QoE metrics reports
    Reporting of QoE metrics information measured by UEs during their media streaming sessions.
  5GMS Consumption reports
    Reporting of media content consumption information measured by UEs during their media streaming sessions.
  5GMS downlink access logs
    Information on media content access by UEs as recorded by 5GMS AS during their media streaming sessions.
  Invocation of charging and/or QoS policy modifications to 5GMS sessions
    UEs’ invocation of dynamic modifications to charging and/or QoS treatment during their media streaming sessions.
  Invocation of Network Assistance in 5GMS sessions
    UEs’ invocation of dynamic bit rate recommendation and/or delivery boost request/response interactions between the UE and AF during their media streaming sessions.
SA2 has already adopted 5G Media Streaming QoE metrics (as well as QoE metrics for other SA4-defined application services) in TS 23.288, and requests SA4 to define the stage 2 descriptions of the other 5G Media Streaming Event types.

## Slide 7: 5G Media Streaming-related Events for AF exposure (2)
R5
Besides direct event exposure by Data Collection AF to an Event consumer when both entities reside in the same trust domain, mediated event exposure by the NEF is required when the two entities reside in separate trust domains.
Will require stage 3 specification of corresponding Naf_EventExposure and Nnef_EventExposure service APIs.
  Agreement per LS exchange that CT3 would define 5G Media Streaming related Naf_EventExposure and Nnef_EventExposure services APIs in their specifications.

## Slide 8: Additional events to support 5G Media Streaming: Stage 3 support in TS 29.517
Feature number | AfEventNotification.event value (from AfEvent enumeration) | AfEventNotification additional property | Data type of additional property
1 | SVC_EXPERIENCE | svcExprcInfos | array(ServiceExperienceInfoPerApp)
2 | UE_MOBILITY | ueMobilityInfos | array(UeMobilityCollection)
3 | UE_COMM | ueCommInfos | array(UeCommunicationCollection)
4 | EXCEPTIONS | excepInfos | array(ExceptionInfo)
7 | USER_DATA_CONGESTION | congestionInfos | array(UserDataCongestionCollection)
8 | PERF_DATA | perfDataInfos | array(PerformanceDataCollection)
9 | DISPERSION | dispersionInfos | array(DispersionCollection)
10 | COLLECTIVE_BEHAVIOUR | collBhvrInfs | array(CollectiveBehaviourInfo)
New | MS_ACCESS_LOG | mediaStreamingAccessInfos | array(MediaStreamingAccessLogEntry)
New | MS_UE_QOE | mediaStreamingUeQoeInfos | array(MediaStreamingUeQoeReport)
New | MS_UE_CONSUMPTION | mediaStreamingUeConsumption | array(MediaStreamingUeConsumptionReport)
New | MS_NETWORK_ASSISTANCE | mediaStreamingNetworkAssistance | array(MediaStreamingNetworkAssistanceReport)
New | MS_DYNAMIC_POLICY | mediaStreamingDynamicPolicy | array(MediaStreamingDynamicPolicyReport)

## Slide 9: Ndcaf_DataReporting service Stage 2 and Stage 3 (Collaboration A)
Enables data collection client (Direct Data Collection Client over R2, Indirect Data Collection Client over R3, or AS over R4) to obtain its data collection and reporting configuration from, and subsequently send data reports to, the Data Collection AF, assuming in each case that both endpoints reside in the same trust domain.
  SA4 will specify the above functionality in TS 26.531 and TS 26.532.
Application
Service Provider
UE
Data
Collection
AF
Direct
Data Collection
Client
R2
R1
NRF
R8
UE Application
R7
NWDAF
R5
NEF
N33
AS
R4
Indirect
Data Collection
Client
Event Consumer
AF
R6
R3
Provisioning AF

## Slide 10: Nnef_DataReporting service Stage 2 and Stage 3 (Collaboration C)
Same logical functionality as the Ndcaf_DataReporting service, except that either the data collection client or Data Collection AF is assumed to reside in the Trust domain, while its peer entity is assumed to reside outside the Trusted domain
In the context of 5G Media Streaming, the only data collection client of concern is the AS, which in the architecture model as shown, has to acquire its configuration from, and report media streaming access activity to, the Data Collection AF over the R4 reference point via the NEF
SA4 will produce the Stage 2 text for this functionality in TS 26.501.
  CT3 is requested to specify the corresponding RESTful APIs in their specs (TS 29.522)

## Slide 11: Summary of SA4 asks to CT3
From the description in slides 6-10, SA4 is requesting CT3 support to:
  Add a few more Event types regarding Media Streaming data to the existing Naf_EventExposure service.
  Enable these events to be exposed to entities in external trust domain via the Nnef_EventExposure service.
  Enable interaction, via NEF, between entities located in different trust domains in supporting the SA4-defined Ndcaf_DataReporting service operations via the (new) Nnef_DataReporting service.
  SA4 will provide the necessary details (more of that in the following slides) to facilitate the CT3 work.

## Slide 12: Relevant SA4 specs’ content to facilitate CT3 spec work (1)
Naf_EventExposure and Nnef_EventExposure services
  The following Stage 2 and Stage 3 SA4 specifications/clauses containing relevant information on the following types of 5G Media Streaming UE data acquired by the Data Collection Function (instantiated in the 5GMS AF) for subsequent event exposure:
  QoE metrics
    (see TS 26.247 clauses 10.4, 10.5, 10.6; TS 26.501 clause 4.2; TS 26.512 clauses 4.2, 7.8, 11.4)
  Consumption reports
    (see TS 26.501 clause 4.2; TS 26.512 clauses 4.2, 7.7, 11.3)
  Network Assistance invocations
    (see TS 26.238 clause 4.6; TS 26.501 clause 4.2; TS 26.12 clauses 4.2, 11.6)
  Charging and Policy invocations
    (see TS 26.501 clause 4.2; TS 26.512 clauses 4.2, 7.9, 11.5)
    Media streaming access activity
      (see TS 26.501 clauses 5.11, 6.10; TS 26.512 clauses 4.2, 4.11)

## Slide 13: Relevant SA4 specs’ content to facilitate CT3 spec work (2)
Nnef_DataReporting service
  Enables 5GMS AS to obtain its data collection and reporting configuration from, and subsequently report media streaming access activity to, the Data Collection AF, when the two entities are located in different trust domains.
  See TS 26.531, clauses 5.4, 5.5 and TS 26.532, clauses 7.2 (Data Collection and Reporting Configuration API) and 7.3 (Data Reporting API).

## Slide 14: Summary, tasks, and suggested next steps
Above slides summarizes current status and remaining tasks for SA4, CT3 and possibly SA2 in aligning specifications across the WGs to complete the EVEX Work Item.
Request to CT3 on specific tasks for further discussion/agreement.
Agree on high level plan for Rel-17 work completion – target approval of EVEX WI completion at SA#96 (June 2022), involving the following specs:
  SA4: TS’s 26.501, 26.512, 26.531, 26.532
  CT3: TS’s 29.517, TS 29.522 (any others?)
  SA: TS 23.502 (?)
Plan future joint coordination call(s) in April and/or May.
Future meeting schedule of CT3, SA2 and SA4
  CT3#121-e 6-12 Apr 2022
  CT3#122-e 12-20 May 2022
SA2#150-e 6-12 Apr. 2022
SA2#151-e 16-20 May 2022
SA4#118-e 6-14 Apr 2022
SA4#119-e 11-20 May 2022