## Slide 1: Rel-18 Status 5GMS_Pro_Ph2 and Potential Impact for Rel-19
Thomas Stockhammer (Rapporteur)
Qualcomm Technologies
tsto@qti.qualcomm.com
3GPP TSG SA WG4 Meeting #127 S4aI230190
Sophia Antipolis, France 29 January – 2 February 2024

## Slide 2: Relevant Documents and Timelines
SP-230976 WID 5G Media Streaming Protocols Phase 2
S4-231683 Updated Work Plan, Qualcomm Incorporated,
S4-232002 TS 26.510 V0.4.0 editor's draft, BBC,
S4-232008 Permanent Document v0.2.0, Qualcomm Incorporated (Rapporteur)
S4-232009 5GMS Functions are general Media Functions, Qualcomm Incorporated, BBC, Tencent (endorsed)
S4-232010 RTC Functions are general Media Functions, Qualcomm Incorporated (endorsed)
SA4#127 (29 January - 2 February 2024, Sophia Antipolis, FR) | Agree CRs to 26.512 5G Media Streaming Protocols Phase 2 Agree CRs to 26.247 DASH extensions for 5G Media Streaming Phase 2 Agree CR to 26.517 Extensions to MBS User Services to support 5GMS Agree CR to 26.532 Extensions to Event Exposure to support Network Assistance Agree TS 26.510 v2.0.0 to be sent to SA plenary for approval. Complete the permanent document on handling commonalities and inconsistencies across stage-2 specifications of TS26.501 and TS26.506. Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis Endorse work item summary
Supporting IM name
Qualcomm Incorporated
Tencent
BBC
Sony Europe B.V.
Orange
Dolby Laboratories Inc.
AT&T
Ericsson
HuaWei Technologies Co., Ltd
Samsung Electronics, CO., LTD
NTT

## Slide 3: Work Item Objectives Status
# | Objective | Supporters and Efforts | Status
1 | Stage 3 support for uplink streaming as defined in TS 26.501 and based on the conclusions in clause 6.5 of TR 26.804. | explicit supporters Tencent, BBC; expected efforts medium | 
2 | Stage 3 support for end-to-end low latency live streaming as defined in TS 26.501 and based on the conclusions in clause 6.11 of TR 26.804. | explicit supporters Qualcomm, Tencent, BBC; expected efforts medium | 80%, yes
3 | Stage 3 support for 5GMS over MBS and 5GMS hybrid services as defined in TS 26.501 and based on the conclusions in TR 26.804 and TR 26.802 | explicit supporters Qualcomm, BBC; expected efforts medium | 80%, yes
4 | Stage 3 support for multiple media service entry points as defined in TS 26.501 and based on the conclusions in TR 26.804. | explicit supporters Qualcomm, Tencent, BBC; expected efforts medium | 80%, yes
5 | Extensions to 5GMS protocols to support traffic identification based on the conclusions in TR 26.804, clause 6.3. | explicit supporters Ericsson, Qualcomm, Huawei, BBC; expected efforts low | 
6 | Addition of HTTP/3 to the 5GMS protocols as an optional alternative based on the conclusions in clause 6.4 of TR 26.804. | explicit supporters Tencent, BBC; expected efforts low | 
7 | Addition of necessary parameter extensions to the M1, M5, and M6 reference points to provide access to Background Data Transfer based on the conclusions in clause 6.6 of TR 26.804. | explicit supporters Qualcomm, BBC; expected efforts medium | 
8 | Specification of the usage of Oauth 2.0 (according to the SA3 guidelines) for 5GMS protocols based on the conclusions in clause 6.9 of TR 26.804. | explicit supporters Ericsson, BBC, Qualcomm; expected efforts medium | 
9 | Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming based on the conclusions in clause 6.13 of TR 26.804. | Qualcomm, BBC, Dolby, Tencent; expected efforts medium | 
10 | Additional minor enhancements based on feedback from 5G-MAG Reference tool developments. | BBC, Qualcomm, Dolby; expected efforts low | 
11 | Specification of a RESTful API at reference point M3 for the configuration of 5GMS AS instances by 5GMS AF based on the conclusions in TR 26.804. | BBC, Qualcomm, Tencent; expected efforts low | 
12 | Specification of data types for data reporting of ANBR-based Network Assistance invocations and (in liaison with CT3) specification of data types for exposure of events relating to invocation of AF-based and ANBR-based Network Assistance. | Sony, BBC; expected efforts medium | 
13 | Develop a new specification for Generalized media delivery to document interactions and APIs for provisioning and media session handling consolidating the stage-3 specification for reference points M1/RTC-1, M5/RTC-5 and M6/RTC-6 and port general functionalities from TS 26.512 to this new specification. | BBC, Qualcomm, Tencent, Samsung, NTT Expected efforts: high | 

## Slide 4: 1) Uplink streaming
Documents
  S4-231834 26.510: Uplink streaming improvements on draft 0.1.0, Tencent Cloud
Impacted Specification
  TS 26.512
Candidate for TS 26.510: Yes
Status
  80% complete
Expect completion at SA4#127
1 | Stage 3 support for uplink streaming as defined in TS 26.501 and based on the conclusions in clause 6.5 of TR 26.804. | explicit supporters Tencent, BBC; expected efforts medium | 

## Slide 5: 2) Low Latency and Dynamic Policies
Documents
  S4-231972 Low-Latency Streaming and Dynamic Policies, Qualcomm Incorporated, Ericsson
  Note: document was not yet uploaded
Impacted Specification
  TS 26.512
Candidate for TS 26.510: No
Status
  80% complete
Expect completion at SA4#127
2 | Stage 3 support for end-to-end low latency live streaming as defined in TS 26.501 and based on the conclusions in clause 6.11 of TR 26.804. | explicit supporters Qualcomm, Tencent, BBC; expected efforts medium | 80% yes

## Slide 6: 3) 5GMS over MBS
Documents
  S4-231973 5GMS over MBS and 5GMS hybrid services, Qualcomm Incorporated
Impacted Specification
  TS 26.512
Candidate for TS 26.510: No
Status
  80% complete
Expect completion at SA4#127
3 | Stage 3 support for 5GMS over MBS and 5GMS hybrid services as defined in TS 26.501 and based on the conclusions in TR 26.804 and TR 26.802 | explicit supporters Qualcomm, BBC; expected efforts medium | 

## Slide 7: 4) Multiple Media Service Entry Points
Documents
  S4-231471 [5GMS_Pro_Ph2] Multiple media service entry points, Qualcomm Incorporated
  S4-231971 Multiple Service Entry & Uplink streaming: media entry point, Tencent Cloud
Impacted Specification
  TS 26.512
Candidate for TS 26.510: possibly
Status
  80% complete
Expect completion at SA4#127
4 | Stage 3 support for multiple media service entry points as defined in TS 26.501 and based on the conclusions in TR 26.804. | explicit supporters Qualcomm, Tencent, BBC; expected efforts medium | 

## Slide 8: 5) Traffic Identification
Documents
  S4-231754 Traffic Identification, Ericsson LM
Candidate for TS 26.510: possibly
Status
  80% complete
Expect completion at SA4#127
5 | Extensions to 5GMS protocols to support traffic identification based on the conclusions in TR 26.804, clause 6.3. | explicit supporters Ericsson, Qualcomm, Huawei, BBC; expected efforts low | 

## Slide 9: 6) HTTP/3
Documents
  S4-231854 [5GMS_Pro_Ph2] Add HTTP-3 as allowed protocol in 26.512, Tencent (was noted)
Candidate for TS 26.510: yes
Status
  0% complete
Unlikely completion at SA4#127
6 | Addition of HTTP/3 to the 5GMS protocols as an optional alternative based on the conclusions in clause 6.4 of TR 26.804. | explicit supporters Tencent, BBC; expected efforts low | 

## Slide 10: 7) Background Data Traffic
Stage-2 agreement
  S4-232004 [5GMS_Ph2] Addition of Background Data Transfer feature, BBC, Qualcomm Incorporated
Documents
  S4-231194 CR on Background Data Transfer in 5GMS, Qualcomm CDMA Technologies endorsed
  S4-231653 [5GMS_Pro_Ph2] Improvements on Background Data Transfer in 5GMS, Tencent Cloud (noted)
Candidate for TS 26.510: no
Status
  50% complete
Unlikely completion at SA4#127
7 | Addition of necessary parameter extensions to the M1, M5, and M6 reference points to provide access to Background Data Transfer based on the conclusions in clause 6.6 of TR 26.804. | explicit supporters Qualcomm, BBC; expected efforts medium | 

## Slide 11: 8) OAuth2.0
Documents
  S4-231753 Extending 5GMS with Oauth 2.0 support, Ericsson LM
Candidate for TS 26.510: no
Status
  50% complete
Discussion from SA4#126:
  Richard: Is the idea to obtain an authorization code, and use it subsequently in M5
  Thorsten: Yes
  Richard: Do we need this kind of security (oauth) at M5? Understand for M1. We got a security network right. What are you protecting against
  Thorsten: For example, you could have applications using policy templates of other applications that it is not intended to use
  Imed: Just to follow up, this is calls invoked my MSH, not by application. Maybe we need to dig deeper. Where will the MSH get it
  Thorsten: In 26804, we have done some scenarios. People should start looking
Unlikely completion at SA4#127
8 | Specification of the usage of Oauth 2.0 (according to the SA3 guidelines) for 5GMS protocols based on the conclusions in clause 6.9 of TR 26.804. | explicit supporters Ericsson, BBC, Qualcomm; expected efforts medium | 

## Slide 12: 9) Service URL Handler
Documents
Candidate for TS 26.510: no
Status
  60% complete
Unlikely completion at SA4#127
9 | Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming based on the conclusions in clause 6.13 of TR 26.804. | Qualcomm, BBC, Dolby, Tencent; expected efforts medium | 

## Slide 13: 9) Service URL Handler
Documents
Candidate for TS 26.510: no
Status
  60% complete
Unlikely completion at SA4#127
9 | Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming based on the conclusions in clause 6.13 of TR 26.804. | Qualcomm, BBC, Dolby, Tencent; expected efforts medium | 

## Slide 14: 10) 5G-MAG Feedback
Documents
Candidate for TS 26.510: no
Status
  60% complete
Expect completion at SA4#127
10 | Additional minor enhancements based on feedback from 5G-MAG Reference tool developments. | BBC, Qualcomm, Dolby; expected efforts low | 

## Slide 15: 11) M3
Documents
Candidate for TS 26.510: no
Status
  60% complete
Expect completion at SA4#127
11 | Specification of a RESTful API at reference point M3 for the configuration of 5GMS AS instances by 5GMS AF based on the conclusions in TR 26.804. | BBC, Qualcomm, Tencent; expected efforts low | 

## Slide 16: 12) ABNR-based Network Assistance
Documents
Candidate for TS 26.510: no
Status
  60% complete
Expect completion at SA4#127
12 | Specification of data types for data reporting of ANBR-based Network Assistance invocations and (in liaison with CT3) specification of data types for exposure of events relating to invocation of AF-based and ANBR-based Network Assistance. | Sony, BBC; expected efforts medium | 

## Slide 17: 13) ABNR-based Network Assistance
Documents
Candidate for TS 26.510: yes
Status
  60% complete
Expect completion to 75% at SA4#127
13 | Develop a new specification for Generalized media delivery to document interactions and APIs for provisioning and media session handling consolidating the stage-3 specification for reference points M1/RTC-1, M5/RTC-5 and M6/RTC-6 and port general functionalities from TS 26.512 to this new specification. | BBC, Qualcomm, Tencent, Samsung, NTT Expected efforts: high | 

## Slide 18: Conclusions

## Slide 19: Status Check
Of the 13 Work Topics, at least half of them are expected to be completed at SA4#127
However, it is expected that not all topics can be completed
In addition, a proper porting to TS 26.510 needs to be completed
An exception may be warranted with a very clear set of actions to complete the remaining topics based on this slide deck.
Preliminary considerations