## Slide 1: 5G-MAG Views on FS_AMD Advanced Media Delivery
02.05.2024 – Workshop on Advanced Media Delivery with 3GPP SA4
S4aI240054 (also available as CD0149r3 in 5G-MAG)
5G-MAG MEDIA ACTION GROUP
www.5g-mag.com

## Slide 2
5G-MAG MEDIA ACTION GROUP
WHERE MEDIA MEETS CONNECTIVITY

## Slide 3
5G-MAG MEDIA ACTION GROUP
WHERE MEDIA MEETS CONNECTIVITY
We foster collaboration across the global media and telecom industries through pragmatic and member-driven work.
Our focus: new media experiences powered by the Internet, mobile technologies, networks, multimedia systems, codecs, and APIs.
We are an independent international non-for-profit cross-industry association

## Slide 4
Industry, Developers, Users and Stakeholders
Relevant SDOs
Profiles & Guidelines
Explainers & Reports
Use Cases, Requirements
Market views
Industry Consensus
Work Items, Workgroups and Public Communities
Reference Tools
Engagement & Feedback
Validation & Verification
*5G-MAG is a 3GPP Market Representation Partner
MoU
MoU
Joint TF 2023
Part of the MSF Register
Collaboration
3GPP MRP
5G-MAG MEDIA ACTION GROUP
WHERE MEDIA MEETS CONNECTIVITY
Collaboration and Synergies with SDOs and Industry fora
Technology Mix part of 5G-MAG Reference Tools

## Slide 5
Check the Current Topics at 5g-mag.com
Member-, contribution-driven and pragmatic work
Media over IP
Live Contribution and Remote Production beyond just connectivity
  Topics
  5g-mag.com/topics
5G Media Streaming
Driving effective collaboration between media applications and mobile networks
5G Broadcast
Global broadcast standard for TV, radio and emergency alerts on mainstream devices
5G Multicast Broadcast
Scalability for content delivery in mobile networks through point-to-multipoint communication
Media beyond 2D
User experiences beyond traditional 2D services to apps and browsers
eXtended Reality & Immersive Media
Towards the next computing platform converging the digital, physical & virtual worlds
Non-Terrestrial Networks
Media over Satellites, HAPS, UVAs and hybrid TN and NTN networks

## Slide 6: Background
TS 26.501: 5GMS architecture, call flows, and procedures
TS 26.512: 5G Media Streaming protocols
WI 5GMS_Ph2 provides extension to 5GMS
WI 5GMS_Pro_Ph2 provides extension to 5GMS protocols
TS 26.510 generalizes the topic of media delivery
For MBS, TS 26.502 develops User Service architecture. TS 26.517 defines MBS protocols
5G-MAG is developing Reference Tools for these specifications

## Slide 7
Open-source Reference Tools for Multimedia Applications
Our repositories currently contain reference implementations based on specifications developed by:
  Technology into Action
  developer.5g-mag.com
Community of Developers
We bring technology closer to developers
Reference Implementations
To validate, test, demo and create products
Feedback to SDOs
To help improve specifications
IPR-friendly License Model
To encourage contributions from the industry

## Slide 8: Feedback on Specifications from developers
We funnel feedback from developers and users into SDOs
Issues, bugs, feature requests? github.com/5G-MAG/Standards/
GitHub issues
Experts – Users - Developers
Technical Specifications and relevant SDOs
github.com/5G-MAG/
Standards
Discussions at the
5G-MAG Forum
Collaboration with 3GPP SA4

## Slide 9
5G Media Streaming Architecture
5G Core Network components
Multimedia delivery protocols
MBMS & LTE-based 5G Broadcast
5G Multicast Broadcast Services
XR Media Integration in 5G
AI/ML Evaluation Framework
5G-MAG Reference Tools under development
Emergency Alerts over 5G Broadcast
DVB-I over 5G

## Slide 10: Status of 5G Media Streaming development
5G Media Streaming network components developed so far:
5GMS Application Provider
  Web portal for service providers
5GMS Application Server
  Wrapping OpenResty (Nginx)
5GMS Application Function
  Built in the Open5GS framework.
5G Media Streaming Client components developed so far on Android:
5GMS-enabled Media Player
  Wrapping ExoPlayer.
Media Session Handler
  Background service.
5GMS-Aware Application
  App, optionally incorporating the Media Player component.
Notes: Richard

## Slide 11: Status of 5G Media Streaming development
5G Media Streaming feature |  | 5GMS Application Function |  | 5GMS Client
 |  | Provisioning (M1) | Usage (M5) | 
Content hosting |  | Pull-based | Done | Done
QoE metrics reporting |  | Pending release | Pending release | Pending release
Consumption reporting |  | Done | Done | Done
Network Assistance |  |  |  | 
 | Delivery boost | Not applicable | Done | To do
 | Throughput estimation | Not applicable | To do | To do
Dynamic Policies |  | Done | Done | To do
Not implemented and welcome…
  5GC with support for PCF
  5GC with support for NEF

## Slide 12: Under development
Amplifier + TX
Exciter
RF
Modulator / eNodeB
digital I/Q data
MCE
MME
MBMS-GW (Sync)
BM-SC
Content Provider
M1 (data)
,
M2 & S1 (ctrl)
xMB: ctrl & data
Broadcast Core
Stationary reception
rt-wui / VLC / dash.js / …
rt-mbms-mw
(with rt-libflute)
rt-mbms-modem
(using srsRAN) SDR
Qualcomm QRD or CRD
rt-mbms-mw-android
QC MBMS MW
Baseband (HW)
with QC SW to enable ROM
ffmpeg
,
RTP MPEG-TS
or HLS/DASH via rt-libflute
srsRAN mbms-gw
srsRAN mbms-gw
rt-mbms-tx
SDR (BladeRF, Lime, Ettus, …)

## Slide 13: Status of 5G MBS development
Start with Broadcast mode in RAN and 5G Core
  MVP#0: only user plane – MB-UPF
  MVP#0.1: user plane and control plane* – MB-UPF, MB-SMF* and AMF*
Why? Less complexity (MBS session management, implementation)
Continue with Multicast mode in 5G Core (only shared subset with Broadcast)

## Slide 14: Status of 5G MBS development
srsRAN mbms-gw

## Slide 15: Technology into Action

## Slide 16
Workshop on Advanced Media Delivery with 3GPP SA4
Work Topics and Views from 5G-MAG

## Slide 17: Scope of the Work Item FS_AMD
Main focus: segmented media objects in the media plane
interoperability considerations around content delivery protocol features and general technologies for segmented media streaming and the IP/PDU 5G System Layer

## Slide 18: Scope of the Work Item FS_AMD
Document the following additional Key Issues in more detail, in particular how they relate to the 3GPP Media Delivery architecture and/or the MBS User Service architecture (NEXT SLIDE)
Study collaboration scenarios between the Application Service Provider and the 5G System and for each of the key topics.
Based on existing architectures, develop one or more deployment architectures that address the key topics and the collaboration models.
Map the key topics to basic functions and develop high-level call flows.
Identify the issues that need to be solved.
Provide candidate solutions including call flows, protocols and APIs for each of the identified issues.
Coordinate work with other 3GPP groups e.g. SA2, SA3, SA5, SA6 and others as needed.
Coordinate work with external organizations such as DASH-IF, CTA WAVE, ISO/IEC JTC29 WG3 (MPEG Systems), 5G-MAG, DVB or IETF, as needed.
Identify gaps and recommend potential normative work for stage-2 and stage-3, including which existing specifications would be impacted and/or if any new specifications would preferably be developed.

## Slide 19: List of Work Topics and Views from 5G-MAG
Topic | Title
1 | Common Client Metadata
2 | Common Server-and Network-Assisted Streaming
3 | Multi-CDN and Multi-Access Media Delivery
4 | Modem Usage Optimized Media Streaming
5 | DRM and Conditional Access
6 | In-session Unicast Repair for MBS Object Distribution
7 | MBS User Service and Delivery Protocols for eMBMS
8 | Selected MBMS Functionalities not supported in MBS
9 | DASH/HLS Interoperability
10 | Further harmonization of RTC and Streaming for Advanced Media Delivery
11 | Issues identified by Market Representation Partners
12 | Improved QoS support
13 | Impacts and opportunities of QUIC for segmented content delivery

## Slide 20: WT0: TS26.51x outline
Description
The primary focus of this Work Item is the delivery of segmented media objects in the media plane, i.e. at reference points M2, M4 and M7 of the Media Delivery architecture. One of the open issues identified in the Rel-18 feasibility study 5GMS_Pro_Ph2 is the need for a specification that addresses interoperability considerations around content delivery protocol features and general technologies for segmented media streaming and the IP/PDU 5G System Layer. This points to the further study media plane issues to support additional functionalities, but also identifies what needs to be ported from legacy TS 26.512 to a generalised media plane technical specification. The relation to media session handling (as specified in TS 26.510) is identified in TR 26.804, but enhancements to media session handling are not the primary focus of this study.
5G-MAG Views
Update on delivery protocols for segmented media HTTP/1.1, HTTP/2, HTTP/3 together with TCP/IP, secure delivery Extensions to the delivery protocol that are common: HTTP headers, Query parameters, authentication Ingest protocols Non-HTTP contribution protocols at M4 (e.g. SRT, SST, RIST, NDI, WebTransport, Media-over-QUIC) Multi-access cellular bonding for resilience and capacity APIs taking into account the service (see 5G-MAG input to 6G SA1 WS next week as an example on missing API defining latency/jitter)

## Slide 21: WT1: Common Client Metadata
Description
While 3GPP and MPEG in DASH support DASH metrics, the reporting is not common to any player, for example all DASH players as well as HLS players. As an example, CTA WAVE has developed: CTA-5004: Web Application Video Ecosystem Common-Media-Client-Data (CMCD) with an excellent overview here: https://ottverse.com/common-media-client-data-cmcd/. It is worthwhile to study the benefits of integrating commonly supported metrics and client data reporting in 5GMS workflows. The focus is the integration of already defined metrics rather than developing new metrics. Examples of study include support of specific metric keys, player APIs, sending options from client to server (user plane, M5 reference point, EVEX), M3 reference point impact, as well as usage of the data in operations. A study of creating a common harmonized reporting framework and studying the interaction of different frameworks may be included.
5G-MAG Views
5G-MAG supports studying benefits of integration of the CMCD framework for 5GMS – harmonized reporting framework welcome Once done, it would be useful to add Reference Tools, review which metrics are currently defined and check them against an actual service, and if more metrics should be added.

## Slide 22: WT2: Common Server- and Network-Assisted Streaming
Description
MPEG-DASH supports Server and Network Assisted DASH (SAND). Certain profiles of SAND were adopted in TS 26.247, but the industry has generalized the concepts in SAND in efforts such as Content Steering (see ETSI TS 103 998), Web Application Video Ecosystem (WAVE) specification for Common Media Server Data (CMSD), or Addressable Resource Index (ARI) Tracks in MPEG. The study and integration of these technologies into the Media Delivery System and MBS/MBMS workflows is of significant interest, in particular also in combination with existing QoS mechanisms
5G-MAG Views
5G-MAG sees such additions potentially useful for service providers (load balancing, energy-aware steering, decisions based on cost) Content Steering across multiple 5GMS AS instances (i.e. Telco CDNs)? TN / NTN use cases to be taken into account for Content Steering Clarify the relation of CMSD with Network Assistance in 5GMS

## Slide 23: WT3: Multi-CDN and Multi-Access Media Delivery
Description
Content distributors often use multiple Content Delivery Networks (CDNs) to distribute their content to tend-users. As an example, they may upload a copy of their catalogue to each CDN, or more commonly have all CDNs pull the content from a common origin. In advanced deployments, technologies such as Coded Multisource Media Format (CMMF) use Application Layer FEC techniques to stripe different subsets of content across multiple CDNs. Different client implementations may then beneficially use the content on multiple CDNs, potentially guided by the service or network provider. In addition, formats and techniques for generating content for multiple CDN delivery such as MPEG-DASH Part 9 (ReAP) may be taken into account. Further extensions include the ability for a client to use multiple access networks at the same time to support media delivery. Study of integration of different technologies into the Media Delivery System is of relevance to address content provisioning, content hosting, impacts on user plane reference points M2 and M4, and on media session handling at reference point M5 as well as potential benefits in terms of quality and resource usage.

## Slide 24: WT3: Multi-CDN and Multi-Access Media Delivery

## Slide 25: WT3: Multi-CDN and Multi-Access Media Delivery
Description
Content distributors often use multiple Content Delivery Networks (CDNs) to distribute their content to tend-users. As an example, they may upload a copy of their catalogue to each CDN, or more commonly have all CDNs pull the content from a common origin. In advanced deployments, technologies such as Coded Multisource Media Format (CMMF) use Application Layer FEC techniques to stripe different subsets of content across multiple CDNs. Different client implementations may then beneficially use the content on multiple CDNs, potentially guided by the service or network provider. In addition, formats and techniques for generating content for multiple CDN delivery such as MPEG-DASH Part 9 (ReAP) may be taken into account. Further extensions include the ability for a client to use multiple access networks at the same time to support media delivery. Study of integration of different technologies into the Media Delivery System is of relevance to address content provisioning, content hosting, impacts on user plane reference points M2 and M4, and on media session handling at reference point M5 as well as potential benefits in terms of quality and resource usage.
5G-MAG Views
Multi-CDN approaches are in place today. Adding such functionality to 5GMS is welcome ATSSS: Multi-access cellular bonding (dual steer) and multi-path transport protocols for resilience and capacity ATSSS: WiFI plus NG-RAN is not the main use case of interest for 5G-MAG, cellular bonding happens between two carriers of 3GPP systems. ATSSS: What would be interested is to have multiple steer (similar to what it is done today where you are using multiple SIMs connected to different networks.)

## Slide 26: WT4: Modem Usage Optimized Media Streaming
Description
In Rel-18, basic support for Background Data Transfer is added. UE power resources are constrained, and media delivery typically also results in power consumption if the radio is always connected. In order to better support streaming services, requests and access to the modem and the resources should be well balanced. Enhancements to Background Data Transfer to support preload as well as functionality of what is defined in W3C Managed Media Source Extension to minimize active network connections are relevant topics to study with the aim of limiting battery consumption in the UE resulting from media delivery.
5G-MAG Views
Basic support for Background Data Traffic in Rel-18 5G-MAG supports sustainability and energy saving solutions in streaming Particularly relevant for UE energy saving and battery consumption

## Slide 27: WT5: DRM and Conditional Access
Description
DRM and Conditional Access are commonly used by third-party streaming services. However, in case streaming is done through MBS or MBMS, a more careful management of the keys needs to be checked. Scalability of key delivery is an issue. The support for -encrypted content in Unicast/Multicast and Broadcast is relevant. Integration of Content Protection interfaces in the provisioning, for example using CPIX back-end interfaces is of high relevance for the industry and should accordingly be studied. The impacts of these on media plane (reference points M2 and M4) as well as the media session handling APIs (reference points M3, M5) should also be studied.
5G-MAG Views
Signaling of DRM information via ServiceAccessInformation https://github.com/5G-MAG/Standards/issues/49

## Slide 28: WT6: In-session Unicast Repair for MBS Object Distribution
Description
For live and low-latency live services using the Object Distribution Method in MBS, in certain cases the transmission of an object is not successful. In this case, unicast repair for individual MBS Clients can improve the service quality. However, the timing of such requests needs to be carefully studied in order to avoid network overloads or significant latencies in the delivery. A study to extend MBS User Services and object streaming to address in-session repair is of relevance.
5G-MAG Views
This is something supported by other standards Welcome and good for reducing latency Unclear its applicability to: MBS Broadcast Service with parallel unicast resources for repait? MBS Multicast Services with dynamic RAN switching guaranteeing repair/service continuity?

## Slide 29: WT7: MBS User Service and Delivery Protocols for eMBMS
Description
The MBS User Service architecture and protocol follows the modern design philosophies of the 5G System with separation of user services from transport, a service-based architecture and RESTful APIs. At the same time, eMBMS and enTV as used for LTE-based 5G Broadcast support a transparent delivery mode. While interworking in between MBMS and MBS is addressed in TS 23.247, interworking between these two systems at the User Service level is not addressed. In order for MBMS and LTE-based 5G broadcast to leverage MBS User Service technologies, a study is warranted to identify the gaps to fully support this functionality.
5G-MAG Views
5G-MAG is implementing MBMS and LTE-based 5G Broadcast and MBS systems Potentially useful to maintain only one provisioning API and one content ingest interface
  It would be good to understand foreseen differences wrt Nmb9 on the reference point between MBMS-GW and “extended” MBSTF” - given this is under the radar of 5G-MAG Reference Tools

## Slide 30: WT8: Selected MBMS Functionalities not supported in MBS
Description
In completing TS 26.502 and TS 26.517, it is obvious that only a subset of the MBMS functionalities is supported in Rel-17. While many MBMS functionalities are likely not important to be supported for MBS, a systematic analysis of MBMS User Services features and their potential relevance for MBS should be completed and recommendations made on which ones to migrate to MBS User Services specifications and how best to achieve this.
5G-MAG Views
5G-MAG is implementing MBMS and LTE-based 5G Broadcast and MBS systems Potentially useful to maintain only one provisioning API and one content ingest interface

## Slide 31: WT9: DASH/HLS Interoperability
Description
DASH/HLS interoperability is a key issue to support highly scalable distribution systems for CDN-based distribution as well as for MBS/MBMS distribution. Offering common CMAF segments that can be consumed by both DASH and HLS media players promises to address these issues. However, detailed nuances need to be identified to ensure optimized delivery and CTA WAVE has provided detailed guidelines in CTA-5005-A to support this matter. Studying these guidelines and understanding the impacts on the 5GMS System as well as MBS/MBMS distribution is of relevance. In addition, formats and techniques supporting DASH/HLS interoperability such as MPEG-DASH part 9 (ReAP) may be taken into account.
5G-MAG Views
DASH/HLS interoperability is important for 5GMS as well as MBS and MBMS Low-Latency Protocols for Multicast and Broadcast

## Slide 32: WT10: Further harmonization of RTC & Streaming for AMD
Description
With the creation of TS 26.510 in Rel-18, Media delivery across the 5G Media Streaming (5GMS) System and the Real-time media Communication (RTC) System was harmonized. However, not all functionalities from TS 26.512 are yet commonly available for RTC as well. Study of further harmonization is encouraged to fully implement common Media Delivery functions.
5G-MAG Views
WG Content Production is currently looking into this topic for uplink streaming for object-based media (DASH/HLS), WebRTC/RTC and other procolos. Harmonisation is useful in terms of procedures and features Extension to support additional protocols relevant for uplink streaming under study

## Slide 33: WT11: Issues identified by Market Representation Partners
Description
Through the development in 5G-MAG of reference implementations for MBMS, 5GMS and MBS, 5G-MAG is identifying specific problems which are collected in https://github.com/5G-MAG/Standards/issues. While some of the issues are purely related to bug fixes, some of the issues may require study by SA4 and the development of new functionalities in the relevant technical specifications. It is vital to support the industry and MRPs in deploying 3GPP technologies.
5G-MAG Views
GitHub Issues: https://github.com/orgs/5G-MAG/projects/33

## Slide 34: WT12: Improved QoS support
Description
In Rel-18, SA2 has defined a number of new features in the 5G System, especially in the PCF, from which media delivery may benefit. Examples documented in TS 23.501 include the use of Explicit Congestion Notification (ECN) to support Low Latency, Low Loss, Scalable Throughput (L4S) services (clause 5.37.3), PDU Set handling (clause 5.37.5) and QoS Monitoring (clause 5.45), and there are likely others. The impact and usefulness of selected features is preferably studied. The functions identified in this context may be studied in one or more of the above work topics.
5G-MAG Views
This is relevant for content production context in terms of network awareness, congestion notification / assistance on throughput estimation, throughput scalability and fast reaction to trigger adaptation of content encoding,…

## Slide 35: WT13: Impacts & opps QUIC for segmented media delivery
Description
Since the finalisation of the QUIC protocol by the IETF in May 2021, there has been significant deployments of QUIC driven by the usage of HTTP/3 for streaming services. In the IETF, the working group on Media Over QUIC (MOQ) is working towards an extensible protocol for publishing media for ingest and distribution. While QUIC is mostly used today as the underlying protocol of HTTP/3, there is still open questions as to how media segments are delivered over QUIC streams when using HTTP/3 but also considering other QUIC-based protocols such as MOQ. Considering different types of media application, e.g. multi-stream use cases, will be of interest. Studying the various strategies for delivering segmented content over QUIC streams will also bring insights for the network management aspects. For instance, findings in this domain may be relevant to WT#2.1 in the ongoing study in SA2 called FS_XRM_Ph2 (SP-231671) whose deliverable is available as TR 23.700-70.
5G-MAG Views
Media over QUIC is of interest. Currently being studied in 5G-MAG’s WG Content Production Applicability of QUIC into “Beyond2D” use cases, in particular time-sensitive (low latency) use cases (e.g. multi-screen, multi-user watch together,…)

## Slide 36: Visit www.5g-mag.com or Contact us!
This presentation uses images from flaticon.com and unsplash.com
  Join our open communities Follow us