## Slide 1: FS_AMD: Advanced Media Delivery Overview for 5G-MAG
tsto@qti.qualcomm.com
Thomas Stockhammer
Qualcomm Incorporated
Co-Rapporteur of Study Item
April 18, 2024
S4-aI240055 (also CD0149r1)

## Slide 2
6 Work item Rapporteur(s)
[TBC Thomas Stockhammer, Qualcomm Incorporated, tsto@qti.qualcomm.com,] General & for topics 3, 5, 6, 7, 8, 10, 11 and 12.
NOTE1: TSG SA asks SA WG4 to consider Guidance on Rel-19 Rapporteurship (SP-230746).
Iraj Sodagar, Tencent, irajs@live.com, for topics 1, 2, 4, 9 and 13.
NOTE2: Leads for each work topic will be identified as part of the study.
Supporting IM name
AT&T
ATEME
BBC
China Mobile Com. Corporation
China Unicom
Comcast
Dolby France SAS
EBU
Ericsson LM
Huawei Technologies Co Ltd.
InterDigital Communications
Lenovo
NTT
Orange
Qualcomm Incorporated
Rohde &Schwarz
Samsung Electronics Co. Ltd.
Sony Europe B.V.
SWR
Telecom Italia
Tencent
Xiaomi
ZTE

## Slide 3: Background
TS 26.501 defines the 5GMS architecture, call flows, and procedures. TS 26.512 defines the 5G Media Streaming protocols. In the 5GMS_Ph2 work item, extensions to 5G Media Streaming architecture are provided. In the 5GMS_Pro_Ph2, extensions to 5G Media Streaming Protocols were provided and generalized the topic of media delivery by providing TS 26.510. In addition, for MBS, the User Service architecture was developed in TS 26.502 and MBS Protocols are defined in TS 26.517. It is also worth noting that 5G-MAG has defined reference implementations of both 5G Media Streaming and MBS. The implementation provides feedback for potential bugfixes.
However, mobile media delivery is as important as never before with everlasting growth of traffic and new functionalities provided by third-party service providers. Several potential improvement areas and potential extensions have been identified and should be studied further.
The primary focus of this Work Item is the delivery of segmented media objects in the media plane, i.e. at reference points M2, M4 and M7 of the Media Delivery architecture. One of the open issues identified in the Rel-18 feasibility study 5GMS_Pro_Ph2 is the need for a specification that addresses interoperability considerations around content delivery protocol features and general technologies for segmented media streaming and the IP/PDU 5G System Layer. This points to the further study media plane issues to support additional functionalities, but also identifies what needs to be ported from legacy TS 26.512 to a generalised media plane technical specification. The relation to media session handling (as specified in TS 26.510) is identified in TR 26.804, but enhancements to media session handling are not the primary focus of this study.

## Slide 4: 5G-MAG Involvement
https://www.5g-mag.com/post/5g-mag-workshop-with-3gpp-sa4-advanced-media-delivery

## Slide 5: Objectives
Document the following additional Key Issues in more detail, in particular how they relate to the 3GPP Media Delivery architecture and/or the MBS User Service architecture:
  Common Client Metadata.
  Common Server-and Network-Assisted Streaming.
  Multi-CDN and Multi-Access Media Delivery.
  Modem Usage Optimized Media Streaming.
  DRM and Conditional Access.
  In-session Unicast Repair for MBS Object Distribution.
  MBS User Service and Delivery Protocols for eMBMS.
  Selected MBMS Functionalities not supported in MBS.
  DASH/HLS Interoperability.
  Further harmonization of RTC and Streaming for Advanced Medial Delivery.
  Issues identified by Market Representation Partners.
  Improved QoS support.
  Impacts and opportunities of QUIC for segmented content delivery
Study collaboration scenarios between the Application Service Provider and the 5G System and for each of the key topics.
Based on existing architectures, develop one or more deployment architectures that address the key topics and the collaboration models.
Map the key topics to basic functions and develop high-level call flows.
Identify the issues that need to be solved.
Provide candidate solutions including call flows, protocols and APIs for each of the identified issues.
Coordinate work with other 3GPP groups e.g. SA2, SA3, SA5, SA6 and others as needed.
Coordinate work with external organizations such as DASH-IF, CTA WAVE, ISO/IEC JTC29 WG3 (MPEG Systems), 5G-MAG, DVB or IETF, as needed.
Identify gaps and recommend potential normative work for stage-2 and stage-3, including which existing specifications would be impacted and/or if any new specifications would preferably be developed.

## Slide 6: Architecture Baseline

## Slide 7: Specification Idea
TS 26.510
TS 26.51x
TS 26.51x
TS 26.51x

## Slide 8: Vision for Rel-19 work
This study is considered as an extension study of the existing Media Delivery Architecture as well as related stage-3 protocols, APIs and reference points. It is planned to identify topics for normative work to be addressed in the Rel-19 timeline as follows
  Completion of study by 09/2024 for stage-2 and by 12/2024 for stage-3
  Stage-2 normative work until 12/2024 (1 cycle work item, 100% completion within one cycle). An AHG meeting or an SA4#130bis in fall 2024 should be considered to support the completion of the work.
  Stage-3 normative work until 09/2025 (3 cycle work item, 30% 03/2025, 70% 06/2025, 100% 09/2025)
The study may only conclude in a subset of the work topics on what normative work will be addressed in Rel-19. Conclusions in the study may include that certain topics are for further study. Those topics may be addressed with lower priority in Rel-19 timeline, with a clear understanding that they very likely not be addressed in Rel-19 timeline.
The timelines above 09/2024 for stage-2 and 12/2024 are considered are strict deadlines for what is addressed in Rel-19 normative work. This study as well as the follow-up normative work is expected to address the following
  Study:
    TR 26.802: Documents key issues and work topics only related to MBS
    TR 26.804: Documents key issues and work topics primarily related to 5G Media Streaming, but may include also hybid aspects as issues related to topic 1j)
  Stage-2 normative work (note not all work may be done based on topics completed in the study phase and what is not completed)
    TS 26.500 (new) "Media Delivery Architecture" may be created to harmonize commonalities between TS 26.501 and TS 26.506, and to address advances that apply to both.
    TS 26.501: Documents stage-2 enhancements for 5G Media Streaming and creates references to TS 26.500 as needed
    TS 26.502: Documents stage-2 enhancements for MBS and creates references to TS 26.500 as needed
    TS 26.506: Documents stage-2 enhancements for RTC and creates references to TS 26.500 as needed
  Stage-3 normative work (note not all work may be done based on topics completed in the study phase as well as in stage-2)
    TS 26.510: Addresses enhancements to the Media Delivery: Session Handling Reference points and APIs
    TS 26.512: Addresses enhancements to 5G Media Streaming: Protocols and APIs
    TS 26.517: Addresses enhancements to MBS User Services: Protocols and APIs
    TS 26.51x (new): Addresses common Media Delivery Content Delivery Protocols

## Slide 9: Agreements from SA4#127-bis-e
S4-240841 | [FS_AMD] Proposed Time and Work Plan for Advanced Media Delivery | Qualcomm Incorporated (Rapporteur)
S4-240599 | [FS_AMD] Proposed Way forward and CR Template | Qualcomm Tech. Netherlands B.V
CR Template
X.1 Description
X.2 Collaboration Scenario
2. Study collaboration scenarios between the 5G System and Application Provider for each of the key topics.
X.3 Architecture Mapping
3. Based on existing architectures, develop one or more deployment architectures that address the key topics and the collaboration models.
X.4 High-level Call Flow
4. Map the key topics to basic functions and develop high-level call flows.
X.5 Gap Analysis and Requirements
5. Identify the issues that need to be solved.
X.6 Candidate Solutions
6. Provide candidate solutions including call flows, protocols and APIs for each of the identified issues.
X.7 Summary and Conclusions

## Slide 10: Leads and Supporters for Each Work Topic and related Input
Topic | Title | Lead | Explicit Supporters | Related CR number | Status
1 | Common Client Metadata | Thomas Stockhammer, Qualcomm | Qualcomm, Dolby, CMCC, AT&T, Telecom Italia, Comcast, Orange, BBC, EBU, Tencent, ATEME |  | 
2 | Common Server-and Network-Assisted Streaming. | Iraj Sodagar, Tencent | Qualcomm, Dolby, AT&T, Comcast, Tencent, ATEME, Sony Europe B.V. |  | 
3 | Multi-CDN and Multi-Access Media Delivery. | Jason Cloud, Dolby | Qualcomm, Dolby, AT&T, Orange, Samsung Electronics Co. Ltd., Huawei Technologies Co Ltd., ATEME | 26804-0006rev1 26804-xxxx (pCR Samsung) | noted noted
4 | Modem Usage Optimized Media Streaming. | Iraj Sodagar, Tencent | Qualcomm, Dolby, Comcast, BBC, EBU, Tencent |  | 
5 | DRM and Conditional Access. | Thomas Stockhammer, Qualcomm | Qualcomm, Telecom Italia, Comcast, Rohde&Schwarz, Huawei Technologies Co Ltd. |  | 
6 | In-session Unicast Repair for MBS Object Distribution. | Thomas Stockhammer, Qualcomm | Qualcomm, Telecom Italia, Comcast, Orange, BBC, SWR, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., ATEME |  | 
7 | MBS User Service and Delivery Protocols for eMBMS. | Thomas Stockhammer, Qualcomm | Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, ATEME |  | 
8 | Selected MBMS Functionalities not supported in MBS. | Thomas Stockhammer, Qualcomm | Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., ATEME |  | 
9 | DASH/HLS Interoperability. | Iraj Sodagar, Tencent | Qualcomm, Telecom Italia, Comcast, Orange, BBC, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., Tencent |  | 
10 | Further harmonization of RTC and Streaming for Advanced Media Delivery. | open | Qualcomm, CMCC, Comcast, Samsung Electronics Co. Ltd., NTT, InterDigital Communications, Lenovo |  | 
11 | Issues identified by Market Representation Partners. | Thomas Stockhammer, Qualcomm | Qualcomm, Comcast, BBC, Dolby, EBU |  | 
12 | Improved QoS support |  | Ericsson LM, Huawei Technologies Co Ltd., Qualcomm, BBC, InterDigital Communications, Lenovo | 26804-0007rev1 | endorsed
13 | Impacts and opportunities of QUIC for segmented content delivery | Emmanouil Potetsianakis, Xiaomi, emmanouil@xiaomi.com | Xiaomi, Qualcomm, others | 26804-pCR | endorsed

## Slide 11
3GPP SA4 MBS SWG Telco (May 2, 2024, 15:30 – 17:30 CEST, Host Qualcomm) | Workshop with 5G-MAG – get input and feedback on agreed work topics and potential new aspects. Discuss other issues with 5G-MAG Progress definition of work topics Submission Deadline April 30, noon CEST | Target 15% Real
3GPP SA4 MBS SWG Telco (May 7, 2024, 15:30 – 17:30 CEST, Host Qualcomm) | Progress definition of work topics Progress CRs for each work topic Submission Deadline May 6, noon CEST | Target 20% Real
SA4#128 (20 – 24 May 2024, Jeju Island, KR) | Complete documenting each work topic and collaboration scenarios Start developing high-level call flows. Start identifying the issues that need to be solved. Start candidate solutions including call flows, protocols and APIs for each of the identified issues. Progress CRs for each work topic Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis | Target 30% Real
SA#104 (18 – 21 June 2024, China) | No actions | 
SA4#129-e (19 – 23 August 2024, online) | Complete high-level call flows. Progress identifying the issues that need to be solved. Progress candidate solutions including call flows, protocols and APIs for each of the identified issues. Complete identifying gaps and recommend potential normative work for stage-2 for relevant work topics. Agree CRs addressing potential normative work for stage-2 for relevant work topics Progress CRs relevant for stage-3 Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis | Target 50% Real
SA#105 (10– 13 September 2024, Melbourne, AU) | Approve CRs addressing potential normative work for stage-2 for relevant work topics | 
SA4 MBS AHG (September/October 2024, EU, tbc) | Progress candidate solutions including call flows, protocols and APIs for each of the identified issues. Progress identifying gaps for stage-3 for relevant work topics. Progress CRs relevant for potential issues related to stage-3 Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis Post IBC which is Sep 13 – 16 2024 (start Mon 2pm - finish at Fri 2pm), e.g. Sep 17 - 20 Sep 23 – 27 Oct 6 – Oct 10 | Target 70% Real
SA4#130 (18 – 22 November 2024, Orlando, FL, US) | Complete evaluation of candidate solutions including call flows, protocols and APIs for each of the identified issues. Complete identifying gaps and recommend potential normative work for stage-3 for relevant work topics. Agree CRs addressing potential normative work for stage-3 for relevant work topics Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis | Target 90% Real
SA#106 (10 – 13 December 2024, Madrid, ES TBC) | Agree CRs addressing potential normative work for stage-3 for relevant work topics | 

## Slide 12: WT0: TS26.51x outline
Description
  The primary focus of this Work Item is the delivery of segmented media objects in the media plane, i.e. at reference points M2, M4 and M7 of the Media Delivery architecture. One of the open issues identified in the Rel-18 feasibility study 5GMS_Pro_Ph2 is the need for a specification that addresses interoperability considerations around content delivery protocol features and general technologies for segmented media streaming and the IP/PDU 5G System Layer. This points to the further study media plane issues to support additional functionalities, but also identifies what needs to be ported from legacy TS 26.512 to a generalised media plane technical specification. The relation to media session handling (as specified in TS 26.510) is identified in TR 26.804, but enhancements to media session handling are not the primary focus of this study.
Companies interested: Qualcomm, BBC
5G-MAG Interest and Involvement:
Key aspects:
  Delivery protocols for segmented media HTTP/1.1, HTTP/2, HTTP/3 together with TCP/IP, secure delivery
  Extensions to the delivery protocol that are common: HTTP headers, Query parameters, authentication
  Ingest protocols
  APIs

## Slide 13: WT1: Common Client Metadata
Description:
  While 3GPP and MPEG in DASH support DASH metrics, the reporting is not common to any player, for example all DASH players as well as HLS players. As an example, CTA WAVE has developed: CTA-5004: Web Application Video Ecosystem Common-Media-Client-Data (CMCD) with an excellent overview here: https://ottverse.com/common-media-client-data-cmcd/. It is worthwhile to study the benefits of integrating commonly supported metrics and client data reporting in 5GMS workflows. The focus is the integration of already defined metrics rather than developing new metrics. Examples of study include support of specific metric keys, player APIs, sending options from client to server (user plane, M5 reference point, EVEX), M3 reference point impact, as well as usage of the data in operations. A study of creating a common harmonized reporting framework and studying the interaction of different frameworks may be included.
Companies interested: Qualcomm, Dolby, CMCC, AT&T, Telecom Italia, Comcast, Orange, BBC, EBU, Tencent, ATEME Sony Europe B.V.
Work Topic lead: Thomas Stockhammer, Qualcomm
5G-MAG Interest and Involvement:

## Slide 14: WT1: What is CMCD?
A defined set of structured key/value pairs communicating mutually beneficial media-related information from a player to a CDN via either
  A set of custom headers
  A query arg
  A JSON object
Common because the same data structure can be used across all players and all CDNs.
Resources
  Available for free at https://tinyurl.com/cta5004spec
  DASH-IF Special Session available from Will Law
Version 2 is happening as we speak

## Slide 15: WT1: Common Client Metadata
Introduction to CMCD
  Presentation from Will Law for phase 1
  https://github.com/cta-wave/common-media-client-data/issues
  V1 is technical
  V2 is more towards QoE, player health
  MPEG-DASH adds signaling
  Opportunity to contribute by 3GPP until mid of 2024
Implementations
  Dash.js
    CMCDv1 complete
    Two methods (query, header)
    Configuration API
  Others
  All players except native HLS
Options
  DASH client is instructed through MPD elements
  DASH client is instructed through a configuration API
Integration of CMCD in MBS and MBMS
  Yes, relevant
  Options
    MBMS/MBS client reports
    Media Session Handler Reports
Background

## Slide 16: WT2: Common Server-and Network-Assisted Streaming
Description:
  MPEG-DASH supports Server and Network Assisted DASH (SAND). Certain profiles of SAND were adopted in TS 26.247, but the industry has generalized the concepts in SAND in efforts such as Content Steering (see ETSI TS 103 998), Web Application Video Ecosystem (WAVE) specification for Common Media Server Data (CMSD), or Addressable Resource Index (ARI) Tracks in MPEG. The study and integration of these technologies into the Media Delivery System and MBS/MBMS workflows is of significant interest, in particular also in combination with existing QoS mechanisms.
Companies interested: Qualcomm, Dolby, AT&T, Comcast, Tencent, ATEME, Sony Europe B.V.
Work Topic lead: Iraj Sodagar, Tencent
5G-MAG Interest and Involvement:
Overview

## Slide 17: WT2: Common Server-and Network-Assisted Streaming
Background: Published as ETSI TS 103 998 – Content Steering

## Slide 18: ARI Track - Motivation
The following aspects are observed
  In several cases there is a desire that an adaptive streaming client has exact knowledge of the duration and size of addressable resources and possible a subset of those on the server.
  Addressable Resources are Track Files, Segments or Chunks in the CMAF context, but apply equally to DASH or HLS.
  For on-demand services, an exact map of this information may be provided by the Segment Index.
Segment Index is not sufficient. Examples include:
  A solution is required for different operation modes: low-latency live, live, time-shifted, VoD
  The solution is expected to work for different target latency of the client
  The client and network address to operate in different network conditions
  The message also includes information on the content quality
See ISO/IEC 23009-1 5th Edition

## Slide 19: ARI Track in live mode
DASH Packager
CH
CIC
CNC
CNC
CIC
CNC
CNC
CNC
CIC
CNC
CNC
CNC
CIC
HTTP Chunk
HTTP Chunk
DASH Segment
Encoder
CH
CIC
CNC
CNC
CIC
CNC
CNC
CIC
CNC
CNC
CIC
CNC
CNC
ARI Track
1
2
Delay
1
2
Delay
3
Chunking
Segments
1
2
3
Time-Shift
Delay

## Slide 20: WT3: Multi-CDN and Multi-Access Media Delivery
Description:
  Content distributors often use multiple Content Delivery Networks (CDNs) to distribute their content to tend-users. As an example, they may upload a copy of their catalogue to each CDN, or more commonly have all CDNs pull the content from a common origin. In advanced deployments, technologies such as Coded Multisource Media Format (CMMF) use Application Layer FEC techniques to stripe different subsets of content across multiple CDNs. Different client implementations may then beneficially use the content on multiple CDNs, potentially guided by the service or network provider. In addition, formats and techniques for generating content for multiple CDN delivery such as MPEG-DASH Part 9 (ReAP) may be taken into account. Further extensions include the ability for a client to use multiple access networks at the same time to support media delivery. Study of integration of different technologies into the Media Delivery System is of relevance to address content provisioning, content hosting, impacts on user plane reference points M2 and M4, and on media session handling at reference point M5 as well as potential benefits in terms of quality and resource usage.
Companies interested: Qualcomm, Dolby, AT&T, Orange, Samsung Electronics Co. Ltd., Huawei Technologies Co Ltd., ATEME
Work Topic lead: Jason Cloud, Dolby
5G-MAG Interest and Involvement:

## Slide 21: WT3: Multi-CDN and Multi-Access Media Delivery
Background: ETSI TS 103 972 – early draft
SBN 0, 10 symbols
0
3
6
9
1
4
7
2
5
8
10
11
13
14
17
16
19
20
23
26
29
22
25
28
23 FEC symbols
12
15
18
21
24
27
0
1
2
3
10
11
12
13
14
15
16
4
5
6
7
8
9
17
18
19
20
21
22
23
24
25
26
27
28
29
Object

## Slide 22: WT3: ATSSS
S4-240808 | [FS_AMD] Discussion on 5GMS Aspects for Multi Access | Samsung R&D Institute India
Initial discussions at SA4#127-bis-e
Optional feature ATSSS (Access Traffic Steering, Switching, Splitting) in the 5G System in clause 5.32 of TS 23.501
TS 23.501 supports three different steering functionalities (MPTCP, MPQUIC, ATSSS-LL). There exists literature on pros and cons of some of these steering functionalities for video streaming.
References
  Cyriac J,. Emir H., Mea W., Rittwik J., Shankarnarayanan, “Is Multipath TCP (MPTCP) Beneficial for Video Streaming over DASH?, IEEE Symposium on Modeling, Analysis, and Simulation of Computer and Telecommunication Systems, 2016
  Jia z., Jiangchuan L., Cong Z., Yong C., Yong J., Wei G., “MPTCP+: Enhancing Adaptive HTTP Video Streaming over Multipath”, IEEE/ACM 28th Symposium on Quality of Service (IWQoS), 2020
  Samira A., Vanessa T., Christian E.R., Prakash K., Imed B., “A Holistic Survey of Multipath Wireless Video Streaming”, Journal of Network and Computer Applications, March 2023
  Hongjia W., Simone F., Giusepe C., Ozgu A., Anna B., “A Survey on Multipath Transport Protocols Towards 5G Access Traffic Steering, Switching, and Splitting”, IEEE Access, 2021
  Przylucki S., Czerwinski D., “The simulation study on the multipath adaptive video transmission”, International conference of Computational Methods in Engineering Science, 2019

## Slide 23: WT4: Modem Usage Optimized Media Streaming
Description:
  In Rel-18, basic support for Background Data Transfer is added. UE power resources are constrained, and media delivery typically also results in power consumption if the radio is always connected. In order to better support streaming services, requests and access to the modem and the resources should be well balanced. Enhancements to Background Data Transfer to support preload as well as functionality of what is defined in W3C Managed Media Source Extension to minimize active network connections are relevant topics to study with the aim of limiting battery consumption in the UE resulting from media delivery.
Companies interested: Qualcomm, Dolby, Comcast, BBC, EBU, Tencent
Work Topic lead: Iraj Sodagar, Tencent
5G-MAG Interest and Involvement:
Core Issues
  Basic support for Background Data Traffic in Rel-18

## Slide 24: WT4: Modem Usage Optimized Media Streaming
Please see the presentation from WWDC 2023 and MSE GitHub issue.
Discussion in W3C
  https://www.w3.org/2023/07/25-me-minutes.html
    … Tests showed that power usage would go up with MSE, so viewing time would reduce. We can never introduce a regression on iPhone
    … We were given constraints: if we play a YouTube video on iPhone with MSE enabled, we shouldn't see a power regression
    … We tried various ways, and what we found was the primary reason why the power is used, is websites get one segment at a time rather than downloading in bursts
    … The main power usage is when the cellular modem is on. So we looked at how HLS downloads data, it downloads quite a big chunk, then stops
    … 5G is more power hungry than 4G or 3G, it will download more seconds then shut down
    … Apple still wanted to have control, but provide hints. We didn't enable MSE on iPhone, as we'd have those issues
    … MMS provides hints: "start fetching content", "i have enough", "stop fetching content"
    … We wanted to enable on 5G, do we need a carrot and stick approach? If the website does the wrong thing, and finds a way around it, shut it off completely, and don't enable MSE and fallback to HLS
  https://github.com/w3c/media-source/
  https://www.w3.org/TR/media-source-2/#managedmediasource-interface
Support in dash.js
  https://github.com/Dash-Industry-Forum/dash.js/issues/4202
Background Managed Media Source

## Slide 25: WT5: DRM and Conditional Access
Description:
  DRM and Conditional Access are commonly used by third-party streaming services. However, in case streaming is done through MBS or MBMS, a more careful management of the keys needs to be checked. Scalability of key delivery is an issue. The support for -encrypted content in Unicast/Multicast and Broadcast is relevant. Integration of Content Protection interfaces in the provisioning, for example using CPIX back-end interfaces is of high relevance for the industry and should accordingly be studied. The impacts of these on media plane (reference points M2 and M4) as well as the media session handling APIs (reference points M3, M5) should also be studied.
Companies interested: Qualcomm, Telecom Italia, Comcast, Rohde&Schwarz, Huawei Technologies Co Ltd.
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 26: WT5: DRM and Conditional Access
Map Content Protection functions to functions in the 5G Media Streaming System
Document call flows on the back-end as well as towards the clients
Document the call flows for unicast/MBS/MBMS
Identify gaps and optimization potentials for scaling service
Background

## Slide 27: WT6: In-session Unicast Repair for MBS Object Distribution
Description:
  For live and low-latency live services using the Object Distribution Method in MBS, in certain cases the transmission of an object is not successful. In this case, unicast repair for individual MBS Clients can improve the service quality. However, the timing of such requests needs to be carefully studied in order to avoid network overloads or significant latencies in the delivery. A study to extend MBS User Services and object streaming to address in-session repair is of relevance.
Companies interested: Qualcomm, Telecom Italia, Comcast, Orange, BBC, SWR, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 28: WT6: In-session Unicast Repair for MBS Object Distribution
1. The MBS Client identifies the end of the MBS Distribution Session. The latest time for this is the value of the @Expires attribute indicated in the root element of the FDT Instance document. However, according to clause 9.3.2 of TS 26.346 [7], an MBS Client may determine an earlier end of transmission of files,
2. The MBS Client identifies that data is missing from an MBS Object Distribution Session for one or multiple FLUTE transmission objects delivered in the Object Distribution Session following the principles in clause 9.3.3 of TS 26.346 [7].
3. The MBS Client shall select an MBS AS instance repair URL randomly from the list of object‌Repair‌Base‌Locators if present in the ObjectRepair object defined in table 5.2.8-1.
4. For each incomplete FLUTE transmission object defined by a File element in the FDT Instance document and as identified in step 2:
a) The MBS Client shall form the network location location (URL) of the repair object as defined in clause 6.4.2.4 using (i) the value of the File@Content-Location attribute, (ii) the repair URL selected in step 3 (if any) and (iii) the value of object‌Distribution‌Base‌Locator as distribution URL if present in the ObjectRepair object defined in table 5.2.8-1.
b) The MBS Client shall define an appropriate list of byte ranges Range[M] with M the number of independent ranges and Range[m].start the start of the mth range and Range[m].end the end of the mth range from the repair object using the list of received symbols and additional information from the FDT as defined in clause 6.4.2.5.
5. The MBS Client shall then use the object repair procedures as defined as defined in clause 10.2.2 using the following parameters:
- The offsetTime and randomTimePeriod parameters indicated in the ObjectRepair object as defined in table 5.2.8-1.
- For each incomplete FLUTE transmission object in the FDT Instance document, the MBSTF Client shall use from the corresponding FDT File entry the network location location formed in step 4a, the size of the transmission object (in bytes), the entity tag value and the minimal list of byte ranges Range[M] determined in step 4b.
6. The MBS Client uses the received list of byte ranges and the received data in the MBS Object Distribution Session to recover the missing object as defined in clause 6.4.2.6.
Background Post-Session Repair  Need to do this in-session

## Slide 29: WT7: MBS User Service and Delivery Protocols for eMBMS
Description:
  The MBS User Service architecture and protocol follows the modern design philosophies of the 5G System with separation of user services from transport, a service-based architecture and RESTful APIs. At the same time, eMBMS and enTV as used for LTE-based 5G Broadcast support a transparent delivery mode. While interworking in between MBMS and MBS is addressed in TS 23.247, interworking between these two systems at the User Service level is not addressed. In order for MBMS and LTE-based 5G broadcast to leverage MBS User Service technologies, a study is warranted to identify the gaps to fully support this functionality.
Companies interested: : Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 30: WT7: MBS User Service and Delivery Protocols for eMBMS
Open Questions
  Extensions to MBS User Service to support interworking
  Operation of MBS delivery protocols on top of MBMS an 5G Broadcast
  Extension of MBS User service protocols to address common issues and having a common delivery protocol specification for multicast and broadcast.
  Specific needs from 5G Broadcast?
Background – Interworking of MBS and MBMS in TS 23.247, clause 5.2

## Slide 31: WT8: Selected MBMS Functionalities not supported in MBS
Description:
  In completing TS 26.502 and TS 26.517, it is obvious that only a subset of the MBMS functionalities is supported in Rel-17. While many MBMS functionalities are likely not important to be supported for MBS, a systematic analysis of MBMS User Services features and their potential relevance for MBS should be completed and recommendations made on which ones to migrate to MBS User Services specifications and how best to achieve this.
Companies interested: : Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 32: WT9: DASH/HLS Interoperability
Description:
  DASH/HLS interoperability is a key issue to support highly scalable distribution systems for CDN-based distribution as well as for MBS/MBMS distribution. Offering common CMAF segments that can be consumed by both DASH and HLS media players promises to address these issues. However, detailed nuances need to be identified to ensure optimized delivery and CTA WAVE has provided detailed guidelines in CTA-5005-A to support this matter. Studying these guidelines and understanding the impacts on the 5GMS System as well as MBS/MBMS distribution is of relevance. In addition, formats and techniques supporting DASH/HLS interoperability such as MPEG-DASH part 9 (ReAP) may be taken into account.
Companies interested: Qualcomm, Telecom Italia, Comcast, Orange, BBC, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., Tencent
Work Topic lead: Iraj Sodagar
5G-MAG Interest and Involvement:

## Slide 33: WT9: DASH/HLS Interoperability
Background

## Slide 34: WT10: Further harmonization of RTC and Streaming for Advanced Media Delivery
Description:
  With the creation of TS 26.510 in Rel-18, Media delivery across the 5G Media Streaming (5GMS) System and the Real-time media Communication (RTC) System was harmonized. However, not all functionalities from TS 26.512 are yet commonly available for RTC as well. Study of further harmonization is encouraged to fully implement common Media Delivery functions.
Companies interested: Qualcomm, CMCC, Comcast, Samsung Electronics Co. Ltd., NTT, InterDigital Communications, Lenovo
Work Topic lead: Open
5G-MAG Interest and Involvement:

## Slide 35: WT11: Issues identified by Market Representation Partners
Description:
  Through the development in 5G-MAG of reference implementations for MBMS, 5GMS and MBS, 5G-MAG is identifying specific problems which are collected in https://github.com/5G-MAG/Standards/issues. While some of the issues are purely related to bug fixes, some of the issues may require study by SA4 and the development of new functionalities in the relevant technical specifications. It is vital to support the industry and MRPs in deploying 3GPP technologies.
Companies interested: Qualcomm, Comcast, BBC, Dolby, EBU
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:
  Low-Latency Protocols for Multicast and Broadcast
in particular 5G-MAG:

## Slide 36: WT12: Improved QoS support
Description:
  In Rel-18, SA2 has defined a number of new features in the 5G System, especially in the PCF, from which media delivery may benefit. Examples documented in TS 23.501 include the use of Explicit Congestion Notification (ECN) to support Low Latency, Low Loss, Scalable Throughput (L4S) services (clause 5.37.3), PDU Set handling (clause 5.37.5) and QoS Monitoring (clause 5.45), and there are likely others. The impact and usefulness of selected features is preferably studied. The functions identified in this context may be studied in one or more of the above work topics.
Companies interested: Ericsson LM, Huawei Technologies Co Ltd., Qualcomm, BBC, InterDigital Communications, Lenovo
Work Topic lead: open
5G-MAG Interest and Involvement:

## Slide 37: WT13: Impacts and opportunities of QUIC for segmented content delivery
Description:
  Since the finalisation of the QUIC protocol by the IETF in May 2021, there has been significant deployments of QUIC driven by the usage of HTTP/3 for streaming services. In the IETF, the working group on Media Over QUIC (MOQ) is working towards an extensible protocol for publishing media for ingest and distribution. While QUIC is mostly used today as the underlying protocol of HTTP/3, there is still open questions as to how media segments are delivered over QUIC streams when using HTTP/3 but also considering other QUIC-based protocols such as MOQ. Considering different types of media application, e.g. multi-stream use cases, will be of interest. Studying the various strategies for delivering segmented content over QUIC streams will also bring insights for the network management aspects. For instance, findings in this domain may be relevant to WT#2.1 in the ongoing study in SA2 called FS_XRM_Ph2 (SP-231671) whose deliverable is available as TR 23.700-70.
Companies interested: Xiaomi, Qualcomm, others
Work Topic lead: Emmanouil Potetsianakis, Xiaomi
5G-MAG Interest and Involvement:

## Slide 38: Summary
tbd