## Slide 1: Functional requirements for WebRTC signalling
S4aR220035
NTT

## Slide 2: Summary
This document proposes the possible signalling methods and their functional requirements. Minimal set of signalling methods and functionalities are covered in iRTCW and advanced ones are in the scope of FS_eiRTCW. All methods are based on JSON format messages, which is extensible and can be supported wide range of web-based technologies.
Connection model and assumptions are based on Collaboration Scenario 4, which is covering the features of Collaboration Scenario 3.
Discussion points are:
The recognition and confirmation of whether is the minimal signalling for iRTCW.
Regarding connection model and assumptions, is it acceptable? Or what do you think is the element to be added?
According to the discussion and the slides after p3, FS_eiRTCW’s PD should be updated.

## Slide 3: Overview
Following is the list of signalling methods and shows:
Whether it is available in minimal or advanced signalling
Which functional block provides
Where the signal is used
Signalling Method Name | iRTCW/FS_eiRTCW | Provided by WSF/WEBF | Area of use Intra/Inter-operator
Registration | FS_eiRTCW | WSF | Intra-operator
Session Setup | iRTCW and FS_eiRTCW | WSF | Intra- or Inter-operator
Session Disconnection | iRTCW and FS_eiRTCW | WSF | Intra- or Inter-operator
Session Modification | FS_eiRTCW | WSF | Intra- or Inter-operator
Session Notification | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
Conference Setup | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
Conference Modification | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
Network Information Notification | FS_eiRTCW | WSF | Intra-operator
Endpoint Information Notification | FS_eiRTCW | WSF | Intra-operator
User Information Configuration | FS_eiRTCW | WSF or WEBF | Intra-operator
User Information Acquisition | FS_eiRTCW | WSF or WEBF | Intra-operator
Message Notification | FS_eiRTCW | WSF | Intra- or Inter-operator

## Slide 4: Assumptions (1/2)
The proposed methods are based on the following assumptions:
The multiple operator model (i.e., Collaboration Scenario #4) is assumed to see the complete picture first. The single operator model can easily be derived later.
One of the operators is responsible for an immersive RTC service as the host operator. The other collaborative operators, as guest operators, simply provide the connectivity to the primary operator.
A UE which subscribes to the host operator can set up a VR conference room as an immersive RTC service. The UE can invite other UEs for the VR room.
Other UEs in the host operator can join the service.
Other UEs in the guest operators can join the service, too.
All operators are assumed to have its own connection controller (i.e., WebRTC Signalling Server) for QoS-guaranteed and secure connectivity for their own customers (i.e., UEs).
All UEs are assumed to be under the control of the WebRTC Signalling Server of their own operators. UEs should register themselves to their own WebRTC Signalling Server. The first hop of the UE’s C-plane signalling is the WebRTC Signalling Server.

## Slide 5: Assumptions (2/2)
The figure below depicts the model assumption described in the previous slide.

## Slide 6: Signalling Methods - Registration
This method is available in FS_eiRTCW.
By the method:
Bi-directional communication channel (e.g., WebSocket) is opened between a WebRTC Endpoint and a WebRTC Signalling Server, the WebRTC Endpoint can send requests to and receive responses from the WebRTC Signalling Server associated with a specific ID.
Optionally, multiple WebRTC Endpoints can use a shared specific ID and concurrently work with it.
While the WebSocket connection is active, the WebRTC Endpoint is regarded as online. After a certain period of time since the connection is closed, the WebRTC Endpoint is regarded as offline. If the WebRTC Endpoint successfully re-connects before the certain period of time, it remains online.

## Slide 7: Signalling Methods – Session Setup
This method is available in iRTCW and FS_eiRTCW.
With the enhancement of FS_eiRTCW, there are additional features to the method.
By the method:
A WebRTC Endpoint connects to immersive RTC conference or one by one communication.
Media information (i.e., Codec, IP address, Port number, ICE candidates) are exchanged using SDP.
With the enhancement of FS_eiRTCW, a WebRTC Endpoint can connect to an immersive RTC session with generating it at the same time.
With the enhancement of FS_eiRTCW, a WebRTC Endpoint can call other WebRTC Endpoints to the generated immersive RTC session.

## Slide 8: Signalling Methods – Session Disconnection
This method is available in iRTCW and FS_eiRTCW.
With the enhancement of FS_eiRTCW, there are additional features to the method.
By the method:
A WebRTC Endpoint disconnects from the session which the WebRTC Endpoint is joining.
With the enhancement of FS_eiRTCW, the WebRTC Endpoint can disconnect and close the session at the same time.

## Slide 9: Signalling Methods – Session Modification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint changes, adds or removes the media information of the connected immersive RTC session (i.e., Codec, IP address, Port number, ICE candidates) using SDP.

## Slide 10: Signalling Methods – Session Notification
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
Immersive RTC conference related information (i.e., Date, Duration, Title, Participants) or the list of immersive RTC conferences are provided.
The information of the state of the immersive RTC conference (i.e., Ongoing/Closed, Start time, Attendees) is also provided.

## Slide 11: Signalling Methods – Conference Setup
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A new immersive RTC conference is created, assigning related information (i.e., Date, Duration, Title, Participants).

## Slide 12: Signalling Methods – Conference Modification
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A WebRTC Endpoint modifies the information of an immersive RTC conference (i.e., Date, Duration, Title, Participants).

## Slide 13: Signalling Methods – Network Information Notification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint gets the list of available WebRTC Signalling Servers and ICE-related information (e.g., the list of TURN server)
A WebRTC Endpoint gets the information of the service entity (e.g., an instance in Media Function) providing an immersive RTC service. The information includes the list of available service entities, their media information, and their names.

## Slide 14: Signalling Methods – Endpoint Information Notification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint notifies the WebRTC Signalling Server of the media supported by the WebRTC Endpoint.
A WebRTC Endpoint notifies the WebRTC Signalling Server of the preference of media and service (e.g., incoming call rejection).
A WebRTC Endpoint notifies the WebRTC Signalling Server of the state of its user (e.g., active/inactive).

## Slide 15: Signalling Methods – User Information Configuration
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A user configures his or her own user profile (i.e., Name, Profile picture, Status).
A user changes the scope of disclosure of his or her own user profile.
Optionally, when supported, contact list is modified.

## Slide 16: Signalling Methods – User Information Acquisition
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A user gets his or her own user profile.
A user gets other’s user profile if permitted.

## Slide 17: Signalling Methods – Message Notification
This method is available in FS_eiRTCW.
By the method:
A user sends an instant message for their absence.