## Slide 1: Functional requirements for WebRTC signalling
S4aR220040
NTT

## Slide 2: Summary
This document proposes possible signalling methods and their functional requirements.
The minimal set of the methods and requirements should be covered in iRTCW and advanced ones should be in FS_eiRTCW.
All of the methods should be coded in a JSON format, which is extensible and can be supported by a wide range of web-based technologies.
Connection model and assumptions are based on Collaboration Scenario 4, which covers the features of Collaboration Scenario 3.
Discussion points are:
The minimal signalling methods to be specified in iRTCW (as Version 1).
The methods to be investigated in FS_eiRTCW (targeting at Version 2).
According to the discussion and the slides after p3, iRTCW and FS_eiRTCW’s PD should be updated.

## Slide 3: Overview
Following is the list of signalling methods and shows:
Whether it is available in minimal or advanced signalling
Which functional block provides
Where the signal is used
Signalling Method Name | iRTCW/FS_eiRTCW | Provided by WSF/WEBF | Area of use Intra/Inter-operator
1. Registration | FS_eiRTCW | WSF | Intra-operator
2. Session Setup | iRTCW and FS_eiRTCW | WSF | Intra- or Inter-operator
3. Session Disconnection | iRTCW and FS_eiRTCW | WSF | Intra- or Inter-operator
4. Session Modification | FS_eiRTCW | WSF | Intra- or Inter-operator
5. Conference Notification | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
6. Conference Setup | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
7. Conference Modification | FS_eiRTCW | WSF or WEBF | Intra- or Inter-operator
8. Network Information Notification | FS_eiRTCW | WSF | Intra-operator
9. Endpoint Information Notification | FS_eiRTCW | WSF | Intra-operator
10. User Information Configuration | FS_eiRTCW | WSF or WEBF | Intra-operator
11. User Information Acquisition | FS_eiRTCW | WSF or WEBF | Intra-operator
12. Message Notification | FS_eiRTCW | WSF | Intra- or Inter-operator
Minimal set 1
Minimal set 2
Minimal set 3

## Slide 4: Assumptions (1/2)
The proposed methods are based on the following assumptions:
The multiple operator model (i.e., Collaboration Scenario #4) is assumed to see the complete picture first. The single operator model can easily be derived later.
One of the operators is responsible for an immersive RTC service as the host operator. The other collaborative operators, as guest operators, simply provide the connectivity to the host-side operator.
A UE which subscribes to the host operator can set up a VR conference room as an immersive RTC service. The UE can invite other UEs for the VR room.
Other UEs in the host operator can join the service.
Other UEs in the guest operators can join the service, too.
All operators are assumed to have its own connection controller (i.e., WebRTC Signalling Server) for QoS-guaranteed and secure connectivity for their own customers (i.e., UEs).
All UEs are assumed to be under the control of the WebRTC Signalling Server of their own operators. UEs should register themselves to their own WebRTC Signalling Server. The first hop of the UE’s C-plane signalling is the WebRTC Signalling Server.

## Slide 5: Assumptions (2/2)
The figure below depicts the model assumption described in the previous slide.
This figure is based on CS#4 which is comprised of multiple operators (3 operators).
Simpler CS#3, which is comprised of a single operator, can be derived (only lefthand-side).

## Slide 6: Signalling Methods - Registration
This method is available in FS_eiRTCW.
By the method:
A bi-directional communication channel (e.g., WebSocket connection) is opened between a WebRTC Endpoint and a WebRTC Signalling Server. Once the channel is open, the WebRTC Endpoint can send requests to and receive responses from the WebRTC Signalling Server.
Or,
Once the channel is open, the endpoint and server can exchange requests and responses between each other.
A WebRTC Endpoint is identified uniquely by a specific ID (such as a phone number).
Optionally, multiple WebRTC Endpoints can share a specific ID. (Two smartphones can share a single phone number)
While the WebSocket connection is open, The WebRTC Signalling Server regards the WebRTC Endpoint as online.
The connection may be closed by some reason. Even after the connection closure, the WebRTC Endpoint is still regarded as online by the server for a certain period of time. If the WebRTC Endpoint successfully re-connects before the certain period of time, it remains online.

## Slide 7: Signalling Methods – Session Setup
This method is available in iRTCW and FS_eiRTCW.
With the enhancement of FS_eiRTCW, there are additional features to the method.
By the method:
A WebRTC Endpoint connects to an immersive RTC conference or another endpoint.
Media information (i.e., Codec, IP address, Port number, ICE candidates) is exchanged using SDP.
Matching function with ID, name, or matching criteria? (Except for callout P2P connection, this feature should not be mandatory when using an intermediate server.)
With the enhancement of FS_eiRTCW, a WebRTC Endpoint can connect to an immersive RTC conference server and create a conference over the server at the same time.
With the enhancement of FS_eiRTCW, a WebRTC Endpoint can call another WebRTC Endpoint and invite it to a conference.

## Slide 8: Signalling Methods – Session Disconnection
This method is available in iRTCW and FS_eiRTCW.
With the enhancement of FS_eiRTCW, there are additional features to the method.
By the method:
A WebRTC Endpoint disconnects the established session with the conference.
With the enhancement of FS_eiRTCW, the WebRTC Endpoint can close the conference and disconnect the session at the same time.

## Slide 9: Signalling Methods – Session Modification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint changes, adds, or removes the media and its attributes (e.g., Codec, IP address, Port number, ICE candidates) of the connected immersive RTC session by using SDP.

## Slide 10: Signalling Methods – Conference Notification
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
Information about an immersive RTC conference (e.g., starting date, open duration, title, participants) or the list of the scheduled immersive RTC conferences is provided.
Information about the state of the immersive RTC conference (e.g., ongoing or closed, start time, the current attendees) is also provided.

## Slide 11: Signalling Methods – Conference Setup
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A new immersive RTC conference is created, assigning related information (i.e., Date, Duration, Title, Participants).

## Slide 12: Signalling Methods – Conference Modification
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A WebRTC Endpoint modifies the setting of an immersive RTC conference (i.e., Date, Duration, Title, Participants).

## Slide 13: Signalling Methods – Network Information Notification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint gets the list of available WebRTC Signalling Servers and ICE-related information (e.g., the list of TURN servers)
A WebRTC Endpoint gets the information about the service entity (e.g., an instance in the Media Function) that provides an immersive RTC service. The information includes the list of available service entities, their media information, and their names.

## Slide 14: Signalling Methods – Endpoint Information Notification
This method is available in FS_eiRTCW.
By the method:
A WebRTC Endpoint notifies the WebRTC Signalling Server of the media supported by the WebRTC Endpoint.
A WebRTC Endpoint notifies the WebRTC Signalling Server of the preference of media and service (e.g., incoming call rejection).
A WebRTC Endpoint notifies the WebRTC Signalling Server of the state of its user (e.g., active/inactive).

## Slide 15: Signalling Methods – User Information Configuration
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A user configures his or her own user profile (i.e., Name, Profile picture, Status).
A user changes the scope of disclosure of his or her own user profile.
Optionally, when supported, contact list is modified.

## Slide 16: Signalling Methods – User Information Acquisition
This method is available in FS_eiRTCW.
This method can be provided by Web interface.
By the method:
A user gets his or her own user profile.
A user gets other’s user profile if permitted.

## Slide 17: Signalling Methods – Message Notification
This method is available in FS_eiRTCW.
By the method:
A user sends an instant message for their absence.