## Slide 1
Huawei’s view on SA4 R19 plan
S4aR230158
3GPP SA4-e (AH) RTC SWG post 126
Online, 10th Jan 2024

## Slide 2
RTC area
FS_eiRTCW: R18 has defined the general architecture and signaling/media protocol of WebRTC real-time communication. However, the following issues are still not covered or fully discussed:
The scenarios for introducing such new architecture are not clear
The call flows are missing
The impact on current operator’s network, e.g. the relation with the IMS architecture (including interworking details)
The impact on the terminal side.
We suggest getting more groups (at least SA1/SA2 and GSMA) involved in the discussion, to make sure this new architecture are fully understood by all relevant stakeholders so as to be really usable in the future.
IBACS: Finish the call flow definition in R18. Start to define the details for split rendering operation in R19.
Other aspects：
1) DC protocol stack evolution: Currently DC is over SCTP, which has some problems like link setup delay (4RTT) and imperfect unreliable transmission mechanism (depending on the reliability of the FORWARD TSN). This may not meet the future requirements for various XR/AI data transmission. Evolution to QUIC may be considered.
2) SDP negotiation mechanism simplification: Currently, the signaling and media processing of SIP-based SDP negotiation are severely coupled. All signaling-plane NEs are involved in the SDP negotiation process, and need to be aware of the negotiation status at all time. The re-negotiation process and the media connection delay is very long. A new simplified SDP negotiation mechanism should be considered.

## Slide 3: Video area
FS_AI4Media: For R19, it’s suggested to divided the work into two parts：
  High priority (start the normative work in the near future):
  AI model distribution, metadata transmission protocol and data format definition
  Network AI inference architecture for both 5GMS and RTC (in collaboration with SA2)
  KPI definition
  Low priority (requires further research and test verification):
  Split AI inference (AI model split, model compression, and intermediate data compression): how to split AI models for the best effect, compatibility between different inference platforms after split, and problems caused by a large amount of intermediate data transmission.
  Distributed/Federated learning (lack of contribution).
FS_AVATAR: Finish the R18 study, and start normative work in R19
  architecture definition and mapping to WebRTC/IMS (in collaboration with SA2)
  different types of animation technologies (voice, video, text, etc.) and models (2D/3D) considering resource consumption, efficiency and algorithm compatibility