## Slide 1: Graphics Split Rendering In SA4
Source: Nokia
Agenda Item: 4.5
Document for: Discussion
3GPP SA4 RTC SWG Telco Post #130
Online, 15 January 2025

## Slide 2: Real Time Rendering
CPU and GPU operations for XR applications (TR 26.928)
Application
Application Logic
Scene Graph
Objects
Meshes
Textures..
Geometry
Transformations
Lighting
Projection
Clipping
Window-to-Viewport Transformation
Rasterization
Fragment/pixel shading
Screen
Post Processing
Fragment/pixel Shading
Elements necessary for mesh representations (TS 26.928) ©Wikipedia (Mesh_overview.jpg: The original uploader was Rchoetzlein at English Wikipedia.derivative work: Lobsterbake [CC BY-SA 3.0 (https://creativecommons.org/licenses/by-sa/3.0)])
Concept of Split Rendering

## Slide 3
CPU and GPU operations for XR applications (TS 26.928)
Application
Application Logic
Scene Graph
Objects
Meshes
Textures..
Geometry
Transformations
Lighting
Projection, etc...
Rasterization
Fragment/pixel shading
Screen
Post Processing
Anti-Aliasing, etc...
Elements necessary for mesh representations (TS 26.928) ©Wikipedia (Mesh_overview.jpg: The original uploader was Rchoetzlein at English Wikipedia.derivative work: Lobsterbake [CC BY-SA 3.0 (https://creativecommons.org/licenses/by-sa/3.0)])
Input
Display
Compute and energy resource Intensive
Storage intensive
Background: Real Time Rendering

## Slide 4
Application
Application Logic
Scene Graph
Objects
Meshes
Textures..
Geometry
Transformations
Lighting
Projection
Clipping
Window-to-Viewport Transformation
Rasterization
Fragment/pixel shading
Screen
Post Processing
Fragment/pixel Shading
Input
Display
Off-load some of these operations to a powerful server
Background: Split Rendering
Split Rendering Server
Split Rendering Client

## Slide 5
Architectures
RTC  SR_MSE: TS 26.565
IMS  (AR calls) IBACS : TS 26.264, SR_IMS: draft TS 26.567
Step | RTC | IMS
A. Set up Split rendering session | Simple Web Application Protocol (SWAP) and WebRTC data channel | SIP and IMS data channel
B.1 Pose/user input (& other metadata) to SRS | WebRTC data channel (Metadata DC) | IMS data channel metadata aDC
B.2 SRS: Render and encode | RTC AS | MF [DC AS]
B.3 Send encoded media to SRC | RTP | RTP
B.4&5 Decode, process and display | UE | DCMTSI client
Note that SWAP operates over user plane interface RTC-4s
Split Rendering in current SA4 Specs
Studied by SA4 e.g., in TS 26.928, TS 26.998 and TS 26.806

## Slide 6
RTC Split management architecture (source TS 26.565 Figure 5.1.3-1)
Split Rendering in current SA4 Specs
RTC based architecture

## Slide 7
Split Rendering in current SA4 Specs
IMS DC based architecture

## Slide 8
Metadata
Metadata message format for metadata DC defined in TS 26.565 and adopted in draft TS 26.567
Pose and action message payload in JSON format defined in TS 26.119 and adopted in both TS 26.565 and draft TS 26.567
Name | Type | Cardinality | Description
poseInfo | Object | 1..n | An array of pose information objects, each corresponding to a target display time and XR space.
poseTime | number | 1..1 | The time for which the current poses are predicted. This time is expressed in XR system time clock.
xrSpaceId | number | 0..1 | An identifier for the XR space in which the poses are expressed.
poses | Object | 1..n | An array that provides a list of the poses. For view poses, the first pose corresponds to the left view and the second to the right view.
trackableSpaceId | number | 0..1 | A unique identifier of the XR space of the trackable that was agreed upon during session setup. The pose corresponds to the origin of that trackableSpaceId expressed in the XR space identified by xrSpaceId. This is only applicable for trackable pose.
orientation | Object | 1..1 | Represents the orientation of the pose as a quaternion based on the reference XR space identified by xrSpaceId.
x | number | 1..1 | Provides the x coordinate of the quaternion.
y | number | 1..1 | Provides the y coordinate of the quaternion.
z | number | 1..1 | Provides the z coordinate of the quaternion.
w | number | 1..1 | Provides the w coordinate of the quaternion.
position | Object | 0..1 | Represents the position of the pose relative to the XR space identified by xrSpaceId.
x | number | 1..1 | Provides the x coordinate of the position vector.
y | number | 1..1 | Provides the y coordinate of the position vector.
z | number | 1..1 | Provides the z coordinate of the position vector.
confidence | number | 0..1 | Provides a confidence score that reflects the probability for this pose prediction to be correct. For the current pose or a pose in the past, the confidence value would be 1. The confidence can take a value between 0 and 1.
estimatedAtTime | number | 0..1 | The wall clock time when the pose estimation was made. (ref. T1)
fov | Object | 0..1 | Indicates the four sides of the field of view used for the projection of the corresponding XR view. This field is only present if these field of view values have changed from the last sent values. This is only applicable for view poses
angleLeft | number | 1..1 | The angle in radians of the left side of the field of view. For a symmetric field of view this value is negative.
angleRight | number | 1..1 | The angle in radians of the right side of the field of view.
angleUp | number | 1..1 | The angle in radians of the top part of the field of view.
angleDown | number | 1..1 | The angle in radians of the bottom part of the field of view. For a symmetric field of view this value is negative.
Split Rendering in current SA4 Specs