## Slide 1
SEAL-enabled Generic Data
Collection and Reporting Architecture

## Slide 2
What is SEAL?
Service Enabler Application Layer (for vertical applications) – device and network side service platform defined by SA6, with associated APIs defined by CT1 and CT3
  TS 23.434 specifies SEAL functional architecture and the procedures, information flows and high-level APIs for a set of services within SEAL in support of vertical applications over 3GPP systems
  The following services are currently supported by SEAL for vertical application layer:
    Group Management, Location Management, Configuration Management, Identity Management, Key Management, Network Resource Management and Network Slice Capability Management
    Protocols for these services specified in TS 24.544, TS 24.545, TS 25.546, TS 24.547, TS 33.434, TS 25.548 and TS 24.549, respectively

## Slide 3
SEAL Functional Model
Generic on-network functional model (from TS 23.434):
SEAL = Service Enabler Application Layer
VAL = Vertical Application Layer

## Slide 4
Why Consider SEAL for Data Collection and Reporting?
Avoids need for multiple instances of domain-specific data measurement and reporting clients in the UE and corresponding instances of domain-specific data configuration and collection servers in the network, along with more efficient use of downlink and uplink capacity for data collection configuration and reporting functionality, by utilizing a common data collection and reporting service
  Service comprises a client function (DCR-SC) in the UE and a server function (DCR-SS) in the network
  DCR-SC is shared by all UE applications (a.k.a. VAL clients) required to perform data collection and reporting
  DCR-SS is shared by all server applications (a.k.a. VAL servers) wishing to configure data collection and reporting by UE applications and consume the corresponding reports
DCR-SC and DCR-SS act respectively, as domain-agnostic Data Collection Client in the UE and Data Collection AF in the network
TS 23.434 specifies SEAL functional architecture and the procedures, information flows and high-level APIs for a set of services within SEAL in support of vertical applications

## Slide 5
Generic Data Collection and Reporting Architecture
Currently contemplated reference architecture in EVEX:

## Slide 6
Generic DC&R Architecture with SEAL Support – Option A
UE Application
NWDAF
UE
NRF
Data
Collection AF
N33
UE Application
UE Application
(domain-specific)
UE Application
R8
Data Collection
Client
R7
Data Collection
Client
(domain-specific)
Data Collection
Client
SEAL-C
(Common, domain-agnostic)
DC&R
Service client
SEAL-UU
(Common, domain-agnostic)
DC&R
Service server
SEAL-S
Data
Collection AF
(domain-specific)
Data Collection AF
R5
NEF
VAL clients
SEAL client
SEAL server
VAL servers
Examples of domains:
Media Streaming
Group Communications
IMS Multimedia Telephony
XR Gaming
Application Service
Providers
AF
AS
AF
AS
Provisioning
AF
Indirect
DC-Client
Event Consumer AF
AS
R1
R3
R6
R4

## Slide 7
Generic DC&R Architecture with SEAL Support – Option B
UE Application
NWDAF
UE
NRF
UE Application
UE Application
(domain-specific)
UE Applications
R8
SEAL-C
(Common, domain-agnostic)
DC&R
Service client
SEAL-UU
R5
N33
NEF
VAL clients
“SEAL client”
VAL servers
UE
(Common, domain-agnostic)
DC&R
Service server
Application Service
Providers
AF
AS
AF
AS
Provisioning
AF
Indirect
DC-Client
Event Consumer AF
AS
SEAL-S

## Slide 8
Potential Issues with use of SEAL for EVEX (1 of 2)
Main focus of EVEX: enable event exposure of application-related data in media streaming sessions to external service consumers based on the 5GMS architecture
(Direct) Data Collection Client and Data Collection AF already support common functions from 5GMS perspective
  DC-Client Media Session Handler, and DC-AF 5GMS AF
  Both perform multiple tasks re. media streaming services
    Media Session Handler functions:
      Service Access information discovery, session establishment and management, dynamic policy invocation, consumption and QoE metrics reporting, request for network assistance
    5GMS AF functions:
      Supports ASP provisioning of DL/UL sessions, content preparation and content hosting configurations, dynamic policy procedures, and data collection and reporting configuration
      Supports Media Session Handler acquisition of Service Access information and related configurations for dynamic policy invocation, consumption reporting, QoE metrics collection and reporting; reception of consumption and metrics reports from UE; handling of network assistance requests from UE

## Slide 9
Potential Issues with use of SEAL for EVEX (2 of 2)
Adoption of SEAL Option A from 5GMS standpoint
  Would require Media Session Handler and 5GMS AF to support SEAL-C and SEAL-S APIs, respectively, while abandoning use of M5 API
  UE must additionally implement DC&R Service client (“SEAL client”)
  Operator must additionally implement DC&R Service server (“SEAL server”)
Adoption of SEAL Option B from 5GMS standpoint
  MBMS-Aware Application (“VAL client”) must support SEAL-C API while abandoning use of M7 API
  ASP server (“VAL server”) entities must support SEAL-S API while abandoning M1 and (to-be-defined) 5GMS variants of R3, R4 and R6 APIs
  UE must additionally implement DC&R Service client
  Operator must additionally implement DC&R Service server
5GMS is itself a service platform enabling various DL and UL media streaming application
services, as opposed to being a vertical application that could better leverage SEAL

## Slide 10
SEAL for DC&R support of Vertical Applications
While the benefit of adding SEAL to 5GMS is not fully clear, supporting standalone vertical applications for the collection, reporting and exposure of domain-specific UE application related data should consider SEAL for providing a common data collection and reporting service
  SEAL Options A or Option B as shown in previous slides as candidate models
Recommendation on next steps:
  Pursue further study in SA4 on the development of generic UE data collection and reporting architecture that incorporates SEAL, along with the necessary procedures, formats and protocols