## Slide 1: Title: Proposal of “WebRTC with Operator’s Assistance”
NTT
Document for: discussion
Agenda Item: 11.7 Related to S4-220129
3GPP TSG|WG4 Meeting #117-e S4-220130
February 14–23, 2022, Electronic Meeting

## Slide 2: Benefits of WebRTC with Operator’s Assistance
WebRTC
Client
Operator A
i) To IMS
iii) OTT To Other Operators
IMS
Client
WebRTC
Entities
Interworking
WebRTC with operator’s termination and assistance:
  Can connect to IMS clients,
  Can connect to other operator’s clients if NNI is specified,
  OTT WebRTC clients can also connect to other operator’s clients.
ii) To Other Operators
IMS
Entities
WebRTC
Client
Operator A
WebRTC
Client
WebRTC
Entities
WebRTC
Entities
Operator B
NNI
OTT WebRTC
Client
Operator A
WebRTC
Client
WebRTC
Entities
WebRTC
Entities
Operator B
NNI
OTT
OTT’s
WebRTC
Entities
NNI

## Slide 3: WebRTC Non-Browser Clients and C-Plane Definition
We propose considering “WebRTC Non-Browser” clients, which can provides better QoE than browser clients.
WebRTC C-Plane signalling needs to be specified for that purpose.
When WebRTC C-Plane signalling is specified, the native application or conference appliance can be connected to any 3GPP operators.
 |  |  | Location of Servers (e.g. Signalling server, ICE server) | 
 |  |  | In OTT’s NW | In operator’s NW (Operator-Assist)
Client (Terminal) | WebRTC Browser |  | 3GPP Northbound API | TS24.371 (WebRTC access to the IMS)
 | WebRTC Non-Browser*1 | Dedicated for a Specific Service Provider |  | Needs additional Standardization of C-Plane
 |  | Universal for multiple Service Providers | Mostly Out of Scope | 
(*1) Described as “WebRTC device” or “WebRTC native application” in RFC8825
- Use case of WebRTC and Status of standardization -

## Slide 4: NW Architecture Example - Same Operator
Center DN
Operator A
WebRTC Signalling Server(s)
WebRTC
Client A1
WebRTC
Client A2
WebRTC
C-Plane
WebRTC
C-Plane
QoS
Control
(Npcf)
QoS
Control
QoS
Control
(Npcf)
QoS
Control
Edge DN2
SFU or MCU
with STUN/ICE
(R)AN / UPF
WebRTC
U-Plane
Control?
(R)AN / UPF
Edge DN1
WebRTC
U-Plane
PCF
SFU or MCU
with STUN/ICE
Control?

## Slide 5: NW Architecture Example ii) To Other Operators
Center DN
Operator A
WebRTC Signalling Server(s)
WebRTC
Client A1
WebRTC
Client B
Center DN
WebRTC
Signalling Server(s)
PCF
Operator B
WebRTC
C-Plane
SFU?
SFU?
QoS
Control
(Npcf)
QoS
Control
(R)AN / UPF
QoS
Control
(Npcf)
QoS
Control
Edge DN
SFU or MCU
with STUN/ICE
WebRTC
C-Plane
WebRTC
U-Plane
NNI
C-Plane
Control?
NNI
U-Plane
(R)AN / UPF
Edge DN1
WebRTC
U-Plane
PCF
SFU or MCU
with STUN/ICE
Control?
Control?
Control?
Control?

## Slide 6: NW Architecture Example iii) OTT To Other Operators
Center DN
Operator A
WebRTC Signalling Server(s)
WebRTC
Client B
Center DN
WebRTC
Signalling Server(s)
PCF
Operator B
SFU?
SFU?
QoS
Control
(R)AN / UPF
QoS
Control
(Npcf)
QoS
Control
Edge DN
SFU or MCU
with STUN/ICE
WebRTC
C-Plane
WebRTC
U-Plane
NNI
C-Plane
NNI
U-Plane
OTT
Client
(R)AN / UPF
Edge DN1
OTT’s NW
Signalling Server(s)
PCF
NEF
OTT
C-Plane
QoS
Control
(NBI)?
OTT’s
Media Entity
OTT
U-Plane
NNI
C-Plane
Control?
Control?
Control?
QoS
Control??
(Npcf)

## Slide 7: Signalling Protocol Comparison
IMS
WebRTC
(Typical Implementation
of TS24.371)
WebRTC Study Item Proposal
(Example)
ref.) 3GPP APIs
(e.g., NBI, EDGEAPP, …)
Call Control &
Terminal Registration
Conference Management
(e.g., create or deletion
XR rooms?)
3GPP Work
SIP Profiles and Procedures of SIP nodes
TS 24.229 (IMS Base)
TS 29.165 (NNI)
& Other TSs
3GPP Work
SIP over WebSocket almost same as IMS signalling (other signalling protocols are also allowed.)
3GPP Work
API definitions with AsyncAPI for WebRTC Signalling (AsyncAPI is variant of OpenAPI)
3GPP Work
API definitions with OpenAPI for REST APIs
TS 24.371
3GPP Work
API definitions with OpenAPI for REST APIs
+
+
+
+
+
IETF Work
SIP Protocol (RFC3261)
SIP Extension RFCs
IETF / W3C Work
WebRTC Framework
WebSocket Protocol
WebRTC Framework
WebSocket Protocol
IETF Work
HTTP/HTTPs Protocol
IETF Work
HTTP/HTTPS Protocol
IETF / W3C Work
Session model is limited to SIP dialog style.
SIP is complex for user-network interface.
Enhancements of SIP need IETF’s hard work.
Session model can be freely defined.
Only 3GPP work needed for protocol enhancements.
AsyncAPI and OpenAPI are based on JSON style that is very flexible and extensible.

## Slide 8: Summary
Specifications relevant to WebRTC technology or WebRTC services are already there.
  TS24.371, Web Real-Time Communications (WebRTC) access to the IP Multimedia (IM) Core Network (CN) subsystem (IMS); Stage 3; Protocol specification (since Rel-12)
  3GPP Northbound APIs
They give enough hints to realize the cases, where an operator supports WebRTC indirectly (via eP-CSCF or JavaScript).
An unexplored case is to support WebRTC directly. We call it WebRTC with Operator’s Assistance.
It provides more connectivity and better QoE.
It may provide another chance for operators and OTTs.
WebRTC with Operator's Assistance (which involves WebRTC C-plane and NNI) should be studied.

## Slide 9: Comments & Replies (1)
C1. On Slide #2, who provides codes?
R1. Anybody but the RTC APP (and codes) are assumed to comply with 3GPP specs in terms of connectivity and basic features. Similar to VoLTE apps.
C2. On Slide #2, the scenario i) has been covered by the exiting work items in SA2/CT1. This should be excluded from the RTC WID.
R2. Scenario i) expects more direct support of WebRTC (e.g., other than Gm based interface)
C3. On Slide #3, top right case is ??? [Imed’s mail is expected]
C4. On Slide #3, bottom left case is valid, because ??? [Imed’s mail is expected]
R4. Further elaboration is appreciated. Bottom left has two sub-cases: one is provider(OTT)-specific service and another is universal service. The latter case is hard to imagine and then commented as "out of the scope.“
C5. If C-plane is to be specified, SA2/CT1 (and W3C) should be involved.
R5. All RTC work (not only the proposed approach) deal with OTT-MNO relationships and should be consulted with SA2 and CT1. We may use W3C and IETF specs as we did in SIP/IMS.
C6. More study on the proposed operator-assisted approach is needed.
R6. Agree. We can do inside the WebRTC WID or via a stand-alone study item. Supporters are welcome.
→ Regarding C6, “Draft New SID on the enhancements for immersive Real-time Communication for WebRTC” has been proposed.

## Slide 10: Comments & Replies (2)
C7. Why new lightweight C-plane signaling is lightweight? Isn’t it SIP/IMS complete?
R7. New C-plane signaling is not fully compatible SIP/IMS but will be specified to have enough functionality for immersive realtime communication.
C8. WebRTC gateway could use any chosen subset of IMS, and OTT do not have to all of IMS functionalities.
R8. Minimal necessary functionalities for 1:N RTC session may be “call in” and “call out”. These should be studied for interoperability, and it is not more technically difficult to implement them than any subset of IMS.
C9. Is there any performance difference between browser and non-browser?
R9. Media handling (e.g. video audio sync) is not fully tunable via current WebRTC API. Therefore, optimized native apps show better performance than browser. (WebRTC-NV low level API may solve it)
C10. Some 3gpp codecs may not accessible by OTT browser or client apps.
R10. It may depend on ongoing 3GPP discussions including IVAS or some other SWGs. However, eIMS-AGW codec conversion may be helpful for interwork.

## Slide 11: TR 26.998 (conversational & RTC related)
4 Introduction
  4.2 Device Functional arch.
  4.2.1 (four) Functions
  4.2.2 Four Types (incl. STAR, EDGAR)
  4.2.3 AR runtime
  4.2.4 Scene manager
  4.2.5 XR spatial computing
  4.2.6 5G media access function.
  4.3 Procedures (AR media delv. & Spatial comp.)
  4.4 Content formats and codecs
  4.4.4 Media formats
  4.4.5 Compression formants
  4.4.6 Decoder mgt & coord.
  4.5 KPI and metrics
  4.5.1 TR 26.928 on XR
  4.5.2 for AR
  4.5.3 Typical latencies
  4.6 Related work
  4.6.1 3GPP including IVAS and ITT4RT
  4.6.8 WebRTC
5 Core use cases (15 from XR and 7 on AR)
6. Mapping to 5G
  6.1 Five scenarios from 22 UCs
  6.2 DL streaming
  6.3 Interactive (context change)
  6.4 Cognitive
  6.5 AR conv. Services
  6.5.3 Basic (three) arch. & flows
  6.5.3.1 & 2 Sym/Asym.
  6.5.4 MTSI-based
  6.5.5 Data Channel MTSI-based
  6.5.6 Content formats & codecs
  6.5.7 Summary of MTSI and DCMTSI
  6.5.8 Std. areas
  6.6 Shared AR conv.
7 Devices form factor
  7.2 Battery/Power consumption
8 Potential normative work
  8.2 5G-AREA (stage 2)
  8.3 5G MSE (API package)
  8.4 5G RTC, 1) DL split rendering, 2) UL cognitive, 3) Conversational AR serivces
  8.5 MeCAR
  8.8 IMS-based AR conv.

## Slide 12: Relation between 26.998 potential normative work and FS_eiRTCW (1/2)
8.4 5G Real-time Communication
As documented in clause 4.2.6 and further developed in the context of clause 6, there are several use cases that require a 5G Real-time communication. The use cases include:
1) EDGAR-based UEs relying on rendering on the network. In this case, the downlink requires sending pre-rendered viewports with lowest latency, typically in the range below 50ms.
2) Uplink streaming of camera and sensor information for cognitive/spatial computing experiences, in case the environment tracking data and sensor data is used in creating and rendering the scene.
3) Conversational AR services require real-time communication both in the downlink and the uplink, even independent from MTSI for app integration of the communication.
In order to provide adequate QoS as well as possible optimizations when using a 5G System for media delivery, an integration of real-time communication into the 5G System framework is essential.
As identified in clause 4.2.6 and clause 6.5, there is a need for supporting third-party applications in 5G real-time communication as well as server-based real-time streaming. From an app developer perspective, an enabler is preferable, especially to support real-time streaming, for example split-rendering.
Different options may be considered, for example re-use of parts of MTSI such as the IMS data channel and 5G Media Streaming for managed services, or re-use of WebRTC for OTT services. A 5G Real-time communication is expected to be aligned with either IMS or WebRTC but provides additional functions to integrate with the 5G System.
…
In FS_eiRTCW, detailed requirements including C-plane signalling for the common use in several WebRTC implementations will be identified.
Several objectives are focused on identifying enhancements supporting case 3 (AR Conversational),
but the Carrier-Assisted scheme can also help the
case 1 (EDGAR-based UE and rendering on the network) and
case 2 (Cognitive/spatial information up link streaming)
As related options, 5G-RTC has two tracks:
1. (WebRTC-based) iRTCW
2. (MTSI-based) IBACS
FS_eiRTCW will investigate further possibility of WebRTC
not only for OTT services but Operator-Assisted scheme.

## Slide 13: Relation between 26.998 potential normative work and FS_eiRTCW (2/2)
Cont. )
It is proposed to define a general 5G Real-time Communication Media Service Enabler that includes, among others, the following functionalities:
- A protocol stack and content delivery protocol for real-time communication based on RTP
- A set of codecs for different media types
- A common session and connection establishment framework, with instantiations based on SIP and SDP for IMS or SDP and ICE for WebRTC, including further possible investigation of control plane
- A capability exchange mechanism
- A security framework, for example based on SRTP and DTLS for WebRTC
- Uplink and downlink communication
- Suitable control protocols for end-to-end adaptation
- QoS and 5G System integration framework
- Reporting and QoE framework
Objective1
Objective2
Objective6
Objective3
All aspects are basically covered by RTC WIDs, and FS_iRTCW will investigate enhancements.
Objective 4 and 5 are to identify necessary network functionalities, cooperating with
XR conversational applications.

## Slide 14: Different Models between RTC Work Items
iRTCW
(WebRTC-based OTT model)
FS_eiRTCW
(WebRTC-based Carrier Assistance model)
WebRTC
Signalling
Server
NEF
(R)AN / UPF
MCU/SFU
with ICE
U-Plane
OTT-Data NW
QoS
Control
(NBI?)
QoS
Tunnel
Operator NW
(R)AN / UPF
new WebRTC
C-Plane
U-Plane
PCF
OTT
C-Plane
MCU/SFU
with ICE
QoS
Control
Npcf
N7,N4
OTT proprietary
Client
OTT proprietary
Client
Various
Client
Various
Client
With specified C-plane, Operator-Assistance will provide interoperability
as IMS-based model while involving OTT-related elements.
IBACS Expectation
(IMS model)
To be checked..
IMS Client
P-CSCF
(R)AN
C-Plane
Operator NW
S-CSCF
MRFP
MRFC
U-Plane
Mw
ISC
AS
Mp
IMS Client
PCF
Mr’
QoS
Control
N7,
N4
PCF
N7,
N4
WebRTC
Signalling
Server
Operator
NW
OTT-related elements
OTT App
OTT App