## Slide 1: PDU set RTP HE
Saba Ahsan

## Slide 2
List of Open Issues
What is the deliverable to SA2 by Apr/May.
Importance field:
  Definition of importance
  length (3 or 4 bits) and
  guidelines
Burst indication:
  definition of burst,
  length, guidelines,
  extension or part of basic header.
Length of PDU set sequence number: 6 recommended by Lenovo’s paper with possibility for reduction.
Indicating type of PDU set information used to UPF via AF using control plane – the RTP HE id + extensions used
  How does the UPF identify which IP packets contain PDU set information.
PDU set information using RTP header, payload, other HEs.- related to importance field
  Decide on reply to LS – S4-230465

## Slide 3
What is the deliverable to SA2
Create a section in TS 26.522 that SA2 can refer to it.
  Set of requirements in terms of fields
    We still need to define the semantics of
      Burst indication -
      Importance field -
Have one section on Stage 2 at least by the deadline?
Multiple subsections can be filled in the long term.
Let SA2 know in the LS that we define the guidelines by end of Rel-18.
Does SA2 expect us to define how to extract PDU set information or is it set by the RTP sender?
  We can define the PDU set HE where the RTP sender sets it
  The alternative is for the UPF to extract it from the existing RTP headers, payloads, extensions etc.
    We may want to prefer the RTP HE instead of defining these guidelines.

## Slide 4
Burst definition in SA2
In SA2->
Data Burst: A set of multiple PDUs generated and sent by the application in a short period of time. A Data Burst can be composed by one or multiple PDU Sets.
In SA4->
Data Burst: A data burst is set of multiple PDUs generated and sent by the application such that in a short period of time. there is an idle period between two bursts. A Data Burst can be composed by one or multiple PDU Sets.
Considerations:
What is the duration of this idle period?
If we define the time to next burst solution, we should consider some flexibility for the application server to decide.
We should consider that the data burst is used for putting the UEs to sleep and should define burst accordingly.
  It may be okay to indicate the idle period threshold to RAN from the AS. If the bursts are too close the threshold can be zero. We should consider communicating this to SA2.
We should decide if the burst indication is for one flow or multiple flows
  Can possibly be combined at UPF? Or can be done at RAN to consider for all flows and decide when to use power saving.

## Slide 5
Importance
Importance field:
  Scalar value
    We can decide if 0 is highest or lowest.
  Importance is used for discardability in the RAN
  UPF should use the importance field in the PDU set HE only when it is used (successfully SDP O/A and possible indication from AF to UPF via control channel). If it is not used then other methods can be considered.
  The guidelines for adding framemarking may be one way to add the importance field. But we will define detailed guidelines as part of Rel-18 on how the RTP sender sets these fields.
  Do we need to provide guidelines for UPF in the absence of an PDU set RTP HE as requested in the LS 465? This can be implementation specific and may not need to be defined as part of the 5G_RTP specification but are still within SA4 scope.
    We can look into this after we are done with PDU set HE. We can indicate this in reply LS.