## Slide 1: Overview Slides on Advanced Media Delivery for 5G-MAG
tsto@qti.qualcomm.com
Thomas Stockhammer, Qualcomm Incorporated
Rapporteur of Study Item and stage-2 work item
Agenda Item: 8.7
3GPP TSG-SA4 Meeting #131 S4-250024
Geneva, , 17th Feb 2025 - 21st Feb 2025 rev of S4aI250064
Work in Progress

## Slide 2
Summary of Study
Per Topic Introduction
Status and Open Issues
Potential Impacts for 5G-MAG

## Slide 3
Supporting IM name
AT&T
ATEME
BBC
China Mobile Com. Corporation
China Unicom
Comcast
Dolby France SAS
EBU
Ericsson LM
Huawei Technologies Co Ltd.
InterDigital Communications
Lenovo
NTT
Orange
Qualcomm Incorporated
Rohde &Schwarz
Samsung Electronics Co. Ltd.
Sony Europe B.V.
SWR
Telecom Italia
Tencent
Xiaomi
ZTE
Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
26.802 | MBS User Service Enhancements and Extensions. | SA#106 (Dec 24) | Individual CRs for each of the key topics may be provided.
26.804 | Advanced Media Delivery. | SA#106 (Dec 24) | Individual CRs for each of the key topics may be provided.

## Slide 4: Background
TS 26.501 defines the 5GMS architecture, call flows, and procedures. TS 26.512 defines the 5G Media Streaming protocols. In the 5GMS_Ph2 work item, extensions to 5G Media Streaming architecture are provided. In the 5GMS_Pro_Ph2, extensions to 5G Media Streaming Protocols were provided and generalized the topic of media delivery by providing TS 26.510. In addition, for MBS, the User Service architecture was developed in TS 26.502 and MBS Protocols are defined in TS 26.517. It is also worth noting that 5G-MAG has defined reference implementations of both 5G Media Streaming and MBS. The implementation provides feedback for potential bugfixes.
However, mobile media delivery is as important as never before with everlasting growth of traffic and new functionalities provided by third-party service providers. Several potential improvement areas and potential extensions have been identified and should be studied further.
The primary focus of this Work Item is the delivery of segmented media objects in the media plane, i.e. at reference points M2, M4 and M7 of the Media Delivery architecture. One of the open issues identified in the Rel-18 feasibility study 5GMS_Pro_Ph2 is the need for a specification that addresses interoperability considerations around content delivery protocol features and general technologies for segmented media streaming and the IP/PDU 5G System Layer. This points to the further study media plane issues to support additional functionalities, but also identifies what needs to be ported from legacy TS 26.512 to a generalised media plane technical specification. The relation to media session handling (as specified in TS 26.510) is identified in TR 26.804, but enhancements to media session handling are not the primary focus of this study.

## Slide 5: Early 5G-MAG Involvement
https://www.5g-mag.com/post/5g-mag-workshop-with-3gpp-sa4-advanced-media-delivery

## Slide 6: Objectives of the study item
Document the following additional Key Issues in more detail, in particular how they relate to the 3GPP Media Delivery architecture and/or the MBS User Service architecture:
  Common Client Metadata.
  Common Server-and Network-Assisted Streaming.
  Multi-CDN and Multi-Access Media Delivery.
  Modem Usage Optimized Media Streaming.
  DRM and Conditional Access.
  In-session Unicast Repair for MBS Object Distribution.
  MBS User Service and Delivery Protocols for eMBMS.
  Selected MBMS Functionalities not supported in MBS.
  DASH/HLS Interoperability.
  Further harmonization of RTC and Streaming for Advanced Medial Delivery.
  Issues identified by Market Representation Partners.
  Improved QoS support.
  Impacts and opportunities of QUIC for segmented content delivery
Study collaboration scenarios between the Application Service Provider and the 5G System and for each of the key topics.
Based on existing architectures, develop one or more deployment architectures that address the key topics and the collaboration models.
Map the key topics to basic functions and develop high-level call flows.
Identify the issues that need to be solved.
Provide candidate solutions including call flows, protocols and APIs for each of the identified issues.
Coordinate work with other 3GPP groups e.g. SA2, SA3, SA5, SA6 and others as needed.
Coordinate work with external organizations such as DASH-IF, CTA WAVE, ISO/IEC JTC29 WG3 (MPEG Systems), 5G-MAG, DVB or IETF, as needed.
Identify gaps and recommend potential normative work for stage-2 and stage-3, including which existing specifications would be impacted and/or if any new specifications would preferably be developed.

## Slide 7: 5GMS – Media Delivery Architecture Baseline

## Slide 8: Specification Overview for 5G Media Streaming in stage-3
Stage-2 is documents in TS 26.501
TS 26.510
TS 26.512
TS 26.512
TS 26.512
TS 26.510
TS 26.510

## Slide 9: Status of Work Topics after 3GPP SA4#130 (November 2024)
Topic | Title | Lead | Related spec and CR number | Clause in spec | Completion | Rel-19 normative work
0 | Specification Structure | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.15, 6.15 | 100% | no
1 | Common Client Metadata | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.16, 6.16 | 90% | yes
2 | Common Server-and Network-Assisted Streaming | Gilles Teniou, Tencent | TR 26.804 | 5.17, 6.17 | 100% | no
3a | Multi-CDN Media Delivery | Jason Cloud, Dolby | TR 26.804 | 5.19, 6.19 | 80% | yes
3b | Multi-Access Media Delivery | Prakash Kolan, Samsung | TR 26.804 | 5.18, 6.18 | 100% | yes
4 | Modem Usage Optimized Media Streaming | Gilles Teniou, Tencent | TR 26.804 | 5.20, 6.20 | 100% | no
5 | DRM and Conditional Access | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.10, 6.10 | 90% | yes
6 | In-session Unicast Repair for MBS Object Distribution | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.9 | 60% | yes
7 | MBS User Service and Delivery Protocols for eMBMS | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.10 | 60% | yes
8 | Selected MBMS Functionalities not supported in MBS | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.11 | 60% | yes
9 | DASH/HLS Interoperability | Gilles Teniou, Tencent | TR 26.804 | 5.21, 6.21 | 100% | no
10 | Further harmonization of RTC and Streaming for Advanced Media Delivery |  |  | 5.22, 6.22 | 100% | no
11 | Issues identified by Market Representation Partners | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.6, 6.6 | 100% | no
12 | Improved QoS support | Qi Pan, Huawei |  | 5.23, 6.23 | 90% | yes
13 | Impacts and opportunities of QUIC for segmented content delivery | Emmanouil Potetsianakis, Xiaomi | TR 26.804 | 5.4, 6.4 5.24, 6.24 | 100% | no
14 | In-band Signaling of QoS for 5G Media Streaming | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.25, 6.25 | 100% | no
15 | Multi AS dynamic content generation and a sample solution | Rufael Mekuria, Huawei | TR 26.804 | 5.26, 6.26 | 100% | no
16 | Slicing | Prakash Kolan, Samsung | TR 26.942 |  | 100% | yes

## Slide 10
3GPP Advanced Media Delivery
Common Client Metadata.
Common Server-and Network-Assisted Streaming.
Multi-Access Media Delivery.
Media Delivery from multiple service endpoints/location.
Modem Usage Optimized Media Streaming.
DASH/HLS Interoperability.
Further harmonization of RTC and Streaming for Advanced Media Delivery.
Improved QoS support for Media Streaming services.
QUIC-based segmented media delivery.
In-band signalling of QoS for 5G Media Streaming.
Dynamic content generation from multiple sources.
In-session Unicast Repair for MBS Object Distribution.
MBS User Service and Delivery Protocols for eMBMS.
Selected MBMS Functionalities not supported in MBS.
S4-242270 | WID new | Draft New Work Item on Architectural Updates for Advanced Media Delivery | Qualcomm Incorporated, BBC, China Mobile Com. Corporation, Dolby France SAS, NTT, Orange, Huawei Technologies Co Ltd., Comcast, XGN, Ericsson LM, Tencent, ATEME, AT&T, Samsung Electronics Co. Ltd., China Unicom, Telecom Italia, SWR, EBU, Sony Europe B.V., Rohde & Schwarz, ZTE | Agreed in SA4 in Nov ‘24 | Approved by SA in Dec ’24
S4-242269 | Work Plan | [FS_AMD] Time and Work Plan for Advanced Media Delivery | Qualcomm Incorporated (Rapporteur) | Agreed in SA4 in Nov ’24 | Approved by SA in Dec ’24
S4-242268 | CR | [FS_AMD] Advanced Media Delivery Features for MBS User Services | Qualcomm Incorporated, BBC, Huawei Technologies Co Ltd., XGN, Ericsson LM, ATEME, Telecom Italia, EBU | Agreed in SA4 in Nov ’24 | Approved by SA in Dec ’24
S4-242267 | CR | [FS_AMD] Advanced Media Delivery Features for 5G Media Streaming | Qualcomm Incorporated, BBC, Dolby France SAS, Huawei Technologies Co Ltd., Xiaomi, Comcast, Orange, XGN, Ericsson LM, Tencent, ATEME, Samsung Electronics Co. Ltd., Telecom Italia, EBU, Lenovo | Agreed in SA4 in Nov ’24 | Approved by SA in Dec ’24

## Slide 13: Time Plan for AMD
SA#106 (10 – 13 December 2024, Madrid, ES) | Approve CRs addressing potential normative work for stage-2 for relevant work topics Approve stage-2 normative work | 
3GPP SA4 MBS SWG Telco (Dec 19, 2024, 15:30 – 17:30 CET, Host Qualcomm) | Progress work topics Initiate CRs for remaining stage-3 updates Submission Deadline Dec 18, noon CET For stage-2 initiate CRs to 26.501, 26.502, and other relevant specifications. | Target 75% Real
3GPP SA4 MBS SWG Meeting (January 8-10 2025, online, Host Qualcomm) | Progress gaps for stage-3 for relevant work topics. Progress CRs relevant for potential issues related to stage-3 Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis Calls are held each day between 15:00 to 18:15 CET (with 15min break at 16:30). For January 9, 2025, a joint session with 5G-MAG from 15:00 to 16:30 is planned. Submission deadline Jan 6, 23:59 CET For stage-2 progress CRs to 26.501, 26.502, and other relevant specifications. | Target 85% Real
3GPP SA4 MBS SWG Telco (Feb 6, 2025, 15:30 – 17:30 CET, Host Qualcomm) | Progress work topics Progress CRs for remaining stage-3 updates Submission Deadline Feb 5, noon CET For stage-2 progress CRs to 26.501, 26.502, and other relevant specifications. | Target 90% Real
SA4#131 (17 – 21 February 2025, Geneva, Switzerland) | Progress gaps for stage-3 for relevant work topics. Select recommended technologies for 5G Media Streaming and MBS User Services Agree CRs addressing potential normative work for stage-3 for relevant work topics Communicate with other 3GPP working groups and external organizations, in particular 5G-MAG, on need basis For stage-2 agree on CRs to 26.501, 26.502, and other relevant specifications. For stage-3 agree on normative work based on conclusions. | Target 100% Real
SA#107 (12 – 14 March 2025, Incheon, KR) | Approve CRs addressing potential normative work for stage-3 for relevant work topics Approve stage-2 CRs Approve stage-3 normative work item based on conclusions. | 
SA4#131-bis-e (21 – 25 August 2025, online) | Kick off stage-3 | 
SA4#132 (19 – 23 May 2025, Fukuoka, Japan) | Progress stage-3 | 
SA4#133-e (21 – 25 August 2025, online) | Agree stage-3 CRs | 
SA#109 (16 – 19 September 2025, China) | Approve stage-3 CRs | 

## Slide 14: Status of stage-2 work prior to SA4#131
Tracked in Google Sheet here
Topic | Title | Lead | Latest Document and Status | Related spec and CR number | Clause in spec | Completion
1 | Common Client Metadata | Thomas Stockhammer, Qualcomm | S4aI250045 (n) | 26501-0101rev2 |  | 30%
2 | Media delivery from multiple service endpoints/locations | Jason Cloud, Dolby | S4aI250041 (e) | 26501-0103rev2 |  | 30%
3 | Multi-Access Media Delivery | Prakash Kolan, Samsung | S4aI250036 (e) | 26501-0107rev1 |  | 80%
4 | Distributing encrypted and high-value content | Thomas Stockhammer, Qualcomm | S4aI250046 (n) | 26501-0102rev2 |  | 40%
5 | In-session Unicast Repair for MBS Object Distribution | Thomas Stockhammer, Qualcomm | S4aI250039 (e) | 26502-0033rev2 |  | 50%
6 | MBS User Service and Delivery Protocols for eMBMS | Thomas Stockhammer, Qualcomm | S4aI250040 (e) | 26502-0034rev2 |  | 40%
7 | Selected MBMS Functionalities not supported in MBS | Thomas Stockhammer, Qualcomm | S4aI250032 (n) | 26502-0035rev1 |  | 30%
8 | Improved QoS support for Media Streaming services | Qi Pan, Huawei | S4aI250042 (e) | 26501-0104rev1 |  | 70%
9 | Media Streaming aspects of Network Slicing | Prakash Kolan, Samsung | S4-242016 (e) | 26501-0098rev2 | 2, 4.0.6, 5.8.1, 6.9.6, Annex X, Annex Y | 70%
 | Overall progress |  |  |  |  | 49%

## Slide 15: Status of Work Topics after 3GPP SA4#130 (November 2024)
Topic | Title | Lead | Related spec and CR number | Clause in spec | Completion | Rel-19 normative work
0 | Specification Structure | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.15, 6.15 | 100% | no
1 | Common Client Metadata | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.16, 6.16 | 90% | yes
2 | Common Server-and Network-Assisted Streaming | Gilles Teniou, Tencent | TR 26.804 | 5.17, 6.17 | 100% | no
3a | Multi-CDN Media Delivery | Jason Cloud, Dolby | TR 26.804 | 5.19, 6.19 | 80% | yes
3b | Multi-Access Media Delivery | Prakash Kolan, Samsung | TR 26.804 | 5.18, 6.18 | 100% | yes
4 | Modem Usage Optimized Media Streaming | Gilles Teniou, Tencent | TR 26.804 | 5.20, 6.20 | 100% | no
5 | DRM and Conditional Access | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.10, 6.10 | 90% | yes
6 | In-session Unicast Repair for MBS Object Distribution | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.9 | 60% | yes
7 | MBS User Service and Delivery Protocols for eMBMS | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.10 | 60% | yes
8 | Selected MBMS Functionalities not supported in MBS | Thomas Stockhammer, Qualcomm | TR 26.802 | 5.11 | 60% | yes
9 | DASH/HLS Interoperability | Gilles Teniou, Tencent | TR 26.804 | 5.21, 6.21 | 100% | no
10 | Further harmonization of RTC and Streaming for Advanced Media Delivery |  |  | 5.22, 6.22 | 100% | no
11 | Issues identified by Market Representation Partners | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.6, 6.6 | 100% | no
12 | Improved QoS support | Qi Pan, Huawei |  | 5.23, 6.23 | 90% | yes
13 | Impacts and opportunities of QUIC for segmented content delivery | Emmanouil Potetsianakis, Xiaomi | TR 26.804 | 5.4, 6.4 5.24, 6.24 | 100% | no
14 | In-band Signaling of QoS for 5G Media Streaming | Thomas Stockhammer, Qualcomm | TR 26.804 | 5.25, 6.25 | 100% | no
15 | Multi AS dynamic content generation and a sample solution | Rufael Mekuria, Huawei | TR 26.804 | 5.26, 6.26 | 100% | no
16 | Slicing | Prakash Kolan, Samsung | TR 26.942 |  | 100% | yes

## Slide 16: WT1: Common Client Metadata

## Slide 17: WT1: Common Client Metadata
Description:
  While 3GPP and MPEG in DASH support DASH metrics, the reporting is not common to any player, for example all DASH players as well as HLS players. As an example, CTA WAVE has developed: CTA-5004: Web Application Video Ecosystem Common-Media-Client-Data (CMCD) with an excellent overview here: https://ottverse.com/common-media-client-data-cmcd/. It is worthwhile to study the benefits of integrating commonly supported metrics and client data reporting in 5GMS workflows. The focus is the integration of already defined metrics rather than developing new metrics. Examples of study include support of specific metric keys, player APIs, sending options from client to server (user plane, M5 reference point, EVEX), M3 reference point impact, as well as usage of the data in operations. A study of creating a common harmonized reporting framework and studying the interaction of different frameworks may be included.
Companies interested: Qualcomm, Dolby, CMCC, AT&T, Telecom Italia, Comcast, Orange, BBC, EBU, Tencent, ATEME Sony Europe B.V.
Work Topic lead: Thomas Stockhammer, Qualcomm
5G-MAG Interest and Involvement:

## Slide 18: WT1: What is CMCD?
A defined set of structured key/value pairs communicating mutually beneficial media-related information from a player to a CDN via either
  A set of custom headers
  A query arg
  A JSON object
Common because the same data structure can be used across all players and all CDNs.
Resources
  Available for free at https://tinyurl.com/cta5004spec
  DASH-IF Special Session available from Will Law
Version 2 is happening as we speak

## Slide 19: WT1: Common Client Metadata
Introduction to CMCD
  Presentation from Will Law for phase 1
  https://github.com/cta-wave/common-media-client-data/issues
  V1 is technical
  V2 is more towards QoE, player health
  MPEG-DASH adds signaling
  Opportunity to contribute by 3GPP until mid of 2024
Implementations
  Dash.js
    CMCDv1 complete
    Two methods (query, header)
    Configuration API
  Others
  All players except native HLS
Options
  DASH client is instructed through MPD elements
  DASH client is instructed through a configuration API
Integration of CMCD in MBS and MBMS
  Yes, relevant
  Options
    MBMS/MBS client reports
    Media Session Handler Reports
Background

## Slide 20: Selected Use Cases
The use cases which CMCD enables are broad – including robust pre-fetching of content, analytics solutions, forensic debugging, CDN delivery optimisation, alerting and monitoring systems, low latency optimisations, server-side switching, research analytics and content steering decision-making.
In the context of 5G Media Streaming, the CMCD information may be used for several purposes that are elaborated further in the remainder of this clause:
1) Operational optimisation of the 5GMSd AS: The Application Server uses CMCD information to optimise its operation. For example, the 5GMSd AS may choose to pre-fetch content from the 5GMSd Application Provider based on the value of the CMCD Next object request key signalled by the Media Player.
2) Operational optimisation of the 5GMSd AF and 5G Media Streaming: The Application Function uses CMCD information in order to configure the 5G System for optimised media delivery across the User Plane. For example, the 5GMSd AF may invoke service operations on the PCF in order to effect a delivery boost if the CMCD Buffer starvation flag is set by the Media Player.
3) UE data collection on media playback and 5GMS reception, reporting and event exposure by 5GMS System: The Application Function uses the data collection and reporting framework to provide CMCD information to the 5G System or to external 5GMS Application Providers. This could, for example, take the form of a time series event log for audit purposes. Such data could, for example, be useful to determine the quality of reception and to identify anomalies or errors that can occur on players.
Based on clause 5.16.

## Slide 21
CMCD [105] |  |  |  | Media delivery QoE metrics reporting [3GPP TS 26.510 Rel-18] |  |  | Media delivery consumption reporting [3GPP TS 26.510 Rel-18] | 
Scope | Key | Description | Type and unit | Source | Xpath | Description | Data type and property | Description
CMCD-Session | v | CMCD version | Integer | TS 26.247 clause 10.6.2 | ReceptionReport‌@schemaVersion | Schema version |  | 
CMCD-Session | cid | Content identifier | String | TS 26.247 clause 10.6.2 | ReceptionReport‌@contentURI | Content URI | ConsumptionReport.‌mediaPlayerEntry | Media Player Entry URL
 |  |  |  | TS 26.247 clause 10.6.2 | ReceptionReport‌@clientID | Client identifier | ConsumptionReport.‌reportingClientId | Reporting client identifier
CMCD-Session | sid | Session identifier | String | TS 26.247 clause 10.6.2 | ReceptionReport/QoeReport‌@recordingSessionID | Media delivery session identifier | ConsumptionReport.‌sessionId | Media delivery session identifier
CMCD-Session | st | Stream type (live/on-demand) | String token |  |  |  |  | 
CMCD-Session | sf | Streaming format (DASH, HLS, Smooth, other) | String token |  |  |  |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation‌@representationId | RepresentationID |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation‌@subreplevel | Unspecified |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@codecs | Unspecified |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@bandwidth | Representation bit rate? |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@qualityRanking | Unspecified |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/MpdInfo‌@frameRate | Representation frame rate (video representations only)? |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@width | Representation width (video representations only)? |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@height | Representation height (video representations only)? |  | 
 |  |  |  | TS 26.247 clause 10.2.8 | ReceptionReport/QoeReport/‌QoEMetric/MPDInformation/‌MpdInfo‌@mimeType | Representation MIME content type? |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@start | Sampling timestamp (wallclock) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry@mstart | Sampling timestamp (media presentation) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@videoWidth | Width of video viewport (pixels) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@videoHeight | Height of video viewport (pixels) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@screenWidth | Width of screen (pixels) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@screenHeight | Height of screeen (pixels) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/supplementQoEMetric/deviceinformation/Entry@pixelWidth | Width of screen pixel (mm) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@pixelHeight | Height of screen pixel (mm) |  | 
 |  |  |  | TS 26.247 clause 10.2.10 | ReceptionReport/QoeReport/‌supplementQoEMetric/‌deviceinformation/Entry‌@fieldOfView | Horizontal angle subtended at eye by screen (degrees) |  | 
 |  |  |  | TS 26.247 clause 10.2.5 | ReceptionReport/QoeReport/‌QoEMetric/InitialPlayoutDelay | Initial playout delay |  | 
 |  |  |  | TS 26.247 clause 10.2.9 | ReceptionReport/QoeReport/‌QoEMetric/PlayoutDelayfor‌MediaStartup | Media playout start-up delay |  | 
CMCD-Status | rtp | Requested maximum throughput | Integer kbit/s |  |  |  |  | 
CMCD-Status | bs | Buffer starvation | Boolean |  |  |  |  | 
 |  |  |  | TS 26.247 clause 10.2.6 | ReceptionReport/QoeReport/‌QoEMetric/BufferLevel@t | Buffer level timestamp |  | 
 |  |  |  | TS 26.247 clause 10.2.6 | ReceptionReport/QoeReport/‌QoEMetric/BufferLevel@level | Buffer level |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@t | Sampling timestamp (wallclock) |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@duration | Sampling period |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@numBytes | HTTP body bytes downloaded |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@activityTime | Time of incomplete GET |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@inactivityType | Pause, client buffer control, error |  | 
 |  |  |  | TS 26.247 clause 10.2.4 | ReceptionReport/QoeReport/‌QoEMetric/AvgThroughtput@accessbearer | Access bearer used for download |  | 

## Slide 22
minimal overlap between CMCD information and existing reporting mechanisms for 5G Media Streaming (QoE metrics reporting and consumption reporting)
CMCD [105] |  |  |  | Media delivery QoE metrics reporting [3GPP TS 26.510 Rel-18] |  |  | Media delivery consumption reporting [3GPP TS 26.510 Rel-18] | 
Scope | Key | Description | Type and unit | Source | Xpath | Description | Data type and property | Description
CMCD-Object | ot | Object type (init, audio, video, audio-video, subtitle, text, crypto, other) | String token |  |  |  |  | 
CMCD-Object | d | Object duration | Integer ms |  |  |  |  | 
CMCD-Object | br | Encoded bit rate | Integer kbit/s |  |  |  |  | 
CMCD-Object | tb | Top bit rate | Integer kbit/s |  |  |  |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace‌@start | Playback period start time (wallclock) |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace‌@mstart | Playback period start time (media presentation) |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace‌@startType | New playout request, Resume from pause, Start metrics collection, Other |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@representationId | RepresentationID | ConsumptionReportingUnit.‌mediaConsumed | e.g. MPEG-DASH representationID
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@subrepLevel | Greatest value of sub-representation level being rendered |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@start | Time when first media sample rendered (wallclock) | ConsumptionReportingUnit.‌startTime | Start of consumption
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@sstart | Time when first media sample rendered (media presentation) |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@duration | Duration of continuously presented media samples | ConsumptionReportingUnit.‌duration | Duration of consumption
CMCD-Session | pr | Playback rate | Decimal | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@playbackSpeed | Playback speed relative to normal (normal = 1.0) |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@stopReason | Representation switch, Rebuffering, User request, Period end, Presentation end, Metrics collection end, Failure, other |  | 
 |  |  |  | TS 26.510 clause 10.2.7 | ReceptionReport/QoeReport/‌QoEMetric/PlayList/Trace/‌TraceEntry@stopReasonOther | Other stop reason (free text) |  | 
 |  |  |  |  |  |  | ConsumptionReportingUnit.‌clientEndpointAddress | Client endpoint address
 |  |  |  |  |  |  | ConsumptionReportingUnit.‌serverEndpointAddress | Server endpoint address
 |  |  |  |  |  |  | ConsumptionReportingUnit.‌sliceInfo | S-NSSAI
 |  |  |  |  |  |  | ConsumptionReportingUnit.‌dnn | Data Network Name
 |  |  |  |  |  |  | ConsumptionReportingUnit.‌locations | Locations where content was consumed
CMCD-Request | bl | Buffer length | Integer ms |  |  |  |  | 
CMCD-Request | dl | Deadline | Integer ms |  |  |  |  | 
CMCD-Request | mtp | Measured throughput | Integer kbit/s |  |  |  |  | 
CMCD-Request | nor | Next object request | String |  |  |  |  | 
CMCD-Request | nrr | Next range request | String |  |  |  |  | 
CMCD-Request | su | Start-up | Boolean |  |  |  |  | 

## Slide 23
Option 3: Out-of-band reporting of CMCD information at M11d and M5d
Option 1: In-band reporting of CMCD information via reference point M4d and M3d
The preferred solution is Option 1 "In-band reporting of CMCD information via reference points M4d and M3d", for the following reasons:
- In-band reporting reference point M4d is broadly implemented in common media clients nowadays.
- In-band reporting permits operational optimizations by the 5GMSd AS, which is not the case with Option 3 Out-of-band reporting of CMCD information via reference points M11d and M5d. Solely on the basis of this issue, Option 1 and Option 2 would remain valid candidates.
- Passing the CMCD information to the 5GMS AF at reference point M3d (Option 1) permits operational optimisations by the 5GMSd AF, which is not the case with Option 2 In-band reporting of CMCD information via reference points M5d and R4 where the CMCD information is handed directly to the Data Collection AF instantiated in the 5GMS AF, but is not visible to the latter.
- All envisaged use cases can be supported by Option 1.

## Slide 24: Follow-up work
Furthermore, it is recommended:
To monitor the work in CTA WAVE on potential extensions of CMCD and potentially study how these extensions would be beneficial for 5G media streaming,
To collaborate with the other organizations including 5G-MAG, SVTA, DVB and CTA WAVE to implement and validate the usage of CMCD for the considered use cases,
To further study the usage of CMCD when 5GMS is deployed over MBS and/or MBMS,
To further study the aggregation of different reports (Metrics, CMCD, Consumption) in the 5GMS AF and the potential consolidation of information into a single data structure when exposed to the 5GMS Application Provider.
Stage-2, Stage-3, more study
Impacts on stage-3 are expected to:
TS 26.247: DASH
TS 26.510: Session Handling and APIs
TS 26.512: Protocols
TS 26.532: EVEX
TS 29.517: CT4

## Slide 25: WT3: Multi-CDN and Multi-Access Media Delivery
a) Multi-CDN Media Delivery
b) Multi-Access Media Delivery

## Slide 26: WT3: Multi-CDN and Multi-Access Media Delivery
Description:
  Content distributors often use multiple Content Delivery Networks (CDNs) to distribute their content to tend-users. As an example, they may upload a copy of their catalogue to each CDN, or more commonly have all CDNs pull the content from a common origin. In advanced deployments, technologies such as Coded Multisource Media Format (CMMF) use Application Layer FEC techniques to stripe different subsets of content across multiple CDNs. Different client implementations may then beneficially use the content on multiple CDNs, potentially guided by the service or network provider. In addition, formats and techniques for generating content for multiple CDN delivery such as MPEG-DASH Part 9 (ReAP) may be taken into account. Further extensions include the ability for a client to use multiple access networks at the same time to support media delivery. Study of integration of different technologies into the Media Delivery System is of relevance to address content provisioning, content hosting, impacts on user plane reference points M2 and M4, and on media session handling at reference point M5 as well as potential benefits in terms of quality and resource usage.
Companies interested: Qualcomm, Dolby, AT&T, Orange, Samsung Electronics Co. Ltd., Huawei Technologies Co Ltd., ATEME
Work Topic lead: Jason Cloud, Dolby
5G-MAG Interest and Involvement:

## Slide 27: WT3a) Media delivery from multiple service endpoints/locations
A multi-CDN or multiple service location/endpoint content offering generally provides content in a redundant manner at locations that can be differentiated by the client. The study of this Key Issue identifies gaps within the existing 5GMS architecture and recommends solutions to enable the ability use multiple sources or service locations/endpoints both internal and external to the 5GMS System. Multi-source/service location approaches considered include:
DNS-based switching.
MPEG-DASH client-side switching.
Content steering driven switching.
SAND4M-based switching.
CMMF-based multi-source delivery  see presentation in DASH-IF

## Slide 28: Common Server-and Network-Assisted Streaming
Background: Published as ETSI TS 103 998 – Content Steering

## Slide 29: Collaboration 1: Operator provides multiple service locations
5GMSd AS
Multi-CDN Controller
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Media Player+
Multi-CDN Client
DASH/HLS /CMAF M2
Media Player
M4
Multi-CDN Client
5GMSd AF
Provisioning M1
M3
MSH
M5
M10

## Slide 30: Collaboration 2: AS with as one of multiple service locations
5GMS application provider
5GMS-aware application
5GMSd AS
Multi-CDN Controller
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Media Player+
Multi-CDN Client Manager
DASH/HLS /CMAF
Media Player
M4d
Multi-CDN Client
M8
M2
M7d
5GMSd AF
MSH
M5
M10
M1
M3
M6d

## Slide 31: Architecture Options

## Slide 32: Reference Architecture
Multi-source media streaming collaboration scenarios and associated call flows are documented (item 1 in clause 5.19.7).
Reference point M10 is brought into scope of 5GMS for the purposes of content preparation chaining and media delivery between provisioned content distributions (item 4 in clause 5.19.7).
Update the description of the Content Hosting Configuration to describe the ability of the 5GMSd AF to provision Content Distributions in hierarchical or peer-to-peer configurations (item 4 of clause 5.19.7).
Document the capability to signal information to the 5GMSd Client that is required to deliver media from multiple content sources/endpoints using the Media Entry Point (item 6 in clause 5.19.7).
Define the requirements and functions necessary for a Media Player to be interoperable within the 5GMS System (item 7 in clause 5.19.7).
Clarify that the Media Player used for the purposes of multi-source/service location media delivery natively supports the multi-source/service location delivery approach in use (item 8 in clause 5.19.7).
Define a new reference point between a new External Access Client function located with the Media Player and a non-3GPP content hosting function or 5GMSd Application Provider for the purposes of communicating user plane information between the two functions (item 10 in clause 5.19.7).

## Slide 33: Stage-2 Work
Work in progress

## Slide 34: Stage-3 Work
Document the generic MIME content types and references to valid profiles or relevant external specifications for Content Preparation Templates used for the purposes of multi-source/service location content preparation (item 2 of clause 5.19.7).
Extend the ContentHostingConfiguration resource to allow Content Distributions to be declared in hierarchical or peer-to-peer configurations (item 4 of clause 5.19.7).
Extend the ContentHostingConfiguration resource to allow the 5GMSd Application Provider the capability to influence the configuration and deployment of Content Distributions with the 5GMSd AS at the time of provisioning (item 5 of clause 5.19.7).
Clarify the use of the Media Entry Point for the purposes of communicating service location and multi-source/service location configuration information to 5GMSd Clients (item 6 of clause 5.19.7).
Clarify the expectation that the Media Player natively supports the multi-source/service location approach in use (item 8 of clause 5.19.7).
The set of recommended technologies within 5GMS for performing multi-source/service location media delivery (among those listed within clause 5.19.7) is to be determined.
The following are recommended for further study: Verification of Content Preparation Template signalling and implementation within 5GMS specifications (item 3 of clause 5.19.7). This verification may be conducted outside 3GPP.
The following stage 3 extensions are recommended to TS 26.510 [108] and TS 26.512 [16]:

## Slide 35: WT3b) Multi-Access Media Delivery
Media streaming applications traditionally obtain content from a single source over a single path within a network. This imposes several limitations:
Performance is constrained to that of the source and path chosen. Any limits on network bandwidth and latency between the client and that source are directly translated to the client’s achievable Quality of Service (QoS) and Quality of Experience (QoE).
Disruptions or degraded performance caused by the source in use or on any of the network links between the client and source can lead to poor user experience, often in the form of lower playback quality, rebuffering, or complete playback failure.
This Key Issue considers integration of different technologies into the 5G Media Streaming System that addresses these, and similar, issues by allowing media streaming applications to efficiently access content across multiple access networks. Different client implementations may then beneficially use the content on these multiple access networks either serially or concurrently, potentially guided by the service or network provider. Study of integration of different technologies into the 5G Media Streaming System is of relevance to address content provisioning, content hosting, impacts on user plane reference points M2 and M4, and on media session handling at reference point M5 as well as potential benefits in terms of quality and resource usage.

## Slide 36: Collaboration Scenarios and ATSSS
Access Traffic Steering, Switching, and Splitting (ATSSS)
Steering functionality | Application awareness | Application transparency
ATSSS-LL | No | Yes
MPTCP | Yes. 5GMS Client or 5GMS-Aware Application may use API as described in clause 5.18.1.3.2 to control MPTCP behaviour. | Yes. 5GMS Client or 5GMS-Aware Application may use just the standard TCP sockets API as described in clause 5.18.1.3.2 to be transparent with MPTCP functionality.
MPQUIC | Yes. 5GMS Client or 5GMS-Aware Application may use API as described in clause 5.18.1.3.3 to control MPQUIC behaviour. | TBD

## Slide 37: Conclusions
Multi-access media delivery enables media streaming applications to efficiently access content over multiple access networks. This Key Issue has examined existing specification relating to the ATSSS (Access Traffic Steering, Switching and Splitting) architecture in TS 23.501 [23] and TS 23.502 [24] to identify its impact on 5GMS. Topics relating to application awareness and influence on multi-access delivery, potential enhancements to dynamic policy feature of 5GMS to support multiple access paths, and network assistance with multi-access delivery have been studied. The Key Issue has documented collaboration scenarios and the mapping of the ATSSS architecture into the 5GMS architecture.
Based on the conclusions, following are recommended for stage-2:
An informative annex is added to TS 26.501 [15] documenting:
A brief description of multi-access media delivery, based on clause 5.18.1 of the present document.
The mapping of the ATSSS architecture into the 5GMS architecture, as described in clause 5.18.3.2 of the present document.
Based on the conclusions, following are recommended for stage-3:
Changes to the Configuration Settings API and to the Dynamic Status Information API as described in clause 5.18.6.2 of the present document are implemented in TS 26.510 [108] to allow for application configuration and status information exchange for multi-access media delivery.
Very few specifcation changes are needed

## Slide 38: WT5: DRM and Conditional Access

## Slide 39: WT5: DRM and Conditional Access
Description:
  DRM and Conditional Access are commonly used by third-party streaming services. However, in case streaming is done through MBS or MBMS, a more careful management of the keys needs to be checked. Scalability of key delivery is an issue. The support for -encrypted content in Unicast/Multicast and Broadcast is relevant. Integration of Content Protection interfaces in the provisioning, for example using CPIX back-end interfaces is of high relevance for the industry and should accordingly be studied. The impacts of these on media plane (reference points M2 and M4) as well as the media session handling APIs (reference points M3, M5) should also be studied.
Companies interested: Qualcomm, Telecom Italia, Comcast, Rohde&Schwarz, Huawei Technologies Co Ltd.
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 40: Collaboration Scenarios and stage-2
Option 1: The 5GMSd Application Provider runs all DRM and packaging related functions, and the 5GMSd AS only caches the DASH Presentation as a CDN. For DRM acquisition, the UE contacts the 5GMSd Application Provider.
Option 2: The 5GMSd System runs a DRM and packaging service, including a License Server, on the 5GMSd AS. Content is ingested by the 5GMSd AS and all functions of licence hosting, content encoding, content encryption and so on run in the 5GMSd AS.
Option 3: The 5GMSd System runs a content encoding and packaging service, but the License Server is external in the 5GMSd Application Provider. The 5GMSd AS needs to communicate with the License Server for content encoding and packaging.
Option 4: The 5GMSd System generates the presentation manifest, but content encoding, content packaging and content encryption are external in the 5GMSd Application Provider. The 5GMSd AS needs to acquire relevant information for presentation manifest generation.
Option 5: This is similar to Option 2 but, being quite specific in operation, the License Server is handed to the 5GMSd AF alongside the Authorization Server. The main communication is between 5GMSd AS and 5GMSd AF at reference point M3d.
Option 6: This is similar to option 5, but only the License Server is offered by the 5GMSd System, hosted in the 5GMSd AF. Similar to option 4, content encoding, content packaging and content encryption are external in the Media Application Provider. The main communication is between the 5GMSd Provider and the 5GMsd AF at reference point M1d for the exchange of Content Protection Information.
DRM Function | 5GMSd Application Provider | 5GMSd AS | 5GMSd AF | Media Player | Media Session Handler
Authorization Server | 1, 3, 4 | 2 | 5, 6 |  | 
License Server | 1, 3, 4 | 2 | 5, 6 |  | 
Encoder | 1, 4, 6 | 2, 3, 5 |  |  | 
Encryptor/packager | 1, 4, 6 | 2, 3, 5 |  |  | 
Manifest Creator | 1, 6 | 2, 3, 4, 5 |  |  | 
Content Hosting |  | 1, 2, 3, 5, 6 |  |  | 
DRM Client |  |  |  | 1, 2, 3, 4, 5, 6 | 
DASH Client |  |  |  | 1, 2, 3, 4, 5, 6 | 
Media Platform |  |  |  | 1, 2, 3, 4, 5, 6 | 

## Slide 41: Stage-3 Extensions
Based on the considerations in clause 5.10, it is recommended to:
Support the Content Protection Information Exchange Format (CPIX) as specified in ETSI TS 103 799 [143] at reference point M2d by specifying the necessary stage-2 and stage-3 extensions in TS 26.501 [15] and TS 26.512 [16] respectively.
Support the DASH-IF Interoperability Points specified in [144] at reference point M4d for both DASH and HLS by specifying the necessary stage-2 and stage-3 extensions in TS 26.501 [15] and TS 26.512 [16], respectively.
Specification of a Content Preparation Template format in TS 26.512 [16] or TS 26.510 [108] that can configure encryption content preparation tasks in the 5GMS AS.
NOTE: Maintaining functional symmetry with uplink media streaming (where applicable) is generally considered important, but DRM is considered to be applicable only for 5GMS downlink.

## Slide 42: WT12: Improved QoS support

## Slide 43: WT12: Improved QoS support
Description:
  In Rel-18, SA2 has defined a number of new features in the 5G System, especially in the PCF, from which media delivery may benefit. Examples documented in TS 23.501 include the use of Explicit Congestion Notification (ECN) to support Low Latency, Low Loss, Scalable Throughput (L4S) services (clause 5.37.3), PDU Set handling (clause 5.37.5) and QoS Monitoring (clause 5.45), and there are likely others. The impact and usefulness of selected features is preferably studied. The functions identified in this context may be studied in one or more of the above work topics.
Companies interested: Ericsson LM, Huawei Technologies Co Ltd., Qualcomm, BBC, InterDigital Communications, Lenovo
Work Topic lead: Qi Pan (Huawei), Thorsten Lohmar (Ericsson)
5G-MAG Interest and Involvement:

## Slide 44: Key Objectives
Regarding the features described in clause 5.23.1.2, it is proposed to study:
Whether these features of the 5G System can be beneficial and valid for the Media Delivery System in the context of segmented media delivery (i.e., 5G Media Streaming):
Whether ECN marking for L4S can be beneficial and valid.
Whether PDU Set handling can be beneficial and valid.
Whether QoS monitoring can be beneficial and valid.
How to apply these features to the Media Delivery System:
How to integrate the ECN marking for L4S feature into the Media Delivery System.
How to integrate the PDU Set handling feature into the Media Delivery System.
How to integrate the QoS monitoring feature into the Media Delivery System.

## Slide 45: What is QoS monitoring
QoS monitoring comprises of measurements of QoS monitoring parameters and reports of the measurement result for a service data flow (i.e., QoS Flow) and can be enabled based on third-party application requests and/or operator policies configured in the 5GC (i.e. PCF).
The AF may request measurements and subscribe to the event for one or more of the following QoS monitoring parameters by means of the Nnef_AfsessionWithQoS service at reference point N33 or the Npcf_PolicyAuthorization service at reference point N5, which may trigger QoS monitoring for service data flow(s):
Uplink packet delay, downlink packet delay and round-trip packet delay for a service data flow (see clause 5.45.2 of TS 23.501 [23]).
Congestion (see clause 5.45.3 of TS 23.501 [23]).
Data Rate (see clause 5.45.4 of TS 23.501 [23]).
Packet Delay Variation (see clause 5.37.7 of TS 23.501 [23]).
Round-trip packet delay considering the uplink path of one service data flow and the downlink path of another service data flow (see clause 5.37.4 of TS 23.501 [23]).
Using the QoS monitoring mechanisms of the 5G Core, the above parameters can be derived and further exposed to the AF via the PCF or the UPF (directly or further via NEF) as requested.

## Slide 46: Collaboration for L4S
As described in RFC 9330 [149], RFC 9331 [150] and RFC 9332 [151], the purpose of ECN marking for L4S (Low Latency, Low Loss and Scalable Throughput) is to inform a recipient host at the earliest opportunity that an IP packet has experienced network congestion at some point in its routing path. It exposes congestion information by marking ECN bits in the IP header of the user IP packets between the UE and the Application Server. This early notification may be used by the receiving application to report the congestion to its sending peer using a suitable Layer 4 feedback mechanism. Based on this feedback, the sender should reduce the sending bit rate. In the context of adaptive segmented media delivery, application layer rate adaptation may be needed in addition.
For example, a media player consuming a media presentation that receives an ECN-marked downlink packet from a streaming media server may induce a reduction in the sender’s bit rate by switching to a representation of a lower bit rate. To support this functionality, the recipient host needs to support L4S feedback as described in RFC 9330 [149].
Furthermore, early notification of congestion reflected back to an Application Server may be used to improve the current delivery process or to facilitate session establishment for new clients. For example, if significant congestion is detected, the 5GMS AS may update the DASH presentation manifest to remove/add one or more representations.
L4S is based on the idea that delay is mainly caused by the classic congestion control algorithms introduced with TCP. L4S replaces these traditional congestion control algorithms with a class of scalable congestion control algorithms.
The L4S architecture relies on three components to operate:
A scalable congestion control algorithm,
A modified ECN marking behaviour,
An active queue management algorithm that isolates L4S traffic
L4S (Low Latency, Low Loss and Scalable Throughput)

## Slide 47: L4S in deployments
Currently, only Apple platforms have functionality that allows access to ECN status through IP packet metadata [154]. With the proliferation of L4S, it is expected that more APIs will be introduced to enable this access.
This API allows applications to:
Enable ECN metadata access through connection parameters.
Access raw ECN flags from each received packet.
Distinguish between all ECN codepoints (Non-ECT, ECT(0), ECT(1), and CE).
The ECN flags follow the standard encoding defined in RFC 3168 [30]:
00: Not-ECN-Capable Transport (Non-ECT)
10: ECN Capable Transport (0)
01: ECN Capable Transport (1)
11: Congestion Experienced (CE)
For L4S deployment in media delivery, applications can use this API to implement appropriate congestion control responses to ECN marks.
import Network class ECNMonitor { var connection: NWConnection? func setupConnection(to endpoint: NWEndpoint) { // Create connection parameters let parameters = NWParameters() parameters.allowLocalEndpointReuse = true // Enable IP metadata for ECN access parameters.requireIPMetadata = true // Create the connection connection = NWConnection(to: endpoint, using: parameters) // Set up receive handler connection?.receiveMessage { [weak self] content, context, isComplete, error in if let context = context { // Get IP metadata from context let metadata = context.protocolMetadata.first { $0 is NWProtocolIP.Metadata } as? NWProtocolIP.Metadata if let metadata = metadata { // Access ECN flags using nw_ip_metadata_get_ecn_flag let ecnFlag = nw_ip_metadata_get_ecn_flag(metadata) // Interpret ECN flags switch ecnFlag { case 0: // Non-ECT print("Packet is Not-ECN-Capable Transport (Non-ECT)") case 1: // ECT(1) print("Packet is ECN Capable Transport (1)") case 2: // ECT(0) print("Packet is ECN Capable Transport (0)") case 3: // CE print("Packet has Congestion Experienced (CE)") default: print("Unknown ECN flag value") } } } // Continue receiving … } // Start the connection connection?.start(queue: .main) } … }
APIs exists

## Slide 48: Conclusions
This Key Issue has explored several QoS features which could be beneficial to the Media Delivery System, including:
1. ECN marking for L4S,
2. PDU Set handling and
3. QoS monitoring.
Detailed description of the above features is provided in clause 5.23.1.2. High-level call flows for features 1 and 3 are documented in clause 5.23.4, and corresponding gaps are analysed in clause 5.23.5. Finally, candidate solutions to address the identified gaps are provided in clause 5.23.6.
Based on the study of improved QoS support for Media Streaming services, it is recommended to make the following changes to normative specifications.
At stage 2 in TS 26.501 [15]:
1. Integrate ECN marking for L4S into the architectures, high-level call flows and collaboration scenarios for both 5GMSd and 5GMSu.
2. Integrate the QoS monitoring feature into the architectures, high-level call flows and collaboration scenarios for both 5GMSd and 5GMSu.
At stage 3 in TS 26.510 [108]:
1. Integrate ECN marking for L4S into the procedures for both 5GMSd and 5GMSu.
2. Integrate the QoS monitoring feature into the procedures for both 5GMSd and 5GMSu.

## Slide 49: Stage-2 Work
L4S in downlink and uplink streaming

## Slide 50: WT13: Impacts and opportunities of QUIC for segmented content delivery
Description:
  Since the finalisation of the QUIC protocol by the IETF in May 2021, there has been significant deployments of QUIC driven by the usage of HTTP/3 for streaming services. In the IETF, the working group on Media Over QUIC (MOQ) is working towards an extensible protocol for publishing media for ingest and distribution. While QUIC is mostly used today as the underlying protocol of HTTP/3, there is still open questions as to how media segments are delivered over QUIC streams when using HTTP/3 but also considering other QUIC-based protocols such as MOQ. Considering different types of media application, e.g. multi-stream use cases, will be of interest. Studying the various strategies for delivering segmented content over QUIC streams will also bring insights for the network management aspects. For instance, findings in this domain may be relevant to WT#2.1 in the ongoing study in SA2 called FS_XRM_Ph2 (SP-231671) whose deliverable is available as TR 23.700-70.
Companies interested: Xiaomi, Qualcomm, others
Work Topic lead: Emmanouil Potetsianakis, Xiaomi
5G-MAG Interest and Involvement:

## Slide 51: Collaboration Scenarios

## Slide 52: Conclusions
QUIC is a widely deployed and supported protocol built on top of UDP [32]. For the QUIC-aware approaches on delivering segmented media the following technologies have been identified:
MPEG-DASH over HTTP/3 with server push and priority information.
MPEG-DASH Part 6 over WebTransport.
Media-over-QUIC.
Push-based adaptive media streaming over WebTransport with server-side throughput estimation.
The maturity of these technologies varies, from using features of QUIC in existing solutions, to research prototypes built on QUIC and WebTransport. As a result, it appears from the candidate solutions that there is no obvious path at the time of writing for enhancing segmented delivery by leveraging the emergence of the QUIC protocol.
Due to the diversity of the technologies and their different stages of maturity, it is recommended that the following aspects are further studied:
1. The standardized definitions of QUIC client and server APIs and their availability on the market.
2. The standardized definitions of WebTransport client and server APIs and their availability on the market.
3. The fragmentation of QUIC implementations (both on the client and server side) and their performance for segmented media delivery.
4. Evaluation of the identified candidate technologies with regards to QoE metrics (start-up delay, stalling events, etc.).
5. The impact of reporting qlog metrics via the downlink interface (M4) to the UE (bidirectional streams).

## Slide 53: WT6: In-session Unicast Repair for MBS Object Distribution

## Slide 54: WT6: In-session Unicast Repair for MBS Object Distribution
Description:
  For live and low-latency live services using the Object Distribution Method in MBS, in certain cases the transmission of an object is not successful. In this case, unicast repair for individual MBS Clients can improve the service quality. However, the timing of such requests needs to be carefully studied in order to avoid network overloads or significant latencies in the delivery. A study to extend MBS User Services and object streaming to address in-session repair is of relevance.
Companies interested: Qualcomm, Telecom Italia, Comcast, Orange, BBC, SWR, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 55: WT6: In-session Unicast Repair for MBS Object Distribution
1. The MBS Client identifies the end of the MBS Distribution Session. The latest time for this is the value of the @Expires attribute indicated in the root element of the FDT Instance document. However, according to clause 9.3.2 of TS 26.346 [7], an MBS Client may determine an earlier end of transmission of files,
2. The MBS Client identifies that data is missing from an MBS Object Distribution Session for one or multiple FLUTE transmission objects delivered in the Object Distribution Session following the principles in clause 9.3.3 of TS 26.346 [7].
3. The MBS Client shall select an MBS AS instance repair URL randomly from the list of object‌Repair‌Base‌Locators if present in the ObjectRepair object defined in table 5.2.8-1.
4. For each incomplete FLUTE transmission object defined by a File element in the FDT Instance document and as identified in step 2:
a) The MBS Client shall form the network location location (URL) of the repair object as defined in clause 6.4.2.4 using (i) the value of the File@Content-Location attribute, (ii) the repair URL selected in step 3 (if any) and (iii) the value of object‌Distribution‌Base‌Locator as distribution URL if present in the ObjectRepair object defined in table 5.2.8-1.
b) The MBS Client shall define an appropriate list of byte ranges Range[M] with M the number of independent ranges and Range[m].start the start of the mth range and Range[m].end the end of the mth range from the repair object using the list of received symbols and additional information from the FDT as defined in clause 6.4.2.5.
5. The MBS Client shall then use the object repair procedures as defined as defined in clause 10.2.2 using the following parameters:
- The offsetTime and randomTimePeriod parameters indicated in the ObjectRepair object as defined in table 5.2.8-1.
- For each incomplete FLUTE transmission object in the FDT Instance document, the MBSTF Client shall use from the corresponding FDT File entry the network location location formed in step 4a, the size of the transmission object (in bytes), the entity tag value and the minimal list of byte ranges Range[M] determined in step 4b.
6. The MBS Client uses the received list of byte ranges and the received data in the MBS Object Distribution Session to recover the missing object as defined in clause 6.4.2.6.
Background Post-Session Repair  Need to do this in-session

## Slide 56: Conclusions
Clause 4.2.6 of TS 26.502 [29] defines object repair. However, only a post-session repair procedure is defined up to and including Release 18; in-session object repair procedures are declared as being for further study. Accordingly, clause 6.2.4 of TS 26.517 [30] defines an object repair mechanism for FLUTE, but only a post-session repair procedure is defined in clause 6.2.4.2; in-session object repair procedures in clause 6.2.4.3 are for further study.
For live and low-latency live services using the Object Distribution Method in MBS, in certain cases the transmission of an object is not completely successful. In this case, unicast repair for individual MBS Clients can improve the service quality.
It is recommended to support in-session unicast repair in a future version of MBS User Services. For this purpose, the candidate solutions documented in clause 5.9.6 are recommended to be implemented.
For stage-2 impact:
Gap#1 in clause 5.9.5 is expected to be addressed by the candidate solution in clause 5.9.6:
a. Defining a new reference point in TS 26.502 [29].
b. Documenting call flows and procedures for both post-session and in-session unicast repair.
Stage-3 impact is expected to address gaps #2, #3 and #5 in clause 5.9.5 in TS 26.346 [16] and TS 26.517 [30] based on the candidate solutions in clause 5.9.6.
On gap #2 identified in clause 5.9.5, both of the following signalling options are expected to be supported:
Using FDT parameters to signal the time when repairs can be requested using the Expires attribute).
Using LCT header information to signal the time when repairs can be requested using the B-Flag.
On gap #3 identified in clause 5.9.5, the following signalling options exist in the FLUTE File Delivery Table (FDT):
Defining an new FDT extensions parameter to signal the availability time when the object needs to be released.
On gap #4 identified in clause 5.9.5, the execution of MBS object delivery and in-session unicast repair can run in parallel in the MBS Client. However, this should be validated if there are cases this is not the case and whether these cases need to be explicitly stated, for example reduced capability (RedCaP) UEs.
On gap #5 identified in clause 5.9.5, time synchronization can reuse functionalities defined in TS 26.346 [16], but tighter synchronization than 1 second. This work is aligned with the findings and work in clause 5.11.3.6.

## Slide 57: Architecture and Call flows

## Slide 58: WT7: MBS User Service and Delivery Protocols for eMBMS

## Slide 59: WT7: MBS User Service and Delivery Protocols for eMBMS
Description:
  The MBS User Service architecture and protocol follows the modern design philosophies of the 5G System with separation of user services from transport, a service-based architecture and RESTful APIs. At the same time, eMBMS and enTV as used for LTE-based 5G Broadcast support a transparent delivery mode. While interworking in between MBMS and MBS is addressed in TS 23.247, interworking between these two systems at the User Service level is not addressed. In order for MBMS and LTE-based 5G broadcast to leverage MBS User Service technologies, a study is warranted to identify the gaps to fully support this functionality.
Companies interested: : Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 60: WT7: MBS User Service and Delivery Protocols for eMBMS
Open Questions
  Extensions to MBS User Service to support interworking
  Operation of MBS delivery protocols on top of MBMS an 5G Broadcast
  Extension of MBS User service protocols to address common issues and having a common delivery protocol specification for multicast and broadcast.
  Specific needs from 5G Broadcast?
Background – Interworking of MBS and MBMS in TS 23.247, clause 5.2

## Slide 61: WT8: Selected MBMS Functionalities not supported in MBS

## Slide 62: WT8: Selected MBMS Functionalities not supported in MBS
Description:
  In completing TS 26.502 and TS 26.517, it is obvious that only a subset of the MBMS functionalities is supported in Rel-17. While many MBMS functionalities are likely not important to be supported for MBS, a systematic analysis of MBMS User Services features and their potential relevance for MBS should be completed and recommendations made on which ones to migrate to MBS User Services specifications and how best to achieve this.
Companies interested: : Qualcomm, Comcast, SWR, EBU, Rohde&Schwarz, ATEME
Work Topic lead: Thomas Stockhammer
5G-MAG Interest and Involvement:

## Slide 63: Issues not going normative

## Slide 64: WT2: Common Server-and Network-Assisted Streaming
Description:
  MPEG-DASH supports Server and Network Assisted DASH (SAND). Certain profiles of SAND were adopted in TS 26.247, but the industry has generalized the concepts in SAND in efforts such as Content Steering (see ETSI TS 103 998), Web Application Video Ecosystem (WAVE) specification for Common Media Server Data (CMSD), or Addressable Resource Index (ARI) Tracks in MPEG. The study and integration of these technologies into the Media Delivery System and MBS/MBMS workflows is of significant interest, in particular also in combination with existing QoS mechanisms.
Companies interested: Qualcomm, Dolby, AT&T, Comcast, Tencent, ATEME, Sony Europe B.V.
Work Topic lead: Iraj Sodagar, Tencent
5G-MAG Interest and Involvement:
Overview

## Slide 65: User Experience – Content & Device Aware Streaming and Delivery
Controlled fairness of players
A couple of good pointers and resources:
  TR 26.949
  Content-Aware Encoding (Yuriy Reznik, Brightcove)
  Achieving Great Video Quality Without Breaking the Bank (AWS)
  Netflix: Optimized shot-based encodes: Now Streaming!
Take into account devices, users, content, resources, subscription models, latency, etc. for overall quality improvement
Content Complexity
Radio Resources
Device Consumption
GBR QoS?
CBR
CVBR
CAE
AI and Big data may help

## Slide 66: ARI Track - Motivation
The following aspects are observed
  In several cases there is a desire that an adaptive streaming client has exact knowledge of the duration and size of addressable resources and possible a subset of those on the server.
  Addressable Resources are Track Files, Segments or Chunks in the CMAF context, but apply equally to DASH or HLS.
  For on-demand services, an exact map of this information may be provided by the Segment Index.
Segment Index is not sufficient. Examples include:
  A solution is required for different operation modes: low-latency live, live, time-shifted, VoD
  The solution is expected to work for different target latency of the client
  The client and network address to operate in different network conditions
  The message also includes information on the content quality
See ISO/IEC 23009-1 5th Edition

## Slide 67: ARI Track in live mode
DASH Packager
CH
CIC
CNC
CNC
CIC
CNC
CNC
CNC
CIC
CNC
CNC
CNC
CIC
HTTP Chunk
HTTP Chunk
DASH Segment
Encoder
CH
CIC
CNC
CNC
CIC
CNC
CNC
CIC
CNC
CNC
CIC
CNC
CNC
ARI Track
1
2
Delay
1
2
Delay
3
Chunking
Segments
1
2
3
Time-Shift
Delay

## Slide 68: WT4: Modem Usage Optimized Media Streaming
Description:
  In Rel-18, basic support for Background Data Transfer is added. UE power resources are constrained, and media delivery typically also results in power consumption if the radio is always connected. In order to better support streaming services, requests and access to the modem and the resources should be well balanced. Enhancements to Background Data Transfer to support preload as well as functionality of what is defined in W3C Managed Media Source Extension to minimize active network connections are relevant topics to study with the aim of limiting battery consumption in the UE resulting from media delivery.
Companies interested: Qualcomm, Dolby, Comcast, BBC, EBU, Tencent
Work Topic lead: Iraj Sodagar, Tencent
5G-MAG Interest and Involvement:
Core Issues
  Basic support for Background Data Traffic in Rel-18

## Slide 69: WT4: Modem Usage Optimized Media Streaming
Please see the presentation from WWDC 2023 and MSE GitHub issue.
Discussion in W3C
  https://www.w3.org/2023/07/25-me-minutes.html
    … Tests showed that power usage would go up with MSE, so viewing time would reduce. We can never introduce a regression on iPhone
    … We were given constraints: if we play a YouTube video on iPhone with MSE enabled, we shouldn't see a power regression
    … We tried various ways, and what we found was the primary reason why the power is used, is websites get one segment at a time rather than downloading in bursts
    … The main power usage is when the cellular modem is on. So we looked at how HLS downloads data, it downloads quite a big chunk, then stops
    … 5G is more power hungry than 4G or 3G, it will download more seconds then shut down
    … Apple still wanted to have control, but provide hints. We didn't enable MSE on iPhone, as we'd have those issues
    … MMS provides hints: "start fetching content", "i have enough", "stop fetching content"
    … We wanted to enable on 5G, do we need a carrot and stick approach? If the website does the wrong thing, and finds a way around it, shut it off completely, and don't enable MSE and fallback to HLS
  https://github.com/w3c/media-source/
  https://www.w3.org/TR/media-source-2/#managedmediasource-interface
Support in dash.js
  https://github.com/Dash-Industry-Forum/dash.js/issues/4202
Background Managed Media Source

## Slide 70: WT9: DASH/HLS Interoperability
Description:
  DASH/HLS interoperability is a key issue to support highly scalable distribution systems for CDN-based distribution as well as for MBS/MBMS distribution. Offering common CMAF segments that can be consumed by both DASH and HLS media players promises to address these issues. However, detailed nuances need to be identified to ensure optimized delivery and CTA WAVE has provided detailed guidelines in CTA-5005-A to support this matter. Studying these guidelines and understanding the impacts on the 5GMS System as well as MBS/MBMS distribution is of relevance. In addition, formats and techniques supporting DASH/HLS interoperability such as MPEG-DASH part 9 (ReAP) may be taken into account.
Companies interested: Qualcomm, Telecom Italia, Comcast, Orange, BBC, EBU, Rohde&Schwarz, Huawei Technologies Co Ltd., Tencent
Work Topic lead: Iraj Sodagar
5G-MAG Interest and Involvement:

## Slide 71: WT9: DASH/HLS Interoperability
Background

## Slide 73: Outlook

## Slide 74: Advanced Media Delivery  Media Delivery Architecture
How can 5G/6G networks be integrated and combined with modern media delivery systems
3GPP Advanced Media Delivery
Common Client Metadata.
Common Server-and Network-Assisted Streaming.
Multi-Access Media Delivery.
Media Delivery from multiple service endpoints/location.
Modem Usage Optimized Media Streaming.
DASH/HLS Interoperability.
Further harmonization of RTC and Streaming for Advanced Media Delivery.
Improved QoS support for Media Streaming services.
QUIC-based segmented media delivery.
In-band signalling of QoS for 5G Media Streaming.
Dynamic content generation from multiple sources.
In-session Unicast Repair for MBS Object Distribution.
MBS User Service and Delivery Protocols for eMBMS.
Selected MBMS Functionalities not supported in MBS.
https://aws.amazon.com/blogs/media/improve-your-viewers-live-streaming-experience-with-media-quality-aware-resiliency/
Example: Amazon Delivery System architecture
3GPP, 5G and 6G should be compatible with modern media delivery
Collaboration with media organizations (SVTA, DVB?)
5G-MAG should be a facilitator to connect the media industry