## Slide 1: On the Support of IVAS Immersive Split Audio Rendering in MTSI Based Real-Time Communication
Dolby Laboratories Inc.
Agenda: 7.5

## Slide 2: Outline
Recap of IVAS/ISAR Split Immersive Audio rendering feature
  Immersive Audio Split Rendering Scenarios
  Functional overview of IVAS Split Immersive Audio Rendering
  IVAS/ISAR Split Immersive Audio Rendering Specifications
RTP and SDP aspects of IVAS split rendering feature
  Suggested RTP payload format definitions
  Suggested SDP parameter definitions
  MTSI aspects and example call-flows
  Relation with ongoing SR_IMS work
Note: This revision addresses comments received during the joint RTC/Audio SWG telco on Feb. 5 and updates slides 3-7.

## Slide 3: Immersive Audio Split Rendering Scenarios
3GPP TR 26.865 (Immersive Audio for Split Rendering Scenarios; Requirements) describes various non-standalone audio connectivity scenarios
  Non-standalone/split rendering architectures may be attractive for end devices with strict power-constraints or with limited computing resources
  All of the non-standalone scenarios are characterized by an underlying split audio rendering architecture where immersive audio decoding, rendering and head-tracked binaural playback is distributed among at least two of the following entities
    End device/TWS Earbuds or Headphones with pose estimator and binaural decoding/post rendering capabilities
    5G UE with immersive audio decoding and head-tracked pre-rendering capabilities or pass-through
    Cloud/Edge node with immersive audio decoding and head-tracked pre-rendering capabilities
    Note: 5G UE and End device may, e.g. be connected through 5G sidelink
  These scenarios are addressed by the IVAS codec split rendering feature and the ISAR stand-alone split rendering feature
This document presents a realization proposal of IVAS immersive audio SR in MTSI based real-time communication

## Slide 4: Example Voice Call Scenario with IVAS Split Immersive Audio Rendering in Terminal
(Remote) UE 1
UE 2A with presentation engine
UE 2B (with accelerometer, Gyro sensor)/End device
In this example UE 1 is a 5G UE with immersive audio encoding/decoding capabilities
Example split rendering scenario as mentioned in TR 26.865
Head tracked binaural rendering split between UE 2A and UE 2B
The SR downlink from UE 2A to UE 2B may be beyond IMS connectivity layer control
UE 2A is a 5G UE with immersive audio decoding and pre-rendering capabilities.
On uplink, this UE may simply forward the immersive bitstream from UE 2B to UE 1 and may only modify/add E byte OR PI data OR both.
Towards UE1, UE 2A/2B may virtually appear as one entity (UE 2)
UE 2B is a light-weight device with computational constraints for e.g., HMD or earbuds
5G sidelink or non-3GPP connection

## Slide 5: Example Voice/Conf Call Scenario with IVAS Split Immersive Audio Rendering in MRF
(Remote) UE 1
MRF with presentation engine
UE 2B (with accelerometer, Gyro sensor)/End device
In this example, UE 1 is a 5G UE with immersive audio encoding/decoding capabilities
Example split rendering scenario as mentioned in TR 26.865
Head tracked binaural rendering split between MRF and UE 2B
The SR downlink from MRF to UE 2B is assumed to be IMS controlled and may or may not rely on IMS DC
MRF may be inserted in the media path to carry out
  Immersive audio decoding, mixing and pre-rendering
MRF may filter SDP and RTP traffic between UE 1 and UE 2B
  On uplink, MRF may simply forward the immersive bitstream from UE 2B to UE 1 and may only modify/add E byte OR PI data OR both.
UE 2B is a light-weight 5G device with computational constraints for e.g., HMD or ear buds
MRF

## Slide 6: Example Messaging/Streaming Scenario with IVAS Split Immersive Audio Rendering in Terminal (non-MTSI case)
MRF
UE 2A with presentation engine
UE 2B (with accelerometer, Gyro sensor)/End device
Cloud/edge node, e.g. MRF, storing immersive audio bitstream
Example split rendering scenario as mentioned in TR 26.865
Head tracked binaural rendering split between UE 2A and UE 2B
The SR downlink from UE 2A to UE 2B may be beyond IMS connectivity layer control
UE 2A is a 5G UE with immersive audio decoding and pre-rendering capabilities.
On uplink, this UE may simply receive head tracking information from UE 2B.
Towards UE1, UE 2A/2B may virtually appear as one entity (UE 2)
UE 2B is a light-weight device with computational constraints for e.g., HMD or earbuds
5G sidelink or non-3GPP connection

## Slide 7
MRF
UE 2B (with accelerometer, Gyro sensor)/End device
Example split rendering scenario as mentioned in TR 26.865
Head tracked binaural rendering split between MRF and UE 2B
The SR downlink from MRF to UE 2B is assumed to be IMS controlled and may or may not rely on IMS DC
In case not using IMS DC, the SDP/RTP mechanism proposed in Annex A to TS 26.253 also represents a viable solution
Cloud/edge node, e.g. MRF, storing immersive audio bitstream and also having immersive audio decoding and pre-rendering capabilities.
UE 2B is a light-weight 5G device with computational constraints for e.g., HMD or earbuds
5G link
Example Messaging/Streaming Scenario with IVAS Split Immersive Audio Rendering in MRF (non-MTSI case)

## Slide 8: Functional overview of IVAS Split Immersive Audio Rendering
Blocks outside presentation engine and end device are shown only for illustration and are not part of IVAS or ISAR implementation (Figure taken from TS26.253).

## Slide 9: IVAS/ISAR Split Immersive Audio Rendering Specifications
Immersive Audio Split Rendering is a 3GPP Rel-18 feature specified
  As part of IVAS codec
    TS 26.253: Detailed Algorithmic Description including RTP payload format and SDP parameter definitions
    TS 26.258: C code (floating-point)
  As stand-alone feature
    TS 26.249: Immersive Audio for Split Rendering Scenarios; Detailed Algorithmic Description of Split Rendering Functions
  Related 3GPP TRs:
    TR 26.865: Immersive Audio for Split Rendering Scenarios; Requirements
    TR 26.996: Immersive Audio for Split Rendering Scenarios; Performance characterization
RTP/SDP aspects of IVAS Immersive Audio for Split Rendering still being finalized under Rel-19 IVAS_Codec_Ph2 work item

## Slide 10: Suggested RTP payload format definitions
A proposal (S4-241961) has been made and been reviewed at SA4#130 adding SR support to IVAS RTP payload format definition,
  Adding an SR indicator to ToC byte to indicate subsequent SR-ToC byte, indicating
    Diegetic/non-diegetic attribute of SR payload
    Bit rate of SR payload
  Extending E-byte (CMR) mechanism, enabling (for reverse link)
    SR bit rate requests
    SR configurations requests, controlling diegetic/non-diegetic attribute and pose correction axes
  Making use of Reverse direction HEAD_ORIENTATION PI data as one mechanism to convey head-tracker from lightweight end device to presentation engine (pre-renderer)

## Slide 11: Suggested SDP parameter definitions
A proposal (S4-241961) has been made and been reviewed at SA4#130 adding SR support to IVAS SDP parameter definitions, adding
  “SR” to IVAS coded formats (cf)
  SR specific parameters
    sr-dof: Specifying the number of degrees of freedom supported in the head-tracked split rendering session
    sr-tc: Specifying the codec format ‘LCLD’ or ‘LC3plus’ for the binaural transport channels to be used in the session along with max bit rate setting and further parameters of the transport codecs
  SR related offer-answer considerations, specifying rules
    That in an SDP answer “SR” shall not be combined with other IVAS coded formats
    That sr-dof in an answer may be identical to sr-dof in offer or indicate a lower capability
    That sr-tc in an offer shall be open or offer both codec formats ( ‘LCLD’ and ‘LC3plus’) for the binaural transport channels
      An offer from pre-rendering entity shall list the two codec formats in preference order according to defaults associated with pre-rendering domain.
      An offer from the light-weight device shall be open and not include sr-tc at all.
    That sr-tc in an answer shall indicate a single codec format (either ‘LCLD’ or ‘LC3plus’) for the binaural transport channels to be used in the session along with a max bit rate equal or lower than in the offer (if present in the offer)
      An answer from pre-rendering entity shall indicate the default codec format according to pre-rendering domain.
Note: The present proposal has been slightly updated compared to the proposal of Tdoc S4-241961 and a correspondingly revised CR is planned for S4#131 meeting.

## Slide 12: MTSI aspects
An exception will be introduced to the rule that cf-recv shall
  Be open or list all coded formats in offer, or
  List all offered coded formats in answer.
The exception will be that cf-recv in either offer or answer from a lightweight device may either list SR as the only coded format or list all other offered coded formats.
As SR sessions are typically limited to one direction between two directly connected nodes/end points of an IVAS codec session, only directional parameters shall be used to negotiate an IVAS session with SR on that connection.
  When an SR session is accepted, the SDP answer shall not contain any other session parameters for the direction towards the lightweight end device than SR related parameters, PI data related parameters and cmr.
  The other direction (from the lightweight device) remains unconstrained with the only exception that directional parameters shall be used to specify the session on it.

## Slide 13: Relation with ongoing SR_IMS work
Draft TS 26.567v0.4.0 (Split rendering over IMS)
  Relies on Data Channel support, which is optional for MTSI
  Defines a Metadata DC Message Format based on generic metadata formats defined in 26.119, e.g. for pose.
  Defines high-level session establishment procedures assuming DC usage
  Has focus on
    XR with (potentially) a larger multitude of split rendering metadata messages (objects)
    Network-based IMS resources such as Media Function (MF), DC Application Server (DC-AS, DC Signalling Function (DCSF)
For IVAS SR, we propose three steps:
  Specify RTP and SDP means and MTSI support as for other IVAS operations modes, initially not requiring DC support. This
    Is conceptually coherent with current RTP/SDP and MTSI support of IVAS
    Addresses the important case where presentation engine executing IVAS decoding and split pre-rendering is implemented on 5G UE rather than using IMS network resources
    Focuses on (possibly audio-only) immersive telephony and conferencing
    Is assumed to build the basis for later extension to DC support and usage of IMS network resources for pre-rendering
  Specify IVAS SR (and ISAR SR) relying on DC and provisions defined under split rendering over IMS work and focusing on IMS network resource usage for pre-rendering
  Indicate in 26.114 potential preferences for either of the two approaches under given conditions

## Slide 14: Example call-flows
  See S4aR250054_SR call flows.docx